Cisco BTS 10200 Softswitch Release 4.1 CD Jumpstart Procedure for Duplex Systems

August 28, 2004

Corporate Headquarters

Cisco Systems, Inc.

170 West Tasman Drive

San Jose, CA 95134-1706

USA

http://www.cisco.com

Tel: 	408 526-4000

800 553-NETS (6387)

Fax:	408 526-4100

THE SPECIFICATIONS AND INFORMATION REGARDING THE PRODUCTS IN THIS MANUAL ARE SUBJECT TO CHANGE WITHOUT NOTICE. ALL STATEMENTS, INFORMATION, AND RECOMMENDATIONS IN THIS MANUAL ARE BELIEVED TO BE ACCURATE BUT ARE PRESENTED WITHOUT WARRANTY OF ANY KIND, EXPRESS OR IMPLIED. USERS MUST TAKE FULL RESPONSIBILITY FOR THEIR APPLICATION OF ANY PRODUCTS.

THE SOFTWARE LICENSE AND LIMITED WARRANTY FOR THE ACCOMPANYING PRODUCT ARE SET FORTH IN THE INFORMATION PACKET THAT SHIPPED WITH THE PRODUCT AND ARE INCORPORATED HEREIN BY THIS REFERENCE. IF YOU ARE UNABLE TO LOCATE THE SOFTWARE LICENSE OR LIMITED WARRANTY, CONTACT YOUR CISCO REPRESENTATIVE FOR A COPY.

The Cisco implementation of TCP header compression is an adaptation of a program developed by the University of California, Berkeley (UCB) as part of UCB’s public domain version of the UNIX operating system. All rights reserved. Copyright © 1981, Regents of the University of California.

NOTWITHSTANDING ANY OTHER WARRANTY HEREIN, ALL DOCUMENT FILES AND SOFTWARE OF THESE SUPPLIERS ARE PROVIDED “AS IS” WITH ALL FAULTS. CISCO AND THE ABOVE-NAMED SUPPLIERS DISCLAIM ALL WARRANTIES, EXPRESSED OR IMPLIED, INCLUDING, WITHOUT LIMITATION, THOSE OF MERCHANTABILITY, FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT OR ARISING FROM A COURSE OF DEALING, USAGE, OR TRADE PRACTICE.

IN NO EVENT SHALL CISCO OR ITS SUPPLIERS BE LIABLE FOR ANY INDIRECT, SPECIAL, CONSEQUENTIAL, OR INCIDENTAL DAMAGES, INCLUDING, WITHOUT LIMITATION, LOST PROFITS OR LOSS OR DAMAGE TO DATA ARISING OUT OF THE USE OR INABILITY TO USE THIS MANUAL, EVEN IF CISCO OR ITS SUPPLIERS HAVE BEEN ADVISED OF THE POSSIBILITY OF SUCH DAMAGES.

CCIP, CCSP, the Cisco Arrow logo, the Cisco Powered Network mark, the Cisco Systems Verified logo, Cisco Unity, Follow Me Browsing, FormShare, iQ Breakthrough, iQ FastTrack, the iQ Logo, iQ Net Readiness Scorecard, Networking Academy, ScriptShare, SMARTnet, TransPath, and Voice LAN are trademarks of Cisco Systems, Inc.; Changing the Way We Work, Live, Play, and Learn, The Fastest Way to Increase Your Internet Quotient, and iQuick Study are service marks of Cisco Systems, Inc.; and Aironet, ASIST, BPX, Catalyst, CCDA, CCDP, CCIE, CCNA, CCNP, Cisco, the Cisco Certified Internetwork Expert logo, Cisco IOS, the Cisco IOS logo, Cisco Press, Cisco Systems, Cisco Systems Capital, the Cisco Systems logo, Empowering the Internet Generation, Enterprise/Solver, EtherChannel, EtherSwitch, Fast Step, GigaStack, Internet Quotient, IOS, IP/TV, iQ Expertise, LightStream, MGX, MICA, the Networkers logo, Network Registrar, Packet, PIX, Post-Routing, Pre-Routing, RateMUX, Registrar, SlideCast, StrataView Plus, Stratm, SwitchProbe, TeleRouter, and VCO are registered trademarks of Cisco Systems, Inc. and/or its affiliates in the U.S. and certain other countries.

All other trademarks mentioned in this document or Web site are the property of their respective owners. The use of the word partner does not imply a partnership relationship between Cisco and any other company. (0301R)

Cisco BTS 10200 Softswitch Software Upgrade

Copyright © 2004, Cisco Systems, Inc.

All rights reserved.

Table of Contents

Table of Contents	4

Preface	5

Obtaining Documentation	5

World Wide Web	5

Documentation CD-ROM	5

Ordering Documentation	5

Documentation Feedback	6

Obtaining Technical Assistance	6

Cisco.com	6

Technical Assistance Center	7

Cisco TAC Web Site	7

Cisco TAC Escalation Center	8

Chapter 1	9

Audience	9

Document Conventions	10

Supported Hardware	10

Example of Rack-Mounting Configuration	11

Jumpstart Requirements	12

Before You Start	14

Jumpstarting the Element Management System Platforms	15

Jumpstarting the Primary Element Management System	15

Installing the Solaris Operating System	15

Finishing the Solaris Installation on the EMS	16

Jumpstarting the Secondary Element Management System	16

Jumpstarting the Call Agent and Feature Server Platforms	17

Jumpstarting the Primary Call Agent and Feature Server	17

Installing the Solaris Operating System	17

Finishing the Solaris Installation	18

Jumpstarting the Secondary Call Agent and Feature Server	18

Setting Up the Files for Element Management System Configuration	18

Configuring the Primary Element Management System	21

Configuring the Secondary Element Management System	22

Configuring the Primary Call Agent and Feature Server Installation	24

Configuring the Secondary Call Agent and Feature Server Installation	24

Preface

# Obtaining Documentation

These sections explain how to obtain documentation from Cisco Systems.

### World Wide Web

You can access the most current Cisco documentation on the World Wide Web at this URL: http://www.cisco.com/

Translated documentation is available at this URL: http://www.cisco.com/public/countries_languages.shtml

### Documentation CD-ROM

Cisco documentation and additional literature are available in a Cisco Documentation CD-ROM package, which is shipped with your product. The Documentation CD-ROM is updated monthly and may be more current than printed documentation. The CD-ROM package is available as a single unit or through an annual subscription.

### Ordering Documentation

You can order Cisco documentation in these ways:

Registered Cisco.com users (Cisco direct customers) can order Cisco product documentation from the Networking Products MarketPlace: http://www.cisco.com/cgi-bin/order/order_root.pl

Registered Cisco.com users can order the Documentation CD-ROM through the online Subscription Store: http://www.cisco.com/go/subscription

Nonregistered Cisco.com users can order documentation through a local account representative by calling Cisco Systems Corporate Headquarters (California, U.S.A.) at 408 526-7208 or, elsewhere in North America, by calling 800 553-NETS (6387).

### Documentation Feedback

You can submit comments electronically on Cisco.com. In the Cisco Documentation home page, click the Fax or Email option in the “Leave Feedback” section at the bottom of the page.

You can e-mail your comments to mailto:bug-doc@cisco.com.

You can submit your comments by mail by using the response card behind the front cover of your document or by writing to the following address:

Cisco Systems, INC.

Attn: Document Resource Connection

170 West Tasman Drive

San Jose, CA 95134-9883

# Obtaining Technical Assistance

Cisco provides Cisco.com as a starting point for all technical assistance. Customers and partners can obtain online documentation, troubleshooting tips, and sample configurations from online tools by using the Cisco Technical Assistance Center (TAC) Web Site. Cisco.com registered users have complete access to the technical support resources on the Cisco TAC Web Site: http://www.cisco.com/tac

### Cisco.com

Cisco.com is the foundation of a suite of interactive, networked services that provides immediate, open access to Cisco information, networking solutions, services, programs, and resources at any time, from anywhere in the world.

Cisco.com is a highly integrated Internet application and a powerful, easy-to-use tool that provides a broad range of features and services to help you with these tasks:

- Streamline business processes and improve productivity

- Resolve technical issues with online support

- Download and test software packages

- Order Cisco learning materials and merchandise

- Register for online skill assessment, training, and certification programs

If you want to obtain customized information and service, you can self-register on Cisco.com. To access Cisco.com, go to this URL: http://www.cisco.com/

### Technical Assistance Center

The Cisco Technical Assistance Center (TAC) is available to all customers who need technical assistance with a Cisco product, technology, or solution. Two levels of support are available: the Cisco TAC Web Site and the Cisco TAC Escalation Center.

Cisco TAC inquiries are categorized according to the urgency of the issue:

- Priority level 4 (P4)—You need information or assistance concerning Cisco product capabilities, product installation, or basic product configuration.

- Priority level 3 (P3)—Your network performance is degraded. Network functionality is noticeably impaired, but most business operations continue.

- Priority level 2 (P2)—Your production network is severely degraded, affecting significant aspects of business operations. No workaround is available.

- Priority level 1 (P1)—Your production network is down, and a critical impact to business operations will occur if service is not restored quickly. No workaround is available.

The Cisco TAC resource that you choose is based on the priority of the problem and the conditions of service contracts, when applicable.

### Cisco TAC Web Site

You can use the Cisco TAC Web Site to resolve P3 and P4 issues yourself, saving both cost and time. The site provides around-the-clock access to online tools, knowledge bases, and software. To access the Cisco TAC Web Site, go to this URL: http://www.cisco.com/tac

All customers, partners, and resellers who have a valid Cisco service contract have complete access to the technical support resources on the Cisco TAC Web Site. The Cisco TAC Web Site requires a Cisco.com Log in ID and password. If you have a valid service contract but do not have a Log in ID or password, go to this URL to register:  http://tools.cisco.com/RPF/register/register.do

If you are a Cisco.com registered user, and you cannot resolve your technical issues by using the Cisco TAC Web Site, you can open a case online by using the TAC Case Open tool at this URL: http://www.cisco.com/tac/caseopen

If you have Internet access, we recommend that you open P3 and P4 cases through the Cisco TAC Web Site: http://www.cisco.com/tac

### Cisco TAC Escalation Center

The Cisco TAC Escalation Center addresses priority level 1 or priority level 2 issues. These classifications are assigned when severe network degradation significantly impacts business operations. When you contact the TAC Escalation Center with a P1 or P2 problem, a Cisco TAC engineer automatically opens a case.

To obtain a directory of toll-free Cisco TAC telephone numbers for your country, go to this URL: http://www.cisco.com/warp/public/687/Directory/DirTAC.shtml

Before calling, please check with your network operations center to determine the level of Cisco support services to which your company is entitled: for example, SMARTnet, SMARTnet Onsite, or Network Supported Accounts (NSA). When you call the center, please have available your service agreement number and your product serial number.

Chapter 1

This procedure is used for jumpstarting all duplex application platforms, using a CD, prior to installing the Cisco BTS 10200 Softswitch software. The jumpstart procedure is based on the Solaris 8 operating environment.

Caution This is not an upgrade procedure. Performing the steps in this procedure brings down the platform and stops call processing. Proceed only if this is acceptable. Do not run this procedure on an active system that is carrying live traffic. If you have questions, contact Cisco TAC.

This installation removes all existing applications and data. There is no backing out once you execute this procedure. If data is present, perform a data backup using the applicable procedure in the Cisco BTS 10200 Softswitch Operations Manual before you start this procedure.

If you are reinstalling an existing Cisco BTS 10200 Softswitch software version following this jumpstart, you can restore the Cisco BTS 10200 Softswitch data that was previously backed up. Follow the procedure in the Cisco BTS 10200 Softswitch Operations Manual.

If you are installing a new software version following this jumpstart, data previously backed up will become obsolete and cannot be restored on the new software. Data must be reprovisioned. You can restore data backups performed after the software installation in the usual manner.

Note We recommend that you back up data that has been restored or reprovisioned following software installation.

# Audience

This document is intended for system administrators, or those responsible for installing, the Cisco BTS 10200 Softswitch.

# Document Conventions

This document uses the following conventions:

Caution Means reader take note. Notes contain helpful suggestions or references to material not covered in the manual.

Note Means reader be careful. In this situation, you might do something that could result in equipment damage or loss of data.

# Supported Hardware

The following host machines are supported by the Cisco BTS 10200 Softswitch. See the Jumpstart Requirements section for additional details.

• Sun SunFire V120 or Netra 120

• Sun Netra 20

• Sun Fire 1280

• Sun Netra 1405

• Continuous Computing (CCPU) AXmp

# Example of Rack-Mounting Configuration

Figure 1  shows an example of Cisco BTS 10200 Softswitch hardware. Racks may vary depending upon the specific hardware used and local rack-mounting requirements.

Figure 1 Cisco BTS 10200 Softswitch—Example of Rack-Mounting Configuration

# Jumpstart Requirements

Table 1  lists the specific Softswitch platforms to jumpstart. Your system administrator will identify the specific jumpstart server to use for this procedure, and the hostnames and IP addresses of the Element Management System (EMS) and the Call Agent or Feature Server (CA/FS) units to jumpstart.

| Table 1 Platforms and Requirements for Jumpstart |
| --- |
| Platforms | Minimum Requirements for Small Platform |
| Side A (primary) EMS, Side B (secondary) EMS, Side A (primary) CA/FS, and Side B (secondary) CA/FS | Sun SunFire V120 or Netra 120 with 2 GB of RAM, 2 36-GB hard disk, and 2 Ethernet interfaces |

| Platforms | Minimum Requirements for Medium Platform Using Sun Systems |
| --- | --- |
| Side A (primary) EMS, Side B (secondary) EMS, Side A (primary) CA/FS, and Side B (secondary) CA/FS | Sun Netra 20 T4 with 4 GB of RAM, 2 73-GB hard disk, and 2 Ethernet interfaces |

| Platforms | Minimum Requirements for Medium Platform Using Continuous Systems |
| --- | --- |
| Side A (primary) EMS, Side B (secondary) EMS, Side A (primary) CA/FS, and Side B (secondary) CA/FS | CCPU AXmp with 4 GB of RAM, 2 36-GB hard disk, and 2 Ethernet interfaces |

| Platforms | Minimum Requirements for Sun Fire 1280 Systems |
| --- | --- |
| Side A (primary) EMS, Side B (secondary) EMS, Side A (primary) CA/FS, and Side B (secondary) CA/FS | Sun Fire 1280 with 8 GB of RAM At least 4 1.2GHZ CPUs Two 72GB disk drives, one CD-ROM drive Two Sun quad NICs for CA, one quad for EMS |

# Before You Start

The following prerequisites must be satisfied before you start this jumpstart procedure.

Note We recommend that you completely read through this procedure before starting any steps.

This installation procedure should be performed by a user experienced in basic UNIX commands. Some of the steps require the involvement of the system administrator. Before you begin this procedure, perform the following tasks:

• Verify that your system meets the requirements specified in the Jumpstart Requirements section.

• A user experienced in basic UNIX commands should perform this procedure.

• Ensure that the Cisco BTS 10200 Softswitch hardware components are set up and turned on in accordance with manufacturer recommendations.

• Make sure you have the Cisco BTS 10200 Release4.1 Solaris 8 Boot CD and the Cisco BTS 10200 Release4.1 Install CD.

• Ensure that you have a network installation data sheet (NIDS) provided by Cisco.

• By default, jumpstart will set all interfaces on Solaris box at autonegotiation. If you choose to use forced 100MB full-duplex, you need to set all interfaces on Solaris boxes and both Cisco switches to use forced 100 full-duplex.

Note Enter all commands as shown; some commands are case sensitive. Press Enter at the end of each command.

# Jumpstarting the Element Management System Platforms

This section describes how to jumpstart the Cisco BTS 10200 Softswitch EMS platforms.

## Jumpstarting the Primary Element Management System

To jumpstart the primary EMS, complete the following steps.

#### Installing the Solaris Operating System

To install the Solaris operating system onto the Cisco BTS 10200 Softswitch, perform the following procedure.

Step 1 Power on the system and bring it down to an ok> prompt. Insert the Cisco BTS 10200 Release4.1Solaris 8 Boot CD into the CD-ROM drive

Step 2 Type the following commands to install the Solaris 8 operating system (OS):

ok> boot cdrom - install

The process takes approximately 30-45 minutes.

Note By default, the OS will assign the system the host name bts10200 and the IP address and with the default root password opticall.

Step 3 Edit the following file to change the host name and ip address to match your Network Information Data Sheet (NIDS): /etc/nodename, /etc/hosts, /etc/netmasks, /etc/hostname.<primary interface>. Usually the primary interface is hme0, eri0 or ce0.

Step 4 To Find out the primary interface on your system, type the following command:

ifconfig -a.

Step 5 Reboot the system.

Step 6 Insert the BTS 10200 Release 4.1 Install CD into the CD-ROM drive.

Step 7 Log in as root.

Step 8 Make a directory

# mkdir /cdrom

Step 9 Mount the CD:

# mount -F hsfs -o ro /dev/dsk/c0t6d0s0 /cdrom

OR

# mount –F hsfs –o ro /dev/dsk/c0t0d0s0 /cdrom

#### Finishing the Solaris Installation on the EMS

In this section you will finish the Solaris Installation.

Step 1 Change directories by entering the following command:

# cd /cdrom/EMS

Step 2 Finish the installation on the EMS by entering the following command:

# ./EMS_finish.sh

Step 3 Reboot the system.

#### Jumpstarting the Secondary Element Management System

Repeat the procedure in the Jumpstarting the Primary Element Management System  section, on the console of the secondary EMS

# Jumpstarting the Call Agent and Feature Server Platforms

This section describes how to jumpstart the Cisco BTS 10200 Softswitch CA/FS platforms.

## Jumpstarting the Primary Call Agent and Feature Server

To jumpstart the primary CA/FS, complete the following steps on the console of the primary CA/FS.

#### Installing the Solaris Operating System

To install the Solaris operating system onto the Cisco BTS 10200 Softswitch, perform the following procedure.

Step 1 Power on the system and bring it down to an ok> prompt. Insert the Cisco BTS 10200 Release4.1 Solaris 8 Boot CD into the CD-ROM drive

Step 2 Type the following commands to install the Solaris 8 operating system (OS):

ok> boot cdrom - install

The process takes approximately 30-45 minutes.

Note By default, the OS will assign the system the host name bts10200 and the IP address and with the default root password opticall.

Step 3 Edit the following file to change the host name and ip address to match your Network Information Data Sheet (NIDS): /etc/nodename, /etc/hosts, /etc/netmasks, /etc/hostname.<primary interface>. Usually the primary interface is hme0 , eri0 or ce0.

Step 4 To find out the primary interface on your system, type the following command:

ifconfig -a.

Step 5 Reboot the system.

Step 6 Insert the Cisco BTS 10200 Release4.1 Install CD into the CD-ROM drive.

Step 7 Log in as root.

Step 8 Make a directory:

# mkdir /cdrom

Step 9 Mount a CD:

# mount -F hsfs -o ro /dev/dsk/c0t6d0s0 /cdrom

OR

# mount –F hsfs –o ro /dev/dsk/c0t0d0s0 /cdrom

#### Finishing the Solaris Installation

In this section you will finish the Solaris Installation.

Step 1 Change directories by entering the following command:

# cd /cdrom/CA

Step 2 Finish the installation on the CA by entering the following command

# ./CA_finish.sh

Step 3 Reboot the system.

#### Jumpstarting the Secondary Call Agent and Feature Server

Repeat the procedure in the Jumpstarting the Primary Call Agent and Feature Server  section on the console of the secondary CA/FS.

#### Setting Up the Files for Element Management System Configuration

To set up files needed to configure the EMS, complete the following steps.

Step 1 Login as root on Primary EMS.

Step 2    Navigate to the /opt/setup directory by entering the following command:

cd /opt/setup

Step 3 Edit the hostconf file by entering the following command:

TERM=vt100

Export TERM

vi hostconfig

Edit the hostconfig file as appropriate with the information found in the NIDS. The references to ENDFIX are the last octet of the particular computing element IP address found in network 1 of the NIDS.

Step 4 Save and exit the hostconfig file.

Step 5 Generate the hosts file by entering the following command:

./hostgen.sh

Note: If the netmask of all networks are not 255.255.255.0, then manual editing /tmp/hosts and /tmp/netmasks files is required.

Example:

##### /tmp/netmasks file ###########

192.168.100.0		255.255.255.128

192.168.200.0 	255.255.255.192

Step 6 Change directory by entering the following command:

cd /tmp

Step 7 Verify that /tmp/host has the correct values by comparing them to the values in the NIDS.

Step 8 Use the FTP command to go to the IP address of the secondary EMS by entering the following command:

ftp <secems IP address>

Step 9 Log in as root by entering the following command:

root

Step 10 Change directory by entering the following command:

cd /tmp

Step 11 Upload the hosts file to the remote host by entering the following command:

put host

Step 12 Upload the netmasks file to the remote host by entering the following command:

put netmasks

Step 13  Upload the rhosts file to the remote host by entering the following command:

put rhost

Step 14  Upload the ntp.conf file to the remote host by entering the following command:

put ntp.conf

Step 15 Exit by entering the following command:

bye

Step 16 Use the FTP command to go to the IP address of the primary Call Agent by entering the following command:

ftp <prica IP address>

Step 17 Log in as root by entering the following command:

root

Step 18 Change directory by entering the following command:

cd /tmp

Step 19 Repeat Step 11 through Step 14  .

Step 20 Exit by entering the following command:

bye

Step 21 Use the FTP command to go to the IP address of the secondary IP address.

ftp <secca IP address>

Step 22 Log in as root by entering the following command:

root

Step 23 Change directory by entering the following command:

cd /tmp

Step 24 Repeat Step 11 through Step 14  .

Step 25 Exit by entering the following command:

bye

#### Configuring the Primary Element Management System

To configure the primary EMS, complete the following steps:

Step 1  Login as root.

Step 2 Change directory by entering the following command:

cd /opt/setup

Step 3 Run the following script to set up the interfaces by entering the following command:

./setlogic_EMS.sh

Step 4 Verify that the /etc/netmasks and /etc/hosts files have the correct values by comparing them to the values in the NIDS.

Step 5 Set up the mirror for the EMS by entering the following command:

./setup_mirror_ems

Note Do not reboot your system if an error occurs. You must fix the error before moving to the next step.

Step 6 Set up the transparent metadevice (transmeta) for the EMS by entering the following command:

./setup_mirror_trans

Step 7 Reboot by entering the following command:

reboot -- -r

Note Wait for the boot before continuing. Then log in to the EMS of the side in which you are working.

Step 8 Log in to the primary EMS as root.

root

Step 9 Change directory by entering the following command:

cd /opt/setup

Step 10 Synchronize the disk by entering the following command:

./sync_mirror

Note Wait for the disks to synchronize before continuing. The synchronization can be verified by running the Resync_status command from the /opt/utils directory. The display will show the resyncing in progress and report resync completion.

Step 11 Exit the primary EMS.

#### Configuring the Secondary Element Management System

To configure the secondary EMS, complete the following steps.

Step 1  Login as root.

Step 2 Navigate to the /opt/setup directory by entering the following command:

cd /opt/setup

Step 3 Run the following script to set up the interfaces.

./setlogic_EMS.sh

Step 4 Verify that the /etc/netmask and /etc/hosts commands have the correct values.

Step 5 Set up a mirror for the EMS by entering the following command:

./setup_mirror_ems

Step 6  Set up the transparent metadevice (transmeta) for the EMS by entering the following command:

./setup_mirror_trans

Note Do not reboot your system if an error occurs. You must fix the error before moving to the next step.

Step 7 Reboot your system by entering the following command:

reboot -- -r

Note Wait for the boot to finish before continuing. Then log in to the EMS for the side on which you are working.

Step 8 Log in to the secondary EMS as root by entering the following command:

root

Step 9 Change directory by entering the following command:

cd /opt/setup

Step 10 Synchronize the disk by entering the following command:

./sync_mirror

Step 11 Exit the secondary EMS.

#### Configuring the Primary Call Agent and Feature Server Installation

To configure the primary CA and FS, complete the following steps.

Step 1    Login as root.

Step 2 Change directories by entering the following command:

cd /opt/setup

Step 3 Run the following script to set up the interfaces.

./setlogic_CA.sh

Step 4 Verify that the /etc/netmask, /etc/defaultrouter, and /etc/hosts files have the correct values by comparing them to the values in the NIDS. Make sure all three match the NIDS.

Step 5 Set up the mirror for the CA/FS and watch for errors by entering the following command:

./setup_mirror_ca

Note Do not reboot your system if an error occurs. You must fix the error before moving to the next step.

Step 6 Setup trans for the CA/FS and watch for errors by entering the following command:

./setup_trans

Step 7 Reboot your system by entering the following command:

reboot

Step 8 Log in to the primary CA as root by entering the following command:

root

Step 9 Mirror the disks as follows:

a. Change directory by entering the following command:

cd /opt/setup

b. Mirror the disks by entering the following command:

./sync_mirror

#### Configuring the Secondary Call Agent and Feature Server Installation

To configure the primary CA and FS, complete the following steps.

Step 1    Login as root.

Step 2 Change directories by entering the following command:

cd /opt/setup

Step 3 Run the following script to set up the interfaces.

./setlogic_CA.sh

Step 4 Verify that the /etc/netmask, and /etc/hosts files have the correct values by comparing them to the values in the NIDS. Make sure all three match the NIDS.

Step 5 Set up the mirror for the CA/FS and watch for errors by entering the following command:

./setup_mirror_ca

Note Do not reboot your system if an error occurs. You must fix the error before moving to the next step.

Step 6 Setup trans for the CA/FS and watch for errors by entering the following command:

./setup_trans

Step 7 Reboot your system by entering the following command:

reboot

Step 8 Log in to the secondary CA as root by entering the following command:

root

Step 9 Mirror the disks as follows:

a. Change directory by entering the following command:

cd /opt/setup

b. Mirror the disks by entering the following command:

./sync_mirror

Copyright © 2004 Cisco Systems, Inc. All rights reserved.