Cisco BTS 10200 Softswitch Software Upgrade of Release

4.2.0.V11 to 4.4.1.V10

August 25,  2005

Corporate Headquarters

Cisco Systems, Inc.

170 West Tasman Drive

San Jose, CA 95134-1706

USA

http://www.cisco.com

Tel: 	408 526-4000

800 553-NETS (6387)

Fax:	408 526-4100

THE SPECIFICATIONS AND INFORMATION REGARDING THE PRODUCTS IN THIS MANUAL ARE SUBJECT TO CHANGE WITHOUT NOTICE. ALL STATEMENTS, INFORMATION, AND RECOMMENDATIONS IN THIS MANUAL ARE BELIEVED TO BE ACCURATE BUT ARE PRESENTED WITHOUT WARRANTY OF ANY KIND, EXPRESS OR IMPLIED. USERS MUST TAKE FULL RESPONSIBILITY FOR THEIR APPLICATION OF ANY PRODUCTS.

THE SOFTWARE LICENSE AND LIMITED WARRANTY FOR THE ACCOMPANYING PRODUCT ARE SET FORTH IN THE INFORMATION PACKET THAT SHIPPED WITH THE PRODUCT AND ARE INCORPORATED HEREIN BY THIS REFERENCE. IF YOU ARE UNABLE TO LOCATE THE SOFTWARE LICENSE OR LIMITED WARRANTY, CONTACT YOUR CISCO REPRESENTATIVE FOR A COPY.

The Cisco implementation of TCP header compression is an adaptation of a program developed by the University of California, Berkeley (UCB) as part of UCB’s public domain version of the UNIX operating system. All rights reserved. Copyright © 1981, Regents of the University of California.

NOTWITHSTANDING ANY OTHER WARRANTY HEREIN, ALL DOCUMENT FILES AND SOFTWARE OF THESE SUPPLIERS ARE PROVIDED “AS IS” WITH ALL FAULTS. CISCO AND THE ABOVE-NAMED SUPPLIERS DISCLAIM ALL WARRANTIES, EXPRESSED OR IMPLIED, INCLUDING, WITHOUT LIMITATION, THOSE OF MERCHANTABILITY, FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT OR ARISING FROM A COURSE OF DEALING, USAGE, OR TRADE PRACTICE.

IN NO EVENT SHALL CISCO OR ITS SUPPLIERS BE LIABLE FOR ANY INDIRECT, SPECIAL, CONSEQUENTIAL, OR INCIDENTAL DAMAGES, INCLUDING, WITHOUT LIMITATION, LOST PROFITS OR LOSS OR DAMAGE TO DATA ARISING OUT OF THE USE OR INABILITY TO USE THIS MANUAL, EVEN IF CISCO OR ITS SUPPLIERS HAVE BEEN ADVISED OF THE POSSIBILITY OF SUCH DAMAGES.

CCIP, CCSP, the Cisco Arrow logo, the Cisco Powered Network mark, the Cisco Systems Verified logo, Cisco Unity, Follow Me Browsing, FormShare, iQ Breakthrough, iQ FastTrack, the iQ Logo, iQ Net Readiness Scorecard, Networking Academy, ScriptShare, SMARTnet, TransPath, and Voice LAN are trademarks of Cisco Systems, Inc.; Changing the Way We Work, Live, Play, and Learn, The Fastest Way to Increase Your Internet Quotient, and iQuick Study are service marks of Cisco Systems, Inc.; and Aironet, ASIST, BPX, Catalyst, CCDA, CCDP, CCIE, CCNA, CCNP, Cisco, the Cisco Certified Internetwork Expert logo, Cisco IOS, the Cisco IOS logo, Cisco Press, Cisco Systems, Cisco Systems Capital, the Cisco Systems logo, Empowering the Internet Generation, Enterprise/Solver, EtherChannel, EtherSwitch, Fast Step, GigaStack, Internet Quotient, IOS, IP/TV, iQ Expertise, LightStream, MGX, MICA, the Networkers logo, Network Registrar, Packet, PIX, Post-Routing, Pre-Routing, RateMUX, Registrar, SlideCast, StrataView Plus, Stratm, SwitchProbe, TeleRouter, and VCO are registered trademarks of Cisco Systems, Inc. and/or its affiliates in the U.S. and certain other countries.

All other trademarks mentioned in this document or Web site are the property of their respective owners. The use of the word partner does not imply a partnership relationship between Cisco and any other company. (0301R)

Cisco BTS 10200 Softswitch Software Upgrade

Copyright © 2005, Cisco Systems, Inc.

All rights reserved.

| Revision History |
| --- |
| Date | Version | Revised By | Description |
| 2/1/2005 | 1.0 | Jack Daih | Initial Version |
| 2/24/2005 | 2.0 | Jack Daih | Added disk preparation steps |
| 3/17/2005 | 3.0 | Jack Daih | Removed users.tar file extraction since it is being done by the DoTheChange script. |
| 3/30/2005 | 4.0 | Jack Daih | Added extra steps to handle OS patch from 117000-05 to 117350-18 |
| 4/5/2005 | 5.0 | Jack Daih | Added comment for the table radius-profile after row count auditing. The table will be synced from EMS in the “Finalize Upgrade” Chapter 8. |
| 4/11/2005 | 6.0 | Jack Daih | Added additional steps to handle new OS patches that require reboot |
| 8/18/2005 | 7.0 | Jack Daih | Resolved defects: CSCsb62143, CSCsb62129 |
| 8/19/2005 | 8.0 | Jack Daih | Resolved defect CSCsb62176 |
| 8/23/2005 | 9.0 | Jack Daih | Correct typo in referring Appendix J |
| 8/24/2005 | 10.0 | Jack Daih | Correct type in Chapter 2 in the prerequisite section from 4.5.0 to 4.4.1. |

Table of Contents

Table of Contents	4

Preface	9

Obtaining Documentation	9

World Wide Web	9

Documentation CD-ROM	9

Ordering Documentation	9

Documentation Feedback	10

Obtaining Technical Assistance	10

Cisco.com	10

Technical Assistance Center	11

Cisco TAC Web Site	11

Cisco TAC Escalation Center	12

Chapter 1	1

Upgrade Requirements	1

Introduction	1

Assumptions	3

Requirements	3

Important notes about this procedure	4

Chapter 2	5

Preparation	5

Prerequisites	5

Chapter 3	7

Complete one week before the scheduled upgrade	7

Task 1: Pre-construct opticall.cfg for the system to be upgraded to 4.4.1 release	7

Chapter 4	8

Prepare System for Upgrade	8

Task 1: Verify System Status	8

Task 2: Backup user account	8

From EMS Side A	9

Task 3: Pre-check tables	9

From Active EMS	9

Chapter 5	11

Upgrade Side B Systems	11

Task 1: Inhibit EMS mate communication	11

From EMS side A	11

Task 2: Disable Oracle DB replication	11

From EMS side A	11

Task 3: Force side A systems to be active	12

From Active EMS Side B	12

Task 4: Stop applications and shutdown EMS Side B	13

From EMS side B	13

Task 5: Stop applications and shutdown CA/FS Side B	13

From CA/FS side B	13

Task 6: Upgrade EMS side B to the new release	14

From EMS side B	14

Task 7: Upgrade CA/FS Side B to the new release	19

From CA/FS side B	20

Task 8: Migrate oracle data	25

From EMS side B	25

Task 9: To install CORBA on EMS side B, please follow Appendix I.	26

Chapter 6	27

Prepare to Upgrade Side A system	27

Task 1: Force side A system to standby	27

From EMS side A	27

Task 2: Validate release 4.4.1 software operation	28

From EMS side B	28

Chapter 7	29

Upgrade Side A Systems	29

Task 1: Shutdown EMS Side A	29

From EMS Side A	29

Task 2: Shutdown CA/FS Side A	30

From CA/FS side A	30

Task 3: Upgrade EMS side A to the new release	30

From EMS side A	30

Task 4: Upgrade CA/FS side A to the new release	35

From CA/FS side A	35

Task 5: Copying oracle data	40

From EMS side A	40

Task 6: Restore Hub communication	41

From EMS Side B	41

Task 7: To install CORBA on EMS side A, please follow Appendix I.	41

Chapter 8	42

Finalizing Upgrade	42

Task 1: Switchover activity from side B to side A	42

From EMS side B	42

Task 2: Enable Oracle DB replication	42

From EMS side B	42

Task 3: Synchronize handset provisioning data	43

From EMS side A	43

Task 4: Restore the system to normal mode	44

From EMS side A	44

Task 5: Restore customized cron jobs	44

Task 6: Verify system status	45

Appendix A	46

Check System Status	46

From Active EMS side A	46

Appendix B	48

Check Call Processing	48

From EMS side A	48

Appendix C	50

Check Provisioning and Database	50

From EMS side A	50

Check transaction queue	50

Perform database audit	51

Appendix D	52

Check Alarm Status	52

From EMS side A	52

Appendix E	54

Check Oracle Database Replication and Error Correction	54

Check Oracle DB replication status	54

From EMS side A	54

Correct replication error	55

From EMS Side B	55

From EMS Side A	55

Appendix F	57

Check and Sync System Clock	57

Task 1: Check system clock	57

From each machine in a BTS system	57

Task 2: Sync system clock	57

From each machine in a BTS system	57

Appendix G	58

Backout Procedure for Side B Systems	58

Introduction	58

Task 1: Force side A systems to active	59

From EMS side B	60

Task 2: SFTP Billing records to a mediation device	60

From EMS side B	60

Task 3: Sync DB usage	60

From EMS side A	60

Task 4: Shutdown side B systems	61

From EMS side B	61

From CA/FS side B	61

Task 5: Restore side B systems to the old release	61

From CA/FS side B	61

From EMS side B	62

Task 6: Restore EMS mate communication	62

From EMS side A	62

Task 7: Switchover activity to EMS side B	63

From Active EMS side A	63

Task 8: Enable Oracle DB replication on EMS side A	63

From EMS side A	63

Task 9: Synchronize handset provisioning data	64

From EMS side B	64

Task 10: Switchover activity from EMS side B to EMS side A	65

From EMS side B	65

Task 11: Restore system to normal mode	65

From EMS side A	65

Task 12: Verify system status	65

Appendix H	67

System Backout Procedure	67

Introduction	67

Task 1: Disable Oracle DB replication on EMS side B	67

From Active EMS	67

From EMS side B	68

Task 2: Inhibit EMS mate communication	68

From EMS side B	68

Task 3: Force side B systems to active	68

From EMS side A	69

Task 4: FTP Billing records to a mediation device	69

From EMS side A	69

Task 5: Shutdown side A systems	69

From EMS side A	70

From CA/FS side A	70

Task 6: Restore side A systems to the old release	70

From CA/FS side A	70

From EMS side A	71

Task 7: Inhibit EMS mate communication	71

From EMS side A	71

Task 8: Disable Oracle DB replication on EMS side A	71

From EMS side A	72

Task 9: To continue fallback process, please follow Appendix G.	72

Appendix I	73

CORBA Installation	73

Task 1: Open Unix Shell on EMS	73

Task 2: Install OpenORB CORBA Application	73

Remove Installed OpenORB Application	73

Install OpenORB Packages	74

Appendix J	76

Preparing Disks for Upgrade	76

Side A EMS preparation steps	76

Side B EMS preparation steps	78

Side A CA/FS preparation steps	79

Side B CA/FS preparation steps	80

Appendix K	82

Disk Mirroring after Upgrade	82

Configuring the Primary Element Management System	82

Configuring the Secondary Element Management System	83

Configuring the Primary Call Agent and Feature Server Installation	84

Configuring the Secondary Call Agent and Feature Server Installation	85

Preface

# Obtaining Documentation

These sections explain how to obtain documentation from Cisco Systems.

### World Wide Web

You can access the most current Cisco documentation on the World Wide Web at this URL: http://www.cisco.com/

Translated documentation is available at this URL: http://www.cisco.com/public/countries_languages.shtml

### Documentation CD-ROM

Cisco documentation and additional literature are available in a Cisco Documentation CD-ROM package, which is shipped with your product. The Documentation CD-ROM is updated monthly and may be more current than printed documentation. The CD-ROM package is available as a single unit or through an annual subscription.

### Ordering Documentation

You can order Cisco documentation in these ways:

Registered Cisco.com users (Cisco direct customers) can order Cisco product documentation from the Networking Products MarketPlace: http://www.cisco.com/cgi-bin/order/order_root.pl

Registered Cisco.com users can order the Documentation CD-ROM through the online Subscription Store: http://www.cisco.com/go/subscription

Nonregistered Cisco.com users can order documentation through a local account representative by calling Cisco Systems Corporate Headquarters (California, U.S.A.) at 408 526-7208 or, elsewhere in North America, by calling 800 553-NETS (6387).

### Documentation Feedback

You can submit comments electronically on Cisco.com. In the Cisco Documentation home page, click the Fax or Email option in the “Leave Feedback” section at the bottom of the page.

You can e-mail your comments to mailto:bug-doc@cisco.com.

You can submit your comments by mail by using the response card behind the front cover of your document or by writing to the following address:

Cisco Systems, INC.

Attn: Document Resource Connection

170 West Tasman Drive

San Jose, CA 95134-9883

# Obtaining Technical Assistance

Cisco provides Cisco.com as a starting point for all technical assistance. Customers and partners can obtain online documentation, troubleshooting tips, and sample configurations from online tools by using the Cisco Technical Assistance Center (TAC) Web Site. Cisco.com registered users have complete access to the technical support resources on the Cisco TAC Web Site: http://www.cisco.com/tac

### Cisco.com

Cisco.com is the foundation of a suite of interactive, networked services that provides immediate, open access to Cisco information, networking solutions, services, programs, and resources at any time, from anywhere in the world.

Cisco.com is a highly integrated Internet application and a powerful, easy-to-use tool that provides a broad range of features and services to help you with these tasks:

- Streamline business processes and improve productivity

- Resolve technical issues with online support

- Download and test software packages

- Order Cisco learning materials and merchandise

- Register for online skill assessment, training, and certification programs

If you want to obtain customized information and service, you can self-register on Cisco.com. To access Cisco.com, go to this URL: http://www.cisco.com/

### Technical Assistance Center

The Cisco Technical Assistance Center (TAC) is available to all customers who need technical assistance with a Cisco product, technology, or solution. Two levels of support are available: the Cisco TAC Web Site and the Cisco TAC Escalation Center.

Cisco TAC inquiries are categorized according to the urgency of the issue:

- Priority level 4 (P4)—You need information or assistance concerning Cisco product capabilities, product installation, or basic product configuration.

- Priority level 3 (P3)—Your network performance is degraded. Network functionality is noticeably impaired, but most business operations continue.

- Priority level 2 (P2)—Your production network is severely degraded, affecting significant aspects of business operations. No workaround is available.

- Priority level 1 (P1)—Your production network is down, and a critical impact to business operations will occur if service is not restored quickly. No workaround is available.

The Cisco TAC resource that you choose is based on the priority of the problem and the conditions of service contracts, when applicable.

### Cisco TAC Web Site

You can use the Cisco TAC Web Site to resolve P3 and P4 issues yourself, saving both cost and time. The site provides around-the-clock access to online tools, knowledge bases, and software. To access the Cisco TAC Web Site, go to this URL: http://www.cisco.com/tac

All customers, partners, and resellers who have a valid Cisco service contract have complete access to the technical support resources on the Cisco TAC Web Site. The Cisco TAC Web Site requires a Cisco.com Log in ID and password. If you have a valid service contract but do not have a Log in ID or password, go to this URL to register: http://www.cisco.com/register/

If you are a Cisco.com registered user, and you cannot resolve your technical issues by using the Cisco TAC Web Site, you can open a case online by using the TAC Case Open tool at this URL: http://www.cisco.com/tac/caseopen

If you have Internet access, we recommend that you open P3 and P4 cases through the Cisco TAC Web Site: http://www.cisco.com/tac

### Cisco TAC Escalation Center

The Cisco TAC Escalation Center addresses priority level 1 or priority level 2 issues. These classifications are assigned when severe network degradation significantly impacts business operations. When you contact the TAC Escalation Center with a P1 or P2 problem, a Cisco TAC engineer automatically opens a case.

To obtain a directory of toll-free Cisco TAC telephone numbers for your country, go to this URL: http://www.cisco.com/warp/public/687/Directory/DirTAC.shtml

Before calling, please check with your network operations center to determine the level of Cisco support services to which your company is entitled: for example, SMARTnet, SMARTnet Onsite, or Network Supported Accounts (NSA). When you call the center, please have available your service agreement number and your product serial number.

Chapter 1

Upgrade Requirements

# Introduction

Application software loads are designated as Release 900-aa.bb.cc.Vxx, where

aa=major release number, for example, 01

bb=minor release number, for example, 03

cc=maintenance release, for example, 00

Vxx=Version number, for example V04

This procedure can be used on an in-service system, but the steps must be followed as shown in this document in order to avoid traffic interruptions.

|  | Caution Performing the steps in this procedure will bring down and restart individual platforms in a specific sequence. Do not perform the steps out of sequence, as it could affect traffic. If you have questions, contact Cisco support. |
| --- | --- |

This procedure should be performed during a maintenance window.

|  | Note In this document, the following designations are used: EMS = Element Management System; CA/FS = Call Agent / Feature Server Primary is also referred to as "Side A" Secondary is also referred to as "Side B" See Figure 1-1 for a front view of the Softswitch rack. |
| --- | --- |

Figure 1-1   Cisco BTS 10200 Softswitch—Rack Configuration

# Assumptions

The following assumptions are made.

- The installer has a basic understanding of UNIX and Oracle commands.

- The installer has the appropriate user name(s) and password(s) to log on to each EMS/CA/FS platform as root user, and as Command Line Interface (CLI) user on the EMS.

|  | Note Contact Cisco support before you start if you have any questions. |
| --- | --- |

# Requirements

Verify that opticall.cfg has the correct information for each of the following machines.

- Side A EMS

- Side B EMS

- Side A CA/FS

- Side B CA/FS

Determine the oracle and root passwords for the systems you are upgrading. If you do not know these passwords, ask your system administrator.

Refer to local documentation to determine if CORBA installation is required on this system. If unsure, ask your system administrator.

# Important notes about this procedure

Throughout this procedure, each command is shown with the appropriate system prompt, followed by the command to be entered in bold. The prompt is generally one of the following:

- Host system prompt (<hostname>#)

- Oracle prompt (<hostname>$)

- SQL prompt (SQL>)

- CLI prompt (CLI>)

- SFTP prompt (sftp>)

Note the following conventions used throughout the steps in this procedure:

- Enter commands as shown, as they are case sensitive (except for CLI commands).

- Press the Return (or Enter) key at the end of each command, as indicated by " ".

It is recommended that you read through the entire procedure before performing any steps.

It will take approximately 5 hours to complete the entire upgrade process. Please plan accordingly to minimize any negative service impacts.

CDR delimiter customization is not retained after software upgrade. The customer or Cisco engineer must manually customize again to keep the same customization.

There will be no CLI provisioning allowed during entire upgrade process.

Chapter 2

Preparation

This chapter describes the tasks a user must complete at least two weeks before the scheduled upgrade.

Each customer must purchase 8 disks with matching disk size to the existing system that is to be upgraded.

# Prerequisites

- Eight hard disk drives with Cisco BTS 10200 release 4.4.1 pre-staged. Each set of 2 disks must have the same model number in order for disk mirroring to work. Each disk must be prepared in a hardware platform that matches the target system to be upgraded.  Please refer to Appendix J for disk preparation steps.

  - Two disk drives for EMS side A

Pre-installed Solaris 2.8 with patch level Generic_117000-05

Pre-installed EMS application software and databases

- Two disk drives for EMS side B

Pre-installed Solaris 2.8 with patch level Generic_117000-05

Pre-installed EMS application software and databases

- Two disk drives for CA/FS side A

Pre-installed Solaris 2.8 with patch level Generic_117000-05

Pre-installed secure shell

Pre-staged release 4.4.1 load

- Two disk drives for CA/FS side B

Pre-installed Solaris 2.8 with patch level Generic_117000-05

Pre-installed Secure shell

Pre-staged release 4.4.1 load

- Completed Network Information Data Sheets for release 4.4.1.

- There is secure shell (ssh) access to the Cisco BTS 10200 system.

- There is console access to each Cisco BTS 10200 machine.

- Network interface migration has been completed from 2/2 to 4/2.

Chapter 3

# Complete one week before the scheduled upgrade

This chapter describes the tasks a user must complete one week prior to the scheduled upgrade.

# Task 1: Pre-construct opticall.cfg for the system to be upgraded to 4.4.1 release

Step 1   Get a copy of the completed Network Information Data Sheets (NIDS)

Step 2   Get a copy of the new opticall.cfg file for release 4.4.1

Step 3   Fill in value for each parameter defined in the opticall.cfg using data from Network Information Data Sheets and then place the file on the Network File Server (NFS).

|  | Note New parameters added to the 4.4.1 release: NAMED_ENABLED MARKET_TYPE TIMER_B TIMER_F PRIMARY_NTP_SERVER SECONDARY_NTP_SERVER |
| --- | --- |

Chapter 4

Prepare System for Upgrade

Suspend all CLI provisioning activity during the entire upgrade process.

This chapter describes the steps a user must complete the morning or the night before the scheduled upgrade.

# Task 1: Verify System Status

Step 1   Verify that the side A systems are in the active state. Use Appendix A for the detailed verification steps.

Step 2   Verify that call processing is working without error. Use Appendix B for the detailed verification steps.

Step 3   Verify that provisioning system is functioning normally. Use Appendix C for the detailed verification steps.

Step 4   Verify that there are no outstanding major or critical alarms. Use Appendix D for the detailed verification steps.

Step 5   Verify that Oracle database and its replication functions are working properly. Use Appendix E for the detailed verification steps.

Step 6   Verify that the system clock is synchronized between each machines in the system. Use Appendix F for the detailed verification steps.

|  | Caution Do not continue until the above verifications have been made. Call Cisco support if you need assistance. |
| --- | --- |

# Task 2: Backup user account

The user accounts saved in this task is to be restored to side B EMS once it is upgraded to 4.4.1 release.

# From EMS Side A

Step 1   Log in as root

Step 2   Save user account information:

<hostname># mkdir -p /opt/.upgrade

<hostname># tar -cvf /opt/.upgrade/users.tar /opt/ems/users

# Task 3: Pre-check tables

The user accounts saved in this task is to be restored to side B EMS once it is upgraded to 4.4.1 release.

# From Active EMS

Step 1   Log in as CLI user

Step 2   CLI> show feature TID1=ORIGINATION_ATTEMPT_AUTHORIZED;

- Please delete the record if there is return result.

Step 3   CLI> show feature TID2=ORIGINATION_ATTEMPT_AUTHORIZED;

- Please delete the record if there is return result.

Step 4   CLI> show feature TID3=ORIGINATION_ATTEMPT_AUTHORIZED;

- Please delete the record if there is return result.

Step 5   CLI> show feature TID1=D_OF_TRIGGER;

- Please delete the record if there is return result.

Step 6   CLI> show feature TID2=D_OF_TRIGGER;

- Please delete the record if there is return result.

Step 7   CLI> show feature TID3=D_OF_TRIGGER;

- Please delete the record if there is return result.

Step 8   CLI> show feature TID1=ACCOUNT_CODE;

- Please delete the record if there is return result.

Step 9   CLI> show feature TID2=ACCOUNT_CODE;

- Please delete the record if there is return result.

Step 10   CLI> show feature TID3=ACCOUNT_CODE;

- Please delete the record if there is return result.

Step 11   CLI> show service-trigger TID=ORIGINATION_ATTEMPT_AUTHORIZED;

- Please delete the record if there is return result.

Step 12   CLI> show service-trigger TID=D_OF_TRIGGER;

- Please delete the record if there is return result.

Step 13   CLI> show service-trigger TID=ACCOUNT_CODE;

- Please delete the record if there is return result.

Step 14   CLI> exit

Step 15    <hostname># su – oracle

Step 16    <hostname>$ sqlplus optiuser/optiuser

Step 17   sql> select count(*) from vsc where fname is null;

- Make sure the result is 0.

- If the result is not 0, then login as CLI user and change the fname to a valid feature name.

Step 18   sql> exit;

Chapter 5

Upgrade Side B Systems

# Task 1: Inhibit EMS mate communication

In this task, you will isolate the OMS Hub on EMS side A from talking to EMS side B.

# From EMS side A

Step 1   Log in as root

Step 2   <hostname># /opt/ems/utils/updMgr.sh –split_hub

Step 3   <hostname># nodestat

- Verify there is no HUB communication from EMS side A to CA/FS side B.

- Verify OMS Hub mate port status: No communication between EMS

# Task 2: Disable Oracle DB replication

# From EMS side A

Step 1   Log in to Active EMS as CLI user

Step 2   CLI> control bdms id=BDMS01; target-state=forced-standby-active;

Step 3   CLI> control element-manager id=EM01; target-state=forced-standby-active;

Step 4    CLI session will terminate when application platform switchover is complete.

Step 5   Log in as Oracle user:

<hostname># su – oracle

<hostname>$ cd /opt/oracle/admin/utl

Step 6   Set Oracle DB to simplex mode:

<hostname>$ rep_toggle –s optical1 –t set_simplex

- Answer “y” when prompt

- Answer “y” again when prompt

Step 7   <hostname>$ exit

Step 8   <hostname># platform stop all

Step 9   Start applications to activate DB in simplex mod.

<hostname># platform start

# Task 3: Force side A systems to be active

This procedure will force the side A systems to be in active state.

|  | Note In the commands below, "xxx", "yyy" or "zzz" is the instance for the process on your system. |
| --- | --- |

# From Active EMS Side B

Step 1   Log in to Active EMS as CLI user

Step 2   CLI> control call-agent id=CA100; target-state=forced-active-standby;

Step 3   CLI> control feature-server id=FSPTC101; target-state=forced-active-standby;

Step 4   CLI> control feature-server id=FSAIN102; target-state=forced-active-standby;

Step 5   CLI> control bdms id=BDMS01; target-state=forced-active-standby;

Step 6   CLI> control element-manager id=EM01; target-state=forced-active-standby;

# Task 4: Stop applications and shutdown EMS Side B

# From EMS side B

Step 1   Log in as root

Step 2   Record the IP address and netmask for the management interface of the system.

- For an example, if the “eri0” is used for management interface, then execute the following command:

<hostname># ifconfig eri0

- Record the IP address and netmask for the interface to be used in the next task.

IP: _216.12.76.3_ Netmask: _255.255.255.248_ Interface Name: _eri0_

Step 3   <hostname># mv /etc/rc3.d/S99platform /etc/rc3.d/_S99platform

Step 4    <hostname># sync; sync

Step 5   <hostname># platform stop all

Step 6   <hostname># shutdown –i5 –g0 –y

# Task 5: Stop applications and shutdown CA/FS Side B

# From CA/FS side B

Step 1   Log in as root

Step 2   Record the IP address and netmask for the management interface of the system.

- For an example, if the “eri0” is used for management interface, then execute the following command:

<hostname># ifconfig eri0

- Record the IP address and netmask for the interface to be used in the next task.

IP: _216.12.116.13_ Netmask: _255.255.255.0_ Interface Name: _eri0_

Step 3   <hostname># mv /etc/rc3.d/S99platform /etc/rc3.d/_S99platform

Step 4    <hostname># sync; sync

Step 5   <hostname># platform stop all

Step 6   <hostname># shutdown –i5 –g0 –y

# Task 6: Upgrade EMS side B to the new release

# From EMS side B

Step 1   Power off the machine

Step 2   Remove disk0 from slot 0 off the machine and label it as “Release 4.2.0.V11 EMS side B disk0”

- SunFire V120 disk slot lay out:

| CD-ROM | Disk 0 | Disk 1 |
| --- | --- | --- |

- SunFire V240 disk slot lay out:

| Disk 2 | Disk 3 |  |
| --- | --- | --- |
| Disk 0 | Disk 1 | DVD-ROM |

- SunFire V440 disk slot lay out:

| Disk 3 | DVD-ROM |
| --- | --- |
| Disk 2 |  |
| Disk 1 |  |
| Disk 0 |  |

- Netra 1280 disk slot lay out:

|  | DVD-ROM |
| --- | --- |
|  | Disk 1 |
|  | Disk 0 |

- Netra 20 disk slot lay out:

| D I S K 0 | D I S K 1 |  | DVD ROM |
| --- | --- | --- | --- |

- Continuous Hardware disk slot lay out:

| CD-ROM | Disk 0 |  |
| --- | --- | --- |
|  | Disk 1 |  |

Step 3   Remove disk1 from slot 1 off the machine and label it as “Release 4.2.0 EMS side B disk1”

Step 4   Place new disk labeled as “Release 4.4.1 EMS side B disk0” in slot 0

Step 5   Place new disk labeled as “Release 4.4.1 EMS side B disk1” in slot 1

Step 6   Power on the machine and allow the system to boot up by monitoring the boot process thru console

Step 7   Log in as root.

Step 8   Show network interface hardware configuration on disk

<hostname># egrep –i “qfe|ce|eri|bge|hme” /etc/path_to_inst

- The result will show the type of network interface configured in the system. The following example is for “qfe” interface:

"/pci@8,700000/pci@3/SUNW,qfe@0,1" 0 "qfe"
"/pci@8,700000/pci@3/SUNW,qfe@1,1" 1 "qfe"
"/pci@8,700000/pci@3/SUNW,qfe@2,1" 2 "qfe"
"/pci@8,700000/pci@3/SUNW,qfe@3,1" 3 "qfe"

Step 9   Remove network interface hardware configuration

<hostname># cp –p /etc/path_to_inst /etc/path_to_inst.save

<hostname># vi /etc/path_to_inst

- Delete entries returned from the egrep command and save the file

Step 10   Rebuild the hardware configuration

<hostname># reboot -- -r

- Wait for the system to boot up. Then log in as root.

Step 11   Restore interfaces:

- <hostname># ifconfig <primary interface name> plumb

  - Use Interface Name recorded in “Chapter 5, Task 4”

- <hostname># ifconfig <primary interface name> <Interface IP> netmask <NETMASK> broadcast + up

  - Use IP and NETMASK recorded in “Chapter 5, Task 4”

- Add static routes to reach Domain Name Server and Network File Server using “route add …” command:

  - Example: route add -net 10.89.224.1 10.89.232.254

Where: 10.89.224.1 is the destination DNS server IP
              10.89.232.254 is the gateway IP

Step 12   Reset ssh keys:

<hostname># \rm /.ssh/known_hosts

Step 13   sftp the opticall.cfg file from Network File Server (opticall.cfg was constructed in Chapter 3, Task 2) and place it under /etc directory.

Step 14   sftp resolv.conf file from Primary EMS Side A and place it under /etc directory.

<hostname># sftp <Side A EMS IP>

sftp> cd /etc

sftp> get resolv.conf

sftp> exit

Step 15   Run script program to replace the hostname

<hostname># cd /opt/ems/upgrade

<hostname># DoTheChange -s

- The system will reboot when the script DoTheChange completes its run

Step 16    Wait for the system to boot up. Then log in as root.

Step 17   Editing /etc/default/init:

<hostname># vi /etc/default/init

- Remove lines and keep only the following lines:

#

TZ=US/Central

CMASK=022

For an example:

The original /etc/default/init file before line removal:

# @(#)init.dfl 1.5 99/05/26

#

# This file is /etc/default/init.  /etc/TIMEZONE is a symlink to this file.

# This file looks like a shell script, but it is not.  To maintain

# compatibility with old versions of /etc/TIMEZONE, some shell constructs

# (i.e., export commands) are allowed in this file, but are ignored.

#

# Lines of this file should be of the form VAR=value, where VAR is one of

# TZ, LANG, CMASK, or any of the LC_* environment variables.

#

TZ=US/Central

CMASK=022

LC_COLLATE=en_US.ISO8859-1

LC_CTYPE=en_US.ISO8859-1

LC_MESSAGES=C

LC_MONETARY=en_US.ISO8859-1

LC_NUMERIC=en_US.ISO8859-1

LC_TIME=en_US.ISO8859-1

The /etc/default/init file after line removal:

# @(#)init.dfl 1.5 99/05/26

#

# This file is /etc/default/init.  /etc/TIMEZONE is a symlink to this file.

# This file looks like a shell script, but it is not.  To maintain

# compatibility with old versions of /etc/TIMEZONE, some shell constructs

# (i.e., export commands) are allowed in this file, but are ignored.

#

# Lines of this file should be of the form VAR=value, where VAR is one of

# TZ, LANG, CMASK, or any of the LC_* environment variables.

#

TZ=US/Central

CMASK=022

Step 18   Verify interface hardware configuration match to the host configuration:

<hostname># egrep –i “qfe|ce|eri|bge|hme” /etc/path_to_inst

<hostname># ls –l /etc/hostname.*

- If the interface names match from the above two outputs, please continue on Step 19.

- If the interface names do NOT match, please match them by changing the postfix of hostname.*.

For an example:

Output from “egrep –i “qfe|ce|eri|bge|hme” /etc/path_to_inst” is:

"/pci@1f,4000/network@1,1" 0 "hme"

"/pci@1f,4000/pci@4/SUNW,qfe@0,1" 0 "qfe"

"/pci@1f,4000/pci@4/SUNW,qfe@1,1" 1 "qfe"

"/pci@1f,4000/pci@4/SUNW,qfe@2,1" 2 "qfe"

"/pci@1f,4000/pci@4/SUNW,qfe@3,1" 3 "qfe"

Output from “ls -l /etc/hostname.*” is:

-rw-r--r--   1 root     other          14 May 16 16:03 /etc/hostname.hme0

-rw-r--r--   1 root     other         14 May 16 16:04 /etc/hostname.hme0:1

-rw-r--r--   1 root     other         14 May 16 16:04 /etc/hostname.eri0

-rw-r--r--   1 root     other         14 May 16 16:04 /etc/hostname.eri0:1

After change, the output should be:

-rw-r--r--   1 root     other          14 May 16 16:03 /etc/hostname.hme0

-rw-r--r--   1 root     other         14 May 16 16:04 /etc/hostname.hme0:1

-rw-r--r--   1 root     other         14 May 16 16:04 /etc/hostname.qfe0

-rw-r--r--   1 root     other         14 May 16 16:04 /etc/hostname.qfe0:1

Step 19   Reboot the machine to pick up new TIMEZONE setting:

<hostname># sync; sync; reboot

- Wait for the system to boot up. Then log in as root.

Step 20   <hostname># /opt/ems/utils/updMgr.sh –split_hub

Step 21   <hostname># /etc/rc2.d/S75cron stop

Step 22   CDR delimiter customization is not retained after software upgrade. If this system has been customized, either the Customer or Cisco Support Engineer must manually customize again to keep the same customization.

- <hostname># cd /opt/bdms/bin

- <hostname># vi platform.cfg

- Find the section for the command argument list for the BMG process

- Customize the CDR delimiters in the “Args=” line

- Example:

Args=-port 15260 -h localhost -u optiuser -p optiuser -fmt default_formatter -UpdIntvl 3300 -ems_local_dn blg-aSYS14EMS.cisco.com -FD comma -RD linefeed

Step 23   <hostname># platform start –i oracle

Step 24   Log in as Oracle user.

<hostname># su – oracle

<hostname>$ cd /opt/oracle/admin/utl

Step 25   Set Oracle DB to simplex mode:

<hostname>$ rep_toggle –s optical2 –t set_simplex

- Answer “y” when prompt

- Answer “y” again when prompt

# Task 7: Upgrade CA/FS Side B to the new release

# From CA/FS side B

Step 1   Power off the machine

Step 2   Remove disk0 from slot 0 off the machine and label it as “Release 4.2.0.V11 CA/FS side B disk0”

- SunFire V120 disk slot lay out:

| CD-ROM | Disk 0 | Disk 1 |
| --- | --- | --- |

- SunFire V240 disk slot lay out:

| Disk 2 | Disk 3 |  |
| --- | --- | --- |
| Disk 0 | Disk 1 | DVD-ROM |

- SunFire V440 disk slot lay out:

| Disk 3 | DVD-ROM |
| --- | --- |
| Disk 2 |  |
| Disk 1 |  |
| Disk 0 |  |

- Netra 1280 disk slot lay out:

|  | DVD-ROM |
| --- | --- |
|  | Disk 1 |
|  | Disk 0 |

- Netra 20 disk slot lay out:

| D I S K 0 | D I S K 1 |  | DVD ROM |
| --- | --- | --- | --- |

- Continuous Hardware disk slot lay out:

| CD-ROM | Disk 0 | Disk 2 |
| --- | --- | --- |
|  | Disk 1 | Disk 3 |

Step 3   Remove disk1 from slot 1 off the machine and label it as “Release 4.2.0 CA/FS side B disk1”

Step 4   Place new disk labeled as “Release 4.4.1 CA/FS side B disk0” in slot 0

Step 5   Place new disk labeled as “Release 4.4.1 EMS side B disk1” in slot 1

Step 6   Power on the machine using and allow the system to boot up by monitoring the boot process thru console

Step 7   Log in as root.

Step 8   Show network interface hardware configuration on disk

<hostname># egrep –i “qfe|ce|eri|bge|hme” /etc/path_to_inst

- The result will show the type of network interface configured in the system. The following example is for “qfe” interface:

"/pci@8,700000/pci@3/SUNW,qfe@0,1" 0 "qfe"
"/pci@8,700000/pci@3/SUNW,qfe@1,1" 1 "qfe"
"/pci@8,700000/pci@3/SUNW,qfe@2,1" 2 "qfe"
"/pci@8,700000/pci@3/SUNW,qfe@3,1" 3 "qfe"

Step 9   Remove network interface hardware configuration

<hostname># cp –p /etc/path_to_inst /etc/path_to_inst.save

<hostname># vi /etc/path_to_inst

- Delete entries returned from the egrep command and save the file

Step 10   Rebuild the hardware configuration

<hostname># reboot -- -r

- Wait for the system to boot up. Then log in as root.

Step 11   Restore interfaces:

- <hostname># ifconfig <primary interface name> plumb

  - Use Interface Name recorded in “Chapter 5, Task 5”

- <hostname># ifconfig <primary interface name> <Interface IP> netmask <NETMASK> broadcast + up

  - Use IP and NETMASK recorded in “Chapter 5, Task 5”

- Add static routes to reach Domain Name Server and Network File Server using “route add …” command:

  - Example: route add -net 10.89.224.1 10.89.232.254

Where: 10.89.224.1 is the destination DNS server IP
              10.89.232.254 is the gateway IP

Step 12   Reset ssh keys:

<hostname># \rm /.ssh/known_hosts

Step 13   sftp the opticall.cfg file from Network File Server (opticall.cfg was constructed in Chapter 3, Task 2) and place it under /etc directory.

Step 14   sftp resolv.conf file from Primary CA/FS Side A and place it under /etc directory.

<hostname># sftp <Side A CA/FS IP>

sftp> cd /etc

sftp> get resolv.conf

sftp> exit

Step 15   Run script program to replace the hostname

<hostname># cd /opt/ems/upgrade

<hostname># DoTheChange -s

- The system will reboot when the script DoTheChange completes its run

Step 16    Wait for the system to boot up. Then log in as root.

Step 17   Editing /etc/default/init:

<hostname># vi /etc/default/init

- Remove lines and keep only the following lines:

#

TZ=US/Central

CMASK=022

For an example:

The original /etc/default/init file before line removal:

# @(#)init.dfl 1.5 99/05/26

#

# This file is /etc/default/init.  /etc/TIMEZONE is a symlink to this file.

# This file looks like a shell script, but it is not.  To maintain

# compatibility with old versions of /etc/TIMEZONE, some shell constructs

# (i.e., export commands) are allowed in this file, but are ignored.

#

# Lines of this file should be of the form VAR=value, where VAR is one of

# TZ, LANG, CMASK, or any of the LC_* environment variables.

#

TZ=US/Central

CMASK=022

LC_COLLATE=en_US.ISO8859-1

LC_CTYPE=en_US.ISO8859-1

LC_MESSAGES=C

LC_MONETARY=en_US.ISO8859-1

LC_NUMERIC=en_US.ISO8859-1

LC_TIME=en_US.ISO8859-1

The /etc/default/init file after line removal:

# @(#)init.dfl 1.5 99/05/26

#

# This file is /etc/default/init.  /etc/TIMEZONE is a symlink to this file.

# This file looks like a shell script, but it is not.  To maintain

# compatibility with old versions of /etc/TIMEZONE, some shell constructs

# (i.e., export commands) are allowed in this file, but are ignored.

#

# Lines of this file should be of the form VAR=value, where VAR is one of

# TZ, LANG, CMASK, or any of the LC_* environment variables.

#

TZ=US/Central

CMASK=022

Step 18   Verify interface hardware configuration match to the host configuration:

<hostname># egrep –i “qfe|ce|eri|bge|hme” /etc/path_to_inst

<hostname># ls –l /etc/hostname.*

- If the interface names match from the above two outputs, please continue on Step 19.

- If the interface names do NOT match, please match them by changing the postfix of hostname.*.

For an example:

Output from “egrep –i “qfe|ce|eri|bge|hme” /etc/path_to_inst” is:

"/pci@1f,4000/network@1,1" 0 "hme"

"/pci@1f,4000/pci@4/SUNW,qfe@0,1" 0 "qfe"

"/pci@1f,4000/pci@4/SUNW,qfe@1,1" 1 "qfe"

"/pci@1f,4000/pci@4/SUNW,qfe@2,1" 2 "qfe"

"/pci@1f,4000/pci@4/SUNW,qfe@3,1" 3 "qfe"

"/pci@1f,2000/pci@1/SUNW,qfe@0,1" 4 "qfe"

"/pci@1f,2000/pci@1/SUNW,qfe@1,1" 5 "qfe"

"/pci@1f,2000/pci@1/SUNW,qfe@2,1" 6 "qfe"

"/pci@1f,2000/pci@1/SUNW,qfe@3,1" 7 "qfe"

Output from “ls -l /etc/hostname.*” is:

-rw-r--r--   1 root     other         14 Jun 10 11:25 hostname.hme0

-rw-r--r--   1 root     other         14 Jun 10 11:25 hostname.eri0

-rw-r--r--   1 root     other         13 Jun 10 11:25 hostname.eri1

-rw-r--r--   1 root     other         13 Jun 10 11:25 hostname.eri1:1

-rw-r--r--   1 root     other         14 Jun 10 11:25 hostname.eri1:2

-rw-r--r--   1 root     other         12 Jun 10 11:25 hostname.eri1:3

-rw-r--r--   1 root     other         13 Jun 10 11:25 hostname.eri2

-rw-r--r--   1 root     other         13 Jun 10 11:25 hostname.eri2:1

-rw-r--r--   1 root     other         14 Jun 10 11:25 hostname.eri2:2

-rw-r--r--   1 root     other         12 Jun 10 11:25 hostname.eri2:3

After change, the output should be:

-rw-r--r--   1 root     other         14 Jun 10 11:25 hostname.hme0

-rw-r--r--   1 root     other         14 Jun 10 11:25 hostname.qfe0

-rw-r--r--   1 root     other         13 Jun 10 11:25 hostname.qfe1

-rw-r--r--   1 root     other         13 Jun 10 11:25 hostname.qfe1:1

-rw-r--r--   1 root     other         14 Jun 10 11:25 hostname.qfe1:2

-rw-r--r--   1 root     other         12 Jun 10 11:25 hostname.qfe1:3

-rw-r--r--   1 root     other         13 Jun 10 11:25 hostname.qfe2

-rw-r--r--   1 root     other         13 Jun 10 11:25 hostname.qfe2:1

-rw-r--r--   1 root     other         14 Jun 10 11:25 hostname.qfe2:2

-rw-r--r--   1 root     other         12 Jun 10 11:25 hostname.qfe2:3

Step 19   Reboot the machine to pick up new TIMEZONE setting:

<hostname># sync; sync; reboot

- Wait for the system to boot up. Then log in as root.

Step 20   Check for configuration errors

<hostname># cd /opt/Build

<hostname># checkCFG –u

- Correct errors generated by checkCFG

- Once the result is clean without errors, then proceed to the next step.

Step 21   <hostname># install.sh –upgrade

- Enter “900-04.02.00.V11”, then enter “y” to confirm

- Answer “y” when prompted

- The upgrade process will apply OS patches

Step 22   Wait for the system to boot up. Then Log in as root.

Step 23   <hostname># /opt/Build/install.sh –upgrade

Step 24   Answer "y" when prompted. This process will take up to 15 minutes to complete.

Step 25   Answer "y" when prompted for reboot after installation.

Step 26    Wait for the system to boot up. Then Log in as root.

Step 27   <hostname># platform start

Step 28   <hostname># mv /etc/rc3.d/_S99platform /etc/rc3.d/S99platform

# Task 8: Migrate oracle data

# From EMS side B

Step 1   Copying data.

<hostname>$ cd /opt/oracle/admin/upd

<hostname>$ java dba.dmt.DMMgr –loadconfig ./config/4.2.0_to_4.4.1.cfg

<hostname>$ java dba.dmt.DMMgr –reset upgrade

<hostname>$ java dba.dmt.DMMgr –upgrade all

Step 2   Verify the FAIL=0 is reported.

<hostname>$ grep "FAIL=" DMMgr.log

Step 3   Verify there is no constraint warning reported.

<hostname>$ grep constraint DMMgr.log | grep –i warning

Step 4   If FAIL count is not 0 on step 2 or there is constraint warning on step 3, sftp /opt/oracle/admin/upd/DMMgr.log file off system, call Cisco support for immediate technical assistance.

Step 5   <hostname>$ cd /opt/oracle/opticall/create

Step 6   <hostname>$ dbinstall optical2 -load dbsize

Step 7   <hostname>$ exit

Step 8   <hostname># /etc/rc2.d/S75cron start

Step 9   <hostname># platform start

Step 10   <hostname># mv /etc/rc3.d/_S99platform /etc/rc3.d/S99platform

# Task 9: To install CORBA on EMS side B, please follow Appendix I.

Chapter 6

Prepare to Upgrade Side A system

# Task 1: Force side A system to standby

This procedure will force the side A system to standby and force the side B system to active.

|  | Note In the commands below, "xxx", "yyy" or "zzz" is the instance for the process on your system. |
| --- | --- |

# From EMS side A

Step 1   Log in as CLI user.

Step 2   CLI> control feature-server id=FSPTC101; target-state=forced-standby-active;

Step 3   CLI> control feature-server id=FSAIN102; target-state=forced-standby-active;

Step 4   CLI> control call-agent id=CA100; target-state=forced-standby-active;

Step 5   CLI> control bdms id=BDMS01; target-state=forced-standby-active;

Step 6   CLI> control element-manager id=EM01; target-state=forced-standby-active;

Step 7   CLI session will terminate when the last CLI command completes.

|  | Note If the system failed to switchover from side A to side B, please contact Cisco TAC to determine whether the system should fallback. If fallback is needed, please following Appendix G. |
| --- | --- |

# Task 2: Validate release 4.4.1 software operation

To verify the stability of the newly installed 4.4.1 Release, let CA/FS side B carry live traffic for period of time. Monitor the Cisco BTS 10200 Softswitch and the network. If there are any problems, please investigate and contact Cisco support if necessary.

# From EMS side B

Step 1   Verify that call processing by using the detailed steps in the Appendix B.

Step 2   <hostname># su – oracle

Step 3   <hostname>$ java dba.adm.DBUsage –sync

- Verify Number of tables “unable-to-sync” is 0.

Step 4   <hostname>$ exit

Step 5   Log in as CLI user

Step 6   CLI> audit database type=row-count;

- Please ignore the row count mismatch on the table: radius-profile. The table will be synced from EMS in the “Finalize Upgrade” Chapter 8.

- Verify there are no other mismatches in the report and the database is not empty.

Step 7   CLI> audit lnp-profile;

- If the audit resulted in an error due to mismatched “release-cause”, please run the following command to correct the error:

CLI> change lnp-profile id=xxx; release-cause=26;

Step 8   Verify the SUP config is set up correctly

- CLI> show sup-config;

- Verify refresh rate is set to 86400.

- If not, do the following

- CLI> change sup-config type=refresh_rate; value=86400;

Step 9   <hostname># ls /opt/bms/ftp/billing

- If there are files listed, then sftp the files to a mediation device on the network and remove the files from the /opt/bms/ftp/billing directory.

|  | Note Once the system proves stable and you decide to move ahead with the upgrade, then you must execute subsequent tasks. If fallback is needed at this stage, please follow the fallback procedure in Appendix G. |
| --- | --- |

Chapter 7

Upgrade Side A Systems

# Task 1: Shutdown EMS Side A

# From EMS Side A

Step 1   Log in as root

Step 2   Record the IP address and netmask for the management interface of the system.

- For an example, if the “eri0” is used for management interface, then execute the following command:

<hostname># ifconfig eri0

- Record the IP address and netmask for the interface to be used in the next task.

IP: _216.12.76.2_ Netmask: _255.255.255.248_ Interface Name: _eri0_

Step 3   <hostname># mv /etc/rc3.d/S99platform /etc/rc3.d/_S99platform

Step 4   <hostname># sync; sync

Step 5   <hostname># platform stop all

Step 6   <hostname># shutdown –i5 –g0 -y

# Task 2: Shutdown CA/FS Side A

# From CA/FS side A

Step 1   Log in as root

Step 2   Record the IP address and netmask for the management interface of the system.

- For an example, if the “eri0” is used for management interface, then execute the following command:

<hostname># ifconfig eri0

- Record the IP address and netmask for the interface to be used in the next task.

IP: _216.12.116.12_ Netmask: _255.255.255.0_ Interface Name: _eri0_

Step 3   <hostname># mv /etc/rc3.d/S99platform /etc/rc3.d/_S99platform

Step 4   <hostname># sync; sync

Step 5   <hostname># platform stop all

Step 6   <hostname># shutdown –i5 –g0 -y

# Task 3: Upgrade EMS side A to the new release

# From EMS side A

Step 1   Power off the machine

Step 2   Remove disk0 from slot 0 off the machine and label it as “Release 4.2.0.V11 EMS side A disk0”

- SunFire V120 disk slot lay out:

| CD-ROM | Disk 0 | Disk 1 |
| --- | --- | --- |

- SunFire V240 disk slot lay out:

| Disk 2 | Disk 3 |  |
| --- | --- | --- |
| Disk 0 | Disk 1 | DVD-ROM |

- SunFire V440 disk slot lay out:

| Disk 3 | DVD-ROM |
| --- | --- |
| Disk 2 |  |
| Disk 1 |  |
| Disk 0 |  |

- Netra 1280 disk slot lay out:

|  | DVD-ROM |
| --- | --- |
|  | Disk 1 |
|  | Disk 0 |

- Netra 20 disk slot lay out:

| D I S K 0 | D I S K 1 |  | DVD ROM |
| --- | --- | --- | --- |

- Continuous Hardware disk slot lay out:

| CD-ROM | Disk 0 |  |
| --- | --- | --- |
|  | Disk 1 |  |

Step 3   Remove disk1 from slot 1 off the machine and label it as “Release 4.2.0 EMS side A disk1”

Step 4   Place new disk labeled as “Release 4.4.1 EMS side A disk0” in slot 0

Step 5   Place new disk labeled as “Release 4.4.1 EMS side A disk1” in slot 1

Step 6   Power on the machine and allow the system to boot up by monitoring the boot process thru console

Step 7   Log in as root.

Step 8   Show network interface hardware configuration on disk

<hostname># egrep –i “qfe|ce|eri|bge|hme” /etc/path_to_inst

- The result will show the type of network interface configured in the system. The following example is for “qfe” interface:

"/pci@8,700000/pci@3/SUNW,qfe@0,1" 0 "qfe"
"/pci@8,700000/pci@3/SUNW,qfe@1,1" 1 "qfe"
"/pci@8,700000/pci@3/SUNW,qfe@2,1" 2 "qfe"
"/pci@8,700000/pci@3/SUNW,qfe@3,1" 3 "qfe"

Step 9   Remove network interface hardware configuration

<hostname># cp –p /etc/path_to_inst /etc/path_to_inst.save

<hostname># vi /etc/path_to_inst

- Delete entries returned from the egrep command and save the file

Step 10   Rebuild the hardware configuration

<hostname># reboot -- -r

- Wait for the system to boot up. Then log in as root.

Step 11   Restore interfaces:

- <hostname># ifconfig <primary interface name> plumb

  - Use Interface Name recorded in “Chapter 5, Task 4”

- <hostname># ifconfig <primary interface name> <Interface IP> netmask <NETMASK> broadcast + up

  - Use IP and NETMASK recorded in “Chapter 5, Task 4”

- Add static routes to reach Domain Name Server and Network File Server using “route add …” command:

  - Example: route add -net 10.89.224.1 10.89.232.254

Where: 10.89.224.1 is the destination DNS server IP
              10.89.232.254 is the gateway IP

Step 12   Reset ssh keys:

<hostname># \rm /.ssh/known_hosts

Step 13   sftp the opticall.cfg file from Network File Server (opticall.cfg was constructed in Chapter 3, Task 2) and place it under /etc directory.

Step 14   sftp resolv.conf file from Primary EMS Side A and place it under /etc directory.

<hostname># sftp <Side A EMS IP>

sftp> cd /etc

sftp> get resolv.conf

sftp> exit

Step 15   Run script program to replace the hostname

<hostname># cd /opt/ems/upgrade

<hostname># DoTheChange -s

- The system will reboot when the script DoTheChange completes its run

Step 16    Wait for the system to boot up. Then log in as root.

Step 17   Editing /etc/default/init:

<hostname># vi /etc/default/init

- Remove lines and keep only the following lines:

#

TZ=US/Central

CMASK=022

For an example:

The original /etc/default/init file before line removal:

# @(#)init.dfl 1.5 99/05/26

#

# This file is /etc/default/init.  /etc/TIMEZONE is a symlink to this file.

# This file looks like a shell script, but it is not.  To maintain

# compatibility with old versions of /etc/TIMEZONE, some shell constructs

# (i.e., export commands) are allowed in this file, but are ignored.

#

# Lines of this file should be of the form VAR=value, where VAR is one of

# TZ, LANG, CMASK, or any of the LC_* environment variables.

#

TZ=US/Central

CMASK=022

LC_COLLATE=en_US.ISO8859-1

LC_CTYPE=en_US.ISO8859-1

LC_MESSAGES=C

LC_MONETARY=en_US.ISO8859-1

LC_NUMERIC=en_US.ISO8859-1

LC_TIME=en_US.ISO8859-1

The /etc/default/init file after line removal:

# @(#)init.dfl 1.5 99/05/26

#

# This file is /etc/default/init.  /etc/TIMEZONE is a symlink to this file.

# This file looks like a shell script, but it is not.  To maintain

# compatibility with old versions of /etc/TIMEZONE, some shell constructs

# (i.e., export commands) are allowed in this file, but are ignored.

#

# Lines of this file should be of the form VAR=value, where VAR is one of

# TZ, LANG, CMASK, or any of the LC_* environment variables.

#

TZ=US/Central

CMASK=022

Step 18   Verify interface hardware configuration match to the host configuration:

<hostname># egrep –i “qfe|ce|eri|bge|hme” /etc/path_to_inst

<hostname># ls –l /etc/hostname.*

- If the interface names match from the above two outputs, please continue on Step 19.

- If the interface names do NOT match, please match them by changing the postfix of hostname.*.

For an example:

Output from “egrep –i “qfe|ce|eri|bge|hme” /etc/path_to_inst” is:

"/pci@1f,4000/network@1,1" 0 "hme"

"/pci@1f,4000/pci@4/SUNW,qfe@0,1" 0 "qfe"

"/pci@1f,4000/pci@4/SUNW,qfe@1,1" 1 "qfe"

"/pci@1f,4000/pci@4/SUNW,qfe@2,1" 2 "qfe"

"/pci@1f,4000/pci@4/SUNW,qfe@3,1" 3 "qfe"

Output from “ls -l /etc/hostname.*” is:

-rw-r--r--   1 root     other          14 May 16 16:03 /etc/hostname.hme0

-rw-r--r--   1 root     other         14 May 16 16:04 /etc/hostname.hme0:1

-rw-r--r--   1 root     other         14 May 16 16:04 /etc/hostname.eri0

-rw-r--r--   1 root     other         14 May 16 16:04 /etc/hostname.eri0:1

After change, the output should be:

-rw-r--r--   1 root     other          14 May 16 16:03 /etc/hostname.hme0

-rw-r--r--   1 root     other         14 May 16 16:04 /etc/hostname.hme0:1

-rw-r--r--   1 root     other         14 May 16 16:04 /etc/hostname.qfe0

-rw-r--r--   1 root     other         14 May 16 16:04 /etc/hostname.qfe0:1

Step 19   Reboot the machine to pick up new TIMEZONE setting:

<hostname># sync; sync; reboot

- Wait for the system to boot up. Then log in as root.

Step 20   CDR delimiter customization is not retained after software upgrade. If this system has been customized, either the Customer or Cisco Support Engineer must manually customize again to keep the same customization.

- <hostname># cd /opt/bdms/bin

- <hostname># vi platform.cfg

- Find the section for the command argument list for the BMG process

- Customize the CDR delimiters in the “Args=” line

- Example:

Args=-port 15260 -h localhost -u optiuser -p optiuser -fmt default_formatter -UpdIntvl 3300 -ems_local_dn blg-aSYS14EMS.cisco.com -FD comma -RD linefeed

Step 21   <hostname># platform start

# Task 4: Upgrade CA/FS side A to the new release

# From CA/FS side A

Step 1   Power off the machine

Step 2   Remove disk0 from slot 0 off the machine and label it as “Release 4.2.0.V11 CA/FS side A disk0”

- SunFire V120 disk slot lay out:

| CD-ROM | Disk 0 | Disk 1 |
| --- | --- | --- |

- SunFire V240 disk slot lay out:

| Disk 2 | Disk 3 |  |
| --- | --- | --- |
| Disk 0 | Disk 1 | DVD-ROM |

- SunFire V440 disk slot lay out:

| Disk 3 | DVD-ROM |
| --- | --- |
| Disk 2 |  |
| Disk 1 |  |
| Disk 0 |  |

- Netra 1280 disk slot lay out:

|  | DVD-ROM |
| --- | --- |
|  | Disk 1 |
|  | Disk 0 |

- Netra 20 disk slot lay out:

| D I S K 0 | D I S K 1 |  | DVD ROM |
| --- | --- | --- | --- |

- Continuous Hardware disk slot lay out:

| CD-ROM | Disk 0 | Disk 2 |
| --- | --- | --- |
|  | Disk 1 | Disk 3 |

Step 3   Remove disk1 from slot 1 off the machine and label it as “Release 4.2.0 CA/FS side A disk1”

Step 4   Place new disk labeled as “Release 4.4.1 CA/FS side A disk0” in slot 0

Step 5   Place new disk labeled as “Release 4.4.1 CA/FS side A disk1” in slot 1

Step 6   Power on the machine and allow the system to boot up by monitoring the boot process thru console

Step 7   Log in as root.

Step 8   Show network interface hardware configuration on disk

<hostname># egrep –i “qfe|ce|eri|bge|hme” /etc/path_to_inst

- The result will show the type of network interface configured in the system. The following example is for “qfe” interface:

"/pci@8,700000/pci@3/SUNW,qfe@0,1" 0 "qfe"
"/pci@8,700000/pci@3/SUNW,qfe@1,1" 1 "qfe"
"/pci@8,700000/pci@3/SUNW,qfe@2,1" 2 "qfe"
"/pci@8,700000/pci@3/SUNW,qfe@3,1" 3 "qfe"

Step 9   Remove network interface hardware configuration

<hostname># cp –p /etc/path_to_inst /etc/path_to_inst.save

<hostname># vi /etc/path_to_inst

- Delete entries returned from the egrep command and save the file

Step 10   Rebuild the hardware configuration

<hostname># reboot -- -r

- Wait for the system to boot up. Then log in as root.

Step 11   Restore interfaces:

- <hostname># ifconfig <interface name> plumb

  - Use Interface Name recorded in “Chapter 7, Task 2”

- <hostname># ifconfig <interface name> <Interface IP> netmask <NETMASK> broadcast + up

  - Use IP and NETMASK recorded in “Chapter 7, Task 2”

- Add static routes to reach Domain Name Server and Network File Server using “route add …” command:

  - Example: route add -net 10.89.224.1 10.89.232.254

Where: 10.89.224.1 is the destination DNS server IP
              10.89.232.254 is the gateway IP

Step 12   Reset ssh keys:

<hostname># \rm /.ssh/known_hosts

Step 13   sftp the opticall.cfg and resolv.conf from Secondary CA/FS side B and place it under /etc directory.

<hostname># sftp <Side B CA/FS IP>

sftp> cd /etc

sftp> get resolv.conf

sftp> get opticall.cfg

sftp> exit

Step 14   Run script program to replace the hostname

<hostname># cd /opt/ems/upgrade

<hostname># DoTheChange -p

- The system will reboot when the script DoTheChange completes its run

Step 15    Wait for the system to boot up. Then Log in as root.

Step 16   Verify interface hardware configuration match to the host configuration:

<hostname># egrep –i “qfe|ce|eri|bge|hme” /etc/path_to_inst

<hostname># ls –l /etc/hostname.*

- If the interface names match from the above two outputs, please continue on Step 17.

- If the interface names do NOT match, please match them by changing the postfix of hostname.*.

For an example:

Output from “egrep –i “qfe|ce|eri|bge|hme” /etc/path_to_inst” is:

"/pci@1f,4000/network@1,1" 0 "hme"

"/pci@1f,4000/pci@4/SUNW,qfe@0,1" 0 "qfe"

"/pci@1f,4000/pci@4/SUNW,qfe@1,1" 1 "qfe"

"/pci@1f,4000/pci@4/SUNW,qfe@2,1" 2 "qfe"

"/pci@1f,4000/pci@4/SUNW,qfe@3,1" 3 "qfe"

"/pci@1f,2000/pci@1/SUNW,qfe@0,1" 4 "qfe"

"/pci@1f,2000/pci@1/SUNW,qfe@1,1" 5 "qfe"

"/pci@1f,2000/pci@1/SUNW,qfe@2,1" 6 "qfe"

"/pci@1f,2000/pci@1/SUNW,qfe@3,1" 7 "qfe"

Output from “ls -l /etc/hostname.*” is:

-rw-r--r--   1 root     other         14 Jun 10 11:25 hostname.hme0

-rw-r--r--   1 root     other         14 Jun 10 11:25 hostname.eri0

-rw-r--r--   1 root     other         13 Jun 10 11:25 hostname.eri1

-rw-r--r--   1 root     other         13 Jun 10 11:25 hostname.eri1:1

-rw-r--r--   1 root     other         14 Jun 10 11:25 hostname.eri1:2

-rw-r--r--   1 root     other         12 Jun 10 11:25 hostname.eri1:3

-rw-r--r--   1 root     other         13 Jun 10 11:25 hostname.eri2

-rw-r--r--   1 root     other         13 Jun 10 11:25 hostname.eri2:1

-rw-r--r--   1 root     other         14 Jun 10 11:25 hostname.eri2:2

-rw-r--r--   1 root     other         12 Jun 10 11:25 hostname.eri2:3

After change, the output should be:

-rw-r--r--   1 root     other         14 Jun 10 11:25 hostname.hme0

-rw-r--r--   1 root     other         14 Jun 10 11:25 hostname.qfe0

-rw-r--r--   1 root     other         13 Jun 10 11:25 hostname.qfe1

-rw-r--r--   1 root     other         13 Jun 10 11:25 hostname.qfe1:1

-rw-r--r--   1 root     other         14 Jun 10 11:25 hostname.qfe1:2

-rw-r--r--   1 root     other         12 Jun 10 11:25 hostname.qfe1:3

-rw-r--r--   1 root     other         13 Jun 10 11:25 hostname.qfe2

-rw-r--r--   1 root     other         13 Jun 10 11:25 hostname.qfe2:1

-rw-r--r--   1 root     other         14 Jun 10 11:25 hostname.qfe2:2

-rw-r--r--   1 root     other         12 Jun 10 11:25 hostname.qfe2:3

Step 17   Reboot the machine to pick up new TIMEZONE setting:

<hostname># sync; sync; reboot

- Wait for the system to boot up. Then log in as root.

Step 18   <hostname># /opt/Build/install.sh –upgrade

- Enter “900-04.02.00.V11”, then enter “y” to confirm

- Answer “y” when prompted

- The upgrade process will apply OS patches

Step 19   Wait for the system to boot up. Then Log in as root.

Step 20   <hostname># /opt/Build/install.sh –upgrade

Step 21   Answer "y" when prompted. This process will take up to 15 minutes to complete.

Step 22   Answer "y" when prompted for reboot after installation.

Step 23   Wait for the system to boot up. Then Log in as root.

Step 24   <hostname># platform start

Step 25   <hostname># mv /etc/rc3.d/_S99platform /etc/rc3.d/S99platform

# Task 5: Copying oracle data

# From EMS side A

Step 1   <hostname># /etc/rc2.d/S75cron stop

Step 2   Copying data.

<hostname>$ su – oracle

<hostname>$ cd /opt/oracle/admin/upd

<hostname>$ java dba.dmt.DMMgr –loadconfig

<hostname>$ java dba.dmt.DMMgr –reset copy

<hostname>$ java dba.dmt.DMMgr –copy all

Step 3   Verify the FAIL=0 is reported.

<hostname>$ grep "FAIL=" DMMgr.log

Step 4   Verify there is no constraint warning reported.

<hostname>$ grep constraint DMMgr.log | grep –i warning

Step 5   If FAIL count is not 0 on step 3 or there is constraint warning on step 4, sftp /opt/oracle/admin/upd/DMMgr.log file off system, call Cisco support for immediate technical assistance.

Step 6   <hostname>$ exit

Step 7   <hostname># /etc/rc2.d/S75cron start

Step 8   <hostname># mv /etc/rc3.d/_S99platform /etc/rc3.d/S99platform

# Task 6: Restore Hub communication

# From EMS Side B

Step 1   Log in as CLI user

Step 2   <hostname># /opt/ems/utils/updMgr.sh –restore_hub

# Task 7: To install CORBA on EMS side A, please follow Appendix I.

Chapter 8

Finalizing Upgrade

# Task 1: Switchover activity from side B to side A

This procedure will force the active system activity from side B to side A.

# From EMS side B

|  | Note In the commands below, "xxx", "yyy" or "zzz" is the instance for the process on your system. |
| --- | --- |

Step 1   Log in to EMS side B as CLI user.

Step 2   CLI> control call-agent id=CA100; target-state=forced-active-standby;

Step 3   CLI> control feature-server id=FSPTC101; target-state=forced-active-standby;

Step 4   CLI> control feature-server id=FSAIN102; target-state=forced-active-standby;

Step 5   CLI> control bdms id=BDMS01; target-state=forced-active-standby;

Step 6   CLI> control element-manager id=EM01; target-state=forced-active-standby;

Step 7   CLI shell session should be terminated when last CLI commands completes.

# Task 2: Enable Oracle DB replication

# From EMS side B

Step 1   Restore Oracle DB to duplex mode:

<hostname># su - oracle

<hostname>$ cd /opt/oracle/admin/utl

<hostname>$ rep_toggle –s optical2 –t set_duplex

- Answer “y” when prompt

- Answer “y” again when prompt

Step 2   <hostname>$ exit

Step 3   <hostname># platform stop all

Step 4   Start applications to activate DB in duplex mode.

<hostname># platform start

# Task 3: Synchronize handset provisioning data

# From EMS side A

|  | Note In the commands below, "xxx", "yyy" or "zzz" is the instance for the process on your system. |
| --- | --- |

Step 1   Log in as ciscouser (password: ciscosupport)

Step 2   CLI> sync termination master=CA100; target=EMS;

- Verify the transaction is executed successfully.

Step 3   CLI> sync radius-profile master=EMS; target=FSPTC101;

- Verify the transaction is executed successfully.

Step 4   CLI> sync sc1d master=FSPTC101; target=EMS;

- Verify the transaction is executed successfully

Step 5   CLI> sync sc2d master=FSPTC101; target=EMS;

- Verify the transaction is executed successfully

Step 6   CLI> sync sle master=FSPTC101; target=EMS;

- Verify the transaction is executed successfully

Step 7   CLI> sync subscriber-feature-data master=FSPTC101; target=EMS;

- Verify the transaction is executed successfully

Step 8   CLI> exit

# Task 4: Restore the system to normal mode

This procedure will remove the forced switch and restore the system to NORMAL state.

# From EMS side A

|  | Note In the commands below, "xxx", "yyy" or "zzz" is the instance for the process on your system. |
| --- | --- |

Step 1   Log in as CLI user.

Step 2   CLI> control call-agent id=CA100; target-state=normal;

Step 3   CLI> control feature-server id=FSPTC101; target-state=normal;

Step 4   CLI> control feature-server id=FSAIN102; target-state=normal;

Step 5   CLI> control bdms id=BDMS01; target-state=normal;

Step 6   CLI> control element-manager id=EM01; target-state=normal;

Step 7   CLI> exit

# Task 5: Restore customized cron jobs

Please add back customer specific cron jobs to the system using crontab command. Please do not simply copies the old crontab file over the new one. You may need to compare the backed up version of the crontab file to the new crontab file and restore the previous settings. This should be done for all machines in the system.

# Task 6: Verify system status

Verify that the system is operating properly before you leave the site.

Step 1   Verify that the side A systems are in the active state. Use Appendix A for this procedure.

Step 2   Verify that call processing is working without error. Use Appendix B for this procedure.

Step 3   Verify that provisioning is operational from CLI command line, and verify database. Use Appendix C for this procedure.

Step 4   Verify that there are no outstanding major or critical alarms. Use Appendix D for this procedure.

Step 5   Use Appendix E to verify that Oracle database and replication functions are working properly.

Step 6   If you have answered NO to any of the above questions (Step 1-5) do not proceed. Instead, use the backout procedure in Appendix H. Contact Cisco support if you need assistance.

Once the site has verified that all critical call-thru testing has successfully completed and the upgrade is complete, Appendix F should be executed to gather an up to date archive file of the system.

You have completed the Cisco BTS 10200 system upgrade process successfully.

For Disk Mirroring, please refer to Appendix K.

Appendix A

Check System Status

The purpose of this procedure is to verify the system is running in NORMAL mode, with the side A systems in ACTIVE state and the side B systems in STANDBY state.

|  | Note In the commands below, "xxx", "yyy" or "zzz" is the instance for the process on your system, and DomainName is your system domain name. |
| --- | --- |

# From Active EMS side A

Step 1   Log in as CLI user.

Step 2   CLI> status system;

System response:

Checking Call Agent status ... Checking Feature Server status ... Checking Billing Server status ... Checking Billing Oracle status ... Checking Element Manager status ... Checking EMS MySQL status ... Checking ORACLE status ... CALL AGENT STATUS IS... -> APPLICATION INSTANCE -> Call Agent [CA146] PRIMARY STATUS -> ACTIVE_NORMAL SECONDARY STATUS -> STANDBY_NORMAL FEATURE SERVER STATUS IS... -> APPLICATION INSTANCE -> Feature Server [FSPTC235] PRIMARY STATUS -> ACTIVE_NORMAL SECONDARY STATUS -> STANDBY_NORMAL FEATURE SERVER STATUS IS... -> APPLICATION INSTANCE -> Feature Server [FSAIN205] PRIMARY STATUS -> ACTIVE_NORMAL SECONDARY STATUS -> STANDBY_NORMAL BILLING SERVER STATUS IS... -> APPLICATION INSTANCE -> Bulk Data Management Server [BDMS01] PRIMARY STATUS -> ACTIVE_NORMAL SECONDARY STATUS -> STANDBY_NORMAL BILLING ORACLE STATUS IS... -> Daemon is running! ELEMENT MANAGER STATUS IS... -> APPLICATION INSTANCE -> Element Manager [EM01] PRIMARY STATUS -> ACTIVE_NORMAL SECONDARY STATUS -> STANDBY_NORMAL EMS MYSQL STATUS IS ... -> Daemon is running! ORACLE STATUS IS... -> Daemon is running! Reply : Success:

Appendix B

Check Call Processing

This procedure verifies that call processing is functioning without error. The billing record verification is accomplished by making a sample phone call and verify the billing record is collected correctly.

# From EMS side A

Step 1   Log in as CLI user.

Step 2   Make a new phone call on the system. Verify that you have two-way voice communication. Then hang up both phones.

Step 3   CLI> report billing-record tail=1;

.. CALLTYPE=TOLL SIGSTARTTIME=2004-05-03 17:05:21 SIGSTOPTIME=2004-05-03 17:05:35 CALLELAPSEDTIME=00:00:00 INTERCONNECTELAPSEDTIME=00:00:00 ORIGNUMBER=4692551015 TERMNUMBER=4692551016 CHARGENUMBER=4692551015 DIALEDDIGITS=9 4692551016# 5241 ACCOUNTCODE=5241 CALLTERMINATIONCAUSE=NORMAL_CALL_CLEARING ORIGSIGNALINGTYPE=0 TERMSIGNALINGTYPE=0 ORIGTRUNKNUMBER=0 TERMTRUNKNUMBER=0 OUTGOINGTRUNKNUMBER=0 ORIGCIRCUITID=0 TERMCIRCUITID=0 ORIGQOSTIME=2004-05-03 17:05:35 ORIGQOSPACKETSSENT=0 ORIGQOSPACKETSRECD=7040877 ORIGQOSOCTETSSENT=0 ORIGQOSOCTETSRECD=1868853041 ORIGQOSPACKETSLOST=805306368 ORIGQOSJITTER=0 ORIGQOSAVGLATENCY=0 TERMQOSTIME=2004-05-03 17:05:35 TERMQOSPACKETSSENT=0 TERMQOSPACKETSRECD=7040877 TERMQOSOCTETSSENT=0 TERMQOSOCTETSRECD=1868853041 TERMQOSPACKETSLOST=805306368 TERMQOSJITTER=0 TERMQOSAVGLATENCY=0 PACKETIZATIONTIME=0 SILENCESUPPRESSION=1 ECHOCANCELLATION=0 CODECTYPE=PCMU CONNECTIONTYPE=IP OPERATORINVOLVED=0 CASUALCALL=0 INTERSTATEINDICATOR=0 OVERALLCORRELATIONID=CA14633 TIMERINDICATOR=0 RECORDTYPE=NORMAL RECORD CALLAGENTID=CA146 ORIGPOPTIMEZONE=CDT ORIGTYPE=ON NET TERMTYPE=ON NET NASERRORCODE=0 NASDLCXREASON=0 ORIGPOPID=69 TERMPOPID=69 TERMPOPTIMEZONE=CDT DIALPLANID=cdp1 CALLINGPARTYCATEGORY=Ordinary Subscriber CALLEDPARTYINDICATOR=No Indication Reply : Success: Entry 1 of 1 returned from host: priems44

Step 4   Verify that the attributes in the CDR match the call just made.

Appendix C

Check Provisioning and Database

# From EMS side A

The purpose of this procedure is to verify that provisioning is functioning without error. The following commands will add a "dummy" carrier then delete it.

Step 1   Log in as CLI user.

Step 2   CLI> add carrier id=8080;

Step 3   CLI> show carrier id=8080;

Step 4   CLI> delete carrier id=8080;  

Step 5   CLI> show carrier id=8080;

- Verify message is: Database is void of entries.

# Check transaction queue

In this task, you will verify that the OAMP transaction queue status. The queue should be empty.

Step 1   CLI> show transaction-queue;

- Verify there is no entry shown. You should get following reply back:

Reply : Success: Database is void of entries.

- If the queue is not empty, wait for the queue to empty. If the problem persists, contact Cisco support.

Step 2   CLI>exit

# Perform database audit

This task may take up to one hour to complete.

In this task, you will perform a full database audit and correct any errors, if necessary.

Step 1   CLI> audit database type=full;

Step 2   Check the audit report and verify there is no discrepancy or errors. If errors are found, please try to correct them. If you are unable to correct, please contact Cisco support.

Appendix D

Check Alarm Status

The purpose of this procedure is to verify that there are no outstanding major/critical alarms.

# From EMS side A

Step 1   Log in as CLI user.

Step 2  CLI> show alarm

- The system responds with all current alarms, which must be verified or cleared before proceeding with next step.

|  | Tip Use the following command information for reference material ONLY. |
| --- | --- |

Step 3   To monitor system alarm continuously.

CLI> subscribe alarm-report severity=all; type=all;

|  | Valid severity: MINOR, MAJOR, CRITICAL, ALL Valid types: CALLP, CONFIG, DATABASE, MAINTENANCE, OSS, SECURITY, SIGNALING, STATISTICS, BILLING, ALL, SYSTEM, AUDIT |
| --- | --- |

Step 4   System will display alarms if alarm is reported.

<------------------- START ALARM REPORT --------------------> TIMESTAMP: 20040503174759 DESCRIPTION: General MGCP Signaling Error between MGW and CA. TYPE & NUMBER: SIGNALING (79) SEVERITY: MAJOR ALARM-STATUS: OFF ORIGIN: MGA.PRIMARY.CA146 COMPONENT-ID: null ENTITY NAME: S0/DS1-0/1@64.101.150.181:5555 GENERAL CONTEXT: MGW_TGW SPECIFC CONTEXT: NA FAILURE CONTEXT: NA <------------------- END ALARM REPORT ---------------------->

Step 5   To stop monitoring system alarm.

CLI> unsubscribe alarm-report severity=all; type=all;

Step 6   Exit CLI.

CLI> exit

Appendix E

Check Oracle Database Replication and Error Correction

Perform the following steps on the Active EMS side A to check the Oracle database and replication status.

# Check Oracle DB replication status

# From EMS side A

Step 1   Log in as root.

Step 2   Log in as oracle.

<hostname># su – oracle

Step 3   Enter the command to check replication status and compare contents of tables on the side A and side B EMS databases:

<hostname>$dbadm –C rep

Step 4   Verify that “Deferror is empty?” is “YES”.

OPTICAL1::Deftrandest is empty?           YES

OPTICAL1::dba_repcatlog is empty?       YES

OPTICAL1::Deferror is empty?              YES (Make sure it is “YES”

OPTICAL1::Deftran is empty?                  YES

OPTICAL1::Has no broken job?               YES

OPTICAL1::JQ Lock is empty?                YES

OPTICAL2::Deftrandest is empty?          YES

OPTICAL2::dba_repcatlog is empty?      YES

OPTICAL2::Deferror is empty?             YES (Make sure it is “YES”

OPTICAL2::Deftran is empty?                YES

OPTICAL2::Has no broken job?              YES

OPTICAL2::JQ Lock is empty?               YES

Step 5   If the “Deferror is empty?” is “NO”, please try to correct the error using steps in “Correct replication error” below. If you are unable to clear the error or if any of the individual steps fails, please contact Cisco support.

# Correct replication error

|  | Note You must run the following steps on standby EMS side B first, then on active EMS side A. |
| --- | --- |

# From EMS Side B

Step 1   Log in as root

Step 2   <hostname># su – oracle

Step 3   <hostname>$ dbadm –C db

Step 4   For each table that is out of sync, please run the following step:

<hostname>$ dbadm -A copy -o <OWNER> -t <TABEL NAME>

- Enter “y” to continue

- Please contact Cisco support if the above command fails.

Step 5   <hostname>$ dbadm –A truncate_deferror

- Enter “y” to continue

# From EMS Side A

Step 1   <hostname>$ dbadm –A truncate_deferror

- Enter “y” to continue

Step 2   Re-verify that “Deferror is empty?” is “YES” and none of tables is out of sync.

<hostname>$dbadm –C db

OPTICAL1::Deftrandest is empty?           YES

OPTICAL1::dba_repcatlog is empty?       YES

OPTICAL1::Deferror is empty?              YES ( Make sure it is “YES”

OPTICAL1::Deftran is empty?                  YES

OPTICAL1::Has no broken job?               YES

OPTICAL1::JQ Lock is empty?                YES

OPTICAL2::Deftrandest is empty?          YES

OPTICAL2::dba_repcatlog is empty?      YES

OPTICAL2::Deferror is empty?             YES ( Make sure it is “YES”

OPTICAL2::Deftran is empty?                YES

OPTICAL2::Has no broken job?              YES

OPTICAL2::JQ Lock is empty?               YES

Appendix F

Check and Sync System Clock

This section describes steps to verify the system clock among machines in a BTS system is in sync. Otherwise, correctional steps are provided to sync up the clock in the system.

# Task 1: Check system clock

# From each machine in a BTS system

Step 1   Log in as root.

Step 2   <hostname># date

- Check and verify the date and time is in agreement with other machines in the system.

- If the date and time shown on one machine does not agree with others, please follow the steps in the Task 2 to sync up the clock.

# Task 2: Sync system clock

# From each machine in a BTS system

Step 1   <hostname># /etc/rc2.d/S79xntp stop

Step 2   <hostname># cd /opt/BTSxntp/bin

Step 3   <hostname># ntpdate <NTP server IP address>

Step 4   <hostname># /etc/rc2.d/S79xntp start <Return

Appendix G

Backout Procedure for Side B Systems

# Introduction

This procedure allows you to back out of the upgrade procedure if any verification checks (in "Verify Call/System Status" section) failed. This procedure is intended for the scenario in which the side B systems have been upgraded to the new load, while the side A systems are still at the previous load. The procedure will back out the side B systems to the previous load.

This backout procedure will:

- Restore the side A systems to active mode without making any changes to it

- Revert to the previous application load on the side B systems

- Restart the side B systems in standby mode

- Verify that the system is functioning properly with the previous load

|  | Note In addition to performing this backout procedure, you should contact Cisco support when you are ready to retry the upgrade procedure. |
| --- | --- |

The flow for this procedure is shown in.

Figure F-1   Flow of Backout Procedure— Side B Only

# Task 1: Force side A systems to active

This procedure will force the side A systems to forced active state, and the side B systems to forced standby state.

|  | Note In the commands below, "xxx", "yyy" or "zzz" is the instance for the process on your system. |
| --- | --- |

# From EMS side B

Step 1   Log in as CLI user.

Step 2   CLI> control call-agent id=CA100; target-state=forced-active-standby;

Step 3   CLI> control feature-server id=FSPTC101; target-state=forced-active-standby;

Step 4   CLI> control feature-server id=FSAIN102; target-state=forced-active-standby;

Step 5   CLI> control bdms id=BDMS01; target-state=forced-active-standby;

Step 6   CLI> control element-manager id=EM01; target-state=forced-active-standby;

Step 7   CLI session will terminate when the last CLI command completes.

# Task 2: SFTP Billing records to a mediation device

# From EMS side B

Step 1   Log in as root

Step 2   <hostname># ls /opt/bms/ftp/billing

Step 3   If there are files listed, then SFTP the files to a mediation device on the network and remove the files from the /opt/bms/ftp/billing directory

# Task 3: Sync DB usage

# From EMS side A

In this task, you will sync db-usage between two releases.

Step 1   Log in as root

Step 2   <hostname># su – oracle

Step 3   <hostname>$ java dba.adm.DBUsage –sync

- Verify Number of tables out-of-sync is 0.

Step 4   <hostname>$ exit

# Task 4: Shutdown side B systems

# From EMS side B

Step 1   Log in as root.

Step 2  <hostname># sync; sync

Step 3  <hostname># halt

# From CA/FS side B

Step 1   Log in as root.

Step 2   <hostname># sync; sync

Step 3  <hostname># halt

# Task 5: Restore side B systems to the old release

# From CA/FS side B

Step 1   Power off the machine using toggle switch by toggle the switch down for 5 seconds

Step 2   Remove disk0 from slot 0 off the machine

Step 4   Place disk labeled “Release 4.2.0.V11 CA/FS side B disk0” in slot 0

Step 6   Power on the machine using toggle switch by toggle the switch up for 5 seconds

- Allow the system to boot up by monitoring the boot process thru console

Step 7   Log in as root.

Step 8  <hostname># platform start

Step 9  <hostname># mv /etc/rc3.d/_S99platform /etc/rc3.d/S99platform

# From EMS side B

Step 1   Power off the machine using toggle switch by toggle the switch down for 5 seconds

Step 2   Remove disk0 from slot 0 off the machine

Step 4   Place disk labeled “Release 4.2.0.V11 EMS side B disk0” in slot 0

Step 6   Power on the machine using toggle switch by toggle the switch up for 5 seconds

- Allow the system to boot up by monitoring the boot process thru console

Step 7   Log in as root.

Step 8   <hostname># platform start

Step 9   <hostname># mv /etc/rc3.d/_S99platform /etc/rc3.d/S99platform

# Task 6: Restore EMS mate communication

In this task, you will restore the OMS Hub communication from EMS side A to side B.

# From EMS side A

Step 1   Log in as root

Step 2   <hostname># /opt/ems/utils/updMgr.sh –restore_hub

Step 3   <hostname># nodestat

- Verify OMS Hub mate port status is established.

- Verify HUB communication from EMS side A to CA/FS side B is established.

# Task 7: Switchover activity to EMS side B

# From Active EMS side A

Step 1   Log in as CLI user.

Step 2   CLI> control bdms id=BDMS01; target-state=forced-standby-active;

Step 3   CLI> control element-manager id=EM01; target-state=forced-standby-active;

Step 4    CLI Log in session will be terminated when switchover is completed.

# Task 8: Enable Oracle DB replication on EMS side A

# From EMS side A

Step 1   Log in as Oracle user:

<hostname># su - oracle

<hostname>$ cd /opt/oracle/admin/utl

Step2   Restore Oracle DB replication:

<hostname>$ rep_toggle –s optical1 –t set_duplex

- Answer “y” when prompt

- Answer “y” again when prompt

Step 3   <hostname>$ exit

Step 4   <hostname># platform stop all

Step 5   Start applications to activate DB in duplex mod.

<hostname># platform start

# Task 9: Synchronize handset provisioning data

# From EMS side B

|  | Note In the commands below, "xxx", "yyy" or "zzz" is the instance for the process on your system. |
| --- | --- |

Step 1   Log in as ciscouser (password: ciscosupport)

Step 2   CLI> sync termination master=CA100; target=EMS;

- Verify the transaction is executed successfully.

Step 3   CLI> sync sc1d master=FSPTC101; target=EMS;

- Verify the transaction is executed successfully

Step 4   CLI> sync sc2d master=FSPTC101; target=EMS;

- Verify the transaction is executed successfully

Step 5   CLI> sync sle master=FSPTC101; target=EMS;

- Verify the transaction is executed successfully

Step 6   CLI> sync subscriber-feature-data master=FSPTC101; target=EMS;

- Verify the transaction is executed successfully

Step 7   CLI> exit

# Task 10: Switchover activity from EMS side B to EMS side A

# From EMS side B

Step 1   Log in as CLI user.

Step 2   CLI> control bdms id=BDMS01; target-state=forced-active-standby;

Step 3   CLI> control element-manager id=EM01; target-state=forced-active-standby;

Step 4    CLI Log in session will be terminated when switchover is completed.

# Task 11: Restore system to normal mode

# From EMS side A

Step 1   Log in as CLI user.

Step 2   CLI> control feature-server id=FSPTC101; target-state=normal;

Step 3   CLI> control feature-server id=FSAIN102; target-state=normal;

Step 4   CLI> control call_agent id=CA100; target-state=normal;

Step 5   CLI> control bdms id=BDMS01; target-state=normal;

Step 6   CLI> control element-manager id=EM01; target-state=normal;

Step 7   CLI> exit

# Task 12: Verify system status

Verify that the system is operating properly before you leave the site.

Step 1   Verify that the side A systems are in the active state. Use Appendix A for this procedure.

Step 2   Verify that call processing is working without error. Use Appendix B for this procedure.

Step 3   Verify that provisioning is operational from CLI command line, and verify database. Use Appendix C for this procedure.

Step 4   Verify that there are no outstanding major or critical alarms. Use Appendix D for this procedure.

Step 5   Use Appendix E to verify that Oracle database and replication functions are working properly.

Step 6   If you answered NO to any of the above questions (Step 1 through Step 5), Contact Cisco support for assistance.

You have completed the side B of Cisco BTS 10200 system fallback process successfully.

Appendix H

System Backout Procedure

# Introduction

This procedure allows you to back out of the upgrade procedure if any verification checks (in "Verify system status" section) failed. This procedure is intended for the scenario in which both the side A and side B systems have been upgraded to the new load. The procedure will back out the entire system to the previous load.

This backout procedure will:

- Revert to the previous application load on the side A systems

- Restart the side A systems and place it in active mode

- Revert to the previous application load on the side B systems

- Restart the side B systems and place it in active mode

- Verify that the system is functioning properly with the previous load

|  | Note In addition to performing this backout procedure, you should contact Cisco support when you are ready to retry the upgrade procedure. |
| --- | --- |

# Task 1: Disable Oracle DB replication on EMS side B

# From Active EMS

Step 1   Log in as CLI user.

Step 2   CLI> control bdms id=BDMS01; target-state=forced-active-standby;

Step 3   CLI> control element-manager id=EM01; target-state=forced-active-standby;

Step 4   CLI> exit

# From EMS side B

Step 1   Log in as Oracle user:

<hostname># su – oracle

<hostname>$ cd /opt/oracle/admin/utl

Step 2   Set Oracle DB to simplex mode:

<hostname>$ rep_toggle –s optical2 –t set_simplex

- Answer “y” when prompt

- Answer “y” again when prompt

Step 3   <hostname>$ exit

Step 4   <hostname># platform stop all

Step 5   Start applications to activate DB in simplex mode.

<hostname># platform start

# Task 2: Inhibit EMS mate communication

In this task, you will isolate the OMS Hub on EMS side B from talking to CA/FS side A.

# From EMS side B

Step 1   Log in as root

Step 2   <hostname># /opt/ems/utils/updMgr.sh –split_hub

Step 3   <hostname># nodestat

- Verify there is no HUB communication from EMS side B to CA/FS side A.

# Task 3: Force side B systems to active

This procedure will force the side B systems to go active.

|  | Note In the commands below, "xxx", "yyy" or "zzz" is the instance for the process on your system. |
| --- | --- |

# From EMS side A

Step 1   Log in as CLI user.

Step 2   CLI> control call-agent id=CA100; target-state=forced-standby-active;

Step 3   CLI> control feature-server id=FSPTC101; target-state=forced-standby-active;

Step 4   CLI> control feature-server id=FSAIN102; target-state=forced-standby-active;

Step 5   CLI> control bdms id=BDMS01; target-state=forced-standby-active;

Step 6   CLI> control element-manager id=EM01; target-state=forced-standby-active;

Step 7   CLI session will terminate when the last CLI command completes.

# Task 4: FTP Billing records to a mediation device

# From EMS side A

Step 1   Log in as root

Step 2   <hostname># ls /opt/bms/ftp/billing

Step 3   If there are files listed, then SFTP the files to a mediation device on the network and remove the files from the /opt/bms/ftp/billing directory

# Task 5: Shutdown side A systems

# From EMS side A

Step 1   Log in as root.

Step 2  <hostname># sync; sync

Step 3  <hostname># shutdown –i5 –g0 –y

# From CA/FS side A

Step 1   Log in as root.

Step 2   <hostname># sync; sync

Step 3  <hostname># shutdown –i5 –g0 –y

# Task 6: Restore side A systems to the old release

# From CA/FS side A

Step 1   Power off the machine using toggle switch by toggle the switch down for 5 seconds

Step 2   Remove disk0 from slot 0 off the machine

Step 4   Place disk labeled “Release 4.2.0.V11 CA/FS side A disk0” in slot 0

Step 6   Power on the machine using toggle switch by toggle the switch up for 5 seconds

- Allow the system to boot up by monitoring the boot process thru console

Step 7   Log in as root.

Step 8  <hostname># platform start

Step 9  <hostname># mv /etc/rc3.d/_S99platform /etc/rc3.d/S99platform

# From EMS side A

Step 1   Power off the machine using toggle switch by toggle the switch down for 5 seconds

Step 2   Remove disk0 from slot 0 off the machine

Step 4   Place disk labeled “Release 4.2.0.V11 EMS side A disk0” in slot 0

Step 6   Power on the machine using toggle switch by toggle the switch up for 5 seconds

- Allow the system to boot up by monitoring the boot process thru console

Step 7   Log in as root.

Step 8   <hostname># platform start

Step 9  <hostname># mv /etc/rc3.d/_S99platform /etc/rc3.d/S99platform

# Task 7: Inhibit EMS mate communication

In this task, you will isolate the OMS Hub on EMS side A from talking to side B.

# From EMS side A

Step 1   Log in as root

Step 2   <hostname># /opt/ems/utils/updMgr.sh –split_hub

Step 3   <hostname># nodestat

- Verify there is no HUB communication from EMS side A to CA/FS side B.

- Verify OMS Hub mate port status: No communication between EMS

# Task 8: Disable Oracle DB replication on EMS side A

# From EMS side A

Step 1   <hostname># /etc/rc2.d/S75cron stop

Step 2   Log in as Oracle user.

<hostname># su – oracle

<hostname>$ cd /opt/oracle/admin/utl

Step 3   Set Oracle DB to simplex mode:

<hostname>$ rep_toggle –s optical1 –t set_simplex

- Answer “y” when prompt

- Answer “y” again when prompt

Step 4   <hostname>$ exit

Step 5   <hostname># platform start

Step 6   <hostname># /etc/rc2.d/S75cron start

Step 7   <hostname># mv /etc/rc3.d/_S99platform /etc/rc3.d/S99platform

# Task 9: To continue fallback process, please follow Appendix G.

You have completed the Cisco BTS 10200 system fallback process successfully

Appendix I

CORBA Installation

This procedure describes how to install the Common Object Request Broker Architecture (CORBA) application on Element Management System (EMS) of the Cisco BTS 10200 Softswitch.

Note This installation process is used for both side A and side B EMS.

Caution This CORBA installation will remove existing CORBA application on EMS machines. Once you have executed this procedure, there is no backout. Do not start this procedure until you have proper authorization. If you have questions, please contact Cisco Support.

# Task 1: Open Unix Shell on EMS

Perform these steps to open a Unix shell on EMS.

Step 1   Ensure that your local PC or workstation has connectivity via TCP/IP to communicate with EMS units.

Step 2   Open a Unix shell or a XTerm window.

Note If you are unable to open a Xterm window, please contact you system administrator immediately.

# Task 2: Install OpenORB CORBA Application

### Remove Installed OpenORB Application

Step 1   Log in as root to EMS

Step 2   Enter the following command to remove the existing OpenORB package:

<hostname># pkgrm BTScis

- Respond with a “y” when prompted

<hostname># pkgrm BTSoorb

- Respond with a “y” when prompted

Step 3   Enter the following command to verify that the CORBA application is removed:

<hostname># pgrep cis3

The system will respond by displaying no data, or by displaying an error message. This verifies that the CORBA application is removed.

### Install OpenORB Packages

The CORBA application files are available for installation once the Cisco BTS 10200 Softswitch is installed.

Step 1   Log in as root to EMS

Step 2   <hostname># cd /opt/Build

Step 3   <hostname># cis-install.sh

You will get the following response, please answer appropriately:

The NameService & CIS modules listen on a specific host interface.

***WARNING*** This host name or IP address MUST resolve on the CORBA

client machine in the OSS. Otherwise, communication failures may occur.

Enter the host name or IP address [ <hostname> ]:

Step 4   If you are running EPOM or you network does not support SSLIOP (secure CORBA protocol), please answer “n”. Otherwise, answer “y” (default).

Should SSLIOP be enabled [ Y ]:

Step 5   The system will give several prompts before and during the installation process. Some prompts are repeated. Respond with a “y” when prompted.

Step 6   It will take about 2-3 minutes for the installation to complete.

Step 7   Verify CORBA Application is running On EMS:

<hostname># pgrep ins3

Note System will respond by displaying the Name Service process ID, which is a number between 2 and 32,000 assigned by the system during CORBA installation. By displaying this ID, the system confirms that the ins3 process was found and is running.

<hostname># pgrep cis3

Note The system will respond by displaying the cis3 process ID, which is a number between 2 and 32,000 assigned by the system during CORBA installation. By displaying this ID, the system confirms that the cis3 process was found and is running.

Step 8   If you do not receive both of the responses described in Step 7, or if you experience any verification problems, do not continue. Contact your system administrator. If necessary, call Cisco SUPPORT for additional technical assistance.

Appendix J

# Preparing Disks for Upgrade

This software upgrade will need 8 disks: 2 for each machine. Each set of 2 disks must have the same model number in order for disk mirroring to work.

The NIDS information required for disk preparation must be different from that used on the system to be upgraded.

# Side A EMS preparation steps

Step 1   Locate a system with the identical hardware as the target machine to be jumpstarted

Step 2   Locate a set of 2 disks with the same make and model number with one disk labeled as “Release 4.4.1 EMS side A disk0” and the other labeled as “Release 4.4.1 EMS side A disk1”.

Step 3   Put each disk into corresponding disk slots in the preparation machine

Step 4   Jumpstart the machine with Solaris 2.8 OS patch Generic_117000-05 and setup disk mirroring

Step 5   <hostname># cd /etc/default

Step 6   <hostname># vi login

- Comment out the line: CONSOLE=/dev/console

Step 7   Configured the network interfaces with 4/2 configuration

Step 8   Stage Cisco BTS 10200 release 4.4.1 to the /opt/Build directory.

Step 9   Construct opticall.cfg and placed it under /etc directory.

<hostname># cd /opt/Build

<hostname># cp /opt/Build/opticall.cfg /etc/.

<hostname># vi /etc/opticall.cfg

  - Fill in all required information and then save the file.

<hostname># ./checkCFG

  - To verify the information entered are free of errors.

Step 10   FTP opticall.cfg to EMS side B and placed it under /etc directory.

Step 11   FTP opticall.cfg to CA/FS side A and placed it under /etc directory.

Step 12   FTP opticall.cfg to CA/FS side B and placed it under /etc directory.

Note: The EMS side A and side B installation must be started in parallel.

Step 11   Install Cisco BTS 10200 release 4.4.1 application software.

<hostname># cd /opt/Build

<hostname># install.sh

  - Answer “y” when prompt.

  - The installation process will install Secure Shell which causes system to be rebooted.

  - Wait for the system to boot up and log back in as root.

Step 12   When the application install completes, rename “S99platform” file.

<hostname># cd /etc/rc3.d

<hostname># mv S99platfrom _S99platform

Step 13   Remove all network interface configuration information from the machine:

<hostname>#  \rm /etc/hostname.*

Step 14   Shutdown the system

<hostname>#  shutdown –i5 –g0 -y

Step 15   Power off the machine and remove the disks to be used for upgrade.

# Side B EMS preparation steps

Step 1   Locate a system with the identical hardware as the target machine to be jumpstarted

Step 2   Locate a set of 2 disks with the same make and model number with one disk labeled as “Release 4.4.1 EMS side B disk0” and the other labeled as “Release 4.4.1 EMS side B disk1”.

Step 3   Put each disk into corresponding disk slots in the preparation machine

Step 4   Jumpstart the machine with Solaris 2.8 OS patch Generic_117000-05 and setup disk mirroring

Step 5   <hostname># cd /etc/default

Step 6   <hostname># vi login

- Comment out the line: CONSOLE=/dev/console

Step 7   Configured the network interfaces with 4/2 configuration

Step 8   Stage Cisco BTS 10200 release 4.4.1 to the /opt/Build directory.

Step 9   Install Cisco BTS 10200 release 4.4.1 application software.

<hostname># cd /opt/Build

<hostname># install.sh

  - Answer “y” when prompt.

  - The installation process will install Secure Shell which causes system to be rebooted.

  - Wait for the system to boot up and log back in as root.

Step 10   When the application install completes, rename “S99platform” file.

<hostname># cd /etc/rc3.d

<hostname># mv S99platfrom _S99platform

Step 11   Remove all network interface configuration information from the machine:

<hostname>#  \rm /etc/hostname.*

Step 12   Shutdown the system

<hostname>#  shutdown –i5 –g0 -y

Step 13   Power off the machine and remove the disks to be used for upgrade.

# Side A CA/FS preparation steps

Step 1   Locate a system with the identical hardware as the target machine to be jumpstarted

Step 2   Locate a set of 2 disks with the same make and model number with one disk labeled as “Release 4.4.1 CA/FS side A disk0” and the other labeled as “Release 4.4.1 CA/FS side A disk1”.

Step 3   Put each disk into corresponding disk slots in the preparation machine

Step 4   Jumpstart the machine with Solaris 2.8 OS patch Generic_117000-05 and setup disk mirroring

Step 5   <hostname># cd /etc/default

Step 6   <hostname># vi login

- Comment out the line: CONSOLE=/dev/console

Step 7   Configured the network interfaces with 4/2 configuration

Step 8   Stage Cisco BTS 10200 release 4.4.1 to the /opt/Build directory.

Step 9   Install BTSbase, BTSinst, BTSossh and BTShard packages:

- <hostname># cd /opt/Build

- <hostname># pkgadd –d . BTSbase

- Answer “y” when prompt

- <hostname># pkgadd –d . BTSinst

- Answer “y” when prompt

- <hostname># pkgadd –d . BTSossh

- Answer “y” when prompt

- <hostname># pkgadd –d . BTShard

- Answer “y” when prompt

- <hostname># mv S99platfrom _S99platform

- <hostname># shutdown –i6 –g0 -y

- Wait for system to boot up and login as root.

Step 10   Remove all network interface configuration information from the machine:

<hostname>#  \rm /etc/hostname.*

Step 11   Update version information:

<hostname># cd /opt/ems/utils

<hostname># echo “900-04.02.00.V11” > Version

Step 12   Shutdown and power off the machine and remove the disks to be used for upgrade.

# Side B CA/FS preparation steps

Step 1   Locate a system with the identical hardware as the target machine to be jumpstarted

Step 2   Locate a set of 2 disks with the same make and model number with one disk labeled as “Release 4.4.1 CA/FS side B disk0” and the other labeled as “Release 4.4.1 CA/FS side B disk1”.

Step 3   Put each disk into corresponding disk slots in the preparation machine

Step 4   Jumpstart the machine with Solaris 2.8 OS patch Generic_117000-05 and setup disk mirroring

Step 5   <hostname># cd /etc/default

Step 6   <hostname># vi login

- Comment out the line: CONSOLE=/dev/console

Step 7   Configured the network interfaces with 4/2 configuration

Step 8   Stage Cisco BTS 10200 release 4.4.1 to the /opt/Build directory.

Step 9   Install BTSbase, BTSinst, BTSossh and BTShard packages:

- <hostname># cd /opt/Build

- <hostname># pkgadd –d . BTSbase

- Answer “y” when prompt

- <hostname># pkgadd –d . BTSinst

- Answer “y” when prompt

- <hostname># pkgadd –d . BTSossh

- Answer “y” when prompt

- <hostname># pkgadd –d . BTShard

- Answer “y” when prompt

- <hostname># mv S99platfrom _S99platform

- <hostname># shutdown –i6 –g0 -y

- Wait for system to boot up and login as root.

Step 10   Remove all network interface configuration information from the machine:

<hostname>#  \rm /etc/hostname.*

Step 11   Update version information:

<hostname># cd /opt/ems/utils

<hostname># echo “900-04.02.00.V11” > Version

Step 12   Shutdown and power off the machine and remove the disks to be used for upgrade.

Appendix K

# Disk Mirroring after Upgrade

This software upgrade will need 4 new disks: 1 for each machine. Each set of 2 disks must have the same model number in order for disk mirroring to work.

## Configuring the Primary Element Management System

To configure the primary EMS, complete the following steps:

Step 1    Login as root.

Step 2    Change directory by entering the following command:

cd /opt/setup

Step 3   Run the setlogic_EMS.sh script to set up the interfaces by entering the following command:

./setlogic_EMS.sh

Step 4    Verify that the /etc/netmasks and /etc/hosts files have the correct values by comparing them to the values in the NIDS.

Step 5    Set up the mirror for the EMS by entering the following command:

./setup_mirror_ems

Note Do not reboot your system if an error occurs. You must fix the error before moving to the next step.

Step 6    Set up the transparent metadevice (transmeta) for the EMS by entering the following command:

./setup_mirror_trans

Step 7    Reboot by entering the following command:

reboot -- -r

Note Wait for the boot before continuing. Then log in to the EMS of the side in which you are working.

Step 8    Log in to the primary EMS as root.

root

Step 9    Change directory by entering the following command:

cd /opt/setup

Step 10    Synchronize the disk by entering the following command:

./sync_mirror

Note Wait for the disks to synchronize before continuing. The synchronization can be verified by running the Resync_status command from the /opt/utils directory. The display will show the resyncing in progress and report resync completion.

Step 11    Exit the primary EMS.

## Configuring the Secondary Element Management System

To configure the secondary EMS, complete the following steps:

Step 1    Login as root.

Step 2    Navigate to the /opt/setup directory by entering the following command:

cd /opt/setup

Step 3    Run the setlogic_EMS.sh script to set up the interfaces.

./setlogic_EMS.sh

Step 4    Verify that the /etc/netmask and /etc/hosts commands have the correct values.

Step 5    Set up a mirror for the EMS by entering the following command:

./setup_mirror_ems

Note  Do not reboot your system if an error occurs. You must fix the error before moving to the next step.

Step 6    Set up the transparent metadevice (transmeta) for the EMS by entering the following command:

./setup_mirror_trans

Step 7    Reboot your system by entering the following command:

reboot -- -r

Note Wait for the boot to finish before continuing. Then log in to the EMS for the side on which you are working.

Step 8    Log in to the secondary EMS as root by entering the following command:

root

Step 9    Change directory by entering the following command:

cd /opt/setup

Step 10    Synchronize the disk by entering the following command:

./sync_mirror

Step 11    Exit the secondary EMS.

## Configuring the Primary Call Agent and Feature Server Installation

To configure the primary CA and FS, complete the following steps:

Step 1    Login as root.

Step 2    Change directories by entering the following command:

cd /opt/setup

Step 3    Run the ./setlogic_CA.sh script to set up the interfaces.

./setlogic_CA.sh

Step 4    Verify that the /etc/netmask, /etc/defaultrouter, and /etc/hosts files have the correct values by comparing them to the values in the NIDS. Make sure all three match the NIDS.

Step 5    Set up the mirror for the CA/FS and watch for errors by entering the following command:

./setup_mirror_ca

Note  Do not reboot your system if an error occurs. You must fix the error before moving to the next step.

Step 6    Setup trans for the CA/FS and watch for errors by entering the following command:

./setup_trans

Step 7    Reboot your system by entering the following command:

reboot

Step 8    Log in to the primary CA as root by entering the following command:

root

Step 9    Mirror the disks as follows:

a. Change directory by entering the following command:

cd /opt/setup

b. Mirror the disks by entering the following command:

./sync_mirror

## Configuring the Secondary Call Agent and Feature Server Installation

To configure the primary CA and FS, complete the following steps:

Step 1    Login as root.

Step 2    Change directories by entering the following command:

cd /opt/setup

Step 3    Run the ./setlogic_CA.sh script to set up the interfaces.

./setlogic_CA.sh

Step 4    Verify that the /etc/netmask, and /etc/hosts files have the correct values by comparing them to the values in the NIDS. Make sure all three match the NIDS.

Step 5    Set up the mirror for the CA/FS and watch for errors by entering the following command:

./setup_mirror_ca

Note  Do not reboot your system if an error occurs. You must fix the error before moving to the next step.

Step 6    Setup trans for the CA/FS and watch for errors by entering the following command:

./setup_trans

Step 7    Reboot your system by entering the following command:

reboot

Step 8    Log in to the secondary CA as root by entering the following command:

root

Step 9    Mirror the disks as follows:

a. Change directory by entering the following command:

cd /opt/setup

b. Mirror the disks by entering the following command:

./sync_mirror