Cisco BTS 10200 Softswitch

Application Installation

Release 4.5.13, 4.5.0V14 and above, 4.5.1

January 2,  2007

Corporate Headquarters

Cisco Systems, Inc.

170 West Tasman Drive

San Jose, CA 95134-1706

USA

http://www.cisco.com

Tel: 	408 526-4000

800 553-NETS (6387)

Fax:	408 526-4100

THE SPECIFICATIONS AND INFORMATION REGARDING THE PRODUCTS IN THIS MANUAL ARE SUBJECT TO CHANGE WITHOUT NOTICE. ALL STATEMENTS, INFORMATION, AND RECOMMENDATIONS IN THIS MANUAL ARE BELIEVED TO BE ACCURATE BUT ARE PRESENTED WITHOUT WARRANTY OF ANY KIND, EXPRESS OR IMPLIED. USERS MUST TAKE FULL RESPONSIBILITY FOR THEIR APPLICATION OF ANY PRODUCTS.

THE SOFTWARE LICENSE AND LIMITED WARRANTY FOR THE ACCOMPANYING PRODUCT ARE SET FORTH IN THE INFORMATION PACKET THAT SHIPPED WITH THE PRODUCT AND ARE INCORPORATED HEREIN BY THIS REFERENCE. IF YOU ARE UNABLE TO LOCATE THE SOFTWARE LICENSE OR LIMITED WARRANTY, CONTACT YOUR CISCO REPRESENTATIVE FOR A COPY.

The Cisco implementation of TCP header compression is an adaptation of a program developed by the University of California, Berkeley (UCB) as part of UCB’s public domain version of the UNIX operating system. All rights reserved. Copyright © 1981, Regents of the University of California.

NOTWITHSTANDING ANY OTHER WARRANTY HEREIN, ALL DOCUMENT FILES AND SOFTWARE OF THESE SUPPLIERS ARE PROVIDED “AS IS” WITH ALL FAULTS. CISCO AND THE ABOVE-NAMED SUPPLIERS DISCLAIM ALL WARRANTIES, EXPRESSED OR IMPLIED, INCLUDING, WITHOUT LIMITATION, THOSE OF MERCHANTABILITY, FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT OR ARISING FROM A COURSE OF DEALING, USAGE, OR TRADE PRACTICE.

IN NO EVENT SHALL CISCO OR ITS SUPPLIERS BE LIABLE FOR ANY INDIRECT, SPECIAL, CONSEQUENTIAL, OR INCIDENTAL DAMAGES, INCLUDING, WITHOUT LIMITATION, LOST PROFITS OR LOSS OR DAMAGE TO DATA ARISING OUT OF THE USE OR INABILITY TO USE THIS MANUAL, EVEN IF CISCO OR ITS SUPPLIERS HAVE BEEN ADVISED OF THE POSSIBILITY OF SUCH DAMAGES.

CCIP, CCSP, the Cisco Arrow logo, the Cisco Powered Network mark, the Cisco Systems Verified logo, Cisco Unity, Follow Me Browsing, FormShare, iQ Breakthrough, iQ FastTrack, the iQ Logo, iQ Net Readiness Scorecard, Networking Academy, ScriptShare, SMARTnet, TransPath, and Voice LAN are trademarks of Cisco Systems, Inc.; Changing the Way We Work, Live, Play, and Learn, The Fastest Way to Increase Your Internet Quotient, and iQuick Study are service marks of Cisco Systems, Inc.; and Aironet, ASIST, BPX, Catalyst, CCDA, CCDP, CCIE, CCNA, CCNP, Cisco, the Cisco Certified Internetwork Expert logo, Cisco IOS, the Cisco IOS logo, Cisco Press, Cisco Systems, Cisco Systems Capital, the Cisco Systems logo, Empowering the Internet Generation, Enterprise/Solver, EtherChannel, EtherSwitch, Fast Step, GigaStack, Internet Quotient, IOS, IP/TV, iQ Expertise, LightStream, MGX, MICA, the Networkers logo, Network Registrar, Packet, PIX, Post-Routing, Pre-Routing, RateMUX, Registrar, SlideCast, StrataView Plus, Stratm, SwitchProbe, TeleRouter, and VCO are registered trademarks of Cisco Systems, Inc. and/or its affiliates in the U.S. and certain other countries.

All other trademarks mentioned in this document or Web site are the property of their respective owners. The use of the word partner does not imply a partnership relationship between Cisco and any other company. (0301R)

Cisco BTS 10200 Softswitch Application Installation Release 4.5

Copyright © 2006, Cisco Systems, Inc.

All rights reserved.

| Revision History |
| --- |
| Date | Version | Revised By | Description |
| 4/10/2005 | 1.0 | Andy Chan | Initial Version |
| 4/13/2005 | 2.0 | Andy Chan | Changes on the name of files, add description about DB license |
| 4/28/2005 | 3.0 | Andy Chan | Minor change on db_license |
| 5/8/2005 | 4.0 | Andy Chan | Add named process in Appendix D, and some minor change |
| 5/9/2005 | 5.0 | Heather Dinsdale | Fixed table in Appendix A. |
| 8/23/2005 | 6.0 | Andy Chan | Add LAF section into 4.5 installation doc |
| 8/23/2005 | 7.0 | Andy Chan | Minor change in LAF section |
| 8/23/2005 | 8.0 | Heather Dinsdale | Made minor changes to LAF section. |
| 9/7/2005 | 9.0 | Andy Chan | Minor change on the Appendix E |
| 10/14/2005 | 10.0 | Andy Chan | Minor check in based on the defects CSCsc08686, CSCsc14301 and CSCsc07052 |
| 11/6/2005 | 11.0 | Andy Chan | Make some IRDP description change based on CSCsc14379 |
| 2/14/2006 | 12.0 | Andy Chan | Add more information about MBA |
| 2/22/2006 | 13.0 | Andy Chan | Add information about external oracle engine |
| 3/14/2006 | 14.0 | Andy Chan | Modify the CD-ROM drive dev name |
| 7/26/2006 | 15.0 | Andy Chan | Minor changes based on TWC feedback, CSCse81267, CSCse81286, and add in instruction for ISADS in appendix G and H |
| 9/28/06 | 16.0 | Andy Chan | Add comments into section “Enter Addresses in the Primary EMS Configuration File” (CSCsb77853) and some minor change. |
| 11/7/2006 | 17.0 | Andy Chan | Add patch procedure for 4.5.1V14 |
| 1/2/2007 | 18.0 | Andy Chan | Add recommendation for LAF archive server location, and a few wordings in “Remove the Build Directory to Free Disk Space” section and add table for jumpstart version. Also add the patch procedure for 4.5.1V14IP01. |

## Table of Contents

Table of Contents	4

Preface	6

Obtaining Documentation	6

Obtaining Technical Assistance	7

Chapter 1	10

Application Installation for Duplex Systems	10

Purpose	10

Prerequisites	10

Before You Start	13

Overview of the Installation Procedure	13

Open UNIX Shells and Create Log Files	15

Adding Static Routes	16

Verify Host Tables	17

Verify Available Disk Space For Installation	18

Load the BTS10200 Application Disk on the EMS and CA/FS Platforms	19

Load the BTS10200 Database Disk on the EMS Platforms	27

Load the BTS10200 Oracle Engine Disk on the EMS Platforms	32

Enter IP Addresses and Host Names in the opticall.cfg File	37

Run Verification Script to Validate Platform and DNS Data	40

Install the Primary EMS	42

Install Secondary EMS	44

Install the Primary CA/FS	46

Install the Secondary CA/FS	48

Add patch BTS_04_05_01_V14_IP00 into the release 4.5.1V14	50

Provisioning DB License	53

CORBA Installation	54

Installing the Mini-Browser Adaptor (MBA) Application on another machine	58

Start All Cisco BTS 10200 Softswitch Application Platforms	59

Add patch BTS_04_05_01_V14_IP01 into the release 4.5.1V14	60

Remove the Build Directory to Free Disk Space	61

Enabling Log Archive Facility (LAF) process	61

Appendix A	62

General Software Installation Procedure	62

Installation Scenarios	62

Package Information	65

Installation Steps and Utilities	68

Appendix B	73

Configure the Ethernet Switch for 4.X Load	73

Appendix C	75

A Template of opticall.cfg in Release 4.5.1V14	75

Appendix D	86

How To Enable DNS Caching Server (NAMED process)	86

Appendix E	88

Setting Up the Non-Interactive SSH Login to External Archive Server for LAF Process	88

Appendix F	90

Place the external oracle engine	90

Appendix G	93

Enabling the Internal Secondary Authoritative DNS Server (ISADS) before fresh installation	93

Appendix H	99

Enabling the Internal Secondary Authoritative DNS Server (ISADS) after fresh installation/upgrade	99

Appendix I	101

Apply patch for 4.5.1V14IP00 to CA host	101

Appendix J	104

Apply patch for 4.5.1V14IP00 to EMS host	104

Appendix K	105

Apply patch for 4.5.1V14IP01 to EMS host	105

Appendix L	111

Remove patch for 4.5.1V14IP01 from EMS hosts	111

## Preface

This document describes the steps needed to install the Cisco BTS 10200 Softswitch Application Installation software, release 4.5

## Obtaining Documentation

The following sections provide sources for obtaining documentation from Cisco Systems.

### World Wide Web

You can access the most current Cisco documentation on the World Wide Web at the following sites:

- http://www.cisco.com

- http://www-china.cisco.com

- http://www-europe.cisco.com

### Documentation CD-ROM

Cisco documentation and additional literature are available in a CD-ROM package, which ships with your product. The Documentation CD-ROM is updated monthly and may be more current than printed documentation. The CD-ROM package is available as a single unit or as an annual subscription.

### Ordering Documentation

Cisco documentation is available in the following ways:

- Registered Cisco Direct Customers can order Cisco Product documentation from the Networking Products MarketPlace:

http://www.cisco.com/en/US/partner/ordering/index.shtml

- Registered Cisco.com users can order the Documentation CD-ROM through the online Subscription Store:

http://www.cisco.com/go/subscription

- Nonregistered Cisco.com users can order documentation through a local account representative by calling Cisco corporate headquarters (California, USA) at 408 526-7208 or, in North America, by calling 800 553-NETS(6387).

### Documentation Feedback

If you are reading Cisco product documentation on the World Wide Web, you can submit technical comments electronically. Click Feedback in the toolbar and select Documentation. After you complete the form, click Submit to send it to Cisco.

You can e-mail your comments to bug-doc@cisco.com.

To submit your comments by mail, use the response card behind the front cover of your document, or write to the following address:

Attn Document Resource Connection
Cisco Systems, Inc.
170 West Tasman Drive
San Jose, CA 95134-9883

We appreciate your comments.

## Obtaining Technical Assistance

Cisco provides Cisco.com as a starting point for all technical assistance. Customers and partners can obtain documentation, troubleshooting tips, and sample configurations from online tools. For Cisco.com registered users, additional troubleshooting tools are available from the TAC website.

### Cisco.com

Cisco.com is the foundation of a suite of interactive, networked services that provides immediate, open access to Cisco information and resources at anytime, from anywhere in the world. This highly integrated Internet application is a powerful, easy-to-use tool for doing business with Cisco.

Cisco.com provides a broad range of features and services to help customers and partners streamline business processes and improve productivity. Through Cisco.com, you can find information about Cisco and our networking solutions, services, and programs. In addition, you can resolve technical issues with online technical support, download and test software packages, and order Cisco learning materials and merchandise. Valuable online skill assessment, training, and certification programs are also available.

Customers and partners can self-register on Cisco.com to obtain additional personalized information and services. Registered users can order products, check on the status of an order, access technical support, and view benefits specific to their relationships with Cisco.

To access Cisco.com, go to the following website:

http://www.cisco.com

### Technical Assistance Center

The Cisco TAC website is available to all customers who need technical assistance with a Cisco product or technology that is under warranty or covered by a maintenance contract.

#### Contacting TAC by Using the Cisco TAC Website

If you have a priority level 3 (P3) or priority level 4 (P4) problem, contact TAC by going to the TAC website:

http://www.cisco.com/tac

P3 and P4 level problems are defined as follows:

- P3—Your network performance is degraded. Network functionality is noticeably impaired, but most business operations continue.

- P4—You need information or assistance on Cisco product capabilities, product installation, or basic product configuration.

In each of the above cases, use the Cisco TAC website to quickly find answers to your questions.

To register for Cisco.com, go to the following website:

http://www.cisco.com/register/

If you cannot resolve your technical issue by using the TAC online resources, Cisco.com registered users can open a case online by using the TAC Case Open tool at the following website:

http://www.cisco.com/tac/caseopen

#### Contacting TAC by Telephone

If you have a priority level 1 (P1) or priority level 2 (P2) problem, contact TAC by telephone and immediately open a case. To obtain a directory of toll-free numbers for your country, go to the following website:

http://www.cisco.com/warp/public/687/Directory/DirTAC.shtml

P1 and P2 level problems are defined as follows:

- P1—Your production network is down, causing a critical impact to business operations if service is not restored quickly. No workaround is available.

- P2—Your production network is severely degraded, affecting significant aspects of your business operations. No workaround is available.

Chapter 1

Application Installation for Duplex Systems

## Purpose

This procedure is used to install the Cisco Broadband Telephony Services (BTS) 10200 Softswitch application software (releases 4.5.13, 4.5.0V14 and above, or 4.5.1), and  Oracle software, on Cisco BTS 10200  Softswitch hardware that is currently not carrying live traffic. The specific units on which this application will be installed are:

- Side A (primary) Element Management System (EMS)

- Side B (secondary) EMS

- Side A (primary) call agent/feature server (CA/FS)

- Side B (secondary) CA/FS

|  | Caution This is not an upgrade procedure. Performing the steps in this procedure will bring the platform down and stop call processing. Do not start this procedure unless you have authorization from your supervisor. Do not run it on an active system that is carrying live traffic. If you have questions, contact Cisco TAC. |
| --- | --- |

|  | Note Cisco recommends that you back up data periodically following software installation and provisioning. |
| --- | --- |

## Prerequisites

The following prerequisites must be satisfied before Cisco can prepare and ship the Cisco BTS 10200 Softswitch software to your site.

1. Obtain a copy of the network site survey that Cisco provides, fill in the network configuration data you want your system to have, and return the survey to Cisco. The Cisco BTS 10200 Softswitch uses this information to communicate with your network. Cisco uses this information to create the customized configuration file for your system.

2. Cisco will provide you with a network installation data sheet (NIDS). The system administrator must ensure that the applicable DNS domain names and IP addresses from the NIDS have been entered into the primary and secondary DNS servers. DNS lookup of host names is required for this procedure. This ensures that the system can resolve all qualified domain names.

If you would like to enter any parameters different than the values on the NIDS, or use a different DNS server, contact Cisco TAC for an evaluation of the potential impact of the changes. Obtain Cisco TAC concurrence of any changes to these data sheets.

|  | Caution Do not continue with this procedure until the system administrator has confirmed the DNS server has the correct IP addresses and host or domain names. Otherwise, the Cisco BTS 10200 Softswitch platforms will not be able to communicate properly. |
| --- | --- |

After your Cisco BTS 10200 Softswitch software arrives, the following prerequisites must be satisfied before starting this application installation procedure.

|  | Note This installation procedure should be performed by a user experienced in basic Unix commands. Some of the prerequisites require the involvement of the system administrator. |
| --- | --- |

1. Verify that there is sufficient disk space on each host machine for this installation. Each EMS requires at least 10 GB, and each CA requires at least 6 GB. For all other hardware requirement, please refer to “Cisco BTS 10200 Softswitch Release Notes for Release 4.5.1”.

2. You must have copies of the completed network site survey and NIDS provided by Cisco for your specific system. If you would like to enter any parameters different than the values on these data sheets, contact Cisco TAC for an evaluation of the potential impact of the changes. Obtain Cisco TAC concurrence on any changes.

3. Verify that you have the correct version of  “BTS 10200 Application Disk” CD and “BTS 10200 Database Disk” CD, as specified on the data sheets.

4.  If your BTS contract also include oracle license, then you will also receive “BTS 10200 Oracle Engine Disk” CD. However, if your contract does not include oracle license, you must execute the procedures in “Oracle Engine Software Creation Procedure for BTS10200 R4.5.0/4.5.1/5.0” to create an oracle engine before this installation.

5. Before the installation, user must follow “Cabling, VLAN, and IRDP Setup Procedure for 4-2 Configuration" to connect the systems and setup the network configuration. Also user must perform jumpstart on all Cisco BTS 10200 machines. The following table illustrates which jumpstart should be used for which load.

| BTS load | Jumpstart version | Jumpstart document |
| --- | --- | --- |
| Rel4.5.0, rel4.5.13 and rel4.5.1V01 or below | Solaris!Sun!sparc!10!0!10001 | BTS_Jumpstart_Procedure_for_Solaris-Sun-Sparc-10-0-10001 |
| Rel4.5.1V02 or beyond | Solaris!Sun!sparc!10!0!0503!V02 | BTS_Jumpstart_Procedure_for_Solaris-Sun-Sparc-10-0-0503-V02 |

|  | Note User should enable IRDP (Internet Router Discovery Protocol) in the management network, but with a lower priority than that of signaling network. For details please refer to the above document (Cabling, VLAN, and IRDP Setup Procedure for 4-2 Configuration). |
| --- | --- |

6. Before you start the installation, make sure your network administrator set up and configure the Ethernet switch that connected to the BTS 10200 Softswitch properly (disable the auto-negotiation and enforce 100Mbps duplex link speed). For detail, refer to Appendix B, “Configure the Ethernet switch for 4.X load.”

7. Also verify the memory in each CA box has at least 4GB if user chose “medium4G,” “router,” “localLnp,” or “localLnpRN” for MEM_CFG_SELECTION in opticall.cfg, and 2GB if user chose “small” or “demo.”, and 8G if user chose “medium”. If the system does not meet this requirement, installation will abort.

8. For fresh installation, if you choose to start NAMED process for the system local cache, you must execute the steps in Appendix D before this installation. If you choose to run secondary DNS servers in the Cisco BTS 10200 system using NAMED process (available only from rel4.5.1V14), you must execute the steps in Appendix G before this installation.

9. However, if you must set up the NAMED process as secondary DNS server after this fresh installation (available only from rel4.5.1V14), you must follow Appendix H.

## Before You Start

Perform the following steps before starting the installation procedure:

Step 1   Check with your system administrator to ensure that the requirements in the Prerequisites section have been satisfied.

Step 2   Ensure that the Cisco BTS 10200 Softswitch hardware components have been set up and turned on in accordance with manufacturer recommendations.

## Overview of the Installation Procedure

This procedure is used to install the Cisco BTS 10200 Softswitch application software, Release 4.5.X, and/or Oracle software, on Cisco BTS 10200 Softswitch hardware that is currently not carrying live traffic. The phases of the procedure are as follows:

- Transfer the application files to each of the specified platforms

- Enter the IP addresses and host names into the opticall.cfg file

- Run the verification script to validate IP addresses and host names

- Install the application files on each of the specified platforms

- Start all Cisco BTS 10200 Softswitch application platforms (automatically)

- Remove the Build subdirectory to free disk space (recommended)

Cisco recommends that you completely read through this procedure before starting any steps.

The basic flow of this procedure is illustrated in Figure 1.

Figure 1 Cisco BTS 10200 Softswitch Application Installation Procedure

|  | Note In all the steps in this procedure, enter the commands as shown; some commands are case sensitive. Press Enter at the end of each command. |
| --- | --- |

## Open UNIX Shells and Create Log Files

Perform the following steps to open UNIX shells on the primary and secondary EMS platforms and on the primary and secondary CA/FS platforms. These four shells will be used throughout the application installation procedure.

You will need the network site survey and NIDS (referred to in this procedure as data sheets) that were provided to you by the system administrator.

Step 1 Ensure that you have console access to all four units: primary EMS, secondary EMS, primary CA/FS, and secondary CA/FS.

Step 2  From the console, login as root.

console login: root

Step 3 Enter the root password for the applicable unit (these can be obtained from your system administrator) at the password prompt in each of the four shells. The system will respond with a command prompt.

Step 4 Create a troubleshooting logfile at the command prompt in each of the four shells.

script /opt/mylog

|  | Note If SSH is available on Cisco BTS 10200 system, you can login to those units through SSH. However, right after the jumpstart, you cannot install the BTS application through a ssh session. (But you can do upgrade/install through a ssh session after the first application installation) SFTP should also be available in the system after the jumpstart to transfer files between the nodes. FTP is no longer available to transfer the files between the systems in and after release 4.5 |
| --- | --- |

## Adding Static Routes

The following are the steps to add static routes to all Cisco BTS 10200 systems.

Step 1  From the shell/window of primary Call Agent, change directory to /opt/utils

cd /opt/utils

Step 2	 Edit S96StaticRoutes with your favorite editor.

Step 3  Add the subnet of NTP server, DNS server, external archive server and any other machines which user want to have access to Cisco BTS 10200 system, like the following, to the file:

route add -net <destination network> <network gateway>

|  | Note All NTP, DNS traffic, traffic to external archive server, and traffic from other machine to BTS system (eg. login), should all go through management networks. This is particularly important in CA system because CA has both management and signaling network. If user does not specify explicitly in this file, those traffic will be directed to signaling network. |
| --- | --- |

Step 4  Make sure there are softlink pointing from /etc/rc3.d/S96StaticRoutes to /opt/utils/S96StaticRoutes.

Step 5	After editing, close the file, and run S96StaticRoutes.

/etc/rc3.d/S96StaticRoutes

Step 6	Repeat Step 1 to Step 5 on secondary CA.

Step 7  Verify the connectivity by pinging the DNS server, NTP server, external archive server, or any machine that user just added in that file.

## Verify Host Tables

Use the following steps to verify the host tables.

Step 1   At the command prompt in each of the four shells, display the host table stored in the unit.

more /etc/hosts

Step 2   In each of the four shells, examine the display. Verify that the IP addresses and host names of both EMS units and both CA/FS units are displayed and that they match the entries in the data sheet.

If any entries are missing or do not match those in data sheet, stop and call your system administrator.

|  | Note Press the spacebar to view additional segments of the display; enter q to quit the display. Ignore other entries in the display (other than those specified for EMS and CA/FS in this step). |
| --- | --- |

Step 3   System administrator—When there is a mismatch in Step 2, there are two possible solutions:

a. Edit the host tables to match those in data sheet .

b. If values other than those in the data sheet are required, contact Cisco TAC before proceeding; Cisco TAC will assist you in evaluating the impact of these changes. Do not continue unless you have received concurrence from Cisco TAC.

|  | Note If this step was performed, repeat the previous steps as needed to restart this procedure. |
| --- | --- |

## Verify Available Disk Space For Installation

Use the following steps to verify your disk space availability before the software installation.

Step 1   At the command prompt in each of the four shells, display the available disk space of the host.

df -k

|  | Note The available capacity of each disk partition will be shown in kilobytes. |
| --- | --- |

Step 2   For each EMS, verify that there is sufficient disk space in /opt (10 GB on each EMS) for this installation. If there is less than 10 GB available in /opt on any one of the EMS hosts, stop. Ask your system administrator to correct the problem.

Step 3   For each CA, verify that there is sufficient disk space in /opt (6 GB on each CA) for this installation. If there is less than 6 GB available in /opt on any one of the CA hosts, stop. Ask your system administrator to correct the problem.

Step 4   If the disk space for /opt is less than specified above, ask your system administrator to assign more disk space. This step is necessary only if you had less than 10 GB free on an EMS or less than 6 GB free on a CA in Step 2 or Step 3. After your system administrator has freed up sufficient disk space, and notified you to proceed, repeat Step 1 through Step 3.

|  | Note If you logged off, repeat the steps in the Open UNIX Shells and Create Log Files section, then repeat the steps in the Verify Available Disk Space For Installation section. |
| --- | --- |

## Load the BTS10200 Application Disk on the EMS and CA/FS Platforms

This section describes how to transfer the BTS application software load (K9-opticall.tar.gz) from the CD to the host machine in preparation for software installation.

### Load the Cisco BTS 10200 Application Disk

Perform these steps to load the software from the “Cisco BTS 10200 Application Disk” CD.

Step 1   Verify with the system administrator that you have the correct version of “BTS 10200 Application Disk” CD as specified on the data sheets. Do not proceed until you have verified this.

Step 2   Insert the application CD into the CD-ROM drive of the primary EMS unit.

|  | Caution Do not remove the CD until directed to do so in this procedure. It must remain in the CD-ROM drive of the primary EMS, and not be moved from machine to machine. There is a step later in this procedure that indicates when it is time to remove the CD-ROM. |
| --- | --- |

### Load the K9-opticall.tar.gz File on the Primary EMS

This section describes how to load the K9-opticall.tar.gz file on the primary EMS.

|  | Note Some steps indicate the time taken by the system to complete an operation. Actual times may vary depending on factors such as network speed and file size. |
| --- | --- |

In the primary EMS xterm or terminal window, perform the following steps to load K9-opticall.tar.gz on the primary EMS.

Step 1   At the command prompt of the primary EMS, navigate to the CD-ROM.

cd /cdrom/cdrom0

Step 2   This troubleshooting step is only necessary if you received an error response while attempting to navigate to the CD-ROM. If you did not receive an error response, go to Step 3.

a. If you receive the system response, cdrom not found, manually open and close the CD-ROM tray on the primary EMS unit. Wait 30 seconds and try the command again.

cd /cdrom/cdrom0

b. If you still receive an error response, it is possible that the CD-ROM driver is not yet mounted on the primary EMS. Enter the following command to create a directory:

mkdir -p /cdrom

|  | Note If the system responds that this directory already exists, you should ignore the response and continue with the next substep. |
| --- | --- |

c. Navigate to the CD ROM.

cd /cdrom

d. Make a new directory.

mkdir -p cdrom0

e. Enter either one of the following command to mount the CD-ROM drive:

- A system with Continuous Computing hardware, please run:

mount -o ro -F hsfs /dev/dsk/c0t6d0s0 /cdrom/cdrom0

- Other hardware platform (eg. SunFire, Netra1280) please run:

mount -o ro -F hsfs /dev/dsk/c0t0d0s0 /cdrom/cdrom0

f. At the command prompt of the primary EMS, navigate to the CD-ROM:

cd /cdrom/cdrom0

Step 3   Check that the proper file (K9-opticall.tar.gz) is present on the CD-ROM:

ls

The file K9-opticall.tar.gz should be present.

Step 4   Copy the file on the CD-ROM to the /opt directory:

cp K9-opticall.tar.gz /opt

There will be a delay of 2 to 5 minutes while the file is copied and the command prompt reappears. Wait for the prompt.

|  | Note If the system displays any error messages during (or at the end of) this process, stop immediately and notify your system administrator. |
| --- | --- |

Step 5 	When the command prompt reappears, unzip and untar the file.

cd /opt; gzip –cd K9-opticall.tar.gz | tar –xvf –

There will be a delay of 2 to 5 minutes while the file is being unzipped and expanded, and the command prompt reappears. Wait for the prompt.

### Transfer and Load the K9-opticall.tar.gz File on the Secondary EMS

This section describes how to transfer and load the K9-opticall.tar.gz file on the secondary EMS.

|  | Caution Do not remove the CD until directed to do so in this procedure. It must remain in the CD-ROM drive of the primary EMS and not be moved from machine to machine. There is a step later in this procedure that indicates when it is time to remove the CD-ROM. |
| --- | --- |

Perform the following steps to transfer and load K9-opticall.tar.gz on the secondary EMS. Refer to the data sheets for addresses and names of the applicable units.

Step 1   Click the shell (window) for the secondary EMS.

Step 2   At the command prompt of the secondary EMS, start an SFTP session directed to the primary EMS.

cd /opt; sftp <hostname or IP address of primary EMS>

Step 3   At the password prompt, enter the root password for the primary EMS. The password can be obtained from your system administrator. The system will respond with an SFTP prompt.

Step 4   When the SFTP prompt appears, navigate to the CD-ROM.

cd /cdrom/cdrom0

Step 5   Check that the proper file (K9-opticall.tar.gz) is present on the CD-ROM.

ls

The file K9-opticall.tar.gz should be present.

Step 6   At the SFTP prompt, transfer the application file to the /opt directory.

get K9-opticall.tar.gz

There will be a delay of 2 to 5 minutes while the file is being transferred, and the command prompt reappears. Wait for the prompt.

|  | Note If the system displays any error messages during (or at the end of) this process, stop immediately and notify your system administrator. |
| --- | --- |

Step 7 	  After the transfer is complete and the SFTP prompt reappears, exit the SFTP session.

exit

Step 8 	  When the command prompt of the secondary EMS reappears, unzip and untar the file.

cd /opt; gzip –cd K9-opticall.tar.gz | tar –xvf -

There will be a delay of 2 to 3 minutes while the file is being unzipped and expanded, and the command prompt reappears. Wait for the prompt.

### Transfer and Load the K9-opticall.tar.gz File on the Primary CA/FS

This section describes how to transfer and load the K9-opticall.tar.gz file on the primary CA/FS.

|  | Caution Do not remove the CD until directed to do so in this procedure. It must remain in the CD-ROM drive of the primary EMS and not be moved from machine to machine. There is a step later in this procedure that indicates when it is time to remove the CD-ROM. |
| --- | --- |

Perform the following steps to transfer and load K9-opticall.tar.gz on the primary CA/FS. Refer to the data sheets for addresses and names of the applicable units.

Step 1   Click the shell (window) for the primary CA/FS.

Step 2   At the command prompt of the primary CA/FS, start an SFTP session directed to the primary EMS.

cd /opt; sftp <hostname or IP address of primary EMS>

Step 3   At the password prompt, enter the root password for the primary EMS. The system will respond with an SFTP prompt.

Step 4   When the SFTP prompt appears, navigate to the CD-ROM.

cd /cdrom/cdrom0

Step 5   Check that the proper file (K9-opticall.tar.gz) is present on the CD-ROM.

ls

The K9-opticall.tar.gz file should be present.

Step 6   At the SFTP prompt, transfer the application file to the /opt directory.

get K9-opticall.tar.gz

There will be a delay of 2-3 minute while the file is being transferred, and the command prompt reappears. Wait for the prompt.

|  | Note If the system displays any error messages during (or at the end of) this process, stop immediately and notify your system administrator. |
| --- | --- |

Step 7   After the transfer is complete and the SFTP prompt reappears, exit the SFTP session.

exit

Step 8 	 When the command prompt of the primary CA reappears, unzip and untar the file.

cd /opt; gzip -cd K9-opticall.tar.gz | tar –xvf -

There will be a delay of 2 to 5 minutes while the file is being expanded, and the command prompt reappears. Wait for the prompt.

### Transfer and Load K9-opticall.tar.gz file on the Secondary CA/FS

This section describes how to transfer and load the K9-opticall.tar.gz file on the secondary CA/FS.

|  | Caution Do not remove the CD until directed to do so in this procedure. It must remain in the CD-ROM drive of the primary EMS and not be moved from machine to machine. There is a step later in this procedure that indicates when it is time to remove the CD-ROM. |
| --- | --- |

Perform the following steps to transfer and load K9-opticall.tar.gz on the secondary CA/FS. Refer to the data sheets for addresses and names of the applicable units.

Step 1   Click the shell (window) for the secondary CA/FS.

Step 2   At the command prompt of the secondary CA/FS, start an SFTP session directed to the primary EMS.

cd /opt; sftp <hostname or IP address of primary EMS>

Step 3   At the password prompt, enter the root password for the primary EMS. The system will respond with an SFTP prompt.

Step 4   When the SFTP prompt appears, navigate to the CD-ROM.

cd /cdrom/cdrom0

Step 5   Check that the proper file (K9-opticall.tar.gz) is present on the CD-ROM.

ls

The  K9-opticall.tar.gz file should be present.

Step 6   At the SFTP prompt, transfer the application file to the /opt directory.

get  K9-opticall.tar.gz

There will be a delay of 2-3 minute while the file is being transferred, and the command prompt reappears. Wait for the prompt.

|  | Note If the system displays any error messages during (or at the end of) this process, stop immediately and notify your system administrator. |
| --- | --- |

Step 7   After the transfer is complete and the SFTP prompt reappears, exit the SFTP session.

exit

Step 8  When the command prompt of the secondary CA reappears, unzip and untar the file.

cd /opt; gzip –cd K9-opticall.tar.gz | tar –xvf -

There will be a delay of 2 to 5 minutes while the file is being expanded, and the command prompt reappears. Wait for the prompt.

|  | Caution Do not remove the CD-ROM until directed to do so in this procedure. It must remain in the CD-ROM drive of the primary EMS and not be moved from machine to machine. There is a step later in this procedure that indicates when it is time to remove the CD-ROM. |
| --- | --- |

### Remove Cisco BTS 10200 Softswitch Application CD-ROM

Perform these steps to remove the “BTS 10200 Application Disk” CD-ROM from the CD-ROM drive of the primary EMS.

Step 1   Click the shell (window) for the primary EMS.

Step 2   At the command prompt of the primary EMS, enter the following command:

umount /cdrom/cdrom0

Step 3   Manually eject the CD-ROM.

Step 4   After the “BTS 10200 Application Disk” CD-ROM comes out of the CD-ROM drive, place it in the CD case.

## Load the BTS10200 Database Disk on the EMS Platforms

This section describes how to transfer the BTS database software from the CD to the EMS machines in preparation for installation.

### Load the BTS 10200 Database Disk CD

Perform these steps to load the software from the “BTS 10200 Database Disk” CD.

Step 1   Verify with the system administrator that you have the correct version of “BTS 10200 Database Disk” CD as specified on the data sheets. Do not proceed until you have verified this.

Step 2   Insert the BTS10200 Database Disk CD into the CD-ROM drive of the primary EMS unit.

|  | Caution Do not remove the CD-ROM until directed to do so in this procedure. It must remain in the CD-ROM drive of the primary EMS and not be moved from machine to machine. There is a step later in this procedure that indicates when it is time to remove the CD-ROM. |
| --- | --- |

### Load the K9-btsdb.tar.gz and K9-extora.tar.gz files on the Primary EMS

In the primary EMS xterm or terminal window, perform the following steps to load the K9-btsdb.tar.gz and K9-extora.tar.gz files on the primary EMS:

Step 1   At the command prompt of the primary EMS, navigate to the CD-ROM.

cd /cdrom/cdrom0

If necessary, repeat the command cd /cdrom/cdrom0.

Step 2   This troubleshooting step is only necessary if you received an error response while attempting to navigate to the CD-ROM. If you did not receive an error response, go to Step 3.

a. If you receive a system response, cdrom not found, manually open and close the CD-ROM tray on the primary EMS unit. Wait 30 seconds and try the command again (cd /cdrom/cdrom0).

b. If you still receive an error response, it is possible that the CD-ROM driver is not yet mounted on the primary EMS. Enter the following command to create a directory:

mkdir -p /cdrom

|  | Note If the system responds that this directory already exists, you should ignore the response and continue with the next substep. |
| --- | --- |

c. Navigate to the CD-ROM

cd /cdrom

d. Create a new directory.

mkdir -p cdrom0

e. Enter either one of the following command to mount the CD-ROM drive:

- A system with Continuous Computing hardware, please run:

mount -o ro -F hsfs /dev/dsk/c0t6d0s0 /cdrom/cdrom0

- Other hardware platform (eg. SunFire, Netra1280) please run:

mount -o ro -F hsfs /dev/dsk/c0t0d0s0 /cdrom/cdrom0

f. At the command prompt of the primary EMS, navigate to the CD-ROM.

cd /cdrom/cdrom0

Step 3   Check that the proper files K9-btsdb.tar.gz and K9-extora.tar.gz are present on the CD-ROM.

ls

The K9-btsdb.tar.gz and K9-extora.tar.gz files should be present.

Step 4   Copy the files from the CD-ROM.

cp K9-btsdb.tar.gz /opt

cp K9-extora.tar.gz /opt

Step 5   There will be a delay of approximately 30 seconds while the files are copied and the command prompt reappears. Wait for the prompt.

|  | Note If the system displays any error messages during (or at the end of) this process, stop immediately and notify your system administrator. |
| --- | --- |

Step 6 	When the command prompt reappears, unzip and untar the file.

cd /opt;

gzip –cd K9-btsdb.tar.gz | tar xvf –

gzip –cd K9-extora.tar.gz | tar xvf -

Step 7   There will be a delay of 30 seconds while the file is being unzipped and  expanded, and the command prompt reappears. Wait for the prompt.

### Transfer and Load K9-btsdb.tar.gz and K9-extora.tar.gz on the Secondary EMS

In this section, you will transfer and load the K9-btsdb.tar.gz file on the secondary EMS.

|  | Caution Do not remove the CD-ROM until directed to do so in this procedure. It must remain in the CD-ROM drive of the primary EMS and not be moved from machine to machine. There is a step later in this procedure that indicates when it is time to remove the CD-ROM. |
| --- | --- |

Perform the following steps to transfer and load K9-btsdb.tar.gz and K9-extora.tar.gz on the secondary EMS. Refer to the data sheets for addresses and names of the applicable units.

Step 1   Click the shell (window) for the secondary EMS.

Step 2   At the command prompt of the secondary EMS, start an SFTP session directed to the primary EMS.

cd /opt; sftp <hostname or IP address of primary EMS>

Step 3   At the password prompt, enter the root password for the primary EMS (can be obtained from your system administrator). The system will respond with an SFTP prompt.

Step 4   When the SFTP prompt appears, navigate to the CD-ROM.

cd /cdrom/cdrom0

Step 5   Check that the proper files K9-btsdb.tar.gz and K9-extora.tar.gz are present on the CD-ROM.

ls

The K9-btsdb.tar.gz and K9-extora.tar.gz files should be present.

Step 6   At the SFTP prompt, transfer the BTS database files to the preselected directory.

get K9-btsdb.tar.gz

get K9-extora.tar.gz

There will be a delay of approximately 30 seconds while the file is being transferred, and the command prompt reappears. Wait for the prompt.

|  | Note If the system displays any error messages during (or at the end of) this process, stop immediately and notify your system administrator. |
| --- | --- |

Step 7   After the transfer is complete and the SFTP prompt reappears, exit the SFTP session.

exit

Step 8 	  When the command prompt reappears, untar and unzip the files.

cd /opt

gzip -cd K9-btsdb.tar.gz | tar –xvf –

gzip –cd K9-extora.tar.gz | tar –xvf -

There will be a delay of 30 seconds while the file is being expanded, and the command prompt reappears. Wait for the prompt.

### Remove BTS 10200 Database Disk CD

Perform these steps to remove the “BTS 10200 Database Disk”  CD from the CD-ROM drive of the primary EMS.

Step 1   Click the shell (window) for the primary EMS.

Step 2   At the command prompt of the primary EMS, enter the following command:

umount /cdrom/cdrom0

Step 3   Manually eject the CD-ROM.

Step 4   After the CD-ROM is ejected from the CD-ROM drive, place it in the CD case.

## Load the BTS10200 Oracle Engine Disk on the EMS Platforms

|  | Caution If you have not received the BTS10200 Oracle Engine Disk because your BTS order does not include Oracle license, you must perform the procedures in the “Oracle Engine Software Creation Procedure for BTS10200 R4.5.0/4.5.1/5.0” to create the oracle engine tar file (opticall_BASE.tar.gz). Then place the Oracle engine tar file in the /opt/Build/ora-engine directory. See Appendix F for more details on how to place the Oracle engine tar file that you created. If you have received the Oracle Engine Disk, meaning your BTS10200 order includes Oracle engine, please following steps in this section to load the Oracle engine tar file. |
| --- | --- |

This section describes how to transfer the Oracle engine software from the CD to the EMS machines in preparation for installation.

### Load the BTS 10200 Oracle Engine Disk

Perform these steps to install from the “BTS 10200 Oracle Engine Disk”.

Step 1   Verify with the system administrator that you have the correct version of “BTS 10200 Oracle Engine Disk” as specified on the data sheets. Do not proceed until you have verified this.

Step 2   Insert the “BTS 10200 Oracle Engine Disk” into the CD-ROM drive of the primary EMS unit.

|  | Caution Do not remove the disk from CD-ROM until directed to do so in this procedure. It must remain in the CD-ROM drive of the primary EMS and not be moved from machine to machine. There is a step later in this procedure that indicates when it is time to remove it from CD-ROM. |
| --- | --- |

### Load the K9-oraengine.tar.gz file on the Primary EMS

In the primary EMS xterm or terminal window, perform the following steps to load the K9-oraengine.tar.gz file on the primary EMS:

Step 1   At the command prompt of the primary EMS, navigate to the CD-ROM.

cd /cdrom/cdrom0

If necessary, repeat the command cd /cdrom/cdrom0.

Step 2   This troubleshooting step is only necessary if you received an error response while attempting to navigate to the CD-ROM. If you did not receive an error response, go to Step 3.

a. If you receive a system response, cdrom not found, manually open and close the CD-ROM tray on the primary EMS unit. Wait 30 seconds and try the command again (cd /cdrom/cdrom0).

b. If you still receive an error response, it is possible that the CD-ROM driver is not yet mounted on the primary EMS. Enter the following command to create a directory:

mkdir -p /cdrom

|  | Note If the system responds that this directory already exists, you should ignore the response and continue with the next substep. |
| --- | --- |

c. Navigate to the CD-ROM

cd /cdrom

d. Create a new directory.

mkdir -p cdrom0

e. Enter either one of the following command to mount the CD-ROM drive:

- A system with Continuous Computing hardware, please run:

mount -o ro -F hsfs /dev/dsk/c0t6d0s0 /cdrom/cdrom0

- Other hardware platform (eg. SunFire, Netra1280) please run:

mount -o ro -F hsfs /dev/dsk/c0t0d0s0 /cdrom/cdrom0

f. At the command prompt of the primary EMS, navigate to the CD-ROM.

cd /cdrom/cdrom0

Step 3   Check that the proper file K9-oraengine.tar.gz is present on the CD-ROM.

ls

The K9-oraengine.tar.gz file should be present.

Step 4   Copy the file from the CD-ROM.

cp K9-oraengine.tar.gz /opt

There will be a delay of approximately 5-10 minutes while the file is copied and the command prompt reappears. Wait for the prompt.

|  | Note If the system displays any error messages during (or at the end of) this process, stop immediately and notify your system administrator. |
| --- | --- |

Step 5 	When the command prompt reappears, untar and unzip the file.

cd /opt;  gzip –cd  K9-oraengine.tar.gz | tar –xvf -

There will be a delay of  up to several minutes while the file is being unzipped and expanded, and the command prompt reappears. Wait for the prompt. Do not untar the file /opt/Build/ora-engine/opticall_BASE.tar.gz"

### Transfer and Load K9-oraengine.tar.gz on the Secondary EMS

In this section, you will transfer and load the K9-oraengine.tar.gz file on the secondary EMS.

|  | Caution Do not remove the CD-ROM until directed to do so in this procedure. It must remain in the CD-ROM drive of the primary EMS and not be moved from machine to machine. There is a step later in this procedure that indicates when it is time to remove the CD-ROM. |
| --- | --- |

Perform the following steps to transfer and load K9-oraengine.tar.gz on the secondary EMS. Refer to the data sheets for addresses and names of the applicable units.

Step 1   Click the shell (window) for the secondary EMS.

Step 2   At the command prompt of the secondary EMS, start an SFTP session directed to the primary EMS.

cd /opt; sftp <hostname or IP address of primary EMS>

Step 3   At the password prompt, enter the root password for the primary EMS (can be obtained from your system administrator). The system will respond with an SFTP prompt.

Step 4   When the SFTP prompt appears, navigate to the CD-ROM.

cd /cdrom/cdrom0

Step 5   Check that the proper file (K9-oraengine.tar.gz) is present on the CD-ROM.

ls

The K9-oraengine.tar.gz file should be present.

Step 6   At the SFTP prompt, transfer the oracle engine file to the preselected directory.

get K9-oraengine.tar.gz

There will be a delay of up to 30 minutes while the file is being transferred, and the command prompt reappears. Wait for the prompt.

|  | Note If the system displays any error messages during (or at the end of) this process, stop immediately and notify your system administrator. |
| --- | --- |

Step 7   After the transfer is complete and the SFTP prompt reappears, exit the SFTP session.

exit

Step 8 	  When the command prompt reappears, unzip and untar the file.

cd /opt; gzip –cd K9-oraengine.tar.gz | tar –xvf -

There will be a delay of up to several minutes while the file is being unzipped and expanded, and the command prompt reappears. Wait for the prompt. Do not untar the file /opt/Build/ora-engine/opticall_BASE.tar.gz"

### Remove BTS 10200 Oracle Engine Disk from CD-ROM

Perform these steps to remove the “BTS 10200 Oracle Engine Disk” from the CD-ROM drive of the primary EMS.

Step 1   Click the shell (window) for the primary EMS.

Step 2   At the command prompt of the primary EMS, enter the following command:

umount /cdrom/cdrom0

Step 3   Manually eject the CD-ROM.

Step 4   After the CD is ejected from the CD-ROM drive, place it in the CD case.

## Enter IP Addresses and Host Names in the opticall.cfg File

This section describes how to copy the opticall.cfg file from the install directory. It then describes how to edit the file with the data supplied in the opticall.cfg data sheet. Finally, the section describes how to copy the updated /etc/opticall.cfg file to the other three platforms (secondary EMS and primary and secondary CA/FS).

### Enter Addresses in the Primary EMS Configuration File

Perform the following steps to enter data into the configuration file on the primary EMS. You will need the data sheets provided to your system administrator by Cisco.

|  | Note If you are using the NIDS generator, a copy of opticall.cfg will be produced as a result. You can also use this opticall.cfg and put it into /etc. Then continue on next section Run Verification Script on Primary EMS |
| --- | --- |

Step 1   In the primary EMS shell, navigate to the install directory.

cd /opt/Build

Step 2   Verify that the opticall.cfg file is present.

ls opticall.cfg

|  | Note If the system responds with file not found, stop immediately. Call Cisco TAC for assistance. |
| --- | --- |

Step 3   Copy the opticall.cfg file to the etc directory.

cp opticall.cfg /etc

Step 4   Open the file for editing.

vi /etc/opticall.cfg

The system will display the contents of the file.  The file has the format like this: PARAMETER=NAME.

Note No space around “=”

|  | Note If the system responds with file not found, stop immediately. Call Cisco TAC for assistance. |
| --- | --- |

Step 5   Verify that the parameters in the opticall.cfg file match the contents of the opticall.cfg data sheet, located in the NIDS. Then edit the values in the opticall.cfg to match the one from the NIDS data sheet. Review the opticall.cfg data sheet for correct entries for each item.

Step 6   Save and exit the opticall.cfg file.

|  | Note The parameters in opticall.cfg are applied to the system only during fresh install/upgrade. Changing these parameters after that will not take effect until the next re-install/upgrade. Any changes to these parameters should be done only with a full understanding of the impact of such changes to the system, after consultation with Cisco. |
| --- | --- |

### Run Verification Script on Primary EMS

Use the following steps to run the script to verify that the DNS server is configured correctly and that all the IP addresses entered in the DNS are reachable.

Step 1   In the primary EMS shell, navigate to the install directory.

cd /opt/Build

Step 2   Run the following command:

./checkCFG

Step 3   The system will display a message “Validating opticall.cfg input file....” If no errors are found, the system will display the No errors found message.

Example of checkCFG validation run:

-------------------------------------------------------------

---         CHECKING SYSTEM CONFIGURATION BEGIN           ---

-------------------------------------------------------------

INFO: OS patch level Generic_108528-29 is up to date.

Validating opticall.cfg input file...

Checking installation list...

Checking installation list Complete...

Determine nodetype for host secems53...

Nodetype EM is determined for host secems53...

No errors found...

The BTS 10200 System is configured as a DUPLEX system...

Checking BTS internal DNS entries in /etc/hosts file

Validating opticall.cfg input file is completed...

-------------------------------------------------------------

---         CHECKING SYSTEM CONFIGURATION END             ---

-------------------------------------------------------------

Step 4   If the system does display an error, repeat Step 4 through Step 6 of the Enter Addresses in the Primary EMS Configuration File. Make sure that all data has been entered exactly as shown on the supplied data sheets. Remember that values are case sensitive. Correct any values in opticall.cfg that differ from those on the data list.

|  | Note Perform this step only once. |
| --- | --- |

Step 5   If the system still displays an error, stop and call your system administrator to resolve this problem. If necessary, call Cisco TAC for advice.

### Copy Updated opticall.cfg File to Other EMS and CA/FS Platforms

Use the following steps to copy the updated opticall.cfg file from the primary EMS to the /etc directory on the other three platforms.

Step 1   Click the shell (window) for the secondary EMS.

Step 2   At the command prompt of the secondary EMS, start an SFTP session directed to the primary EMS.

cd /etc; sftp <hostname or IP address of primary EMS>

Step 3   At the password prompt, enter the root password for the primary EMS. The password can be obtained from your system administrator. The system will respond with an SFTP prompt.

Step 4   When the SFTP prompt appears, navigate to the /etc directory.

cd /etc

Step 5   Check that the proper file (opticall.cfg) is present in the /etc directory.

ls opticall.cfg

The opticall.cfg file should be present.

Step 6   At the SFTP prompt, transfer the configuration file to the preselected directory.

get opticall.cfg

|  | Note If the system displays any error messages during (or at the end of) this process, stop immediately and notify your system administrator. |
| --- | --- |

Step 7   After the transfer is complete and the SFTP prompt reappears, exit the SFTP session.

exit

Step 8   Repeat Step 1 through Step 7 for the primary CA/FS (use primary CA/FS shell).

Step 9   Repeat Step 1 through Step 7 for the secondary CA/FS (use secondary CA/FS shell).

## Run Verification Script to Validate Platform and DNS Data

This section describes how to run the script to verify that the DNS server is configured correctly and that all of the IP addresses entered in the DNS are reachable.

### Run the Verification Script on the Secondary EMS

Use the following steps to run the verification script on the secondary EMS.

Step 1   In the secondary EMS shell, navigate to the install directory.

cd /opt/Build

Step 2   Run the following command:

./checkCFG

Step 3   The system will display a message Validating.... If no errors are found, the system will display the No errors found message.

Step 4   If the system does display an error, repeat Step 4 through Step 6 of the Enter Addresses in the Primary EMS Configuration File section. Make sure that all data has been entered exactly as shown on the supplied data sheets. Remember that values are case sensitive. Correct any values in opticall.cfg that differ from those on the data list.

|  | Note Perform this step only once. |
| --- | --- |

Step 5   If the system still displays an error, stop and call your system administrator to resolve this problem. If necessary, call Cisco TAC for advice.

Step 6   Repeat Step 1 through Step 5 for the primary CA/FS.

Step 7   Repeat Step 1 through Step 5 for the secondary CA/FS.

## Install the Primary EMS

|  | Warning The primary side EMS and secondary side EMS need to be installed simultaneously. |
| --- | --- |

|  | Warning Do not use the file extension .orig if you choose to backup your Solaris system files, such as /etc/named.conf. Doing so will create undesired results. Instead, use unique identifiers for these backup files, such as <filename>.save or <filename>.mmddyy. |
| --- | --- |

Use the following steps to install the primary EMS:

|  | Note If this is a new installation, start at Step 3. If you already have a previous version of the Cisco BTS 10200 Softswitch software, start at Step 1. |
| --- | --- |

Step 1   At the prompt of the primary EMS, enter the command to stop the platform.

platform stop all

Step 2   If the system prompts that the platform is running, or the platform is running in active mode and prompts to continue [y/n], respond with y.

|  | Note It will take 1 to 2 minutes for the platform to stop. Wait for the prompt to reappear. |
| --- | --- |

Step 3   At the prompt of the primary EMS, enter the following command to navigate to the install directory:

cd /opt/Build

Step 4   Enter the following command:

./install.sh

|  | Note Refer to General Software Installation Procedure for any additional information needed. |
| --- | --- |

Step 5   A banner will appear as follows:

-------------------------------------------------------------

---                                                       ---

---         BTS 10200 INSTALLATION IS IN PROGRESS.        ---

---                                                       ---

-------------------------------------------------------------

Installation date: 07/05/03-13:59:04

Installation options: install.sh

Installing from /opt/Build

INFO: Oracle DB requires parallel installation on EMS side A and B.

If mate <zzzzz> installation is not running, you must run 'install.sh'

on <zzzzz> after kicking off installation on this machine.

Continue?  [y,n,?,q]y

You are installing xxxxx on yyyyy...

Continue?  [y,n,?,q]y

|  | Note Read the banner to verify that you are about to install the correct version of Cisco BTS 10200 Softswitch. Verify that xxxxx = <Opticall version specified on the CD-ROM label> and yyyyy = <host name of primary EMS as shown on the data sheets> and zzzzz = < host name of secondary EMS as shown on the data sheets>. |
| --- | --- |

a. If there is any mismatch between the display and the data sheets, enter n and press Enter. Stop immediately and locate the correct CD-ROM to install. Do not continue with this procedure until you have called Cisco TAC and confirmed that you have the correct CD-ROM.

b. If there is a perfect match between the display and the data sheets, enter y. Allow about 1 hour for this automatic installation to complete.

Step 6 	  If any OS patch/Solaris packages is needed during installation, it will be added into the system automatically. After that, the system will automatically reboot. After reboot, user needs to re-login to the system and repeat from step 3 again.

Step 7   While the primary EMS is installing, proceed to the Install Secondary EMS section.

Step 8    If prompt for reboot after installation, type y and enter return.  If no reboot request is prompted, user can manually bring up the platform. See section “Start All Cisco BTS 10200 Softswitch Application Platforms”

## Install Secondary EMS

Use the following steps to install the secondary EMS.

|  | Note If this is a new installation start at Step 3. If you already have a previous version of the Cisco BTS 10200 Softswitch software installed start at Step 1. |
| --- | --- |

Step 1   At the prompt of the secondary EMS, enter the command to stop the platform.

platform stop all

Step 2   If the system prompts that the platform is running, or the platform is running in active mode and prompts to continue [y/n], respond with y.

|  | Note It will take 1 to 2 minutes for the platform to stop. Wait for the prompt to reappear. |
| --- | --- |

Step 3   At the prompt of the secondary EMS, enter the following command to navigate to the install directory:

cd /opt/Build

Step 4   Enter the following command:

./install.sh

|  | Note Refer to General Software Installation Procedure for any additional information needed. |
| --- | --- |

Step 5   A banner will appear as follows:

-------------------------------------------------------------

---                                                       ---

---         BTS 10200 INSTALLATION IS IN PROGRESS.        ---

---                                                       ---

-------------------------------------------------------------

Installation date: 07/05/03-14:04:47

Installation options: install.sh

Installing from /opt/Build

INFO: Oracle DB requires parallel installation on EMS side A and B.

If mate <zzzzz> installation is not running, you must run 'install.sh'

on <zzzzz> after kicking off installation on this machine.

Continue?  [y,n,?,q]y

You are installing xxxxx on yyyyy...

Continue?  [y,n,?,q]y

|  | Note Read the banner to verify that you are about to install the correct version of Cisco BTS 10200 Softswitch. Verify that xxxxx = <Opticall version specified on the CD-ROM label> and yyyyy = <host name of primary EMS as shown on the data sheets> and zzzzz = < host name of secondary EMS as shown on the data sheets>. |
| --- | --- |

a. If there is any mismatch between the display and the data sheets, enter n and press Enter. Stop immediately and locate the correct CD-ROM to install. Do not continue with this procedure until you have called Cisco TAC and confirmed that you have the correct CD-ROM.

b. If there is a perfect match between the display and the data sheets, enter y. Allow one and a half hour for this automatic installation to complete.

Step 6 	  If any OS patch/Solaris packages is needed during installation, it will be added into the system automatically. After that, the system will automatically reboot. After reboot, user needs to re-login to the system and repeat from step 3 again.

Step 7   While the secondary EMS is installing, proceed to the Install the Primary CA/FS section.

Step 8    If prompted for reboot after installation, type y and enter return.  If no reboot request is prompted, user can manually bring up the platform. See section “Start All Cisco BTS 10200 Softswitch Application Platforms”

## Install the Primary CA/FS

|  | Warning The primary side CA/FS and secondary side CA/FS also need to be installed simultaneously. |
| --- | --- |

Use the following steps to install the primary CA and FS:

|  | Note If this is a new installation start at Step 3. If you already have a previous version of the Cisco BTS 10200 Softswitch software installed, start at Step 1. |
| --- | --- |

Step 1   At the prompt of the primary CA/FS, enter the command to stop the platform.

platform stop all

Step 2   If the system prompts that the platform is running, or the platform is running in active mode and prompts to continue [y/n], respond with y.

|  | Note It will take 1 to 2 minutes for the platform to stop. Wait for the prompt to reappear. |
| --- | --- |

Step 3   At the prompt of the primary CA/FS, enter the following command to navigate to the install directory:

cd /opt/Build

Step 4   Enter the following command:

./install.sh

|  | Note Refer to General Software Installation Procedure for any additional information needed. |
| --- | --- |

Step 5   A banner will appear as follows:

-------------------------------------------------------------

---                                                       ---

---         BTS 10200 INSTALLATION IS IN PROGRESS.        ---

---                                                       ---

-------------------------------------------------------------

Installation date: 07/05/03-14:10:53

Installation options: install.sh

Installing from /opt/Build

You are installing xxxxx on yyyyy...

Continue?  [y,n,?,q]y

|  | Note Read the banner to verify that you are installing the correct version of Cisco BTS 10200 Softswitch. Verify that xxxxx = <Cisco BTS 10200 Softswitch version specified on the CD-ROM label> and yyyyy = <host name of primary CA/FS as shown on the data sheets> |
| --- | --- |

a. If there is any mismatch between the display and the data sheets, enter n and press Enter. Stop immediately and locate the correct CD-ROM to install. Do not continue with this procedure until you have called Cisco TAC and confirmed that you have the correct CD-ROM.

b. If there is a perfect match between the display and the data sheets, enter y. Allow 15 to 20 minutes for this automatic installation to complete.

Step 6 	  If any OS patch/Solaris packages is needed during installation, it will be added into the system automatically. After that, the system will automatically reboot. After reboot, user needs to re-login to the system and repeat from step 3 again.

Step 7   While the primary CA/FS is installing, proceed to the Install the Secondary CA/FS section.

Step 8    If prompt for reboot after installation, type y and enter return.  If no reboot request is prompted, user can manually bring up the platform. See section Start All Cisco BTS 10200 Softswitch Application Platforms.

## Install the Secondary CA/FS

Use the following steps to install the secondary CA and FS:

|  | Note If this is a new installation start at Step 3. If you already have a previous version of the Cisco BTS 10200 Softswitch software installed, start at Step 1. |
| --- | --- |

Step 1   At the prompt of the secondary CA/FS, enter the command to stop the platform.

platform stop all

Step 2   If the system prompts that the platform is running, or the platform is running in active mode and prompts to continue [y/n], respond with y.

|  | Note It will take 1 to 2 minutes for the platform to stop. Wait for the prompt to reappear. |
| --- | --- |

Step 3   At the prompt of the secondary CA/FS, enter the following command to navigate to the install directory:

cd /opt/Build

Step 4   Enter the following command:

./install.sh

|  | Note Refer to General Software Installation Procedure for any additional information needed. |
| --- | --- |

Step 5   A banner will appear as follows:

-------------------------------------------------------------

---                                                       ---

---         BTS 10200 INSTALLATION IS IN PROGRESS.        ---

---                                                       ---

-------------------------------------------------------------

Installation date: 07/05/03-14:10:53

Installation options: install.sh

Installing from /opt/Build

You are installing xxxxx on yyyyy...

Continue?  [y,n,?,q]y

|  | Note Read the banner to verify that you are installing the correct version of Cisco BTS 10200 Softswitch. Verify that xxxxx = <Cisco BTS 10200 Softswitch version specified on the CD-ROM label> and yyyyy = <host name of primary CA/FS as shown on the data sheets>. |
| --- | --- |

a. If there is any mismatch between the display and the data sheets, enter n and press Enter. Stop immediately and locate the correct CD-ROM to install. Do not continue with this procedure until you have called Cisco TAC and confirmed that you have the correct CD-ROM.

b. If there is a perfect match between the display and the data sheets, enter y. (This accepts the default value of y to continue with the install.)

Allow 15 to 20 minutes for this automatic installation to complete. Wait for the prompt to reappear, indicating that the installation has completed.

Step 6 	  If any OS patch/Solaris packages is needed during installation, it will be added into the system automatically. After that, the system will automatically reboot. After reboot, user needs to re-login to the system and repeat from step 3 again.

Step 7    If prompt for reboot after installation, type y and enter return.  If no reboot request is prompted, user can manually bring up the platform. See section Start All Cisco BTS 10200 Softswitch Application Platforms.

## Add patch BTS_04_05_01_V14_IP00 into the release 4.5.1V14

|  | Note This section applies only to the release 4.5.1V14 load. If you are installing another load, please skip this section. However, if you are installing the release 4.5.1V14 load, you must follow this procedure to apply the patches. Otherwise the BTS system will not function properly. This procedure must be applied before you start provisioning. You should receive a CD labeled “BTS_04_05_01_V14_IP00” which contains these patches. |
| --- | --- |

### Shutdown the platforms in all BTS hosts

After all the BTS hosts finish reboot, shutdown the platform as follows:

Step 1   In each of the four UNIX shells (primary EMS, secondary EMS, primary CA/FS, secondary CA/FS), shutdown the platform

platform stop

Answer “y” when prompted, if the platform is running in active state.

### Insert the BTS_04_05_01_V14_IP00 CD into the CD-ROM drive

Perform these steps to insert the “BTS_04_05_01_V14_IP00” CD into the CD-ROM drive.

Step 1   Verify with the system administrator that you have the correct version of “BTS_04_05_01_V14_IP00” CD.

Step 2   Insert the “BTS_04_05_01_V14_IP00” CD into the CD-ROM drive of the primary EMS system.

|  | Caution Do not remove the CD-ROM until directed to do so in this procedure. It must remain in the CD-ROM drive of the primary EMS and not be moved from machine to machine. There is a step later in this procedure that indicates when it is time to remove the CD. |
| --- | --- |

### Copy the  BTS_04_05_01_V14_IP00.tar file into the Primary EMS

In the primary EMS xterm or terminal window, perform the following steps to copy the BTS_04_05_01_V14_IP00.tar file into the primary EMS:

Step 1   At the command prompt of the primary EMS, navigate to the CD-ROM.

cd /cdrom/cdrom0

Step 2   If the cdrom directory is not mounted, please follow step 2 of the sub-section “Load the K-9-optical.tar.gz File on the Primary EMS” to mount the cdrom.

Step 3   Check that the proper file BTS_04_05_01_V14_IP00.tar is present on the CD-ROM.

ls

The file BTS_04_05_01_V14_IP00.tar should be present.

Step 4   Copy the files from the CD-ROM to /opt directory.

cp BTS_04_05_01_V14_IP00.tar /opt

### Transfer BTS_04_05_01_V14_IP00.tar file to the other BTS hosts

This section describes how to transfer BTS_04_05_01_V14_IP00.tar to the other BTS hosts.

|  | Caution Do not remove the CD until directed to do so in this procedure. It must remain in the CD-ROM drive of the primary EMS and not be moved from machine to machine. There is a step later in this procedure that indicates when it is time to remove the CD-ROM. |
| --- | --- |

Step 1   Click the shell (window) for the secondary EMS.

Step 2   At the command prompt of the secondary EMS, start an SFTP session directed to the primary EMS.

cd /opt; sftp <hostname or IP address of primary EMS>

Step 3   When the SFTP prompt appears, navigate to the /opt directory.

cd /opt

Step 4   At the SFTP prompt, transfer the BTS_04_05_01_V14_IP00.tar  file to the /opt directory.

get BTS_04_05_01_V14_IP00.tar

Step 5   Repeat Step 1-4 with primary CA/FS and Secondary CA/FS.

### Apply the patch to the BTS system

For CA/FS hosts, please follow appendix I.

For EMS hosts, please follow appendix J.

### Remove BTS_04_05_01_V14_IP00.tar file and remove “BTS_04_05_01_V14_IP00” CD

Perform these steps to remove the tar file and the “BTS 10200 ***** Disk” CD from the CD-ROM drive of the primary EMS.

Step 1    In each of the UNIX shell of the BTS host,

cd /opt

rm –rf BTS_04_05_01_V14_IP00

\rm –f BTS_04_05_01_V14_IP00.tar

Step 2   Click the shell (window) for the primary EMS.

Step 3   At the command prompt of the primary EMS, enter the following command:

umount /cdrom/cdrom0

Step 4   Manually eject the CD-ROM.

Step 5   After the CD-ROM is ejected from the CD-ROM drive, place it in the CD case.

## Provisioning DB License

Prior to the 4.X release, users had to manually provision the DB License. Starting with Release 4.5, the installation process automatically loads the DB License based on the memory configuration size. This is the maximum size of each table user can provision. User will have the option later on to set their DB License limit based on their contract through CLI.

## CORBA Installation

Note:  If user does not need to install corba application on BTS system, skip this section.

This procedure describes how to install the Common Object Request Broker Architecture (CORBA) application on the primary (Side A) Element Management System (EMS) of the Cisco BTS 10200 Softswitch. After completing the installation on the primary side you will repeat the steps on the secondary (Side B) EMS. When the installation procedures are complete, refer to the appropriate related documents to provision your Softswitch system. The CORBA installation is intended for use by central office (CO) technicians and maintenance personnel who are responsible for maintaining CORBA

applications. A familiarity with telco products and networking systems is recommended.

Caution This CORBA installation removes any existing CORBA application on both EMS machines. Once you execute this procedure, it cannot be canceled. There is no back out. Do not start this procedure until you have proper authorization. If you have questions, contact Cisco TAC.

Note The commands are case sensitive. Enter the following commands exactly as shown, and press Enter at the end of each command line.

Open Unix Shell on the Primary (Side A) EMS

Perform these steps to open a Unix shell on the primary (Side A) EMS.

Step 1 Ensure that your local PC or workstation has connectivity via TCP/IP to communicate with the primary EMS unit.

Step 2 Open a Unix shell or xterm window.

Step 3 At the prompt, type ssh and the IP address or domain name of the primary EMS. For example:

ssh root@<name or IP address>

The system will respond with a login prompt.

Step 4 At the login prompt, type the following user name:

root

Step 5 At the Password prompt, enter the root password for the primary EMS (this can be obtained from your system administrator). The system will respond with a command prompt.

|  | Note If the system displays any error messages during (or at the end of) this process, stop immediately and notify your system administrator. |
| --- | --- |

Installing the CORBA Application for OpenORB Users

The CORBA application files are available for installation once the Cisco BTS 10200 Softswitch is installed. Perform these steps to install the CORBA application on the primary EMS.

Step 1 At the primary EMS prompt, enter the following command to navigate to the EMS install directory:

cd /opt/Build/

Note If the EMS install area has been removed, follow the EMS install procedure to create the area.

Step 2 Enter the cis-install.ch command:

./cis-install.sh

(For rel4.5.1V08 and beyond, skip step 3 - 4)

Step 3 When prompted

Enter the host name or IP address [ XXXXX ]:

Enter the hostname of the primary side EMS.

Step 4 When prompted

Should SSLIOP be enabled [Y/N]:

Enter your choice based on your choice. Y is default.

Step 5 Allow up to one minute for this automatic installation to complete. The system will give several prompts before and during the installation process. Some prompts are repeated. Respond with a y to each prompt.

Verifying the CORBA Application Is Running On the Primary EMS for OpenORB Users

Perform these steps to verify that the CORBA application is running on the primary EMS.

Step 1 At the primary EMS prompt, enter the following command to verify that the Name Service process is running: pgrep ins3

The system will respond by displaying the Name Service process ID, which is a number between 2 and 32,000 assigned by the system during CORBA installation. By displaying this ID, the system confirms that the ins3 process was found and is running.

Step 2 At the prompt, enter the following command to verify that the CORBA interface servant (cis3) process is running: pgrep cis3

The system will respond by displaying the cis3 process ID, which is a number between 2 and 32,000 assigned by the system during CORBA installation. By displaying this ID, the system confirms that the cis3 process was found and is running.

Installing the CORBA Application on Side B (Secondary) EMS

To install the CORBA application on the Side B (secondary) EMS, repeat all of the steps in the “Verifying the CORBA Application Is Running On the Primary EMS for OpenORB Users” section above except replace primary EMS hostname with secondary EMS hostname.

## Installing the Mini-Browser Adaptor (MBA) Application on another machine

This section is only for those who need to install MBA package. For more information about this package, please refer to the document “Cisco BTS10200 Softswitch SIP Protocol Provisioning Guide”.

|  | Note Never install this package in any Cisco BTS 10200 EMS or CA/FS nodes. This software is intended to be installed on a separate host. The requirements for the separate MBA host machine are provided in the “Cisco BTS 10200 Softswitch Release Notes”. Load the specified Solaris operating system first, and then follow the steps below to install the MBA software. |
| --- | --- |

|  | Note The software for both the GUI-FS and the MBA are included in the software supplied with your Cisco BTS 10200 Softswitch. |
| --- | --- |

Here are the steps to install MBA package on another machine

Step 1	Repeat Step 1 to Step 5 in section Load the K9-opticall.tar.gz File on the Primary EMS, except loading the K9-opticall.tar.gz into the machine you intended to install the MBA package.

Step 2	cd /opt/Build

Step 3 Run mba-install.sh

Step 4 When prompted

Enter the DNS name of the local system:

Type the domain name of your current machine, and hit Enter.

Step 5 When prompted

Enter the DNS name of the POTS Feature Server system:

Type the domain name of the POTS Feature Server (usually same as the CA).

|  | Note MBA automatically starts when the installation script is finished. |
| --- | --- |

Step 6.  Verify MBA execution by monitoring the MBA.log file located in /opt/ems/log.

## Start All Cisco BTS 10200 Softswitch Application Platforms

Use the following steps to start all the Cisco BTS 10200 Softswitch application platforms:

Step 1   In each of the four Unix shells (primary EMS, secondary EMS, primary CA/FS, and secondary CA/FS), make sure that the installation has completed successfully and rebooted. After reboot, your connection to the box will be disconnected. Reconnect to each box using:

ssh -l root xxx.xxx.xxx.xxx

Step 2   After installation and reboot, the platforms will automatically start. Check the status of the platform using:

nodestat

If the platforms do not come up successfully, contact your system administrator to evaluate the problem.

Step 3 	 If no reboot is involved, user can manually start up the platform. At the command prompt, enter the command to start all application platforms in all four boxes.

platform start

Enter y when prompted. This will start all three platforms in CA/FS or 2 platforms in EMS. It will take up to 15 minutes for each platform to start. If you see any error messages, contact your system administrator to evaluate the problem.

## Add patch BTS_04_05_01_V14_IP01 into the release 4.5.1V14

|  | Note Again this section applies only to the release 4.5.1V14 load. And this patch is only needed to apply for system which uses CORBA for connection (see section “CORBA Installation”). Other than that user can skip this section. If the system does not use CORBA for connection, but uses a feature called “Virtual IP”, please contact TAC/AS for how to fix the problem. |
| --- | --- |

If user decided this patch is necessary for their system, please contact Advanced Service (AS) group to obtain the software. Then follow the procedure in Appendix K to apply this patch.

|  | Note Appendix L shows the procedure to remove this patch, just in case user wants to remove this patch. However, user will not be able to remove this patch after they execute the next section “Remove the Build Directory to Free Disk Space”. |
| --- | --- |

## Remove the Build Directory to Free Disk Space

Cisco recommends that you free the disk space occupied by the build directory that was generated during the installation process because it is no longer needed. Use the following steps to free disk space:

Step 1   In each of the four Unix shells (these UNIX shells should be started up by the root user. See section “Open UNIX shells and Create Log Files”), remove the Build directory.

rm -rf /opt/Build

Step 2   In each of the four shells, verify that the Build directory is deleted.

cd /opt; ls

The Build directory should not be in the list.

Step 3 	 Remove the following tar files.

rm –f  K9-opticall.tar.gz  K9-btsdb.tar.gz K9-extora.tar.gz K9-oraengine.tar.gz

Step 4   When finished, exit all hosts.

exit

## Enabling Log Archive Facility (LAF) process

If utilizing the Log Archive Facility (LAF) feature, you must set up the authorization for non-interactive SSH login to the external archive server for Cisco BTS 10200 to access, and turn the LAF processes to active state. (Right after the fresh installation and platform start, LAF process is in dormant state). The steps to set up the authorization in external archive server and turn the LAF processes to active is listed in Appendix E.

If you are not enabling this feature, skip this section.

Appendix A

General Software Installation Procedure

This appendix is to be used as a reference when performing the Cisco BTS 10200 Softswitch Application Installation procedure:

## Installation Scenarios

This section describes software installation scenarios that the installation process can support. Each installation scenario is determined by options supplied in the command line at the time the installation process is invoked. Scenarios are also determined by parameter values supplied in the configuration file opticall.cfg.

Installation validates system network interface and DNS setup at the beginning of the installation process. It there are no errors found, then the Cisco BTS 10200 Softswitch Application Software is installed on the Call Agent, Feature Server AIN, and POTS. The Cisco BTS 10200 Softswitch Application Software and Oracle DB are also installed on your EMS machines.

At the end of the installation, you should get a message indicating whether the installation has completed successfully or failed. If the installation is successful, then you can invoke the platform control program to start the application. Otherwise, an error message will result when you try to invoke the platform program.

### Supported Command Line Options

This section describes all available command line options in releases 4.5 for a customized installation. The entire installation process is controlled by install.sh. The available options are as follows:

- Install.sh

- Install.sh –clearshm

- Install.sh -cleardb

- Install.sh -createdb

- Install.sh -dbonly

- Install.sh -force

- Install.sh –help

- Install.sh –update_cfg

#### Install.sh

This is a default installation option by not giving any command line option. It validates system network interface and DNS setup at the beginning of installation process. If there are no errors found, then it installs all Cisco BTS 10200 Softswitch software packages on the CA/FS, and EMS machines, which includes all Oracle DB packages. Cisco BTS 10200 Softswitch packages are described in the ”Package Information” section.

#### Install.sh -clearshm

Installation program validates system network interface and DNS setup at the beginning of the installation process. If there are no errors found, clean Shared-Memory DB as follows:

- CA/FS - Clears Shared-Memory DB

- EMS - Not applicable

If this option is used on the CA/FS, then you are required to use “Install.sh -cleardb” or “Install.sh -createdb” to cleanup Oracle DB.

#### Install.sh -cleardb

Installation program validates system network interface and DNS setup at the beginning of installation process. It there are no errors found, then all provisioned data is removed from Oracle DB as follows:

- CA/FS - Not applicable

- EMS - Remove all provisioned data with schema untouched

If this option is used on the EMS, then you are required to use “Install.sh -clearshm” to cleanup CA/FS Shared-MemoryDB.

#### Install.sh -createdb

Installation program validates system network interface and DNS setup at the beginning of installation process. It there are no errors found, re-creates Oracle DB as follows:

- CA/FS - Not applicable

- EMS - Re-creates Oracle DB schema and data

If this option is used on the EMS, then you are required to use “Install.sh -clearshm” to cleanup CA/FS Shared-Memory DB.

#### Install.sh -dbonly

Installation program validates system network interface and DNS setup at the beginning of the installation process. If there are no errors found, re-create Oracle DB as follows:

- CA/FS - Not applicable

- EMS - Installs Oracle DB and creates new DB schema

If this option is used on the EMS, then are required to use “Install.sh -clearshm” to cleanup CA/FS Shared-Memory DB.

#### Install.sh -force

Installation bypasses validation process on all required parameters, system network interface, and DNS setup. It installs the Cisco BTS 10200 Softswitch Application Software on Call Agent, Feature Server AIN and POTS; and installs the Cisco BTS 10200 Softswitch Application Software and Oracle DB on EMS machines.

This scenario is needed to support cases where systems must be installed before the network and DNS can be setup.

|  | Note The validation process can still run after installing the Cisco BTS 10200 Softswitch software but before running application software to verify any discrepancies. |
| --- | --- |

#### Install.sh -help

This option will print help information when needed to guide you if you are not sure about choosing installation options.

Install.sh –update_cfg

This option will update the /etc/opticall.cfg to the format of the version which is going to be installed.

## Package Information

The Cisco BTS 10200 Softswitch application software is divided into packages. Each

package pulls files together according to their logical relation and dependency. The installation utilizes the SUN packaging utility to install packages in order to guarantee correctness of software delivery.

|  | Release 4.5 CA/FS |
| --- | --- |
| 1 | BTSacct - User accounting |
| 2 | BTSain - AIN Feature Server application platform |
| 3 | BTSaincat – Catalog files for AIN shared memory |
| 4 | BTSbase - EMS base directory structure |
| 5 | BTSca - Call Agent application platform |
| 6 | BTScacat – Catalog files for CA shared memory |
| 7 | BTScalib - Call Agent specific shared libraries |
| 8 | BTSfalib - AIN Feature Server specific shared libraries |
| 9 | BTSfplib - POTS/CTX Feature Server specific shared libraries |
| 10 | BTSfslib- Common Feature Server shared libraries |
| 11 | BTShard - Hardens security (no longer there after 4.5.1V04) |
| 12 | BTShmn - Hardware monitor |
| 13 | BTSinst - Installation related programs |
| 14 | BTSjava - SUN JDK package |
| 15 | BTSlib - Common shared libraries |
| 16 | BTSoamp - Primary EMS applications (java classes) |
| 17 | BTSoms - OMS hub related files and directories |
| 18 | BTSossh - Secure shell package |
| 19 | BTSpots - POTS/CTX Feature Server application platform |
| 20 | BTSpotscat – Catalog files for POTS shared memory |
| 21 | BTSsmg - OMS system manager |
| 22 | BTSsnmp - SNMP agent and its information base |
| 23 | BTStools - CA/FS related utilities/tools |
| 24 | BTStzone - BTS timezone (no longer there after 4.5.1V04) |
| 25 | BTSutil - Common java classes and libraries |
| 26 | BTSxntp – Time synchronization package |

|  | Release 4.5 EMS |
| --- | --- |
| 1 | BTSacct - User accounting |
| 2 | BTSbase - EMS base directory structure |
| 3 | BTSbdms - Bulk Data Management application platform |
| 4 | BTSbmlib - Bulk Data Manager specific libraries |
| 5 | BTSemlib - Element Manager specific libraries |
| 6 | BTSems - EMS application platform |
| 7 | BTSemsql - Second mysql DB instance for logging activities |
| 8 | BTShard - Hardens security (no longer there after 4.5.1V04) |
| 9 | BTShmn - Hardware monitor |
| 10 | BTSinst - Installation related programs |
| 11 | BTSjava - SUN JDK package |
| 12 | BTSlib - Common shared libraries |
| 13 | BTSmgp - Telnet management package for EMS |
| 14 | BTSmysql - Mysql database |
| 15 | BTSoamp - Primary EMS applications (java classes) |
| 16 | BTSoms - OMS hub related files and directories |
| 17 | BTSora - Oracle database engine |
| 18 | BTSorada - Oracle database schema and data |
| 19 | BTSoradm - Oracle common administrative scripts and sql files |
| 20 | BTSoramg – Oracle replication heartbeat |
| 21 | BTSordba – Oracle database utilities |
| 22 | BTSoreng – Validate the Oracle Engine |
| 23 | BTSoropt - Oracle Database PL/SQL, trigger, CLI, and preloaded data |
| 24 | BTSorscm - Oracle Database tablespace, schema and replication |
| 25 | BTSortbs - Oracle Database table sizing files |
| 26 | BTSossh - Secure shell package |
| 27 | BTSsec - Security and user account |
| 28 | BTSsmg - OMS system manager |
| 29 | BTSsnmp - SNMP agent and its information base |
| 30 | BTSsup - OMAP status update process |
| 31 | BTSutil - Common java classes and libraries |
| 32 | BTStools - CA/FS related utilities/tools |
| 33 | BTStzone – Cisco BTS 10200 timezone (no longer there after 4.5.1V04) |
| 34 | BTSxntp – time synchronization package |
| 35 | SFWncur - SUN ncurses library package for EMS |
| 36 | SMCapache - Apache HTTP server package for EMS |

## Installation Steps and Utilities

This section describes programs and utilities for software installation and application management.

### Install.sh

This script will install the EMS Application software, provisioning database, and BILLING database on the EMS machines with Solaris 10. It also installs partial EMS Application, such as OMS hub, Hardware Monitor, Call Agent and Feature Server Application software on CA/FS machines with Solaris 10.

#### Installing a Fresh Software Load with Jumpstart

- Make sure DNS server and local cache daemon are configured and in service

- Make sure opticall.cfg is configured according to network site survey sheets

- Run checkCFG to validate parameters values in opticall.cfg prior to installation (this is done by installation as well)

- Install application software

  - cd /net/yensid/rel30/<release>/Build

  - ./install.sh

#### Upgrading a Software Load to a New Load without Schema or Internal Data Structure Changes

- cd /net/yensid/rel30/<release>/Build

- ./install.sh -aponly

#### Upgrading a Software Load to a Newer Load with Schema or Internal Data Structure Changes

You have two choices available depending on what system is upgraded:

- For a lab system, a fresh installation is recommended since outage is not a concern and re-provisioning of data can be done in after hours.

- For a production system, a comprehensive upgrade procedure must be followed. It also might involve OS upgrades. This procedure is only available when the software release is ready to be shipped.

### Platform

Usage:

/etc/init.d/platform -h

/etc/init.d/platform start [-noping | -noirdp | -bypass] [-i PROCESS]

/etc/init.d/platform stop [-f | -i PROCESS]

Description:

start : start all Cisco BTS 10200 PROCESS.

stop : stop Cisco BTS 10200 application instances

-bypass : start application without error checking (includes -noping, -noirdp).

-noping : start application without mate pinging.

-noirdp : start application using static routing.

-nocopy: start application without saving current shared memory database

-h help : print this usage information.

-f force : terminate all Cisco BTS 10200 PROCESS.

-i instance: Cisco BTS 10200 application instance.

Location:

/opt/bts/bin/platform

This script is used for starting and terminating EMS, CA and FS Applications. Applications include:

a. On Element Manager:

  - EM01

  - BDMS01

b. On Call Agent and Feature Server:

  - CAxxx where xxx is the instance number, default is CA146

  - FSAINyyy where yyy is the instance number, default is FSAIN201

  - FSPTCzzz where zzz is the instance number, default is FSPTC235

Examples:

Step 1   To start all CA, FS, EMS Applications, enter:

platform start

Step 2   To start all CA, FS, EMS Applications, without error checking, enter:

platform start -bypass

Step 3   To start all CA, FS, EMS Applications, without checking for IRDP, enter : platform start –noirdp

Step 4	 To start all CA, FS, EMS Applications, without saving current  shared memory database, enter:

platform start –nocopy

Step 5   To stop all CA, FS, EMS Applications, enter:

platform stop

Step 6   To start an individual CA, FS, EMS Application, enter:

platform start -i APP -- where APP can be:

a. EM01

b. BDMS01

c. CAXXX

d. FSAINXXX

e. FSPTCXXX

Step 7   To stop an individual CA, FS, EMS Application, enter:

platform start -i APP -- where APP can be:

a. EM01

b. BDMS01

c. CAXXX

d. FSAINXXX

e. FSPTCXXX

where XXX represent the instance number of CA, FSPTC or FSAIN

nodestat

### Usage:

### nodestat:  shows full details of node information, including application instance status, database status, interface status, etc.

### nodestat -apponly: shows only the status of application instances.

This utility will print useful information in a tabular format with primary/secondary info. The following table is the explanation of status that nodestat displays:

| Status | Explanation |
| --- | --- |
| N/A | -- Not Applicable |
| OOS | -- out of service: means the application is not running |
| INS | -- in-service: means the application is running normally |
| ACTIVE | -- an application instance is running in normal ACTIVCE state |
| STANDBY | -- an application instance is running in normal STANDBY state |
| FAULTY | -- an application instance is running in abnormal FAULTY state |
| UNKNOWN | -- unable to get application instance state information |

Appendix B

Configure the Ethernet Switch for 4.X Load

The following is a procedure for disabling auto speed negotiation between the networks cards on the Cisco BTS 10200 Softswitch and Ethernet switch.

Note: This only needs to be done for the duplex system with the 2950 Catalyst switch for release 4.1 and above.

You need to first set up the 2950 Catalyst switch to force 100 megabit duplex. To do so, first log into the 2950 through console access, then perform the following command:

int f0/1

speed 100

duplex full

!

int f0/2

speed 100

duplex full

!

int f0/3

speed 100

duplex full

.

.

.

.

.

.

.

int f0/24

speed 100

duplex full

Appendix C

A Template of opticall.cfg in Release 4.5.1V14

########################################################################

# Copyright (c) 2002-2006 by Cisco Systems, Inc.

#

#   AUTHOR      DATE            REVISION

#   ---------   ----------      ----------------------------------------

#   J.Daih      05/04/2000      initial

#   J.Daih      08/15/2000      changed domain names for redundancy

#   J.Daih      08/23/2000      added section info

#   J.Daih      04/25/2001      change mgcp to only one name and

#                               added critical route IP for pmg

#   J.Daih      12/11/2001      change CLASS parameter

#   J.Daih      02/04/2002      Added new parameter DNS_FOR_CAxxx_SIA_COM

#                               and TARGET_MARKET

#   J.Daih      07/01/2002      Added new parameters:

#                               DNS_FOR_FSAIN_SIDE_A_SGW_COM

#                               DNS_FOR_FSAIN_SIDE_B_SGW_COM

#                               DNS_FOR_FSPTC_SIDE_A_SGW_COM

#                               DNS_FOR_FSPTC_SIDE_B_SGW_COM

#   A.Chan      04/15/2003      Added new parameters:

#                               DNS_FOR_CAxxx_H3A_COM

#                               DNS_FOR_CAxxx_MGA_COM

#   A.Chan      04/16/2003      Added new parameters:

#                               DNS_FOR_CA_SIDE_A_BLG_LINK_MONITOR

#                               DNS_FOR_CA_SIDE_B_BLG_LINK_MONITOR

#   A.Chan      05/02/2003      Added new flag:

#                               MEM_CFG_SELECTION

#   A.Chan      06/06/2003      Add new parameters:

#                               DNS_FOR_FSPTCxxx_GFS_COM

#   A.Chan      06/31/2004      Add new parameters:

#                               BROKER_DNS_FOR_PMG_IN_EMS

#                               BROKER_DNS_FOR_PMG_IN_CA

#                               DNS_FOR_EMS_SIDE_A_OMS_SLAVE_HUB

#                               DNS_FOR_EMS_SIDE_B_OMS_SLAVE_HUB

#   A.Chan      08/18/2004      Add NTP servers

#   A.Chan      11/03/2004      Remove SGA parameters

#   A.Chan      11/02/2004      Add MARKET_TYPE and NAMED_ENABLED,

#                               remove NSCD_NAMED_ENABLED

#   A.Chan      05/22/2005      remove TARGET_MARKET

#   A.CHan      06/21/2005      add LAF parameters

#   A.Chan      09/01/2005      add NSCD_ENABLED

#   A.Chan      09/14/2005      remove DNS_FOR_CA_MGCP_COM

#   Kefu He     07/27/2006      add BILLING_FILENAME_TYPE

#

#

#  FILE: opticall.cfg

#

#  PURPOSE: This is a configuration file used for installing a BTS 10200

#           system which composed of a redundant Call Agent entity, a

#           redundant AIN Feature Server entity, a redundant POTS Feature

#           Server entity, and a redundant Element Manager entity. A Call

#           Agent, AIN/POTS Feature Servers can be installed on a same

#           host or separate hosts. An Element Manager is installed on

#           one host.

#

#

#  APPLICATION TYPES: 1. CA     -- Call Agent

#                     2. FSAIN  -- AIN Feature Server

#                     3. FSPTC  -- POTS/CENTRIX Feature Server

#                     4. EM     -- Element Manager

#

# FIVE HARDWARE CONFIGURATIONS ARE SUPPORTED:

#

#    CONFIGURATION 1:   CA/FSAIN/FSPTC -- on a same host

#                       EM             -- on one host

#    CONFIGURATION 2:   CA/FSAIN -- on a same host

#                       FSPTC    -- on one host

#                       EM       -- on one host

#    CONFIGURATION 3:   CA/FSPTC -- on a same host

#                       FSAIN    -- on one host

#                       EM       -- on one host

#    CONFIGURATION 4:   CA          -- on one host

#                       FSPTC/FSAIN -- on one host

#                       EM          -- on one host

#    CONFIGURATION 5:   CA    -- on one host

#                       FSPTC -- on one host

#                       FSAIN -- on one host

#                       EM    -- on one host

#

#############################################################################

# Note:  The parameters below are applied to the system only during fresh

#        install/upgrade. Changing these parameters will not take effect until

#        the next re-install/upgrade. Any changes to these parameters should be

#        done only with a full understanding of the impact of such changes to the

#        system, after consultation with Cisco.

#############################################################################

#++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++

#+++++++++++++++++++++  REQUIRED  COMMON  LIST  +++++++++++++++++++++++

#

# A CORBA specific identifier to uniquely identify a site of a BTS 10200 system.

#

SITEID=

#

# This flag will guide installation process to set gdrs daemon process

# which will reconfig ss7 redundancy in a Geographically Distributed

# Redundancy & Survivability system. Valid values are: "y" or "n".

#

GDRS_ENABLED=n

#

# This flag will guide installation process to enable or disable H323

# processes to suite customer's needs. Valid values are: "y" or "n".

#

H323_ENABLED=y

#

# This flag will determine whether nscd (Name Server Cache Daemon)

# will be enabled or disabled in the system.   Cisco recommends

# strongly that nscd be enabled. Vaild values are: "y" or "n".

# "y" = enable, "n" = disbaled. Default is "y".

#

NSCD_ENABLED=y

#

# This flag will guide installation process to enable or disable

# Domain Name Server process (named) to suit customer's

# needs. Valid values are: "cache_only", "secondary_dns_all_hosts",

# "secondary_dns_CA_only" or "n". Default is "n"

# n                           : do not start up the named process.

# cache_only                  : start up the named process as cache server only

# secondary_dns_all_hosts     : start up the named process as internal secondary

#                               authoritative DNS server in all BTS hosts in

#                               this system.

# secondary_dns_CA_only       : start up the named process as internal secondary

#                               authoritative DNS server in CA hosts only.

#

NAMED_ENABLED="n"

#

# This flag indicate the customer type of market. The valid values

# are T1 and CABLE. This flag determine what nscd (local cache) configuration

# to use.

# T1   : mostly with fixed assignment IP addresses such as IADs and few or no

#        DHCP assigned addresses

# CABLE: large universes of DHCP assigned IP addresses

#

MARKET_TYPE=

#

# This flag will enabled/disable following processes related to SS7 call processing

# at time when each application platform is installed:

#       1. SGA in Call Agent

#       2. TSA in Feature Server POTS

#       3. TSA in Feature Server AIN

#

# The possible values are "y" and "n", default is set to "y".

SS7_ENABLED=y

# IPSEC_ENABLED variable will activate/deactivate the PacketCable Security

# feature on BTS 10200. Possible values for IPSEC_ENABLED are "y" or "n".

# The default is set to "n".

#

IPSEC_ENABLED=

#

# This flag will guide the installation which mem.cfg to use

# The allowable values are "small", "medium4G", "medium", "demo", "router"

# , "localLnp" and "localLnpRN"

# if the flag is "small", it will point to small size mem.cfg

# if the flag is "medium4G", it will point to medium size mem.cfg which requires 4G of memory

# if the flag is "medium", it will point to medium size mem.cfg which requires 8G of memory

# if the flag is "demo", it will use a mem.cfg for demo and lab use only

# if the flag is "router", it will use a mem.cfg for route server

# if the flag is "localLnp", it will use a mem.cfg which supports local LNP

# with onboard LNP database (DN2GN table)

# if the flag is "localLnpRN", it will use a mem.cfg which supports local LNP

# with onboard LNP database (DN2RN table)

#

MEM_CFG_SELECTION=

# A BTS 10200 system hardware configuration indicator. Refer to the heading

# to determine a proper value for your system.

# for all possible configurations, see comments in header section.

#

CONFIGURATION=1

# Parameters used by Feature Server AIN and POTS TSA process

# For IN-1/AIN0.1 Services BTS10200 can communicate to SIGTRAN based Signaling

# Gateways over SUA. The option chosen here MUST support SSN based

# Routing-Keys on the Signaling Gateway. Please select appropriate option

# as per the Signaling Gateway you are planning to use. If you are using

# Cisco-ITP Signaling Gateway you MUST chose SUA. The default is set to SUA.

# Note: Currently this parameter only support SUA.

#

SGW_OPTION=SUA

# This is a DNS name which is used in platform.cfg file by pmg when DNS for RED

# ping fails. It helps pmg to determine the failure is on the local host or is

# on DNS server. So, the pmg can take proper action accordingly.

# In 4,2 configuration, one should be set to return IP address(es) of the router(s)

# in EMS management network, and another one in CA/FS signalling network

#

BROKER_DNS_FOR_PMG_IN_EMS=

BROKER_DNS_FOR_PMG_IN_CA=

# These are the NTP servers used by BTS system to sync the time.

# All the servers should be in the same line and separated by space

# They should be double-quoted together as "x.x.x.x y.y.y.y z.z.z.z"

# During upgrade, all servers from ntp.conf will be automatically added here.

# So in order to remove one ntp server, this server needs

# to be removed from both opticall.cfg and /etc/BTSxntp/etc/ntp.conf

# before upgrade

#

NTP_SERVERS=

# The following parameters are related to  Log Archive Facility (LAF) process

# If  they are left blank, LAF process will be turned off.

# If user want to use this feature, he/she must provide info about

# the external archive system, target directory and the disk quota (in G)

# for each platform.

# Example: CA146_LAF_PARAMETER="yensid /CA146_trace_log 20"

# Also the target directory must be set up in that external archive system.

#

CAxxx_LAF_PARAMETER=

FSPTCxxx_LAF_PARAMETER=

FSAINxxx_LAF_PARAMETER=

EMS_LAF_PARAMETER=

BDMS_LAF_PARAMETER=

# The following parameter is related to Billing Subsystem, used by BMG process.

# Currently BTS supports two different billing record file naming conventions:

# default naming convention and PacketCable naming convention.

# The values of this parameter are:

#     - "Default", Default naming convention.

#     - "PacketCable", PacketCable naming convention.

# The default value of this parameter is "Default".

#

BILLING_FILENAME_TYPE=Default

#++++++++++++++++  END  OF  REQUIRED  COMMON  LIST  +++++++++++++++++++

#++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++

#######################  HOST  NAME  LIST   ############################

#

# These are used for determining a BTS 10200 system duplex/simplex mode.

# EMS_SIDE_A_HN and EMS_SIDE_B_HN host names are used by a SNMP

# agent to send traps from a Call Agent to an EMS. They are also

# used by an EGA process to communicate to an EMS at startup.

#

# Examples: A simplex system:

#                   CA: CA_SIDE_A_HN=prica10

#                       CA_SIDE_B_HN=prica10

#                  AIN: FSAIN_SIDE_A_HN=prica10

#                       FSAIN_SIDE_B_HN=prica10

#                 POTS: FSPTC_SIDE_A_HN=prica10

#                       FSPTC_SIDE_B_HN=prica10

#                  EMS: EMS_SIDE_A_HN=priems10

#                       EMS_SIDE_B_HN=priems10

#

#           A duplex system:

#                   CA: CA_SIDE_A_HN=prica10

#                       CA_SIDE_B_HN=secca10

#                  AIN: FSAIN_SIDE_A_HN=prica10

#                       FSAIN_SIDE_B_HN=secca10

#                 POTS: FSPTC_SIDE_A_HN=prica10

#                       FSPTC_SIDE_B_HN=secca10

#                  EMS: EMS_SIDE_A_HN=priems10

#                       EMS_SIDE_B_HN=secems10

#

CA_SIDE_A_HN=

CA_SIDE_B_HN=

FSAIN_SIDE_A_HN=

FSAIN_SIDE_B_HN=

FSPTC_SIDE_A_HN=

FSPTC_SIDE_B_HN=

EMS_SIDE_A_HN=

EMS_SIDE_B_HN=

########################################################################

#=======================================================================

#==================   APPLICATION  INSTANCE  LIST   ====================

#

# Application instances to be installed on a target HOST according to

# HARDWARE CONFIGURATION. Each item in a list must be space separated

# and within a double quote. All letters must be CAPITALIZED.

CA_INSTALLING_LIST="CA146"

FSAIN_INSTALLING_LIST="FSAIN205"

FSPTC_INSTALLING_LIST="FSPTC235"

EMS_INSTALLING_LIST="EM01"

BDMS_INSTALLING_LIST="BDMS01"

#=============  END  OF  APPLICATION  INSTANCE  LIST   =================

#=======================================================================

#-----------------------------------------------------------------------

#--------------  PMG(red,kam)  REQUIRED  DNS  NAMES   ------------------

#

# These are qualified domain names used by RDM and KAM

# processes in CA/FSAIN/FSPTC/EM.  They are used for communication with

# the mate by KAM and RDM.  These DNS names should NOT be used by any

# other processes for any purpose.  Each name should return two IP addresses.

DNS_FOR_CA_SIDE_A_RED=red-asysCA.domainname

DNS_FOR_CA_SIDE_B_RED=red-bsysCA.domainname

DNS_FOR_FSAIN_SIDE_A_RED=red-asysAIN.domainname

DNS_FOR_FSAIN_SIDE_B_RED=red-bsysAIN.domainname

DNS_FOR_FSPTC_SIDE_A_RED=red-asysPTC.domainname

DNS_FOR_FSPTC_SIDE_B_RED=red-bsysPTC.domainname

DNS_FOR_EMS_SIDE_A_RED=red-asysEMS.domainname

DNS_FOR_EMS_SIDE_B_RED=red-bsysEMS.domainname

#------------  END  OF  PMG(red,kam)  REQUIRED  DNS  NAMES   -----------

#-----------------------------------------------------------------------

#=======================================================================

#=====================  CA  REQUIRED  DNS  NAMES  ======================

#

# These are qualified DNS names used by BLG process in

# Call Agents to communicate with BMG in EMS for billing. Each

# name should return two IP addresses of a EMS host.

DNS_FOR_CA_SIDE_A_BLG_COM=blg-asysEMS.domainname

DNS_FOR_CA_SIDE_B_BLG_COM=blg-bsysEMS.domainname

# These are qualified DNS names used to LHM to monitor billing links

# Each name should return two IP addresses of a CA host

DNS_FOR_CA_SIDE_A_BLG_LINK_MONITOR=blg-asysCA.domainname

DNS_FOR_CA_SIDE_B_BLG_LINK_MONITOR=blg-bsysCA.domainname

# These are qualified DNS names used by a MGA process in

# Call Agents for communication to external devices.

# Each name resolves to two IP addresses in the same subnet as primary

# and secondary interfaces respectively. Each instance must have a

# unique DNS name and two uniquely assocaited LOGICAL IP addresses.

# This name should return two LOGICAL IP addresses.

DNS_FOR_CAxxx_MGA_COM=mga-sysCAxxx.domainname

# These are qualified DNS names used by pmg in each application

# to help determine what actions are needed if there is a redundancy

# communication failure.

# Each name should return two IP addresses of a Call Agent.

DNS_FOR_CA_SIDE_A_CRIT_COM=crit-asysCA.domainname

DNS_FOR_CA_SIDE_B_CRIT_COM=crit-bsysCA.domainname

# These are old DNS names used by SIA process in Call Agents.

# This name should return four IP addresses (two addresses from each

# side of Call Agent). However, in 4.1 or above, it is not used

# by SIA process anymore (except in simplex). But it is still used by

# KMS and installation to identify the physical network interfaces.

DNS_FOR_CA_SIA_COM=sia-sysCA.domainname

# These are qualified DNS names used by a SIA process in

# Call Agents for communication to external devices.

# Each name resolves to two IP addresses in the same subnet as primary

# and secondary interfaces respectively. Each instance must have a

# unique DNS name and two uniquely assocaited LOGICAL IP addresses.

# This name should return two LOGICAL IP addresses.

DNS_FOR_CAxxx_SIA_COM=sia-sysCAxxx.domainname

# These are qualified DNS names used by a H3A process in

# Call Agents for communication to external devices.

# Each name resolves to two IP address in the same subnet as primary

# and secondary interfaces respectively. Each instance must have a

# unique DNS name and two uniquely assocaited LOGICAL IP addresses.

# This name should return two LOGICAL IP addresses.

DNS_FOR_CAxxx_H3A_COM=h3a-sysCAxxx.domainname

# These are qualified DNS names used by a SIM process in

# Call Agents for LOCAL communication.

# Each name resolves to two logical IP addresses in the same subnet

# as the third virtual interface of management network(s) . Each instance

# must have a unique DNS name and two uniquely assocaited LOGICAL IP

# addresses. They must NOT be the same as the domain names of POTS

# and ASM. (i.e. DNS_FOR_FSPTCxxx_POTS_COM and DNS_FOR_FSAINxxx_ASM_COM)

# For a simplex, use the host name for this parameter

DNS_FOR_CAxxx_SIM_COM=sim-sysCAxxx.domainname

# These are qualified DNS names used by a ANM process in

# Call Agents for LOCAL communication.

# Each name should return two IP addresses of a Call Agent host.

DNS_FOR_CA_SIDE_A_ANM_COM=anm-asysCA.domainname

DNS_FOR_CA_SIDE_B_ANM_COM=anm-bsysCA.domainname

# These are qualified DNS names used by a SGA process in

# Call Agents for EXTERNAL communication.

# Each name should return two IP addresses of a Call Agent host

# Accessible to external devices.

DNS_FOR_CA_SIDE_A_SGA_COM=sga-asysCA.domainname

DNS_FOR_CA_SIDE_B_SGA_COM=sga-bsysCA.domainname

# These are qualified DNS names used by a BSM process in

# Call Agents for ISDN Backhaul  communication.

# Each name should return one IP address of a Call Agent host.

DNS_FOR_CA_SIDE_A_1_BSM_COM=bsm-a1sysCA.domainname

DNS_FOR_CA_SIDE_A_2_BSM_COM=bsm-a2sysCA.domainname

DNS_FOR_CA_SIDE_B_1_BSM_COM=bsm-b1sysCA.domainname

DNS_FOR_CA_SIDE_B_2_BSM_COM=bsm-b2sysCA.domainname

#===============  END  OF  CA  REQUIRED  DNS  NAMES  ===================

#=======================================================================

#+++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++

#++++++++++++++++   FSAIN  REQUIRED  DNS  NAMES   ++++++++++++++++++++++

#

# These are qualified DNS names used by a ASM process in AIN

# Feature Servers for LOCAL communication.

# Each name should return two logical IP addresses of a AIN Feature

# Server which must be in the same subnet as the third virtual interface

# of management network(s) . Each instance must have a unique DNS name

# and two uniquely assocaited LOGICAL IP addresses.

# They must NOT be the same as the domain names of SIM and POTS.

# (i.e. DNS_FOR_CAxxx_SIM_COM and DNS_FOR_FSPTCxxx_POTS_COM)

# For a simplex system, use host name for this parameter

DNS_FOR_FSAINxxx_ASM_COM=asm-sysAINxxx.domainname

# These are qualified DNS names used by pmg in each application

# to help determine what actions are needed if there is a redundancy

# communication failure.

# Each name should return two IP addresses of a AIN Feature Server.

DNS_FOR_FSAIN_SIDE_A_CRIT_COM=crit-asysAIN.domainname

DNS_FOR_FSAIN_SIDE_B_CRIT_COM=crit-bsysAIN.domainname

# These are qualified DNS names used by a TSA process in Feature Server

# AIN for Signaling Gateway communication.

# Each name should return two IP addresses of an AIN Feature Server host.

DNS_FOR_FSAIN_SIDE_A_SGW_COM=sgw-asysAIN.domainname

DNS_FOR_FSAIN_SIDE_B_SGW_COM=sgw-bsysAIN.domainname

#++++++++++++ END  OF  FSAIN  REQUIRED  DNS  NAMES   +++++++++++++++++++

#+++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++++

#-----------------------------------------------------------------------

#----------------   FSPTC  REQUIRED  DNS  NAMES   ----------------------

#

# This is fully qualified DNS name used by the POTS process

# in Feature_Server FSPTC. Each name should return two logical

# IP addresses of a POTS/CENTRIX Feature Server which match the

# subnet of the third virtual interface of management network(s).

# Each instance must have a unique DNS name and two uniquely

# assocaited LOGICAL IP addresses.

# They must NOT  be the same as the domain names of SIM and ASM

# (i.e. DNS_FOR_CAxxx_SIM_COM and DNS_FOR_FSAINxxx_ASM_COM)

# For a simplex system, use host name for this parameter.

DNS_FOR_FSPTCxxx_POTS_COM=pots-sysPTCxxx.domainname

# These are qualified DNS names used by pmg in each application

# to help determine what actions are needed if there is a redundancy

# communication failure.

# Each name should return two IP addresses of a POTS/CENTRIX Feature Server.

DNS_FOR_FSPTC_SIDE_A_CRIT_COM=crit-asysPTC.domainname

DNS_FOR_FSPTC_SIDE_B_CRIT_COM=crit-bsysPTC.domainname

# These are qualified DNS names used by a TSA process in Feature Server

# POTS/CENTRIX for Signaling Gateway communication.

# Each name should return two IP address of a POTS Feature Server host.

DNS_FOR_FSPTC_SIDE_A_SGW_COM=sgw-asysPTC.domainname

DNS_FOR_FSPTC_SIDE_B_SGW_COM=sgw-bsysPTC.domainname

# This is qualified DNS name used by GFS module of the POTS process

# in Feature_Server FSPTC

# Each name should return two logical IP addresses of a POTS/CENTRIX

# Feature Server which match the subnet of its two physical interfaces

DNS_FOR_FSPTCxxx_GFS_COM=gfs-sysPTCxxx.domainname

#-----------  END  OF  FSPTC  REQUIRED  DNS  NAMES  --------------------

#-----------------------------------------------------------------------

#=======================================================================

#==================   EMS  REQUIRED  DNS  NAMES   ======================

#

# These are qualified DNS names used by pmg in each application

# to help determine what actions are needed if there is a redundancy

# communication failure.

# Each name should return two IP addresses of a EMS.

DNS_FOR_EMS_SIDE_A_CRIT_COM=crit-asysEMS.domainname

DNS_FOR_EMS_SIDE_B_CRIT_COM=crit-bsysEMS.domainname

# These are qualified DNS names used by OMSHub in both side of EMS

# to talk to a slave Hub in each CA/FSAIN/FSPTC host, and also from

# EMS side A hub to EMS side B hub. Each name in the first six parameters

# should return two IP addresses of a CA/FSAIN/FSPTC host. The last

# two parameters should return two IP address of a EMS host.

# Note: When CA/FSAIN/FSPTC are in one host, the OMS_SLAVE_HUB for FSAIN

#       and FSPTC are not used at all and are not checked by checkCFG.

DNS_FOR_CA_SIDE_A_OMS_SLAVE_HUB=oms-asysCA.domainname

DNS_FOR_CA_SIDE_B_OMS_SLAVE_HUB=oms-bsysCA.domainname

DNS_FOR_FSAIN_SIDE_A_OMS_SLAVE_HUB=oms-asysAIN.domainname

DNS_FOR_FSAIN_SIDE_B_OMS_SLAVE_HUB=oms-bsysAIN.domainname

DNS_FOR_FSPTC_SIDE_A_OMS_SLAVE_HUB=oms-asysPTC.domainname

DNS_FOR_FSPTC_SIDE_B_OMS_SLAVE_HUB=oms-bsysPTC.domainname

DNS_FOR_EMS_SIDE_A_OMS_SLAVE_HUB=oms-asysEMS.domainname

DNS_FOR_EMS_SIDE_B_OMS_SLAVE_HUB=oms-bsysEMS.domainname

#================ END  OF  EMS  REQUIRED  DNS  NAMES   =================

#=======================================================================

########################################################################

#                                                                                                                                           #

#     E N D   O F   O P T I C A L L . C F G   D E F I N I T I O N                                           #

#                                                                                                                                           #

########################################################################

Appendix D

How To Enable DNS Caching Server (NAMED process)

- Edit the /etc/resolv.conf file to look like this:

domain test.com

search  test.com

options retry:1 retrans:1

nameserver 127.0.0.1

nameserver <primary dns server ip address>

nameserver <secondary dns server ip address>

Where test.com is your domain name

Create /etc/named.conf file:

options {

directory 	“/var/named”;

forwarders { master dns server ip ; secondary dns server ip;};

forward only;

listen-on  { 127.0.0.1; };

};

zone “.” {

type hint;

file “named.cache”;

};

zone “0.0.127.in-addr.arpa” {

type master;

file “named.localhost”;

};

- Execute: mkdir /var/named

- Create /var/named/named.cache file:

;Start of /var/named/named.cache

; Internal root server definition.

; First line defines the name server for the domain "."

.       99999999        IN      NS      dns1.test.com.

.       99999999        IN      NS      dns2.test.com.

; "A" record for server defined above.

dns1.test.com.            IN      A       <dns1 ip address>

dns2.test.com.            IN      A       <dns2 ip address>

; End of the file

Note: Do not forget a dot “.” After each dns server name.

- Create /var/named/named.localhost file:

; Start of  named.localhost

;

$TTL 28800

@       IN      SOA     localhost.test.com. root.localhost.test.com. (

5002     ; Serial

10800    ; Refresh

3600     ; Retry

604800   ; Expire

864000 ) ; Minimum ttl of 1 day

IN      NS      localhost.test.com.

1       IN      PTR     localhost.

localhost.test.com.   IN      A       <The telnet (hme0) ip address>

;End of the file

Where localhost is the machine that you are installing the caching server onto to.

- Execute: /usr/sbin/in.named

- ps –ef | grep named – Make sure named is running.

Appendix E

Setting Up the Non-Interactive SSH Login to External Archive Server for LAF Process

Note The external archive system is recommended to be located so it can be accessed by the management network. If this is the case, the static routes in the CA system should be explicitly set so the traffic to the external archive system is routed through the management network (see section “Adding Static Routes”). Otherwise the traffic will be routed through the default network (i.e. signaling network) and may not be able to reach the external archive system.

Step 1 Log in to the Cisco BTS 10200 primary EMS as root.

Step 2 From the EMS, login to the external archive server via ssh to get the external archive server added to the /.ssh/known_hosts file.

Step 3 Log off from the external archive server.

Step 4 While still logged in on the primary EMS as root, generate an SSH key.

a. Execute cd /opt/BTSossh/bin.

b. Execute ssh-keygen -t rsa.

c. Hit enter to accept the default file name for the key (/.ssh/id_rsa).

d. Enter y if prompted to choose whether to overwrite the existing file.

e. Hit enter when prompted to enter a passphrase (no passphrase).

f. Transfer the resulting file (/.ssh/id_rsa.pub) to a temporary location on the external archive server.

Step 5 Set up the external archive server with the key generated in Step 4.

a. Login to the external archive system as root.

b. If a /.ssh/authorized_keys file does not exist on the external archive system, rename the id_rsa.pub file (copied from the Cisco BTS 10200 EMS) to /.ssh/authorized_keys. If the file does exist, append the id_rsa.pub file to it.

Step 6 On the primary EMS, execute ssh root@abcd, where abcd is the IP address or fully-qualified domain name of the external archive server.

Step 7 Verify that login to the external archive server is successful and that no prompts for username or password are issued.

Step 8	Run enableLAF in EMS platform directories (i.e. /opt/ems/bin and /opt/bdms/bin)

Step 9 Repeat Steps 1-8 for the secondary EMS, primary CA and secondary CA. (In CA, the platform directories are /opt/OptiCall/CAxxx/bin, /opt/OptiCall/FSPTCyyy/bin, /opt/OptiCall/FSAINzzz/bin).

Note Billing has a similar mechanism/steps to SFTP their Call Detail Blocks (CDB) files to an external machine. If the LAF and Billing use the same target machine, then in both EMS, perform Steps 1-7 only once. You must still run Step 8 to enable LAF. And you must still run Steps 1 -9 in CA nodes.

Appendix F

# Place the external oracle engine

This appendix is only needed if your BTS contract does not include oracle license. If this is the case, you must follow the procedures in the “Oracle Engine Software Creation Procedure for BTS10200 R4.5.0/4.5.1/5.0” to create the oracle engine tar file (opticall_BASE.tar.gz).  Then place the Oracle engine tar file in the /opt/Build/ora-engine directory of EMS hosts.  This appendix describe the steps to upload the oracle engine tar file into the staging area of EMS.

If you decide to use sftp:

Step 1  In primary EMS, create a directory /opt/Build/ora-engine if not present

mkdir –p /opt/Build/ora-engine

Step 2  From the machine where the oracle engine opticall_BASE.tar.gz is created, cd to the directory where the oracle engine locate.

Step 3  sftp to the primary EMS

sftp <hostname or IP address of primary EMS>

Step 4  At the password prompt, enter the root password for the primary EMS. The password can be obtained from your system administrator. The system will respond with an SFTP prompt.

Step 5   When the SFTP prompt appears, navigate to /opt/Build

cd /opt/Build/ora-engine

Step 6  Put the oracle engine tar file into it

sftp> put opticall_BASE.tar.gz

Step 7  After the transfer is complete and the SFTP prompt reappears, exit the SFTP session.

exit

Step 8  Repeat step 1-7, using secondary EMS instead of primary EMS.

If you choose to use CD to load the oracle engine tar file:

Step 1  In primary EMS, create a directory /opt/Build/ora-engine if not present

mkdir –p /opt/Build/ora-engine

Step 2  Insert the oracle engine CD that you created into the CD-ROM of primary EMS

Step 3   At the command prompt of the primary EMS, navigate to the CD-ROM.

cd /cdrom/cdrom0

Step 4   This troubleshooting step is only necessary if you received an error response while attempting to navigate to the CD-ROM. If you did not receive an error response, go to Step 5.

a. If you receive the system response, cdrom not found, manually open and close the CD-ROM tray on the primary EMS unit. Wait 30 seconds and try the command again.

cd /cdrom/cdrom0.

b. If you still receive an error response, it is possible that the CD-ROM driver is not yet mounted on the primary EMS. Enter the following command to create a directory:

mkdir -p /cdrom

|  | Note If the system responds that this directory already exists, you should ignore the response and continue with the next substep. |
| --- | --- |

c. Navigate to the CD ROM.

cd /cdrom

d. Make a new directory.

mkdir -p cdrom0

e. Enter either one of the following command to mount the CD-ROM drive:

- A system with Continuous Computing hardware, please run:

mount -o ro -F hsfs /dev/dsk/c0t6d0s0 /cdrom/cdrom0

- Other hardware platform (eg. SunFire, Netra1280) please run:

mount -o ro -F hsfs /dev/dsk/c0t0d0s0 /cdrom/cdrom0

f. At the command prompt of the primary EMS, navigate to the CD-ROM:

cd /cdrom/cdrom0

Step 5   Check that the proper file (opticall_BASE.tar.gz or K9-oraengine.tar.gz) is present on the CD:

ls

The file opticall_BASE.tar.gz or K9-oraengine.tar.gz should be present.

Step 6   Copy the file from the CD to the /opt/Build/ora-engine directory. If your oracle engine is bundled in K9-oraengine.tar.gz, then execute these commands:

cd /opt

gzip –cd /cdrom/cdrom0/K9-oraengine.tar.gz | tar –xvf –

Otherwise, simply copy your opticall.BASE.tar.gz file from the CD-ROM into the ora-engine directory

cp opticall_BASE.tar.gz /opt/Build/ora-engine

Step 7  Eject the CD

umount /cdrom/cdrom0

and then manually eject the disk

Step 8  Repeat step 1-7, using secondary EMS instead of primary EMS.

Step 9  Continue on the section “Enter IP Addresses and Host Names in the opticall.cfg File”.

Appendix G

# Enabling the Internal Secondary Authoritative DNS Server (ISADS) before fresh installation

This procedure enables the Internal Secondary Authoritative DNS Server (ISADS) in Call Agent (CA) and/or Element Management System (EMS) before a fresh installation. The purpose of this is to set up a secondary DNS server in the Cisco BTS 10200 host(s), so that if an external DNS server fails, the Cisco BTS 10200 still functions.

WARNING #1: This feature uses a mechanism called incremental zone transfer (IXFR). The PRIMARY DNS server must support NOTIFY of SECONDARY DNS server and IXFR (Incremental Zone Transfer). If BIND is used as the primary, do not use a version of BIND older than Version 9. Please check with the manual or vendor that supplies the DNS program for your primary DNS server. CNR 6.X also support this mechanism.

WARNING #2:  In order to support incremental zone transfer, please ONLY use dynamic update on the primary DNS server. Do not hand edit any database files. CNR automatically uses dynamic update, and for BIND9.X, uses a utility called nsupdate. (Look at the man page of nsupdate for more details.)

To enable the ISADS in the Cisco BTS 10200 host, complete the following steps.

- In the primary DNS server, add the ISADS(s) as the secondary DNS servers for those Cisco BTS 10200-related zones. How to add it depends on what DNS software you are using. The following table is a checklist which Cisco recommends users follow, as well as instructions for implementing BIND9.X and CNR6.X

| What to do | BIND9.X | CNR 6.X |
| --- | --- | --- |
| Allow sending DNS NOTIFY messages to other nameserver(s) when a zone is added/changed/deleted. | In /etc/named.conf, put a parameter “notify yes” to each Cisco BTS 10200-related zone section(s). | On the page List/Add zone, click to edit the zone you want, and then click on the zone transfer settings. For notify, click the “yes” radio button. |
| Allow the Cisco BTS 10200 host(s) to query. | If no any “allow-query” statement is in the /etc/named.conf, keep the file intact. (By default, it allows any machine to query). However, if there is such statement, make sure the IP addresses of the BTS system are added to the allow-query statement. (a) | On the page List/Add zone, click to edit the zone you want, and then click on the Query Settings. If the current list is empty, leave it alone. However, if the current list is not empty, type in the IP addresses of the Cisco BTS 10200 hosts. (a) |
| Provide IXFR service if possible. | In /etc/named.conf, put a parameter “provide-ixfr yes” in the options section. | Click DNS server, click local DNS server, then in Request incremental transfers (IXFR), click the enabled radio button. |
| Notify the ISADS when there is a zone change. | In /etc/named.conf, add a parameter “also-notify {<IP address(es) of the BTS hosts>};” to each Cisco BTS 10200 related zone section(s). (a) | On the page List/Add zone, click Zone Transfer Settings, then for notify-set, type in the IP address(es) of the Cisco BTS 10200 hosts. (a) |
| Add the ISADS as the nameserver of the zone. | For each Cisco BTS 10200-related zone which you want ISADS to be the secondary DNS server, use nsupdate to add the Cisco BTS 10200 host(s) for which ISADS is located as its nameserver(s). For example: nsupdate >update add example.com 86400 IN NS secca53.ipclab.cisco.com. >send (ctrl-C) | On the page List/Add zone, click the zone that you want to edit, and then click Configure RR for that zone. Change the type to NS, and add in the Cisco BTS 10200 FQDN(s) to the space under Data, then click “Add Resource Record.” You may want to rebounce the DNS server to reload the info. |

- The IP address(es) of each Cisco BTS 10200 host should contain two IP addresses of Cisco BTS 10200 in management network. (i.e. The IP addresses of Cisco BTS 10200 host). However, if the DNS server is in the signaling network (not recommended for security reasons), use the IP address(es) of the BTS host network interfaces in the signaling network.

- After you make all the changes to the primary DNS server, rebounce the primary DNS server. (In BIND9.X, use ndc reload. In CNR6.X, click zone, then click DNS server, and hit the

- Edit the /etc/resolv.conf file in each Cisco BTS 10200 host where ISADS is located to look like this:

domain <yourDomain..com>

search  <yourDomain.com>

options retry:1 retrans:1

nameserver 127.0.0.1

nameserver <primary DNS server ip address>

nameserver <another secondary DNS server ip address, but not the Cisco BTS 10200 host>

Where <yourDomain.com> is your domain name,  <primary DNS server ip address> is the IP address of your primary DNS server, and  <another secondary DNS server IP address, but not the Cisco BTS 10200 host> is the IP address of another secondary DNS server, but it cannot be any Cisco BTS 10200 host. This is optional.

- Create /etc/named.conf file in each Cisco BTS 10200 hosts where ISADS is located based on the template from /opt/Build/ISADS/ named.conf_ISADS.template. (You can do this if you have already downloaded K9-opticall.tar.gz into your system and untar and unzip it. If not, you can hand edit this file, but be very careful!!!). The content of this template is as follows:

***************************************************************************

options {

directory "/var/named";        // Working directory

allow-query { localhost; };   // Only allow application from this localhost to query

request-ixfr yes;                    // enable incremental zone transfer, whether possible

max-cache-size 5M;             // The maximum amount of memory to use for the server's cache, in bytes

serial-query-rate 20;           // Limits the number of simultaneous SOA queries to the number per second

listen-on  { 127.0.0.1; };       // listen-on defines the port and IP address(es) on which BIND

//will listen for incoming queries.

};

// Provide a forwarding for all non-authoritative zones

zone "." IN {

type forward;

forwarders { <IP address of the DNS which handle all non-authoritative query>; };

};

// Provide a reverse mapping for the loopback address 127.0.0.1

zone "0.0.127.in-addr.arpa" {

type master;

file "localhost.rev";

notify no;

};

// We are the slave server for <zone1>, for which master is <primary DNS#1>

zone "<zone1>" IN {

type slave;

file "<db file of zone1>";   //the name of the db file should be <zone1>.db

masters {<IP address of primary DNS#1>;};

allow-notify {<IP address of primary DNS#1>;};

min-refresh-time 60;    //Indicates the min time (seconds) when the slave will try to

//refresh the zone from the master.

max-refresh-time 65;    //Indicates the max time (seconds) when the slave will try to

//refresh the zone from the master.

min-retry-time 60;        //The min time between retries if the slave fails to contact the

//master when refresh time has expired

max-retry-time 65;      //The max time between retries if the slave fails to contact the

//master when refresh time has expired

};

// We are the slave server for <zone2>, for which master is <primary DNS#2>

zone "<zone2>" IN {

type slave;

file "<db file of zone2>";  //the name of the db file should be <zone2>.db

masters {<IP address of primary DNS#2>;};

allow-notify {<IP address of primary DNS#2>;};

min-refresh-time 60;    //Indicates the min time (seconds) when the slave will try to

//refresh the zone from the master.

max-refresh-time 65;   //Indicates the max time (seconds) when the slave will try to

//refresh the zone from the master.

min-retry-time 60;      //The min time between retries if the slave fails to contact the

//master when refresh time has expired

max-retry-time 65;      //The max time between retries if the slave fails to contact the

//master when refresh time has expired

};

<repeat as many zones as necessary>

Note:

  - Be very careful if you decide to type this file from scratch. The “named” process is very sensitive to the syntax, such as “;” etc.

  - You must fill in the information in <> from that template. Gather that information beforehand, including

- <IP address of the DNS which handles all non-authoritative query>

  - This is the DNS server you choose to handle all other non-authoritative queries. This can be the primary DNS server.

- <zone1> and/or <zone2> and/or more

  - This is the name of the authoritative zone, in which Cisco BTS 10200 has  full knowledge of. It should be usually in this  format: xxx.xxx.com or xxx.xxx.net.

- <primary DNS#1> and/or <primary DNS#2> and/or more

  - These are the names of the primary DNS servers for different zones. For comment purpose only.

- <IP address of primary DNS#1> and/or <IP address of primary DNS#2> and/or more

  - These are the IP address(es) of the primary DNS servers for different zones. ISADS needs this info to communicate with primary DNS server(s).

  - Other than the parameters in <>, do not change any other parameters in this template without contacting Cisco TAC.

  - Repeat as many zones as necessary. The zones should be limited to only those used by the Cisco BTS 10200. Do not add any unnecessary zones into this /etc/named.conf. If you have any doubt, contact Cisco TAC.

  - Also include all the Cisco BTS 10200-related reverse zones, i.e. X.X.X.in-addr.arpa.

- Make a new directory:

Execute  mkdir -p /var/named

- Create /var/named/localhost.rev file:

************************************************************************

; Start of the localhost.rev

$TTL 86400

@       IN  <localhost.test.com.> <root.localhost.test.com.> (

2004175   	; Serial number

10800     	; Refresh

3600      	; Retry

604800    	; Expire

86400 )   	; Minimum TTL

IN      NS      <localhost.test.com.>

1        IN      PTR     localhost.

<localhost.test.com.>     IN      A       <localhost.test.com ip address>

;End of the file

************************************************************************

Where <localhost.test.com.> is the fully qualified domain name of the machine you are installing the ISADS (i.e. the Cisco BTS 10200 host),  <localhost.test.com ip address> is the IP address of that Cisco BTS 10200 host.

- Run named-checkconf to make sure there is no syntax error in /etc/named.conf.

- In the ISADS, start the named by running svcadm enable dns/server

- Check the process is running by ps –ef | grep named.

- Before/during the installation, when editing /etc/opticall.cfg for the parameter NAMED_ENABLED, assign it to either “secondary_dns_all_hosts” or “secondary_dns_CA_only”.

Checking:

- Run nslookup on the Cisco BTS 10200-related domain names in ISADS to make sure it is solvable. Also make sure the answer is authoritative.

- Modify some IP addresses of Cisco BTS 10200-related domain names in the primary DNS server dynamically. Then after a few seconds, do an nslookup in the ISADS to ensure the modification has taken place in the ISADS.

- After installation, check the alarm to ensure there are no alarms with maintenance 71, 72, 73, 74 and 118.

Appendix H

# Enabling the Internal Secondary Authoritative DNS Server (ISADS) after fresh installation/upgrade

This procedure enables the Internal Secondary Authoritative DNS Server (ISADS) in Call Agent (CA) and/or Element Management System (EMS) after a fresh installation or upgrade. The purpose of this is to set up a secondary DNS server in Cisco BTS 10200 host(s), so that if an external DNS server fails, the Cisco BTS 10200 can still function.

See the previous warning in Appendix G.

Additional warning: Whether possible, Cisco recommends setting up the ISADS before a fresh installation, except for existing system.

Assumption: The secondary side is standby.

To enable the ISADS in Cisco BTS 10200 host, complete the following steps.

  - Follow step (1) of Appendix G.

  - Follow step (2) of Appendix G.

  - If you choose to put ISADS on all Cisco BTS 10200 hosts, shut down the platform on the standby side of both the EMS and CA. If you choose only to put ISADS on CA, shut down the platform on the standby side of CA.

- platform stop

  - Follow steps (3) - (10) of Appendix G. Cisco recommends preparing the /etc/named.conf and /var/named/localhost.rev beforehand, so the amount of time being simplex is dramatically reduced.

  - Do the checking (1) – (2) of Appendix G.

  - If everything is okay, bring up the platform on the standby side:

- platform start

  - Do a switchover to the other side.

- CLI> control call-agent id=CAxxx; target-state=standby-active

- CLI> control feature-server id=FSPTCyyy; target-state=standby-active

- CLI> control feature-server id=FSAINzzz; target-state=standby-active

(If user chooses to put ISADS on all Cisco BTS 10200 hosts), also switch over the EMS.)

- CLI> control billing-manager; id=BDMS01; target-state=standby-active

- CLI> control element-manager; id=EM01; target-state=standby-active

  - Repeat steps (3) – (7) of this appendix, and switch it back so that the primary side is active by using the following commands:

- CLI> control call-agent id=CAxxx; target-state=active-standby

- CLI> control feature-server id=FSPTCyyy; target-state= active-standby

- CLI> control feature-server id=FSAINzzz; target-state= active-standby

(If user chooses to put ISADS on all Cisco BTS 10200hosts, also switch over EMS.)

- CLI> control bdms; id=BDMS01; target-state= active-standby

- CLI> control element-manager; id=EM01; target-state= active-standby

  - In /etc/opticall.cfg of all BTS hosts, change the NAMED_ENABLED=”secondary_dns_all_hosts” or “secondary_dns_CA_only”.

Appendix I

# Apply patch for 4.5.1V14IP00 to CA host

Step 1. extract the tar file

cd /opt

tar -xvf /opt/BTS_04_05_01_V14_IP00.tar

cd /opt/BTS_04_05_01_V14_IP00

Step 2. Verify the checksum for each file is valid

cksum ca_mem_medium.cfg.BTS_04_05_01_V14_IP00

cksum ptc_mem_medium.cfg.BTS_04_05_01_V14_IP00

cksum ain_mem_medium.cfg.BTS_04_05_01_V14_IP00

cksum platform.BTS_04_05_01_V14_IP00

output must match the sums shown in BTS_04_05_01_V14_IP00.cksum

Step 3. Ensure the file has execute permission

chmod 755 platform.BTS_04_05_01_V14_IP00

Step 4. Ensure the file has the correct owner and group

chown oamp:staff ca_mem_medium.cfg.BTS_04_05_01_V14_IP00

chown oamp:staff ptc_mem_medium.cfg.BTS_04_05_01_V14_IP00

chown oamp:staff ain_mem_medium.cfg.BTS_04_05_01_V14_IP00

chown oamp:staff platform.BTS_04_05_01_V14_IP00

Step 5. Patch the files for CA platform and remove data dir

cd /opt/OptiCall/ca/bin

cp -p /opt/BTS_04_05_01_V14_IP00/ca_mem_medium.cfg.BTS_04_05_01_V14_IP00 ca_mem_medium.cfg.BTS_04_05_01_V14_IP00

cd /opt/OptiCall/CAxxx/bin

rm mem_medium.cfg

ln -s /opt/OptiCall/ca/bin/ca_mem_medium.cfg.BTS_04_05_01_V14_IP00 mem_medium.cfg

\rm –rf data

Step 6. Patch the files for FSPTC platform and remove data dir

cd /opt/OptiCall/potsctx/bin

cp -p /opt/BTS_04_05_01_V14_IP00/ptc_mem_medium.cfg.BTS_04_05_01_V14_IP00 ptc_mem_medium.cfg.BTS_04_05_01_V14_IP00

cd /opt/OptiCall/FSPTCyyy/bin

rm mem_medium.cfg

ln -s /opt/OptiCall/potsctx/bin/ptc_mem_medium.cfg.BTS_04_05_01_V14_IP00 mem_medium.cfg

\rm –rf data

Step 7.   Patch the files for FSAIN platform and remove data dir

cd /opt/OptiCall/ain/bin

cp -p /opt/BTS_04_05_01_V14_IP00/ain_mem_medium.cfg.BTS_04_05_01_V14_IP00 ain_mem_medium.cfg.BTS_04_05_01_V14_IP00

cd /opt/OptiCall/FSAINzzz/bin

rm mem_medium.cfg

ln -s /opt/OptiCall/ain/bin/ain_mem_medium.cfg.BTS_04_05_01_V14_IP00 mem_medium.cfg

\rm –rf data

Step 8.  Patch the platform file

cd /opt/bts/bin

mv platform platform.orig

cp -p /opt/BTS_04_05_01_V14_IP00/platform.BTS_04_05_01_V14_IP00 platform.BTS_04_05_01_V14_IP00

ln -s platform.BTS_04_05_01_V14_IP00 platform

Step 9. Update PatchLevel

cp /opt/BTS_04_05_01_V14_IP00/PatchLevel /opt/ems/utils

date >> /opt/ems/utils/PatchLevel

Appendix J

# Apply patch for 4.5.1V14IP00 to EMS host

Step 1. untar BTS_04_05_01_V14_IP00.tar on EMS host.

cd /opt

tar -xvf /opt/BTS_04_05_01_V14_IP00.tar

cd /opt/BTS_04_05_01_V14_IP00

Step 2. Verify the checksum for each file is valid

cksum platform.BTS_04_05_01_V14_IP00

output must match the sums shown in BTS_04_05_01_V14_IP00.cksum

Step 3. Ensure the file has execute permission

chmod +x platform.BTS_04_05_01_V14_IP00

Step 4. Ensure the file has the correct owner and group

chown oamp:staff platform.BTS_04_05_01_V14_IP00

Step 5. Save a copy of the original files and put the patches in place.

cd /opt/bts/bin

mv platform platform.orig

cp -p /opt/BTS_04_05_01_V14_IP00/platform.BTS_04_05_01_V14_IP00 platform.BTS_04_05_01_V14_IP00

ln -s platform.BTS_04_05_01_V14_IP00 platform

Step 6. Update PatchLevel

cp /opt/BTS_04_05_01_V14_IP00/PatchLevel /opt/ems/utils

date >> /opt/ems/utils/PatchLevel

Appendix K

# Apply patch for 4.5.1V14IP01 to EMS host

Preliminary steps

==================

  - All previous patches (i.e. 4.5.1V14IP00 ) MUST be installed prior to this patch.

nodestat

Make sure the Build version is 900-04.05.01.V14IP00

2. Transfer the patch tar file to /opt and untar it on both sides of the EMS. Obtain the patch tar file from Advanced Service (AS).

scp or sftp the tar file to /opt

cd /opt

tar -xvf /opt/BTS_04_05_01_V14_IP01.tar

cd /opt/BTS_04_05_01_V14_IP01

3. (FOR EMS side only) Verify the checksum for each file is valid

cksum cis3_ip01.sh.BTS_04_05_01_V14_IP01

output must match the sums shown in BTS_04_05_01_V14_IP01.cksum.

cksum ins3_ip01.sh.BTS_04_05_01_V14_IP01

output must match the sums shown in BTS_04_05_01_V14_IP01.cksum

cksum ip_control_ip01.sh.BTS_04_05_01_V14_IP01

output must match the sums shown in BTS_04_05_01_V14_IP01.cksum

4. (FOR EMS side only) Ensure the file has execute permission

chmod +x cis3_ip01.sh.BTS_04_05_01_V14_IP01

chmod +x ins3_ip01.sh.BTS_04_05_01_V14_IP01

chmod +x ip_control_ip01.sh.BTS_04_05_01_V14_IP01

5. (FOR EMS side only) Ensure the file has the correct owner and group

chown oamp:staff cis3_ip01.sh.BTS_04_05_01_V14_IP01

chown oamp:staff ins3_ip01.sh.BTS_04_05_01_V14_IP01

chown oamp:staff ip_control_ip01.sh.BTS_04_05_01_V14_IP01

6. The 4.5.1.V14 CORBA version has been installed.

7. The 4.5.1.V14.IP00 has been installed.

8. If VIP is not configured, skip step 9.

9. The new VIP or <Virtual IP> must be known in advance. In addition, the Netmask and broadcast associated to the VIP or <VIP Netmask> must be known in advance as well. This value may vary from installation to installation. It may depend in large part on the VIP value assigned.

=====================================================

Install Procedure

=====================================================

1. This procedure assumes the Primary EMS is ACTIVE, and the Secondary EMS is STANDBY.

2. On Primary EMS, save a copy of the original files and put the patches in place.

cd /opt/BTS_04_05_01_V14_IP01

- Edit (vi) ip_control_ip01.sh.BTS_04_05_01_V14_IP01

-> move to line 79

-> change line: MSK=$4

to read    : MSK="<VIP Netmask>"

for example: MSK="255.255.255.0"

note that the double quotes are required

-> move to line 80

-> change line: BCT=$5

to read    : MSK="<VIP Broadcast>"

for example: MSK="10.89.233.255"

note that the double quotes are required

-> save the change and exit.

cp -p /opt/BTScis/bin/cis3  /opt/BTScis/bin/cis3.BKP

cp -p cis3_ip01.sh.BTS_04_05_01_V14_IP01 /opt/BTScis/bin/cis3

cp -p /opt/BTSoorb/bin/ins3  /opt/BTSoorb/bin/ins3.BKP

cp -p ins3_ip01.sh.BTS_04_05_01_V14_IP01 /opt/BTSoorb/bin/ins3

cp -p /opt/BTSsmg/bin/ip_control.sh  /opt/BTSsmg/bin/ip_control.sh.BKP

cp -p ip_control_ip01.sh.BTS_04_05_01_V14_IP01 /opt/BTSsmg/bin/ip_control.sh

- If VIP is configured, do the following steps:

cp -p /etc/inittab  /etc/inittab.BKP

- Edit (vi) /etc/inittab

-> move to the end of file

-> find and change lines:

ns:3:respawn:/sbin/ins3 priems01

cs:3:respawn:/sbin/cis3 10.89.233.126 190.101.50.118

to read:

ns:3:respawn:/sbin/ins3 <VIP Address>

cs:3:respawn:/sbin/cis3 10.89.233.126 190.101.50.118 <VIP Address>

-> save the change and exit.

- If VIP is not configured, do the following steps:

- cp -p /etc/inittab  /etc/inittab.BKP

- Edit (vi) /etc/inittab

-> move to the end of file

-> find and change lines:

ns:3:respawn:/sbin/ins3 priems01

cs:3:respawn:/sbin/cis3 10.89.233.126 190.101.50.118

to read:

ns:3:respawn:/sbin/ins3 10.89.233.126

cs:3:respawn:/sbin/cis3 10.89.233.126 190.101.50.118

note that the second line does not change

note that to use the first IP Address of the second line as the IP Address of the first line

-> save the change and exit.

- Restart the CORBA Services

pkill ins3

pkill cis3

- wait about 1 minutes for CORBA to restart and rebind to the INS

ps -ef | grep INS

-> If there is a java process with parent PID 1, it must be killed. It hung in a critical space.

kill -9 <INS java PID>

ps -ef | grep CIS

-> If there is a java process with parent PID 1, it must be killed. It hung in a critical space.

kill -9 <CIS java PID>

3. On Secondary EMS, save a copy of the original files and put the patches in place.

cd /opt/BTS_04_05_01_V14_IP01

- Edit (vi) ip_control_ip01.sh.BTS_04_05_01_V14_IP01

-> move to line 79

-> change line: MSK=$4

to read    : MSK="<VIP Netmask>"

for example: MSK="255.255.255.0"

note that the double quotes are required

-> move to line 80

-> change line: BCT=$5

to read    : MSK="<VIP Broadcast>"

for example: MSK="10.89.233.255"

note that the double quotes are required

-> save the change and exit.

cp -p /opt/BTScis/bin/cis3  /opt/BTScis/bin/cis3.BKP

cp -p cis3_ip01.sh.BTS_04_05_01_V14_IP01 /opt/BTScis/bin/cis3

cp -p /opt/BTSoorb/bin/ins3  /opt/BTSoorb/bin/ins3.BKP

cp -p ins3_ip01.sh.BTS_04_05_01_V14_IP01 /opt/BTSoorb/bin/ins3

cp -p /opt/BTSsmg/bin/ip_control.sh  /opt/BTSsmg/bin/ip_control.sh.BKP

cp -p ip_control_ip01.sh.BTS_04_05_01_V14_IP01 /opt/BTSsmg/bin/ip_control.sh

- If VIP is configured, do the following steps:

- cp -p /etc/inittab  /etc/inittab.BKP

- Edit (vi) /etc/inittab

-> move to the end of file

-> find and change lines:

ns:3:respawn:/sbin/ins3 priems01

cs:3:respawn:/sbin/cis3 10.89.233.126 190.101.50.118

to read:

ns:3:respawn:/sbin/ins3 <VIP Address>

cs:3:respawn:/sbin/cis3 10.89.233.126 190.101.50.118 <VIP Address>

-> save the change and exit.

- If VIP is not configured, do the following steps:

cp -p /etc/inittab  /etc/inittab.BKP

- Edit (vi) /etc/inittab

-> move to the end of file

-> find and change lines:

ns:3:respawn:/sbin/ins3 priems01

cs:3:respawn:/sbin/cis3 10.89.233.126 190.101.50.118

to read:

ns:3:respawn:/sbin/ins3 10.89.233.126

cs:3:respawn:/sbin/cis3 10.89.233.126 190.101.50.118

note that the second line does not change

note that to use the first IP Address of the second line as the IP Address of the first line

-> save the change and exit.

- Restart the CORBA Services

pkill ins3

pkill cis3

- wait about 1 minutes for CORBA to restart and rebind to the INS

ps -ef | grep INS

-> If there is a java process with parent PID 1, it must be killed. It hung in a critical space.

kill -9 <INS java PID>

ps -ef | grep CIS

-> If there is a java process with parent PID 1, it must be killed. It hung in a critical space.

kill -9 <CIS java PID>

4. If VIP is configured, the EMS must be switched over at least once for the VIP's

netmask and broadcast to take effect.

- Login to the CLI and issue the following CLI command:

CLI> control element_manager id=EMxx; target_state=STANDBY_ACTIVE

########################################################################

#                       Procedure to update the SSH config with the VIP.                                     #

########################################################################

Procedure to update the SSH config with the VIP, if this is desired. Note that the VIP access is only allowed on the side where the ACTIVE EM01 application currently resides.

Do the following steps in both Primary and Secondary EMS if VIP is configured.

1) cd /opt/BTSossh/etc

2) Edit (vi) sshd_config

-> under the existing line for "ListenAddress 127.0.0.1"

-> add a new line for the new VIP: "ListenAddress <VIP Address>"

-> save the file and exit the editor

3) Restart the "sshd" daemon to accept the new configuration.

/etc/init.d/sshd stop

/etc/init.d/sshd start

4) Verify the connectivity to the new address with a new ssh attempt.

This may be attempted from ANY existing connection. You do not really even need to

complete a login.

The fact that you get a password prompt means that you have reached the SSH process.

-> ssh ablancha@<Virtual IP>

-> Just to be safe also re-verify the other addresses listed in the sshd_config to

make sure nothing is broken

#############################################################

#                        This is the end of the patch install procedure                       #

#############################################################

#############################################################

#############################################################

#############################################################

Appendix L

# Remove patch for 4.5.1V14IP01 from EMS hosts

===================================================

Full Backout Procedure

===================================================

In the steps below EMxx and BDMSxx must be replaced with the appropriate

EM and BDMS instance numbers for the system being patched. If you are unsure of the instance number run the "nodestat" command to find it.

1. This section of the backout procedure assumes the EMxx and BDMSxx applications

are active on the primary EMS before you begin the patch backout.

2. On Secondary EMS, restore the original version of the CIS application configuration

pkgrm BTScis

pkgrm BTSoorb

cd /opt/Build

./cis-install.sh

- wait about 1 minute for CORBA to restart and rebind to the INS

3. On Primary EMS, restore the original version of the CIS application configuration

pkgrm BTScis

pkgrm BTSoorb

cd /opt/Build

./cis-install.sh

- Wait about 1 minute for CORBA to restart and rebind to the INS

########################################################################

#                         Procedure to remove the SSH config with the VIP.                                 #

########################################################################

Procedure to remove the SSH config with the VIP, if this was added.

1) cd /opt/BTSossh/etc

2) Edit (vi) sshd_config

-> under the existing line for "ListenAddress 127.0.0.1"

-> delete the line that has the VIP: "ListenAddress <VIP Address>"

-> save the file and exit the editor

3) Restart the "sshd" daemon to accept the new configuration.

-> /etc/init.d/sshd stop

-> /etc/init.d/sshd start

4) Verify the connectivity to the existing address with a new ssh attempt.

This may be attempted from ANY existing connection. You do not really even need to

complete a login.

The fact that you get a password prompt means that you have reached the SSH process.

-> ssh ablancha@<Management IP>

| Corporate Headquarters Cisco Systems, Inc. 170 West Tasman Drive San Jose, CA 95134-1706 USA www.cisco.com Tel: 408 526-4000 800 553-NETS (6387) Fax: 408 526-4100 | European Headquarters Cisco Systems International BV Haarlerbergpark Haarlerbergweg 13-19 1101 CH Amsterdam The Netherlands www-europe.cisco.com Tel: 31 0 20 357 1000 Fax: 31 0 20 357 1100 | Americas Headquarters Cisco Systems, Inc. 170 West Tasman Drive San Jose, CA 95134-1706 USA www.cisco.com Tel: 408 526-7660 Fax: 408 527-0883 | Asia Pacific Headquarters Cisco Systems, Inc. Capital Tower138 Robinson Road #22-01 to #29-01 Singapore 068912 www.cisco.com Tel: +65 6317 7777 Fax: +65 6317 7799 |
| --- | --- | --- | --- |

Cisco Systems has more than 200 offices in the following countries and regions. Addresses, phone numbers, and fax numbers are listed on the Cisco Web site at www.cisco.com/go/offices.

Argentina • Australia • Austria • Belgium • Brazil • Bulgaria • Canada • Chile • China PRC • Colombia • Costa Rica Croatia • Czech Republic • Denmark • Dubai, UAE • Finland • France • Germany • Greece • Hong Kong SAR • Hungary
India • Indonesia • Ireland • Israel • Italy • Japan • Korea • Luxembourg • Malaysia • Mexico • The Netherlands
New Zealand • Norway • Peru • Philippines • Poland • Portugal • Puerto Rico • Romania • Russia • Saudi Arabia
Scotland • Singapore • Slovakia • Slovenia • South Africa • Spain • Sweden • Switzerland • Taiwan • Thailand • Turkey  Ukraine • United Kingdom • United States • Venezuela • Vietnam • Zimbabwe

THE SPECIFICATIONS AND INFORMATION REGARDING THE PRODUCTS IN THIS MANUAL ARE SUBJECT TO CHANGE WITHOUT NOTICE. ALL STATEMENTS, INFORMATION, AND RECOMMENDATIONS IN THIS MANUAL ARE BELIEVED TO BE ACCURATE BUT ARE PRESENTED WITHOUT WARRANTY OF ANY KIND, EXPRESS OR IMPLIED. USERS MUST TAKE FULL RESPONSIBILITY FOR THEIR APPLICATION OF ANY PRODUCTS.

THE SOFTWARE LICENSE AND LIMITED WARRANTY FOR THE ACCOMPANYING PRODUCT ARE SET FORTH IN THE INFORMATION PACKET THAT SHIPPED WITH THE PRODUCT AND ARE INCORPORATED HEREIN BY THIS REFERENCE. IF YOU ARE UNABLE TO LOCATE THE SOFTWARE LICENSE OR LIMITED WARRANTY, CONTACT YOUR CISCO REPRESENTATIVE FOR A COPY.

The Cisco implementation of TCP header compression is an adaptation of a program developed by the University of California, Berkeley (UCB) as part of UCB’s public domain version of the UNIX operating system. All rights reserved. Copyright © 1981, Regents of the University of California.

NOTWITHSTANDING ANY OTHER WARRANTY HEREIN, ALL DOCUMENT FILES AND SOFTWARE OF THESE SUPPLIERS ARE PROVIDED “AS IS” WITH ALL FAULTS. CISCO AND THE ABOVE-NAMED SUPPLIERS DISCLAIM ALL WARRANTIES, EXPRESSED OR IMPLIED, INCLUDING, WITHOUT LIMITATION, THOSE OF MERCHANTABILITY, FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT OR ARISING FROM A COURSE OF DEALING, USAGE, OR TRADE PRACTICE.

IN NO EVENT SHALL CISCO OR ITS SUPPLIERS BE LIABLE FOR ANY INDIRECT, SPECIAL, CONSEQUENTIAL, OR INCIDENTAL DAMAGES, INCLUDING, WITHOUT LIMITATION, LOST PROFITS OR LOSS OR DAMAGE TO DATA ARISING OUT OF THE USE OR INABILITY TO USE THIS MANUAL, EVEN IF CISCO OR ITS SUPPLIERS HAVE BEEN ADVISED OF THE POSSIBILITY OF SUCH DAMAGES.

CCIP, CCSP, the Cisco Arrow logo, the Cisco Powered Network mark, Cisco Unity, Follow Me Browsing, FormShare, and StackWise are trademarks of Cisco Systems, Inc.; Changing the Way We Work, Live, Play, and Learn, and iQuick Study are service marks of Cisco Systems, Inc.; and Aironet, ASIST, BPX, Catalyst, CCDA, CCDP, CCIE, CCNA, CCNP, Cisco, the Cisco Certified Internetwork Expert logo, Cisco IOS, the Cisco IOS logo, Cisco Press, Cisco Systems, Cisco Systems Capital, the Cisco Systems logo, Empowering the Internet Generation, Enterprise/Solver, EtherChannel, EtherSwitch, Fast Step, GigaStack, Internet Quotient, IOS, IP/TV, iQ Expertise, the iQ logo, iQ Net Readiness Scorecard, LightStream, MGX, MICA, the Networkers logo, Networking Academy, Network Registrar, Packet, PIX, Post-Routing, Pre-Routing, RateMUX, Registrar, ScriptShare, SlideCast, SMARTnet, StrataView Plus, Stratm, SwitchProbe, TeleRouter, The Fastest Way to Increase Your Internet Quotient, TransPath, and VCO are registered trademarks of Cisco Systems, Inc. and/or its affiliates in the United States and certain other countries.

All other trademarks mentioned in this document or Website are the property of their respective owners. The use of the word partner does not imply a partnership relationship between Cisco and any other company. (0401R)

# Text boxes

Exit

Remove /opt/Build subdirectory to free disk space (recommended)

Start application platforms

Install secondary CA/FS

Install primary CA/FS

Install secondary EMS

Install primary EMS

Rerun verification script to validate IP addresses and host names

Copy updated opticall.cfg file to other EMS and CA/FS platforms

Run verification script to validate IP address and host names

Enter IP addresses and host names in opticall.cfg file on primary EMS

Load K9-opticall.tar.gz file on EMS and CA/FS platforms from BTS10200 Application Disk

Load K9-btsdb.tar.gz and K9-extora.tar.gz files on EMS from BTS10200 Database Disk

Load K9-oraengine.tar.gz file on EMS from BTS10200 Oracle Engine Disk (conditional)

Verify available disk space for installation

Add static routes and verify host  tables

Open UNIX shells on EMS and CA/FS; create log files on each platform