Cisco BTS 10200 Softswitch                   CD Jumpstart Procedure for                 Solaris 10 (Solaris Sun Sparc 0 0 10001)

August 25,  2006

Corporate Headquarters

Cisco Systems, Inc.

170 West Tasman Drive

San Jose, CA 95134-1706

USA

http://www.cisco.com

Tel: 	408 526-4000

800 553-NETS (6387)

Fax:	408 526-4100

THE SPECIFICATIONS AND INFORMATION REGARDING THE PRODUCTS IN THIS MANUAL ARE SUBJECT TO CHANGE WITHOUT NOTICE. ALL STATEMENTS, INFORMATION, AND RECOMMENDATIONS IN THIS MANUAL ARE BELIEVED TO BE ACCURATE BUT ARE PRESENTED WITHOUT WARRANTY OF ANY KIND, EXPRESS OR IMPLIED. USERS MUST TAKE FULL RESPONSIBILITY FOR THEIR APPLICATION OF ANY PRODUCTS.

THE SOFTWARE LICENSE AND LIMITED WARRANTY FOR THE ACCOMPANYING PRODUCT ARE SET FORTH IN THE INFORMATION PACKET THAT SHIPPED WITH THE PRODUCT AND ARE INCORPORATED HEREIN BY THIS REFERENCE. IF YOU ARE UNABLE TO LOCATE THE SOFTWARE LICENSE OR LIMITED WARRANTY, CONTACT YOUR CISCO REPRESENTATIVE FOR A COPY.

The Cisco implementation of TCP header compression is an adaptation of a program developed by the University of California, Berkeley (UCB) as part of UCB’s public domain version of the UNIX operating system. All rights reserved. Copyright © 1981, Regents of the University of California.

NOTWITHSTANDING ANY OTHER WARRANTY HEREIN, ALL DOCUMENT FILES AND SOFTWARE OF THESE SUPPLIERS ARE PROVIDED “AS IS” WITH ALL FAULTS. CISCO AND THE ABOVE-NAMED SUPPLIERS DISCLAIM ALL WARRANTIES, EXPRESSED OR IMPLIED, INCLUDING, WITHOUT LIMITATION, THOSE OF MERCHANTABILITY, FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT OR ARISING FROM A COURSE OF DEALING, USAGE, OR TRADE PRACTICE.

IN NO EVENT SHALL CISCO OR ITS SUPPLIERS BE LIABLE FOR ANY INDIRECT, SPECIAL, CONSEQUENTIAL, OR INCIDENTAL DAMAGES, INCLUDING, WITHOUT LIMITATION, LOST PROFITS OR LOSS OR DAMAGE TO DATA ARISING OUT OF THE USE OR INABILITY TO USE THIS MANUAL, EVEN IF CISCO OR ITS SUPPLIERS HAVE BEEN ADVISED OF THE POSSIBILITY OF SUCH DAMAGES.

CCIP, CCSP, the Cisco Arrow logo, the Cisco Powered Network mark, Cisco Unity, Follow Me Browsing, FormShare, and StackWise are trademarks of Cisco Systems, Inc.; Changing the Way We Work, Live, Play, and Learn, and iQuick Study are service marks of Cisco Systems, Inc.; and Aironet, ASIST, BPX, Catalyst, CCDA, CCDP, CCIE, CCNA, CCNP, Cisco, the Cisco Certified Internetwork Expert logo, Cisco IOS, the Cisco IOS logo, Cisco Press, Cisco Systems, Cisco Systems Capital, the Cisco Systems logo, Empowering the Internet Generation, Enterprise/Solver, EtherChannel, EtherSwitch, Fast Step, GigaStack, Internet Quotient, IOS, IP/TV, iQ Expertise, the iQ logo, iQ Net Readiness Scorecard, LightStream, MGX, MICA, the Networkers logo, Network Registrar, Packet, PIX, Post-Routing, Pre-Routing, RateMUX, Registrar, ScriptShare, SlideCast, SmartNet, StrataView Plus, Stratm, SwitchProbe, TeleRouter, The Fastest Way to Increase Your Internet Quotient, TransPath, and VCO are registered trademarks of Cisco Systems, Inc. and/or its affiliates in the U.S. and certain other countries.

All other trademarks mentioned in this document or Web site are the property of their respective owners. The use of the word partner does not imply a partnership relationship between Cisco and any other company. (0304R)

Cisco BTS 10200 Softswitch CD Jumpstart Procedure for Duplex Systems

Copyright © 2005-2006, Cisco Systems, Inc.

All rights reserved.

| Revision History |
| --- |
| Date | Version | Revised By | Description |
| 03/16/2005 | 1.0 | Bill Woster | Initial Version |
| 05/13/2005 | 1.1 | Bill Woster | Changes for Release |
| 10/19/2005 | 1.2 | Bill Woster | Changes for Tom Wake and Richard Dawson |
| 02/24/06 | 1.3 | Sandro Gregorat | Added procedure to update savecore directory to the name of the node. |
| 07/12/06 | 1.4 | Sandro Gregorat | Changes according to TWC tk#16595 |
| 07/13/06 | 1.5 | Sandro Gregorat | Updated references to ‘step 8’ becoming ‘step 9’ in ‘Setting Up the Network Configuration Files’ |
| 08/14/06 | 1.6 | Sandro Gregorat | Removed the BTS release version from the document front page. |
| 08/25/06 | 1.7 | Sandro Gregorat | Removed the BTS release version from the footer, the copyright page and from a few steps of the procedure. |

Table of Contents

Table of Contents	4

Preface	5

Obtaining Documentation	5

World Wide Web	5

Documentation CD-ROM	5

Ordering Documentation	5

Documentation Feedback	6

Obtaining Technical Assistance	6

Cisco.com	6

Technical Assistance Center	7

Cisco TAC Web Site	7

Cisco TAC Escalation Center	8

Chapter 1: Jumpstart Prerequisite	9

Audience	10

Supported Hardware and Firmware	10

Chapter 2: Initial Install Jumpstart	12

Before You Start	12

Jumpstarting the BTS10200 System Platforms	13

Installing the Solaris Operating System	13

Setting Up the Network Configuration Files	16

Configuring the Element Management System	18

Configuring the Call Agent and Feature Server Installation	18

Chapter 3: Upgrade Install Jumpstart	20

Finishing the Solaris Upgrade Installation	21

Appendix A:  Mirroring the Disks	24

Appendix B:  Setting the Time Zone	26

Preface

This document describes the steps needed to jumpstart Solaris 10 on the host machines for the Cisco BTS 10200 Softswitch using a jumpstart CD.

# Obtaining Documentation

These sections explain how to obtain documentation from Cisco Systems.

## World Wide Web

You can access the most current Cisco documentation on the World Wide Web at this URL:

http://www.cisco.com/

Translated documentation is available at this URL:

http://www.cisco.com/public/countries_languages.shtml

## Documentation CD-ROM

Cisco documentation and additional literature are available in a Cisco Documentation CD-ROM package, which is shipped with your product. The Documentation CD-ROM is updated monthly and may be more current than printed documentation. The CD-ROM package is available as a single unit or through an annual subscription.

## Ordering Documentation

You can order Cisco documentation in these ways:

Registered Cisco.com users (Cisco direct customers) can order Cisco product documentation from the Networking Products MarketPlace:

http://www.cisco.com/cgi-bin/order/order_root.pl

Registered Cisco.com users can order the Documentation CD-ROM through the online Subscription Store:

http://www.cisco.com/pcgi-bin/marketplace/welcome.pl

Nonregistered Cisco.com users can order documentation through a local account representative by calling Cisco Systems Corporate Headquarters (California, U.S.A.) at 408 526-7208 or, elsewhere in North America, by calling 800 553-NETS (6387).

## Documentation Feedback

You can submit comments electronically on Cisco.com. In the Cisco Documentation home page, click the Fax or Email option in the "Leave Feedback" section at the bottom of the page.

You can e-mail your comments to bug-doc@cisco.com.

You can submit your comments by mail by using the response card behind the front cover of your document or by writing to the following address:

Cisco Systems
Attn: Document Resource Connection
170 West Tasman Drive
San Jose, CA 95134-9883

We appreciate your comments.

# Obtaining Technical Assistance

Cisco provides Cisco.com as a starting point for all technical assistance. Customers and partners can obtain online documentation, troubleshooting tips, and sample configurations from online tools by using the Cisco Technical Assistance Center (TAC) Web Site. Cisco.com registered users have complete access to the technical support resources on the Cisco TAC Web Site.

## Cisco.com

Cisco.com is the foundation of a suite of interactive, networked services that provides immediate, open access to Cisco information, networking solutions, services, programs, and resources at any time, from anywhere in the world.

Cisco.com is a highly integrated Internet application and a powerful, easy-to-use tool that provides a broad range of features and services to help you with these tasks:

Streamline business processes and improve productivity

Resolve technical issues with online support

Download and test software packages

Order Cisco learning materials and merchandise

Register for online skill assessment, training, and certification programs

If you want to obtain customized information and service, you can self-register on Cisco.com. To access Cisco.com, go to this URL:

http://www.cisco.com/

## Technical Assistance Center

The Cisco Technical Assistance Center (TAC) is available to all customers who need technical assistance with a Cisco product, technology, or solution. Two levels of support are available: the Cisco TAC Web Site and the Cisco TAC Escalation Center.

Cisco TAC inquiries are categorized according to the urgency of the issue:

Priority level 4 (P4)—You need information or assistance concerning Cisco product capabilities, product installation, or basic product configuration.

Priority level 3 (P3)—Your network performance is degraded. Network functionality is noticeably impaired, but most business operations continue.

Priority level 2 (P2)—Your production network is severely degraded, affecting significant aspects of business operations. No workaround is available.

Priority level 1 (P1)—Your production network is down, and a critical impact to business operations will occur if service is not restored quickly. No workaround is available.

The Cisco TAC resource that you choose is based on the priority of the problem and the conditions of service contracts, when applicable.

## Cisco TAC Web Site

You can use the Cisco TAC Web Site to resolve P3 and P4 issues yourself, saving both cost and time. The site provides around-the-clock access to online tools, knowledge bases, and software. To access the Cisco TAC Web Site, go to this URL:

http://www.cisco.com/tac

All customers, partners, and resellers who have a valid Cisco service contract have complete access to the technical support resources on the Cisco TAC Web Site. The Cisco TAC Web Site requires a Cisco.com login ID and password. If you have a valid service contract but do not have a login ID or password, go to this URL to register:

http://tools.cisco.com/RPF/register/register.do

If you are a Cisco.com registered user, and you cannot resolve your technical issues by using the Cisco TAC Web Site, you can open a case online by using the TAC Case Open tool at this URL:

http://www.cisco.com/tac/caseopen

If you have Internet access, we recommend that you open P3 and P4 cases through the Cisco TAC Web Site.

## Cisco TAC Escalation Center

The Cisco TAC Escalation Center addresses priority level 1 or priority level 2 issues. These classifications are assigned when severe network degradation significantly impacts business operations. When you contact the TAC Escalation Center with a P1 or P2 problem, a Cisco TAC engineer automatically opens a case.

To obtain a directory of toll-free Cisco TAC telephone numbers for your country, go to this URL:

http://www.cisco.com/warp/public/687/Directory/DirTAC.shtml

Before calling, please check with your network operations center to determine the level of Cisco support services to which your company is entitled: for example, SMARTnet, SMARTnet Onsite, or Network Supported Accounts (NSA). When you call the center, please have available your service agreement number and your product serial number.

Chapter 1: Jumpstart Prerequisite

This document contains both an Initial Install and an Upgrade procedure which are used to jumpstart Solaris 10 for all duplex application platforms.  This process uses a CD and is the first step for installing or upgrading the Cisco BTS 10200 Softswitch software.  It is important to note that an Initial Install requires the new creation of all configuration files which identify the system.  This process is documented in Chapter 2 “Initial Install Jumpstart”.  The upgrade procedure documented in Chapter 3 is designed to save the current configuration files before the Solaris 10 jumpstart and to restore the files after the jumpstart is finished.

IMPORTANT NOTICE:  The user should perform either the initial installation in Chapter 2 or the upgrade installation in Chapter 3.

CAUTION:  This is not a live traffic upgrade procedure. Performing the steps in either the upgrade or install procedure brings down the platform and stops call processing. Proceed only if this is acceptable. Do not run this procedure on an active system that is carrying live traffic. If you have questions, contact Cisco TAC.

This installation removes all existing applications and data. There is no backing out once you execute this procedure. If data is present, perform a data backup using the applicable procedure in the Cisco BTS 10200 Softswitch Operations Manual before you start this procedure.

If you are reinstalling an existing Cisco BTS 10200 Softswitch software version following this jumpstart, you can restore the Cisco BTS 10200 Softswitch data that was previously backed up. Follow the procedure in the Cisco BTS 10200 Softswitch Operations Manual.

If you are installing a new software version following this jumpstart, data previously backed up will become obsolete and cannot be restored on the new software. Data must be re-provisioned. You can restore data backups performed after the software installation in the usual manner.

Note We recommend that you back up data that has been restored or reprovisioned following software installation.

# Audience

This document is intended for system administrators, or those responsible for installing, the Cisco BTS 10200 Softswitch.

# Supported Hardware and Firmware

The following host machines are supported by this jumpstart (note:  not all of these may be supported by specific BTS releases).  The minimum disk size for an installation is 18 gig.  36 gig is required for full functional testing of the BTS installation including live upgrade.  Each supported hardware type has a minimum firmware version level required for correct performance.  The operator must check for the correct firmware version  and upgrade if necessary prior to jumpstarting.   This can be done by  running the following solaris command and comparing the firware version with the recommended version in compatibility list.

# prtconf -V

Hardware Compatibility and Recommended Firmware Version

• Sun Fire V1280          requires Firmware 5.19.2

• Sun Fire V440            requires Firmware 4.17.2

• Sun Fire V240            requires Firmware 4.17.1

• Sun Netra 440             Same as V440

• Sun Netra 240             Same as V240

• Sun Netra 120

• Sun Netra 1405

• Sun Netra 105

• Continuous Computing AX-MP and AX-I  AXi

Note that on the 1280,  the system components must have a firmware version which matches the monitor prom.  On bootup, a console message is displayed for each system component version.    Verify each component version with the monitor prom version.

Note that the znb Ethernet cards are not supported on Solaris 10 and must be replaced with a supported Ethernet device interface

Chapter 2: Initial Install Jumpstart

# Before You Start

The following prerequisites must be satisfied before you start this initial install jumpstart procedure.

Note We recommend that you completely read through this procedure before starting any steps.

This installation procedure should be performed by a user experienced in basic UNIX commands. Some of the steps require the involvement of the system administrator. Before you begin this procedure, perform the following tasks:

• Verify that your system meets the requirements specified in the "Jumpstart Requirements" section.

• A user experienced in basic UNIX commands should perform this procedure.

• Ensure that the Cisco BTS 10200 Softswitch hardware components are set up and turned on in accordance with  manufacturer recommendations.

• Make sure you have the Cisco BTS 10200 Solaris 10 boot/install CD
  (Solaris!Sun!sparc!10!0!10001).

• Ensure that you have a Network Installation Data Sheet (NIDS) provided by Cisco.

This will contain the following information necessary to place the jumpstarted node on the network after the CD installation.

nodename

hosts

netmasks

hostname.<primary interface>.

Note Enter all commands as shown; some commands are case sensitive. Press Enter at the end of each command.

## Jumpstarting the BTS10200 System Platforms

This section describes how to jumpstart install the Solaris operating system on the Cisco BTS 10200 Softswitch platforms for both the EMS and CA node types.  You must execute the following procedure for each of the four nodes in the BTS10200 Softsiwtch.

Note If you need to get to the ok> prompt from the sc> (or om>) prompt type:

sc> reset  -y

sc> console

To jumpstart the primary EMS, complete the following steps:

Step 1 Power on the system and bring it down to an ok> prompt.

Step 2 Type the following commands to restart the system and bring it to a known state:

ok> setenv  auto-boot? false

ok> reset-all

## Installing the Solaris Operating System

To install the Solaris operating system onto the Cisco BTS 10200 Softswitch, perform the following procedure:

Step 1 Insert the BTS 10200 Solaris 10 Boot/Install CD (Solaris!Sun!sparc!10!0!10001)
            into the CD-ROM drive

Step 2 Type the following commands to install the Solaris 10 operating system (OS):

ok> setenv auto-boot? true

ok> boot cdrom - install

The process will take approximately 10 to 20 minutes. The system will prompt for an NFS domain name near the end of the initial installation.  Enter “carriage return”  for the default option “no change”.

Note  If you encounter the following Error: “ERROR Disk is Invalid” Please check to make sure your Hardware configuration match exactly with the list of supported Hardwares.

Note By default, the basic CD jumpstart will assign the system the host name vtghost  and the IP address 192.168.123.1  and with the default root password vtghost.   This generic name and password is used because other products besides BTS are using the basic CD jumpstart procedure.   The password will change to opticall as soon as the finish script is run.

Step 3 Login using user name root and password vtghost.

.

Step 4

Continue with the same BTS 10200 Solaris 10 Boot/Install CD            (Solaris!Sun!sparc!10!0!10001) that is in the CD-ROM drive.  
Mount the CD using the following command:

# mount –F hsfs –o ro /dev/dsk/c0t0d0s0 /cdrom

Step 5

Execute the following two commands for an EMS node

# cd /cdrom/EMS

# ./EMS_finish.sh

Execute the following two commands for a CA node,

# cd /cdrom/CA

# ./CA_finish.sh

Note: To have the vi editor work correctly on the console terminal, you may first need to type the following commands for all shells except C-Shell.

# TERM=vt100

# export TERM

For C-Shell, use

# setenv TERM vt100

Step 4 Edit the /etc/TIMEZONE file and change the TZ setting to the correct setting for your locale.  Reference Appendix B for additional information on how to do this.

Step 5 Create and/or edit the following files to change the host name and IP addresses to match your Network Information Data Sheet (NIDS) for the first management IP address.  This will provide the minimal network capability to later transfer the entire set of  configuration files as defined in the NIDS.

For EMS nodes, the management IP address is on the first working ethernet interface, such as eri0 or ce0.  For CA nodes, the management IP address is on the third working Ethernet interface such as qfe0, bge0, or ce1, depending on the hardware model and the 4 port network interface card that is used.

The example illustrated below indicates changes for nodename prica23 with management ip address 10.89.183.112 which uses the Ethernet interface qfe0 and a netmask of 255.255.255.0

/etc/nodename

always use  the  name of this node. For example purposes,  the following command places the nodename prica23 in /etc/nodename.

echo prica23 > /etc/nodename

/etc/hosts

Add  the entry for the network IP address and this node name.  such as

10.89.183.112	     prica23

/etc/netmasks

Enter the subnet and netmask for the IP address placed in hostname.<working network interface> . For example

10.89.183.0 255.255.255.0

/etc/hostname.<working network interface>.  –

This file always contains the name of this node. For our example, the file hostname.qfe0 will contain prica23 on a single line.

/etc/rc3.d/S96StaticRoutes

This file should be modified to include the subnet default route to enable communication between the EMS and CA nodes on the subnet. Note that all NTP, DNS traffic and traffic from other machine to BTS system (eg. login), should all go through management networks. The static routes are particularly important in the CA system because CA has both management and signaling network. If the user does not specify explicitly a route in this file, the traffic will be directed to the signaling networks.  For example purposes, the following line should be added to this file since 10.89.183.254 is the IP address of the router for the 183 subnet.

route add -net 10.89.0.0 10.89.183.254

/etc/resolv.conf

Edit this file with the appropriate values for your network.  Change the domain, search, and nameserver entries for your network.

/etc/dumpadm.conf

At this point of the installation, the entry DUMPADM_SAVDIR in /etc/dumpadm.conf is using the directory /var/crash/vtghost.

This must be renamed /var/crash/<nodename>.

Follow this procedure:

# uname –S prica23     (if nodename is prica23)

# mv /var/crash/vtghost /var/crash/prica23

# dumpadm -s /var/crash/prica23

Once you have customized the files above, “cat” each one in turn to verify the changes were made correctly.

Step 6 Reboot the system with the following command

# shutdown –i6 –g0 -y

Step 7  Log in as root using password opticall.

## Setting Up the Network Configuration Files

To set up files needed to configure each BTS10200 node, verify that both EMS and both CA machines are properly configured for a network connection to each other.  Then complete the following steps:

Step 1   Login as root on EMS side A.

Step 2    Navigate to the /setup directory by entering the following command:

cd /opt/setup

Step 3 Edit the hostconfig file by entering the following command:

vi hostconfig

Edit the hostconfig file as appropriate with the information found in the NIDS. The references to ENDFIX are the last octet of the particular computing element IP address found in network 1 of the NIDS. If you have questions, contact Cisco TAC.

Step 4 Save and exit the hostconfig file.

Step 5 Generate the ‘host’ and ‘netmasks’ files in /tmp by entering the following command:

./hostgen.sh

Step 6 Change directory by entering the following command:

cd /tmp

Step 7 Verify that /tmp/host has the correct values by comparing them to the values in the NIDS.

Step 8  Some manual intervention is needed if one of the following cases applies:

- The host address of the IPs used on the physical/logical interfaces (last ‘octet’) is not the same on a given host. In this case a manual intervention is expected in order to update the entries in /etc/hosts that do not comply with the values created by the jumpstart procedure.

- The netmasks are different from 255.255.255.0. In this case the /etc/netmasks will need some manual correction.

The /etc/hosts and /etc/netmasks files are rebuilt, as part of the jumpstart procedure in two steps. First two files are generated in /tmp, ‘host’ and ‘netmasks’, by running ‘hostgen.sh’. Later on , ‘setlogic_EMS.sh’ (or ‘setlogic_CA.sh’ in the CallAgent) will make the final changes in the /etc directory. The two files /tmp/host and /tmp/netmasks, produced by hostgen.sh, must be modified as needed.

Step 9 Use the sftp command to transfer the /tmp/host and /tmp/netmask files to the secondary ems.

sftp <secems IP address>

cd /tmp

put host

put netmasks

quit

Step 10 Next, repeat step 9 to transfer the same files to the primary call agent.

Step 11 Next, repeat step 9 to transfer the same files to the secondary call agent

## Configuring the Element Management System

To configure the primary and secondary EMS nodes, complete the following steps on both primary and secondary EMS nodes.

Step 1 Login as root.

Step 2 Change directory by entering the following command:

cd /opt/setup

Step 3 Run the setlogic_EMS.sh script to set up the interfaces by entering the following command:

./setlogic_EMS.sh

Step 4 Verify that the /etc/netmasks and /etc/hosts files have the correct values by comparing them to the values in the NIDS.

Step 5 If  IRDP is enabled on the Managemenet Networks, login as root and activate the IRDP discovery daemon with the following commands:

mv /usr/sbin/.in.rdisc /usr/sbin/in.rdisc

/usr/sbin/in.rdisc –s –f

Step 6 shutdown and reboot the system using the following command:

shutdown –i6 –g0 –y

Step 7 For Field Installations and Lab installations which require mirrored disks, execute the procedure in Appendix A

## Configuring the Call Agent and Feature Server Installation

To configure the primary and secondary CA and FS, complete the following steps on both primary and secondary call agent nodes.

Step 1  Login as root.

Step 2 Change directories by entering the following command:

cd /opt/setup

Step 3 On 1280 systems run ‘ifconfig –a’ and ‘unplumb’ all existing interfaces with the exception of the loopback interface (“lo0”).

Step 4 Run the ./setlogic_CA.sh script to set up the interfaces.

./setlogic_CA.sh

Step 5 Verify that the /etc/netmask, and /etc/hosts files have the correct values by comparing them to the values in the NIDS. Make sure both match the NIDS.

Step 6 Shutdown and reboot the system using the following command

shutdown –i6 –g0 –y

Step 7  For Field Installations and Lab installations which require mirrored disks,  execute the procedure in Appendix A

Chapter 3: Upgrade Install Jumpstart

For an OS upgrade installation, configuration files in the /etc directory are first saved on a remote network disk which will not be formatted during the jumpstart procedure.   It is required that the configsave.sh and configrestore.sh scripts found in the BTS installation disk /opt/ems/utils directory  be used to save and restore he necessary configuration files.

To jumpstart a node, perform the following steps using the console terminal connected to the console port on the node.  Remote network access will not be available during this procedure.  Hence ALL steps  must be performed on the system console.  When finished with this upgrade procedure,  remote access to the node will be disabled.  The installer must enable telnet manually if a remote telnet  session is desired for the BTS installation.

The jumpstart will install an ssh/sftp server.

Step 1.  Obtain a copy of the configsave.sh script as specified above and place it in the / top level directory on the system to be upgraded.

Step 2.  Make the script executable if necessary and invoke the configsave.sh  script.  This will create a hostname.tar file where hostname is the name of the node being upgraded.  Next, use sftp to save the hostname.tar  file somewhere on the network where it can be recovered later.  Next,  issue the following command to determine which working device interface to best use for placing the node on the network during the configuration restore steps.

ifconfig –a

The resulting display will show every Ethernet interface and the ip address it is configured for.  Examine the list of interfaces for an IP address which is readily accessible from any point on the network.  Write down the device name such as eri0, qfe0, qfe1, hme0, etc. which will be the <working network interface> in the network configuration procedure. Also write down the IP address for this device.  This information will be used for the manual creation of essential files during the configuration restore which will place the node on the network.

Step 3.  Halt the system using the halt command.  The ok monitor “ok” prompt should be present.   Next insert the jumpstart CD in the CD rom drive.

Step 4.  Enter the following command at the OK prompt:

boot cdrom – install

Step 5.  The Solaris 10 operating system will install on the node in 20 to 30 minutes.  When finished, the install process will prompt you for changing NFS options.  Respond with entering Carriage Return.  The console will now show the login prompt.

Note By default, the basic CD jumpstart will assign the system the host name vtghost,  the IP address 192.168.123.1  and the default root password vtghost.   This generic name and password is used because other products besides BTS are using the basic CD jumpstart procedure.   The password will change to opticall as soon as the finish script is run.

Step 6  Log into the node using user name root and password vtghost.

Note: To have the vi editor work correctly on the console terminal, you may first need to type the following commands for a bash shell

# TERM=vt100

# export TERM

For a C shell,  use the following command

# setenv TERM vt100

## Finishing the Solaris Upgrade Installation

In this section you will finish the Solaris Upgrade Installation:

Step 7 Mount the CD using the following command:

# mount –F hsfs –o ro /dev/dsk/c0t0d0s0 /cdrom

Step 8  Change directories by entering the following command:

# cd /cdrom/CA  for a Call Agent Node

or

# cd /cdrom/EMS  for an EMS Node

Step 9  Finish the installation on the CA by entering the following command .  Note that when this finish script is run, the password for root will be opticall.

# ./CA_finish.sh

Or Finish the installation on the EMS by entering

# ./EMS_finish.sh

Step 10 Change directory to /etc:

# cd /etc

Step 11 Edit the /etc/TIMEZONE file and change the TZ setting to the correct setting for your locale. See Appendix B for valid time zone settings.

Edit the following files with the minimal changes to place the node on the network.   Once on the network,   ftp or sftp  may be used to retrieve the configrestore.sh and hostname.tar file which was saved in the initial configuration save.  The example illustrated below indicates changes for nodename prica23 with ip address 10.89.183.112 which uses the Ethernet interface eri0 and a netmask of 255.255.255.0

/etc/nodename

always enter  the  name of this node. For example purposes,

prica23

/etc/hosts

Add  the entry for the configuration save IP address and this node name.  such as

10.89.183.112 prica23

/etc/netmasks

Enter the subnet and netmask for the IP address placed in hostname.<working network interface> . For example

10.89.183.0 255.255.255.0

/etc/hostname.<working network interface>.  – always contains the name of this node. For our example, the file hostname.eri0 will contain prica23 on a single line.

Once you have edited the files above, “cat” each one in turn to verify the changes were made correctly.

Step 12 Reboot the system with the following command.  After reboot, the password for root is changed to opticall.

# shutdown –i6 –g0 –y

Step 13  Log into the node using user root and password opticall.  Verify that the node is on the network by pinging the IP address of the node where you saved the hostname.tar configuration file.

Next,  use ftp or sftp to retrieve a copy of the hostname.tar file and the configrestore.sh script from the network file server.  Place both of these in the / directory.  . Execute the following command.

# ./configrestore.sh

Step 14 shutdown and reboot the system using the following command

# shutdown –i6 –g0 -y

Step 15  Log into the system as root with password opticall and execute the following commands on the console.

# ifconfig –a

# netstat -nr

Verify that all Ethernet device interfaces are operational for a BTS install and that the Static routes are configured properly for full network access.  Add any additional routes that are necessary to achieve network wide access to the node.

Note:  When finished with this upgrade procedure,  remote access to the node will be available by ssh and sftp.  Telnet is installed but disabled for root.  Note that a BTS installation must be invoked either through the console or a telnet session.    The installer must enable telnet for root manually if a remote telnet  is desired for the BTS installation.

Step 16  Perform the upgrade procedure for each remaining Call Agent and EMS nodes.  When finished the system is configured and ready for a simplex disk installation of the BTS which is used in most lab installations.

If disk mirroring is required for a field or lab upgrade, execute the procedure described in  Appendix A

Appendix A:  Mirroring the Disks

NOTE:  The following procedure for mirroring disks is necessary for field installations and for lab systems which require mirrored disks. This procedure must then be executed on both EMS nodes and both CA nodes

Step 1  Change Directory to /opt/setup

cd /opt/setup

Step 2 Set up the mirror for each EMS by entering the following command on the  EMS node

./setup_mirror_ems

Set up the mirror for each CA  by entering the following command on the CA node.

./setup_mirror_ca

Note Do not reboot your system if an error occurs. You must fix the error before moving to the next step.

Step 3 Reboot by entering the following command:

reboot -- -r

Note Wait for the boot before continuing. Then log in to the node which you are working.

Step 4 Log in as root.

Step 5 change directory to /opt/setup

cd  /opt/setup

Step 6 Synchronize the disk by entering the following command: (using nohup is an option and since the operation could take 2 to 3 hours, is recommended).

nohup ./sync_mirror &

Note Wait for the disks to synchronize before continuing. The synchronization can be verified by running the Resync_status command from the /opt/utils directory. The display will show the resyncing in progress and report resync completion.

Step 7 Exit the primary EMS or CA node.

Appendix B:  Setting the Time Zone

The /etc/TIMEZONE file contains the entry for the time zone used in determining the local time.  The system must be rebooted for a time zone change to take effect.

By default,  the TZ variable is set as follows

TZ=US/Central

Valid values for TZ can be found in the directory structure under /usr/share/lib/zoneinfo .  The following values are valid for the US :.

ls  /usr/share/lib/zoneinfo/US

Alaska          Central         Hawaii          Mountain        Samoa

Aleutian        East-Indiana    Indiana-Starke  Pacific

Arizona         Eastern         Michigan        Pacific-New

The following values are valid for Europe.

ls /usr/share/lib/zoneinfo/Europe

Amsterdam    Brussels     Helsinki     Luxembourg   Nicosia      San_Marino   Tirane       Warsaw

Andorra      Bucharest    Istanbul     Madrid       Oslo         Sarajevo     Tiraspol     Zagreb

Athens       Budapest     Kaliningrad  Malta        Paris        Simferopol   Uzhgorod     Zaporozhye

Belfast      Chisinau     Kiev         Mariehamn    Prague       Skopje       Vaduz        Zurich

Belgrade     Copenhagen   Lisbon       Minsk        Riga         Sofia        Vatican

Berlin       Dublin       Ljubljana    Monaco       Rome         Stockholm    Vienna

Bratislava   Gibraltar    London       Moscow       Samara       Tallinn      Vilnius

To change the time zone to US Pacific time change

TZ=US/Pacific

To change the time zone to Europe London time change

TZ=Europe/London