Cisco BTS 10200 Softswitch Software Upgrade for Release

4.4.0 to 4.5.0

October 26, 2005

Corporate Headquarters

Cisco Systems, Inc.

170 West Tasman Drive

San Jose, CA 95134-1706

USA

http://www.cisco.com

Tel: 	408 526-4000

800 553-NETS (6387)

Fax:	408 526-4100

THE SPECIFICATIONS AND INFORMATION REGARDING THE PRODUCTS IN THIS MANUAL ARE SUBJECT TO CHANGE WITHOUT NOTICE. ALL STATEMENTS, INFORMATION, AND RECOMMENDATIONS IN THIS MANUAL ARE BELIEVED TO BE ACCURATE BUT ARE PRESENTED WITHOUT WARRANTY OF ANY KIND, EXPRESS OR IMPLIED. USERS MUST TAKE FULL RESPONSIBILITY FOR THEIR APPLICATION OF ANY PRODUCTS.

THE SOFTWARE LICENSE AND LIMITED WARRANTY FOR THE ACCOMPANYING PRODUCT ARE SET FORTH IN THE INFORMATION PACKET THAT SHIPPED WITH THE PRODUCT AND ARE INCORPORATED HEREIN BY THIS REFERENCE. IF YOU ARE UNABLE TO LOCATE THE SOFTWARE LICENSE OR LIMITED WARRANTY, CONTACT YOUR CISCO REPRESENTATIVE FOR A COPY.

The Cisco implementation of TCP header compression is an adaptation of a program developed by the University of California, Berkeley (UCB) as part of UCB’s public domain version of the UNIX operating system. All rights reserved. Copyright © 1981, Regents of the University of California.

NOTWITHSTANDING ANY OTHER WARRANTY HEREIN, ALL DOCUMENT FILES AND SOFTWARE OF THESE SUPPLIERS ARE PROVIDED “AS IS” WITH ALL FAULTS. CISCO AND THE ABOVE-NAMED SUPPLIERS DISCLAIM ALL WARRANTIES, EXPRESSED OR IMPLIED, INCLUDING, WITHOUT LIMITATION, THOSE OF MERCHANTABILITY, FITNESS FOR A PARTICULAR PURPOSE AND NONINFRINGEMENT OR ARISING FROM A COURSE OF DEALING, USAGE, OR TRADE PRACTICE.

IN NO EVENT SHALL CISCO OR ITS SUPPLIERS BE LIABLE FOR ANY INDIRECT, SPECIAL, CONSEQUENTIAL, OR INCIDENTAL DAMAGES, INCLUDING, WITHOUT LIMITATION, LOST PROFITS OR LOSS OR DAMAGE TO DATA ARISING OUT OF THE USE OR INABILITY TO USE THIS MANUAL, EVEN IF CISCO OR ITS SUPPLIERS HAVE BEEN ADVISED OF THE POSSIBILITY OF SUCH DAMAGES.

CCIP, CCSP, the Cisco Arrow logo, the Cisco Powered Network mark, the Cisco Systems Verified logo, Cisco Unity, Follow Me Browsing, FormShare, iQ Breakthrough, iQ FastTrack, the iQ Logo, iQ Net Readiness Scorecard, Networking Academy, ScriptShare, SMARTnet, TransPath, and Voice LAN are trademarks of Cisco Systems, Inc.; Changing the Way We Work, Live, Play, and Learn, The Fastest Way to Increase Your Internet Quotient, and iQuick Study are service marks of Cisco Systems, Inc.; and Aironet, ASIST, BPX, Catalyst, CCDA, CCDP, CCIE, CCNA, CCNP, Cisco, the Cisco Certified Internetwork Expert logo, Cisco IOS, the Cisco IOS logo, Cisco Press, Cisco Systems, Cisco Systems Capital, the Cisco Systems logo, Empowering the Internet Generation, Enterprise/Solver, EtherChannel, EtherSwitch, Fast Step, GigaStack, Internet Quotient, IOS, IP/TV, iQ Expertise, LightStream, MGX, MICA, the Networkers logo, Network Registrar, Packet, PIX, Post-Routing, Pre-Routing, RateMUX, Registrar, SlideCast, StrataView Plus, Stratm, SwitchProbe, TeleRouter, and VCO are registered trademarks of Cisco Systems, Inc. and/or its affiliates in the U.S. and certain other countries.

All other trademarks mentioned in this document or Web site are the property of their respective owners. The use of the word partner does not imply a partnership relationship between Cisco and any other company. (0301R)

Cisco BTS 10200 Softswitch Software Upgrade

Copyright © 2005, Cisco Systems, Inc.

All rights reserved.

| Revision History |
| --- |
| Date | Version | Revised By | Description |
| 8/15/2005 | 1.0 | Jack Daih | Initial Version |
| 8/22/2005 | 2.0 | Jack Daih | Added appendix K to enable disk mirroring after completing upgrade |
| 9/21/2005 | 3.0 | Jack Daih | Added pre-upgrade check steps for verifying obsolete triggers are not present in the system |
| 9/26/2005 | 4.0 | Jack Daih | Added Netra 240 hardware layout and removed Sunfire V120 |
| 10/24/2005 | 5.0 | Jack Daih | Corrected Appendix H and I reference. |
| 10/25/2005 | 6.0 | Jack Daih | Resolving defects: CSCsc28052, CSCsc28271, CSCsc28425, CSCsc28405, CSCsc28237, CSCsc28130, CSCsc28199, CSCsc28222, CSCsc28094 |
| 10/26/2005 | 7.0 | Jack Daih | Corrected Appendix G reference to F. |

Table of Contents

Table of Contents	4

Table of Contents	4

Preface	9

Obtaining Documentation	9

World Wide Web	9

Documentation CD-ROM	9

Ordering Documentation	9

Documentation Feedback	10

Obtaining Technical Assistance	10

Cisco.com	10

Technical Assistance Center	11

Cisco TAC Web Site	11

Cisco TAC Escalation Center	12

Chapter 1	13

Upgrade Requirements	13

Introduction	13

Assumptions	14

Requirements	14

Important notes about this procedure	15

Chapter 2	16

Preparation	16

Referenced documents	16

Prerequisites	17

Chapter 3	19

Complete one week before the scheduled upgrade	19

Task 1: Add new domain names to DNS	19

Task 2: Pre-construct opticall.cfg for the system to be upgraded to 4.5.0 release	20

Task 3: Check mlhg_terminal table	20

From Active EMS	20

Task 4: Check SLE table	21

From Active EMS	21

Task 5: Check Feature table	21

From Active EMS	21

Task 6: Check Feature table and Service-trigger table	21

From Active EMS	21

Task 7: Save customized cron jobs	23

From Each BTS machine	23

Chapter 4	24

Prepare System for Upgrade	24

Task 1: Verify System Status	24

Task 2: Backup user account	24

From EMS Side A	25

Chapter 5	26

Upgrade Side B Systems	26

Task 1: Disable Oracle DB replication	26

From Active EMS	26

From EMS side A	26

Task 2: Force side A systems to active	27

From Active EMS Side B	27

Task 3: Inhibit EMS mate communication	27

From EMS side A	27

Task 4: Stop applications and shutdown EMS side B	28

From EMS side B	28

Task 5: Stop applications and shutdown CA/FS side B	28

From CA/FS side B	28

Task 6: Upgrade EMS side B to the new release	29

From EMS side B	29

Task 7: Upgrade CA/FS Side B to the new release	34

From CA/FS side B	34

Task 8: Migrate oracle data	40

From EMS side B	40

Task 9: To install CORBA on EMS side B, please follow Appendix J.	41

Chapter 6	42

Prepare Side A Systems for Upgrade	42

Task 1: Force side A systems to standby	42

From EMS side A	42

Task 2: Sync Data from EMS side B to CA/FS side B	43

From EMS side B	43

Task 3: Validate release 4.5.0 software operation	43

From EMS side B	43

Task 4: Ftp billing records off the system	44

From EMS side A	44

Chapter 7	45

Upgrade Side A Systems	45

Task 1: Stop applications and shutdown EMS side A	45

From EMS side A	45

Task 2: Stop applications and shutdown CA/FS side A	45

From CA/FS side A	45

Task 3: Upgrade EMS side A to the new release	46

From EMS side A	46

Task 4: Upgrade CA/FS Side A to the new release	50

From CA/FS side A	50

Task 5: Restore EMS mate communication	54

From EMS side B	54

Task 6: Copying oracle data	55

From EMS side A	55

Task 7: To install CORBA on EMS side A, please follow Appendix J.	55

Chapter 8	56

Finalizing Upgrade	56

Task 1: Switchover activity from side B to side A	56

From EMS side B	56

Task 2: Enable Oracle DB replication on EMS side B	56

From EMS side B	56

Task 3: Check and correct sctp-assoc table	57

From EMS side A	57

Task 4: Synchronize handset provisioning data	58

From EMS side A	58

Task 5: Restore customized cron jobs	58

Task 6: Enable disk mirroring	59

Task 7: Verify system status	59

Appendix A	60

Check System Status	60

From Active EMS side A	60

Appendix B	63

Check Call Processing	63

From EMS side A	63

Appendix C	65

Check Provisioning and Database	65

From EMS side A	65

Check transaction queue	65

Perform database audit	65

Appendix D	67

Check Alarm Status	67

From EMS side A	67

Appendix E	69

Check Oracle Database Replication and Error Correction	69

Check Oracle DB replication status	69

From EMS side A	69

Correct replication error	70

From EMS Side B	70

From EMS Side A	70

Appendix F	72

Backout Procedure for Side B Systems	72

Introduction	72

Task 1: Force side A CA/FS to active	73

From EMS side B	74

Task 2: SFTP billing records to a mediation device	74

From EMS side B	74

Task 3: Sync DB usage	74

From EMS side A	74

Task 4: Stop applications and shutdown side B systems	75

From EMS side B	75

From CA/FS side B	75

Task 5: Restore side B systems to the old release	75

From CA/FS side B	75

From EMS side B	76

Task 6: Restore EMS mate communication	76

From EMS side A	77

Task 7: Switchover activity to EMS side B	77

From Active EMS side A	77

Task 8: Enable Oracle DB replication on EMS side A	77

From EMS side A	77

Task 9: Synchronize handset provisioning data	78

From EMS side B	78

Task 10: Switchover activity from EMS side B to EMS side A	79

From EMS side B	79

Task 11: Restore system to normal mode	79

From EMS side A	79

Task 12: Verify system status	79

Appendix G	81

System Backout Procedure	81

Introduction	81

Task 1: Disable Oracle DB replication on EMS side B	81

From Active EMS	81

From EMS side B	82

Task 2: Inhibit EMS mate communication	82

From EMS side B	82

Task 3: Force side B systems to active	82

From EMS side A	83

Task 4: SFTP billing records to a mediation device	83

From EMS side A	83

Task 5: Stop applications	83

From EMS side A	84

From CA/FS side A	84

Task 6: Restore side A systems to the old release	84

From CA/FS side A	84

From EMS side A	85

Task 7: Stop EMS side B billing application	86

From EMS side B	86

Task 8: Start EMS side A applications	86

From EMS side A	86

Task 9: To continue fallback process, please follow Appendix F.	86

Appendix H	87

Preparing Disks for Upgrade	87

Task 1: Locate and label the disks	87

Label disks for EMS Side A	87

Label disks for EMS Side B	87

Label disks for CA/FS Side A	87

Label disks for CA/FS Side B	88

Task 2: Disk slot lay out	88

Task 3: Construct opticall.cfg	89

Task 4: Disk preparation	89

For both EMS side A and B	89

For both CA/FS side A and B	90

Appendix I	92

Disk Mirroring after Upgrade	92

Configuring the Primary Element Management System	92

Configuring the Secondary Element Management System	93

Configuring the Primary Call Agent and Feature Server Installation	94

Configuring the Secondary Call Agent and Feature Server Installation	95

Appendix J	97

CORBA Installation	97

Task 1: Open Unix Shell on EMS	97

Task 2: Install OpenORB CORBA Application	97

Remove Installed OpenORB Application	97

Install OpenORB Packages	98

Preface

# Obtaining Documentation

These sections explain how to obtain documentation from Cisco Systems.

### World Wide Web

You can access the most current Cisco documentation on the World Wide Web at this URL: http://www.cisco.com/

Translated documentation is available at this URL: http://www.cisco.com/public/countries_languages.shtml

### Documentation CD-ROM

Cisco documentation and additional literature are available in a Cisco Documentation CD-ROM package, which is shipped with your product. The Documentation CD-ROM is updated monthly and may be more current than printed documentation. The CD-ROM package is available as a single unit or through an annual subscription.

### Ordering Documentation

You can order Cisco documentation in these ways:

Registered Cisco.com users (Cisco direct customers) can order Cisco product documentation from the Networking Products MarketPlace: http://www.cisco.com/cgi-bin/order/order_root.pl

Registered Cisco.com users can order the Documentation CD-ROM through the online Subscription Store: http://www.cisco.com/go/subscription

Nonregistered Cisco.com users can order documentation through a local account representative by calling Cisco Systems Corporate Headquarters (California, U.S.A.) at 408 526-7208 or, elsewhere in North America, by calling 800 553-NETS (6387).

### Documentation Feedback

You can submit comments electronically on Cisco.com. In the Cisco Documentation home page, click the Fax or Email option in the “Leave Feedback” section at the bottom of the page.

You can e-mail your comments to mailto:bug-doc@cisco.com.

You can submit your comments by mail by using the response card behind the front cover of your document or by writing to the following address:

Cisco Systems, INC.

Attn: Document Resource Connection

170 West Tasman Drive

San Jose, CA 95134-9883

# Obtaining Technical Assistance

Cisco provides Cisco.com as a starting point for all technical assistance. Customers and partners can obtain online documentation, troubleshooting tips, and sample configurations from online tools by using the Cisco Technical Assistance Center (TAC) Web Site. Cisco.com registered users have complete access to the technical support resources on the Cisco TAC Web Site: http://www.cisco.com/tac

### Cisco.com

Cisco.com is the foundation of a suite of interactive, networked services that provides immediate, open access to Cisco information, networking solutions, services, programs, and resources at any time, from anywhere in the world.

Cisco.com is a highly integrated Internet application and a powerful, easy-to-use tool that provides a broad range of features and services to help you with these tasks:

Streamline business processes and improve productivity

Resolve technical issues with online support

Download and test software packages

Order Cisco learning materials and merchandise

Register for online skill assessment, training, and certification programs

If you want to obtain customized information and service, you can self-register on Cisco.com. To access Cisco.com, go to this URL: http://www.cisco.com/

### Technical Assistance Center

The Cisco Technical Assistance Center (TAC) is available to all customers who need technical assistance with a Cisco product, technology, or solution. Two levels of support are available: the Cisco TAC Web Site and the Cisco TAC Escalation Center.

Cisco TAC inquiries are categorized according to the urgency of the issue:

Priority level 4 (P4)—You need information or assistance concerning Cisco product capabilities, product installation, or basic product configuration.

Priority level 3 (P3)—Your network performance is degraded. Network functionality is noticeably impaired, but most business operations continue.

Priority level 2 (P2)—Your production network is severely degraded, affecting significant aspects of business operations. No workaround is available.

Priority level 1 (P1)—Your production network is down, and a critical impact to business operations will occur if service is not restored quickly. No workaround is available.

The Cisco TAC resource that you choose is based on the priority of the problem and the conditions of service contracts, when applicable.

### Cisco TAC Web Site

You can use the Cisco TAC Web Site to resolve P3 and P4 issues yourself, saving both cost and time. The site provides around-the-clock access to online tools, knowledge bases, and software. To access the Cisco TAC Web Site, go to this URL: http://www.cisco.com/tac

All customers, partners, and resellers who have a valid Cisco service contract have complete access to the technical support resources on the Cisco TAC Web Site. The Cisco TAC Web Site requires a Cisco.com Log in ID and password. If you have a valid service contract but do not have a Log in ID or password, go to this URL to register: http://www.cisco.com/register/

If you are a Cisco.com registered user, and you cannot resolve your technical issues by using the Cisco TAC Web Site, you can open a case online by using the TAC Case Open tool at this URL: http://www.cisco.com/tac/caseopen

If you have Internet access, we recommend that you open P3 and P4 cases through the Cisco TAC Web Site: http://www.cisco.com/tac

### Cisco TAC Escalation Center

The Cisco TAC Escalation Center addresses priority level 1 or priority level 2 issues. These classifications are assigned when severe network degradation significantly impacts business operations. When you contact the TAC Escalation Center with a P1 or P2 problem, a Cisco TAC engineer automatically opens a case.

To obtain a directory of toll-free Cisco TAC telephone numbers for your country, go to this URL: http://www.cisco.com/warp/public/687/Directory/DirTAC.shtml

Before calling, please check with your network operations center to determine the level of Cisco support services to which your company is entitled: for example, SMARTnet, SMARTnet Onsite, or Network Supported Accounts (NSA). When you call the center, please have available your service agreement number and your product serial number.

Chapter 1

Upgrade Requirements

# Introduction

Application software loads are designated as Release 900-aa.bb.cc.Vxx, where

- aa=major release number, for example, 01

- bb=minor release number, for example, 03

- cc=maintenance release, for example, 00

- Vxx=Version number, for example V04

This procedure can be used on an in-service system, but the steps must be followed as shown in this document in order to avoid traffic interruptions.

|  | Caution Performing the steps in this procedure will bring down and restart individual platforms in a specific sequence. Do not perform the steps out of sequence, as it could affect traffic. If you have questions, contact Cisco Support. |
| --- | --- |

This procedure should be performed during a maintenance window.

Note   In this document, the following designations are used:

- EMS -- Element Management System

- CA/FS -- Call Agent / Feature Server

- Primary -- Also referred to as "Side A"

- Secondary -- Also referred to as "Side B"

# Assumptions

The following assumptions are made.

- The installer has a basic understanding of UNIX and Oracle commands.

- The installer has the appropriate user name(s) and password(s) to log on to each EMS/CA/FS platform as root user, and as Command Line Interface (CLI) user on the EMS.

|  | Note Contact Cisco Support before you start if you have any questions. |
| --- | --- |

# Requirements

Verify that opticall.cfg has the correct information for each of the following machines.

- Side A EMS

- Side B EMS

- Side A CA/FS

- Side B CA/FS

Determine the oracle and root passwords for the systems you are upgrading. If you do not know these passwords, ask your system administrator.

Refer to local documentation to determine if CORBA installation is required on this system. If unsure, ask your system administrator.

# Important notes about this procedure

Throughout this procedure, each command is shown with the appropriate system prompt, followed by the command to be entered in bold. The prompt is generally one of the following:

- Host system prompt (<hostname>#)

- Oracle prompt (<hostname>$)

- SQL prompt (SQL>)

- CLI prompt (CLI>)

- SFTP prompt (sftp>)

Note the following conventions used throughout the steps in this procedure:

- Enter commands as shown, as they are case sensitive (except for CLI commands).

It is recommended that you read through the entire procedure before performing any steps.

It will take approximately 7 hours to complete the entire upgrade process. Please plan accordingly to minimize any negative service impacts.

CDR delimiter customization is not retained after software upgrade. The customer or Cisco engineer must manually customize again to keep the same customization.

There will be no CLI provisioning allowed during entire upgrade process.

Chapter 2

Preparation

This chapter describes the tasks a user must complete at least two weeks before the scheduled upgrade.

Each customer must purchase 8 disk drives with matching disk size to the existing system that is to be upgraded.

# Referenced documents

Please go to Cisco CCO Web site below to access BTS documentations: http://www.cisco.com/univercd/cc/td/doc/product/voice/bts10200/index.htm

- Site Preparation and Network Communications Requirements: http://www.cisco.com/univercd/cc/td/doc/product/voice/bts10200/bts4_5/install/site45.htm

- Cisco BTS 10200 Network Site Survey (Release 4.5): http://www.cisco.com/univercd/cc/td/doc/product/voice/bts10200/bts4_5/install/bts45nss.doc

- Cisco BTS 10200 NIDS Generator (Release 4.5.0): http://www.cisco.com/univercd/cc/td/doc/product/voice/bts10200/bts4_5/install/nids_45.xls

- Cisco BTS 10200 CD Jumpstart Procedure for Solaris 10: http://www.cisco.com/univercd/cc/td/doc/product/voice/bts10200/bts4_5/install/sol10cdj.doc

- Cabling, VLAN, and IRDP Setup Procedure for 4-2 Configuration (Release 4.4.x): http://www.cisco.com/univercd/cc/td/doc/product/voice/bts10200/bts4_4/install/r44cbl.doc

# Prerequisites

- Create or allocate a BTS system based on exactly the same Sun hardware as the BTS to be upgraded with a fully functioning BTS network including DNS, NTP, and IRDP.

- Two sets of four disk drives jumpstarted with Solaris 10. Each disk must be prepared in a hardware platform that matches the target system to be upgraded.  Please refer to Appendix H to prepare each disk.

  - Two disk drives for EMS side A -- the first disk is normally used for the upgrade and the second disk will be used only when the first disk goes bad. Each disk should already have:

    - Pre-jumpstarted with Solaris 10 OS

    - Pre-staged with BTS 10200 Software Release 4.5.0

    - Pre-installed EMS application software and databases

  - Two disk drives for EMS side B -- the first disk is normally used for the upgrade and the second disk will be used only when the first disk goes bad. Each disk should already have:

    - Pre-jumpstarted with Solaris 10 OS

    - Pre-staged with BTS 10200 Software Release 4.5.0

    - Pre-installed EMS application software and databases

  - Two disk drives for CA/FS side A -- the first disk is normally used for the upgrade and the second disk will be used only when the first disk goes bad. Each disk should already have:

    - Pre-jumpstarted with Solaris 10 OS

    - Pre-staged with BTS 10200 Software Release 4.5.0

  - Two disk drives for CA/FS side B -- the first disk is normally used for the upgrade and the second disk will be used only when the first disk goes bad. Each disk should already have:

    - Pre-jumpstarted with Solaris 10 OS

    - Pre-staged with BTS 10200 Software Release 4.5.0

- Completed Network Information Data Sheets for release 4.5.0.

- There is secure shell (ssh) access to the Cisco BTS 10200 system.

- There is console access to each Cisco BTS 10200 machine.

- A Network File Server (NFS) that is accessible from each BTS machine.

Chapter 3

# Complete one week before the scheduled upgrade

This chapter describes the tasks a user must complete one week before the scheduled upgrade.

# Task 1: Add new domain names to DNS

This task must be performed on Domain Name Servers that are serving the Cisco BTS 10200 system.

Step 1   Log in to Domain Name Servers for Cisco BTS 10200

Step 2   Add domain names for the following opticall.cfg parameters to Domain Name Server database where xxx – is the application instance number specific to the site.

- DNS_FOR_CAxxx_SIM_COM

Note This is a qualified DNS name used by a SIM process in Call Agents for communication to external devices. Each name resolves to two logical IP addresses in the same subnet as primary and secondary interfaces respectively. Each instance must have a unique DNS name and two uniquely associated LOGICAL IP addresses. For a simplex, use the host name for this parameter.

- DNS_FOR_FSAINxxx_ASM_COM

Note This is a qualified DNS name used by the AIN process in Feature Server FSAIN. Each name should return two logical IP addresses of a AIN Feature Server which match the subnet of its two physical interfaces. For a simplex system, use host name for this parameter.

- DNS_FOR_FSPTCxxx_POTS_COM

Note This is a qualified DNS name used by the POTS process in Feature Server FSPTC. Each name should return two logical IP addresses of a POTS/CENTRIX Feature Server which match the subnet of its two physical interfaces. For a simplex system, use host name for this parameter.

# Task 2: Pre-construct opticall.cfg for the system to be upgraded to 4.5.0 release

Step 1   Get a copy of the completed Network Information Data Sheets (NIDS)

Step 2   Get a copy of the new opticall.cfg file for release 4.5.0 from Cisco

Step 3   Fill in value for each parameter defined in the opticall.cfg using data from Network Information Data Sheets and then place the file on the Network File Server (NFS).

Note   New parameters added to the 4.5.0 release:

Where xxx – is the application instance number specific to the site.

- NSCD_ENABLED

- CAxxx_LAF_PARAMETER

- FSPTCxxx_LAF_PARAMETER

- FSAINxxx_LAF_PARAMETER

- EMS_LAF_PARAMETER

- BDMS_LAF_PARAMETER

- DNS_FOR_CAxxx_SIM_COM

- DNS_FOR_FSAINxxx_ASM_COM

- DNS_FOR_FSPTCxxx_POTS_COM

# Task 3: Check mlhg_terminal table

# From Active EMS

Step 1   <hostname># su – oracle

Step 2    <hostname>$ sqlplus optiuser/optiuser

Step 3    sql> select term_id, mlhg_id, mgw_id from mlhg_terminal group by term_id,mlhg_id,mgw_id having count(*) > 1;

Please check:

- Check for duplicated records with TERM_ID, MLHG_ID, MGW_ID

- If there is any record shown from the above query, remove the duplicated records from CLI. Failure to do so will result in an upgrade failure.

# Task 4: Check SLE table

# From Active EMS

Step 1    sql> select fname from sle where fname not in

('SCA','SCR','SCF','DRCW','NSA');

Please check:

- If the above query returns any record, you either have to delete the sle record or upgrade the sle record with a valid fname from CLI. Failure to do so will result in an upgrade failure.

# Task 5: Check Feature table

# From Active EMS

Step 1   sql> select tid1, tid2, tid3 from feature where tid1 not in (select tid from trigger_id) or tid2 not in (select tid from trigger_id) or tid3 not in (select tid from trigger_id);

Please check:

- If the above query returns any record, you either have to change or remove each feature record returned. Failure to do so will result in an upgrade failure.

# Task 6: Check Feature table and Service-trigger table

# From Active EMS

Step 1   From Oracle DB:

sql> select tid from service_trigger where tid not in (select tid from trigger_id);

Please check:

- If the above query returns any record, you either have to change or remove each service-trigger record returned. Failure to do so will result in an upgrade failure.

Step 2   Exit from Oracle:

sql> quit;

<hostname>$ exit

Step 3   Log in as CLI user

Step 4   CLI> show feature tid1=<TRIGGER_ID>

Step 5   CLI> show feature tid2=<TRIGGER_ID>

Step 6   CLI> show feature tid3=<TRIGGER_ID>

Step 7   CLI> show service-trigger tid=<TRIGGER_ID>

Where <TRIGGER_ID> is any one of the following obsolete triggers:

ORIGINATION_ATTEMPT
O_ABANDON
O_ANSWER
O_CALLED_PARTY_BUSY
O_DISCONNECT
O_EXCEPTION
O_NOT_REACHABLE
O_NO_ANSWER
O_REANSWER
O_SUSPEND
ROUTE_SELECTED_FAILURE
T_ABANDON_DP
T_DISCONNECT
T_EXCEPTION
T_NOT_REACHABLE
T_REANSWER
T_SUSPEND

Please check:

- If the above show commands return any record, you either have to change or remove of each TRIGGER_ID record returned. Failure to do so will result in an upgrade failure.

# Task 7: Save customized cron jobs

This upgrade process requires disk replacement. Because of this, all customized cron jobs in the system will be lost. Please save the cron jobs to your network file servers to be restored once the entire system is upgraded to the 4.5.0 release.

# From Each BTS machine

Step 1   Log in as root user

Step 2   <hostname># cd /var/spool/cron/crontab

- Ftp each cron job to a Network File Server where the BTS system has access to.

Chapter 4

Prepare System for Upgrade

Suspend all CLI provisioning activity during the entire upgrade process.

This chapter describes the steps a user must complete the morning or the night before the scheduled upgrade.

# Task 1: Verify System Status

Step 1   Verify that the side A systems are in the active state. Use Appendix A for this procedure.

Step 2   Verify that call processing is working without error. Use Appendix B for this procedure.

Step 3   Verify that provisioning is operational from CLI command line, and verify database. Use Appendix C for this procedure.

Step 4   Verify that there are no outstanding major or critical alarms. Use Appendix D for this procedure.

Step 5   Use Appendix E to verify that Oracle database and replication functions are working properly.

|  | Caution Do not continue until the above verifications have been made. Call Cisco Support if you need assistance. |
| --- | --- |

# Task 2: Backup user account

The user accounts saved in this task is to be restored to side B EMS once it is upgraded to 4.5.0 release.

# From EMS Side A

Step 1   Log in as root

Step 2   Save the /opt/ems/users directory:

<hostname># tar -cvf /opt/.upgrade/users.tar /opt/ems/users

Chapter 5

Upgrade Side B Systems

# Task 1: Disable Oracle DB replication

# From Active EMS

Step 1   Log in to Active EMS as CLI user.

Step 2   CLI> control bdms id=BDMS01; target-state=forced-standby-active;

Step 3   CLI> control element-manager id=EM01; target-state=forced-standby-active;

Step 4    CLI session will terminate when application platform switchover is complete.

# From EMS side A

Note Make sure there is no CLI session established before executing following steps.

Step 1   Log in as Oracle user:

<hostname># su – oracle

<hostname>$ cd /opt/oracle/admin/utl

Step 2   Set Oracle DB to simplex mode:

<hostname>$ rep_toggle –s optical1 –t set_simplex

- Answer “y” when prompt

- Answer “y” again when prompt

Step 3   <hostname>$ exit

Step 4   Restart applications to release Oracle connections:

<hostname># platform stop all

<hostname># platform start

# Task 2: Force side A systems to active

This procedure will force the side A systems to remain active.

|  | Note In the commands below, "xxx", "yyy" or "zzz" is the instance for the process on your system. |
| --- | --- |

# From Active EMS Side B

Step 1   Log in to Active EMS as CLI user.

Step 2   CLI> control call-agent id=CAxxx; target-state=forced-active-standby;

Step 3   CLI> control feature-server id=FSPTCyyy; target-state=forced-active-standby;

Step 4   CLI> control feature-server id=FSAINzzz; target-state=forced-active-standby;

Step 5   CLI> control bdms id=BDMS01; target-state=forced-active-standby;

Step 6   CLI> control element-manager id=EM01; target-state=forced-active-standby;

# Task 3: Inhibit EMS mate communication

In this task, you will isolate the OMS Hub on EMS side A from talking to EMS side B.

# From EMS side A

Step 1   Log in as root

Step 2   <hostname># /opt/ems/utils/updMgr.sh –split_hub

Step 3   <hostname># nodestat

- Verify there is no HUB communication from EMS side A to CA/FS side B

- Verify OMS Hub mate port status: No communication between EMS

# Task 4: Stop applications and shutdown EMS side B

# From EMS side B

Step 1   Log in as root

Step 2   Record the IP address and netmask for the management interface of the system.

- For an example, if the “hme0” is used for management interface, then execute the following command:

<hostname># ifconfig hme0

- Record the IP address and netmask for the interface to be used in the next task.

IP: _____________ Netmask: ____________ Interface Name: ___________

Step 3   <hostname># mv /etc/rc3.d/S99platform /etc/rc3.d/_S99platform

Step 4   <hostname># platform stop all

Step 5   <hostname># sync; sync

Step 6   <hostname># shutdown –i5 –g0 –y

# Task 5: Stop applications and shutdown CA/FS side B

# From CA/FS side B

Step 1   Log in as root

Step 2   Record the IP address and netmask for the management interface of the system.

- For an example, if the “hme0” is used for management interface, then execute the following command:

<hostname># ifconfig hme0

- Record the IP address and netmask for the interface to be used in the next task.

IP: _____________ Netmask: ____________ Interface Name: ___________

Step 3   <hostname># mv /etc/rc3.d/S99platform /etc/rc3.d/_S99platform

Step 4   <hostname># platform stop all

Step 5    <hostname># sync; sync

Step 6   <hostname># shutdown –i5 –g0 –y

# Task 6: Upgrade EMS side B to the new release

# From EMS side B

Step 1   Power off the machine

Step 2   Remove disk0 from slot 0 off the machine and label it as “Release 4.4.0 EMS side B disk0”

- Netra 240 disk slot lay out:

| Disk 0 | Disk 1 |
| --- | --- |
| DVD-ROM |  |

- SunFire V240 disk slot lay out:

| Disk 2 | Disk 3 |  |
| --- | --- | --- |
| Disk 0 | Disk 1 | DVD-ROM |

- SunFire V440 disk slot lay out:

| Disk 3 | DVD-ROM |
| --- | --- |
| Disk 2 |  |
| Disk 1 |  |
| Disk 0 |  |

- Netra 1280 disk slot lay out:

|  | DVD-ROM |
| --- | --- |
|  | Disk 1 |
|  | Disk 0 |

- Netra 20 disk slot lay out:

| D I S K 0 | D I S K 1 |  | DVD ROM |
| --- | --- | --- | --- |

- Continuous Hardware disk slot lay out:

| CD-ROM | Disk 0 | Disk 2 |
| --- | --- | --- |
|  | Disk 1 | Disk 3 |

Step 3   Place new disk labeled as “Release 4.5.0 EMS side B disk0, 1” in slot 0

Step 4   Power on the machine and allow the system to boot up by monitoring the boot process thru console

- For a Netra 1280 machine, please execute the following command from console:

<lom>poweron

- For other type of hardware, please use the power button to turn on the power.

Step 5   Log in as root thru console

Step 6   Remove network interface hardware configuration

<hostname># cp -fp /etc/path_to_inst   /etc/path_to_inst.save

<hostname># \rm –f path_to_inst*

Step 7   Rebuild the hardware configuration

<hostname># reboot -- -r

- Wait for the system to boot up. Then log in as root.

Step 8   Restore interfaces:

- <hostname># ifconfig <primary interface name> plumb

  - Use Interface Name recorded in “Chapter 5, Task 4”

- <hostname># ifconfig <primary interface name> <Interface IP> netmask <NETMASK> broadcast + up

  - Use IP and NETMASK recorded in “Chapter 5, Task 4”

- Add static routes to reach Domain Name Server and Network File Server using “route add …” command:

  - Example: route add -net 10.89.224.1 10.89.232.254

Where: 10.89.224.1 is the destination DNS server IP
              10.89.232.254 is the gateway IP

Step 9   Reset ssh keys:

<hostname># \rm /.ssh/known_hosts

Step 10   sftp the opticall.cfg file from Network File Server (opticall.cfg was constructed in Chapter 3, Task 2) and place it under /etc directory.

Step 11   sftp resolv.conf file from Primary EMS Side A and place it under /etc directory.

<hostname># sftp <Side A EMS IP>

sftp> lcd /etc

sftp> cd /etc

sftp> get resolv.conf

sftp> exit

Step 12   Run script program to replace the hostname

<hostname># cd /opt/ems/upgrade

<hostname># DoTheChange -s

- The system will reboot when the script DoTheChange completes its run

Step 13    Wait for the system to boot up. Then log in as root.

Step 14   Editing /etc/default/init:

<hostname># vi /etc/default/init

- Remove lines and keep only the following lines:

#

TZ=<Timezone>

CMASK=022

For an example:

The original /etc/default/init file before line removal:

# @(#)init.dfl 1.5 99/05/26

#

# This file is /etc/default/init.  /etc/TIMEZONE is a symlink to this file.

# This file looks like a shell script, but it is not.  To maintain

# compatibility with old versions of /etc/TIMEZONE, some shell constructs

# (i.e., export commands) are allowed in this file, but are ignored.

#

# Lines of this file should be of the form VAR=value, where VAR is one of

# TZ, LANG, CMASK, or any of the LC_* environment variables.

#

TZ=US/Central

CMASK=022

LC_COLLATE=en_US.ISO8859-1

LC_CTYPE=en_US.ISO8859-1

LC_MESSAGES=C

LC_MONETARY=en_US.ISO8859-1

LC_NUMERIC=en_US.ISO8859-1

LC_TIME=en_US.ISO8859-1

The /etc/default/init file after line removal:

# @(#)init.dfl 1.5 99/05/26

#

# This file is /etc/default/init.  /etc/TIMEZONE is a symlink to this file.

# This file looks like a shell script, but it is not.  To maintain

# compatibility with old versions of /etc/TIMEZONE, some shell constructs

# (i.e., export commands) are allowed in this file, but are ignored.

#

# Lines of this file should be of the form VAR=value, where VAR is one of

# TZ, LANG, CMASK, or any of the LC_* environment variables.

#

TZ=US/Central

CMASK=022

Step 15   Verify interface hardware configuration match to the host configuration:

<hostname># egrep –i “qfe|ce|eri|bge|hme” /etc/path_to_inst

<hostname># ls –l /etc/hostname.*

- If the interface names match from the above two outputs, please continue on Step 16.

- If the interface names do NOT match, please match them by changing the postfix of hostname.*.

For an example:

Output from “egrep –i “qfe|ce|eri|bge|hme” /etc/path_to_inst” is:

"/pci@1f,4000/network@1,1" 0 "hme"

"/pci@1f,4000/pci@4/SUNW,qfe@0,1" 0 "qfe"

"/pci@1f,4000/pci@4/SUNW,qfe@1,1" 1 "qfe"

"/pci@1f,4000/pci@4/SUNW,qfe@2,1" 2 "qfe"

"/pci@1f,4000/pci@4/SUNW,qfe@3,1" 3 "qfe"

Output from “ls -l /etc/hostname.*” is:

-rw-r--r--   1 root     other          14 May 16 16:03 /etc/hostname.hme0

-rw-r--r--   1 root     other         14 May 16 16:04 /etc/hostname.hme0:1

-rw-r--r--   1 root     other         14 May 16 16:04 /etc/hostname.eri0

-rw-r--r--   1 root     other         14 May 16 16:04 /etc/hostname.eri0:1

After change, the output should be:

-rw-r--r--   1 root     other          14 May 16 16:03 /etc/hostname.hme0

-rw-r--r--   1 root     other         14 May 16 16:04 /etc/hostname.hme0:1

-rw-r--r--   1 root     other         14 May 16 16:04 /etc/hostname.qfe0

-rw-r--r--   1 root     other         14 May 16 16:04 /etc/hostname.qfe0:1

Step 16   Reboot the machine to pick up new TIMEZONE and interface setting:

<hostname># sync; sync; reboot

- Wait for the system to boot up. Then log in as root.

Step 17   <hostname># /opt/ems/utils/updMgr.sh –split_hub

Step 18   <hostname># svcadm disable system/cron

Step 19    CDR delimiter customization is not retained after software upgrade. If this system has been customized, either the Customer or Cisco Support Engineer must manually customize again to keep the same customization.

- <hostname># cd /opt/bdms/bin

- <hostname># vi platform.cfg

- Find the section for the command argument list for the BMG process

- Customize the CDR delimiters in the “Args=” line

- Example:

Args=-port 15260 -h localhost -u optiuser -p optiuser -fmt default_formatter -UpdIntvl 3300 -ems_local_dn blg-aSYS14EMS.cisco.com -FD semicolon -RD verticalbar

Step 20   <hostname># platform start –i oracle

Step 21   Log in as Oracle user.

<hostname># su – oracle

<hostname>$ cd /opt/oracle/admin/utl

Step 22   Set Oracle DB to simplex mode:

<hostname>$ rep_toggle –s optical2 –t set_simplex

- Answer “y” when prompt

- Answer “y” again when prompt

# Task 7: Upgrade CA/FS Side B to the new release

|  | Warning Do not proceed if you don’t have a pre-constructed opticall.cfg file for the system. The opticall.cfg file should already be constructed in Chapter 3, Task 2. |
| --- | --- |

# From CA/FS side B

Step 1   Power off the machine

Step 2   Remove disk0 from slot 0 off the machine and label it as “Release 4.4.0 CA/FS side B disk0”

- Netra 240 disk slot lay out:

| Disk 0 | Disk 1 |
| --- | --- |
| DVD-ROM |  |

- SunFire V240 disk slot lay out:

| Disk 2 | Disk 3 |  |
| --- | --- | --- |
| Disk 0 | Disk 1 | DVD-ROM |

- SunFire V440 disk slot lay out:

| Disk 3 | DVD-ROM |
| --- | --- |
| Disk 2 |  |
| Disk 1 |  |
| Disk 0 |  |

- Netra 1280 disk slot lay out:

|  | DVD-ROM |
| --- | --- |
|  | Disk 1 |
|  | Disk 0 |

- Netra 20 disk slot lay out:

| D I S K 0 | D I S K 1 |  | DVD ROM |
| --- | --- | --- | --- |

- Continuous Hardware disk slot lay out:

| CD-ROM | Disk 0 | Disk 2 |
| --- | --- | --- |
|  | Disk 1 | Disk 3 |

Step 3   Place new disk labeled as “Release 4.5.0 CA/FS side B disk0, 1” in slot 0

Step 4   Power on the machine and allow the system to boot up by monitoring the boot process thru console

- For a Netra 1280 machine, please execute the following command from console:

<lom>poweron

- For other type of hardware, please use the power button to turn on the power.

Step 5   Log in as root thru console

Step 6   Remove network interface hardware configuration

<hostname># cp -fp /etc/path_to_inst   /etc/path_to_inst.save

<hostname># \rm –f path_to_inst*

Step 7   Rebuild the hardware configuration

<hostname># reboot -- -r

- Wait for the system to boot up. Then log in as root.

Step 8   Restore interfaces:

- <hostname># ifconfig <primary interface name> plumb

  - Use Interface Name recorded in “Chapter 5, Task 5”

- <hostname># ifconfig <primary interface name> <Interface IP> netmask <NETMASK> broadcast + up

  - Use IP and NETMASK recorded in “Chapter 5, Task 5”

- Add static routes to reach Domain Name Server and Network File Server using “route add …” command:

  - Example: route add -net 10.89.224.1 10.89.232.254

Where: 10.89.224.1 is the destination DNS server IP
              10.89.232.254 is the gateway IP

Step 9   Reset ssh keys:

<hostname># \rm /.ssh/known_hosts

Step 10   sftp the opticall.cfg file from Network File Server (opticall.cfg was constructed in Chapter 3, Task 2) and place it under /etc directory.

Step 11   sftp resolv.conf file from Primary CA/FS Side A and place it under /etc directory.

<hostname># sftp <Side A CA/FS IP>

sftp> lcd /etc

sftp> cd /etc

sftp> get resolv.conf

sftp> exit

Step 12   Run script program to replace the hostname

<hostname># cd /opt/ems/upgrade

<hostname># DoTheChange -s

- The system will reboot when the script DoTheChange completes its run

Step 13    Wait for the system to boot up. Then log in as root.

Step 14   Editing /etc/default/init:

<hostname># vi /etc/default/init

- Remove lines and keep only the following lines:

#

TZ=<Timezone>

CMASK=022

For an example:

The original /etc/default/init file before line removal:

# @(#)init.dfl 1.5 99/05/26

#

# This file is /etc/default/init.  /etc/TIMEZONE is a symlink to this file.

# This file looks like a shell script, but it is not.  To maintain

# compatibility with old versions of /etc/TIMEZONE, some shell constructs

# (i.e., export commands) are allowed in this file, but are ignored.

#

# Lines of this file should be of the form VAR=value, where VAR is one of

# TZ, LANG, CMASK, or any of the LC_* environment variables.

#

TZ=US/Central

CMASK=022

LC_COLLATE=en_US.ISO8859-1

LC_CTYPE=en_US.ISO8859-1

LC_MESSAGES=C

LC_MONETARY=en_US.ISO8859-1

LC_NUMERIC=en_US.ISO8859-1

LC_TIME=en_US.ISO8859-1

The /etc/default/init file after line removal:

# @(#)init.dfl 1.5 99/05/26

#

# This file is /etc/default/init.  /etc/TIMEZONE is a symlink to this file.

# This file looks like a shell script, but it is not.  To maintain

# compatibility with old versions of /etc/TIMEZONE, some shell constructs

# (i.e., export commands) are allowed in this file, but are ignored.

#

# Lines of this file should be of the form VAR=value, where VAR is one of

# TZ, LANG, CMASK, or any of the LC_* environment variables.

#

TZ=US/Central

CMASK=022

Step 15   Verify interface hardware configuration match to the host configuration:

<hostname># egrep –i “qfe|ce|eri|bge|hme” /etc/path_to_inst

<hostname># ls –l /etc/hostname.*

- If the interface names match from the above two outputs, please continue on Step 16.

- If the interface names do NOT match, please match them by changing the postfix of hostname.*.

For an example:

Output from “egrep –i “qfe|ce|eri|bge|hme” /etc/path_to_inst” is:

"/pci@1f,4000/network@1,1" 0 "hme"

"/pci@1f,4000/pci@4/SUNW,qfe@0,1" 0 "qfe"

"/pci@1f,4000/pci@4/SUNW,qfe@1,1" 1 "qfe"

"/pci@1f,4000/pci@4/SUNW,qfe@2,1" 2 "qfe"

"/pci@1f,4000/pci@4/SUNW,qfe@3,1" 3 "qfe"

"/pci@1f,2000/pci@1/SUNW,qfe@0,1" 4 "qfe"

"/pci@1f,2000/pci@1/SUNW,qfe@1,1" 5 "qfe"

"/pci@1f,2000/pci@1/SUNW,qfe@2,1" 6 "qfe"

"/pci@1f,2000/pci@1/SUNW,qfe@3,1" 7 "qfe"

Output from “ls -l /etc/hostname.*” is:

-rw-r--r--   1 root     other         14 Jun 10 11:25 hostname.hme0

-rw-r--r--   1 root     other         14 Jun 10 11:25 hostname.eri0

-rw-r--r--   1 root     other         13 Jun 10 11:25 hostname.eri1

-rw-r--r--   1 root     other         13 Jun 10 11:25 hostname.eri1:1

-rw-r--r--   1 root     other         14 Jun 10 11:25 hostname.eri1:2

-rw-r--r--   1 root     other         12 Jun 10 11:25 hostname.eri1:3

-rw-r--r--   1 root     other         13 Jun 10 11:25 hostname.eri2

-rw-r--r--   1 root     other         13 Jun 10 11:25 hostname.eri2:1

-rw-r--r--   1 root     other         14 Jun 10 11:25 hostname.eri2:2

-rw-r--r--   1 root     other         12 Jun 10 11:25 hostname.eri2:3

After change, the output should be:

-rw-r--r--   1 root     other         14 Jun 10 11:25 hostname.hme0

-rw-r--r--   1 root     other         14 Jun 10 11:25 hostname.qfe0

-rw-r--r--   1 root     other         13 Jun 10 11:25 hostname.qfe1

-rw-r--r--   1 root     other         13 Jun 10 11:25 hostname.qfe1:1

-rw-r--r--   1 root     other         14 Jun 10 11:25 hostname.qfe1:2

-rw-r--r--   1 root     other         12 Jun 10 11:25 hostname.qfe1:3

-rw-r--r--   1 root     other         13 Jun 10 11:25 hostname.qfe2

-rw-r--r--   1 root     other         13 Jun 10 11:25 hostname.qfe2:1

-rw-r--r--   1 root     other         14 Jun 10 11:25 hostname.qfe2:2

-rw-r--r--   1 root     other         12 Jun 10 11:25 hostname.qfe2:3

Step 16   Reboot the machine to pick up new TIMEZONE and interface setting:

<hostname># sync; sync; reboot

- Wait for the system to boot up. Then log in as root.

Step 17   Check for configuration errors

<hostname># cd /opt/Build

<hostname># checkCFG –u

- Correct errors generated by checkCFG

- Once the result is clean without errors, then proceed to the next step.

Step 18   <hostname># install.sh -upgrade

Step 19   Answer "y" when prompted. This process will take up to 15 minutes to complete.

- Answer "y" if prompted for reboot

- Wait for the system to boot up. Then log in as root.

Step 20   <hostname># platform start

Step 21   <hostname># mv /etc/rc3.d/_S99platform /etc/rc3.d/S99platform

# Task 8: Migrate oracle data

# From EMS side B

Step 1   Copying data.

<hostname>$ su - oracle

<hostname>$ cd /opt/oracle/admin/upd

<hostname>$ java dba.dmt.DMMgr -upgrade -auto ./config/4.4.0_to_4.5.0.cfg

Step 2   Verify the data migration is a success.

<hostname>$ echo $?

- Verify the returned value is 0.

- If not, please sftp /opt/oracle/admin/upd/DMMgr.log file off system and call for immediate technical assistance.

Step 3   <hostname>$ java dba.adm.DBUsage -sync

- Verify Number of tables “unable-to-sync” is 0

- If not, please contract Cisco support

Step 4   <hostname>$ cd /opt/oracle/opticall/create

Step 5   <hostname>$ dbinstall optical2 -load dbsize

Step 6   <hostname>$ exit

Step 7 <hostname># platform start

Step 8 <hostname># svcadm enable system/cron

Step 9 <hostname># mv /etc/rc3.d/_S99platform /etc/rc3.d/S99platform

# Task 9: To install CORBA on EMS side B, please follow Appendix J.

Chapter 6

Prepare Side A Systems for Upgrade

# Task 1: Force side A systems to standby

This procedure will force the side A systems to standby and force the side B systems to active.

|  | Note In the commands below, "xxx", "yyy" or "zzz" is the instance for the process on your system. |
| --- | --- |

# From EMS side A

Step 1   Log in as CLI user

Step 2   CLI> control call-agent id=CAxxx; target-state=forced-standby-active;

Step 3   CLI> control feature-server id=FSPTCzzz; target-state=forced-standby-active;

Step 4   CLI> control feature-server id=FSAINyyy; target-state=forced-standby-active;

Step 5   CLI> control bdms id=BDMS01; target-state=forced-standby-active;

Step 6   CLI> control element-manager id=EM01; target-state=forced-standby-active;

Step 7   CLI session will terminate when the last CLI command completes

|  | Note If the system failed to switchover from side A to side B, please contact Cisco Support to determine whether the system should fallback. If fallback is needed, please following Appendix G. |
| --- | --- |

# Task 2: Sync Data from EMS side B to CA/FS side B

In this task, you will sync from EMS to CA/FS for several inter-platform migrated tables.

# From EMS side B

Step 1   Log in as ciscouser (password: ciscosupport)

Step 2   CLI> sync emergency_number_list master=EMS; target=CAxxx;

Step 3   CLI> sync radius-profile master=EMS; target=FSPTCyyy;

Step 4   CLI> sync pop master=EMS; target=FSPTCyyy;

Step 5   CLI> sync pop master=EMS; target=FSAINzzz;

Step 6   CLI> sync lnp-profile master=EMS; target=CAxxx;

Step 7   CLI> sync lnp-profile master=EMS; target=FSAINzzz;

Step 8   CLI> exit

# Task 3: Validate release 4.5.0 software operation

To verify the stability of the newly installed 4.5.0 Release, let CA/FS side B carry live traffic for period of time. Monitor the Cisco BTS 10200 Softswitch and the network. If there are any problems, please investigate and contact Cisco Support if necessary.

# From EMS side B

Step 1   Verify that call processing using Appendix B.

Step 2   Log in as CLI user.

Step 3   CLI> audit database type=row-count;

- Verify there is no error in the report and the database is not empty.

- If any table shows mis-match, then perform a detailed audit on these tables:

CLI> audit <table name>;

Step 4   Verify the SUP config is set up correctly

- CLI> show sup-config;

- Verify refresh rate is set to 86400.

- If not, do the following

- CLI> change sup-config type=refresh_rate; value=86400;

# Task 4: Ftp billing records off the system

# From EMS side A

Step 1   Log in as root

Step 2   <hostname># ls /opt/bms/ftp/billing

- If there are files listed, then SFTP the files to a mediation device on the network and remove the files from the /opt/bms/ftp/billing directory.

|  | Note Once the system proves stable and you decide to move ahead with the upgrade, then you must execute subsequent tasks. If fallback is needed at this stage, please follow the fallback procedure in Appendix G. |
| --- | --- |

Chapter 7

Upgrade Side A Systems

# Task 1: Stop applications and shutdown EMS side A

# From EMS side A

Step 1   Log in as root

Step 2   Record the IP address and netmask for the management interface of the system.

- For an example, if the “hme0” is used for management interface, then execute the following command:

<hostname># ifconfig hme0

- Record the IP address and netmask for the interface to be used in the next task.

IP: _____________ Netmask: ____________ Interface Name: ___________

Step 3   <hostname># mv /etc/rc3.d/S99platform /etc/rc3.d/_S99platform

Step 4   <hostname># platform stop all

Step 5   <hostname># sync; sync

Step 6   <hostname># shutdown –i5 –g0 –y

# Task 2: Stop applications and shutdown CA/FS side A

# From CA/FS side A

Step 1   Log in as root

Step 2   Record the IP address and netmask for the management interface of the system.

- For an example, if the “hme0” is used for management interface, then execute the following command:

<hostname># ifconfig hme0

- Record the IP address and netmask for the interface to be used in the next task.

IP: _____________ Netmask: ____________ Interface Name: ___________

Step 3   <hostname># mv /etc/rc3.d/S99platform /etc/rc3.d/_S99platform

Step 4   <hostname># platform stop all

Step 5    <hostname># sync; sync

Step 6   <hostname># shutdown –i5 –g0 –y

# Task 3: Upgrade EMS side A to the new release

# From EMS side A

Step 1   Power off the machine

Step 2   Remove disk0 from slot 0 off the machine and label it as “Release 4.4.0 EMS side A disk0”

- Netra 240 disk slot lay out:

| Disk 0 | Disk 1 |
| --- | --- |
| DVD-ROM |  |

- SunFire V240 disk slot lay out:

| Disk 2 | Disk 3 |  |
| --- | --- | --- |
| Disk 0 | Disk 1 | DVD-ROM |

- SunFire V440 disk slot lay out:

| Disk 3 | DVD-ROM |
| --- | --- |
| Disk 2 |  |
| Disk 1 |  |
| Disk 0 |  |

- Netra 1280 disk slot lay out:

|  | DVD-ROM |
| --- | --- |
|  | Disk 1 |
|  | Disk 0 |

- Netra 20 disk slot lay out:

| D I S K 0 | D I S K 1 |  | DVD ROM |
| --- | --- | --- | --- |

- Continuous Hardware disk slot lay out:

| CD-ROM | Disk 0 | Disk 2 |
| --- | --- | --- |
|  | Disk 1 | Disk 3 |

Step 3   Place new disk labeled as “Release 4.5.0 EMS side A disk0, 1” in slot 0

Step 4   Power on the machine and allow the system to boot up by monitoring the boot process thru console

- For a Netra 1280 machine, please execute the following command from console:

<lom>poweron

- For other type of hardware, please use the power button to turn on the power.

Step 5   Log in as root thru console

Step 6   Remove network interface hardware configuration

<hostname># cp -fp /etc/path_to_inst   /etc/path_to_inst.save

<hostname># \rm –f path_to_inst*

Step 7   Rebuild the hardware configuration

<hostname># reboot -- -r

- Wait for the system to boot up. Then log in as root.

Step 8   Restore interfaces:

- <hostname># ifconfig <primary interface name> plumb

  - Use Interface Name recorded in “Chapter 7, Task 1”

- <hostname># ifconfig <primary interface name> <Interface IP> netmask <NETMASK> broadcast + up

  - Use IP and NETMASK recorded in “Chapter 7, Task 1”

- Add static routes to reach Domain Name Server and Network File Server using “route add …” command:

  - Example: route add -net 10.89.224.1 10.89.232.254

Where: 10.89.224.1 is the destination DNS server IP
              10.89.232.254 is the gateway IP

Step 9   Reset ssh keys:

<hostname># \rm /.ssh/known_hosts

Step 10   sftp the opticall.cfg and resolv.conf from Secondary EMS side B and place it under /etc directory.

<hostname># sftp <Side B EMS IP>

sftp> lcd /etc

sftp> cd /etc

sftp> get resolv.conf

sftp> get opticall.cfg

sftp> exit

Step 11   Run script program to replace the hostname

<hostname># cd /opt/ems/upgrade

<hostname># DoTheChange -p

- The system will reboot when the script DoTheChange completes its run

Step 12   Wait for the system to boot up. Then Log in as root.

Step 13   Verify interface hardware configuration match to the host configuration:

<hostname># egrep –i “qfe|ce|eri|bge|hme” /etc/path_to_inst

<hostname># ls –l /etc/hostname.*

- If the interface names match from the above two outputs, please continue on Step 15.

- If the interface names do NOT match, please match them by changing the postfix of hostname.*.

For an example:

Output from “egrep –i “qfe|ce|eri|bge|hme” /etc/path_to_inst” is:

"/pci@1f,4000/network@1,1" 0 "hme"

"/pci@1f,4000/pci@4/SUNW,qfe@0,1" 0 "qfe"

"/pci@1f,4000/pci@4/SUNW,qfe@1,1" 1 "qfe"

"/pci@1f,4000/pci@4/SUNW,qfe@2,1" 2 "qfe"

"/pci@1f,4000/pci@4/SUNW,qfe@3,1" 3 "qfe"

Output from “ls -l /etc/hostname.*” is:

-rw-r--r--   1 root     other         14 May 16 16:03 /etc/hostname.hme0

-rw-r--r--   1 root     other         14 May 16 16:04 /etc/hostname.hme0:1

-rw-r--r--   1 root     other         14 May 16 16:04 /etc/hostname.eri0

-rw-r--r--   1 root     other         14 May 16 16:04 /etc/hostname.eri0:1

After change, the output should be:

-rw-r--r--   1 root     other         14 May 16 16:03 /etc/hostname.hme0

-rw-r--r--   1 root     other         14 May 16 16:04 /etc/hostname.hme0:1

-rw-r--r--   1 root     other         14 May 16 16:04 /etc/hostname.qfe0

-rw-r--r--   1 root     other         14 May 16 16:04 /etc/hostname.qfe0:1

Step 14   Reboot the machine to pick up new interface setting:

<hostname># sync; sync; reboot

- Wait for the system to boot up. Then log in as root.

Step 15   CDR delimiter customization is not retained after software upgrade. If this system has been customized, either the Customer or Cisco Support Engineer must manually customize again to keep the same customization.

- <hostname># cd /opt/bdms/bin

- <hostname># vi platform.cfg

- Find the section for the command argument list for the BMG process

- Customize the CDR delimiters in the “Args=” line

- Example:

Args=-port 15260 -h localhost -u optiuser -p optiuser -fmt default_formatter -UpdIntvl 3300 -ems_local_dn blg-aSYS14EMS.cisco.com -FD semicolon -RD verticalbar

Step 16   <hostname># platform start

# Task 4: Upgrade CA/FS Side A to the new release

# From CA/FS side A

Step 1   Power off the machine

Step 2   Remove disk0 from slot 0 off the machine and label it as “Release 4.4.0 CA/FS side A disk0”

- Netra 240 disk slot lay out:

| Disk 0 | Disk 1 |
| --- | --- |
| DVD-ROM |  |

- SunFire V240 disk slot lay out:

| Disk 2 | Disk 3 |  |
| --- | --- | --- |
| Disk 0 | Disk 1 | DVD-ROM |

- SunFire V440 disk slot lay out:

| Disk 3 | DVD-ROM |
| --- | --- |
| Disk 2 |  |
| Disk 1 |  |
| Disk 0 |  |

- Netra 1280 disk slot lay out:

|  | DVD-ROM |
| --- | --- |
|  | Disk 1 |
|  | Disk 0 |

- Netra 20 disk slot lay out:

| D I S K 0 | D I S K 1 |  | DVD ROM |
| --- | --- | --- | --- |

- Continuous Hardware disk slot lay out:

| CD-ROM | Disk 0 | Disk 2 |
| --- | --- | --- |
|  | Disk 1 | Disk 3 |

Step 3   Place new disk labeled as “Release 4.5.0 CA/FS side A disk0, 1” in slot 0

Step 4   Power on the machine and allow the system to boot up by monitoring the boot process thru console

- For a Netra 1280 machine, please execute the following command from console:

<lom>poweron

- For other type of hardware, please use the power button to turn on the power.

Step 5   Log in as root thru console

Step 6   Remove network interface hardware configuration

<hostname># cp -fp /etc/path_to_inst   /etc/path_to_inst.save

<hostname># \rm –f path_to_inst*

Step 7   Rebuild the hardware configuration

<hostname># reboot -- -r

- Wait for the system to boot up. Then log in as root.

Step 8   Restore interfaces:

- <hostname># ifconfig <interface name> plumb

  - Use Interface Name recorded in “Chapter 7, Task 2”

- <hostname># ifconfig <interface name> <Interface IP> netmask <NETMASK> broadcast + up

  - Use IP and NETMASK recorded in “Chapter 7, Task 2”

- Add static routes to reach Domain Name Server and Network File Server using “route add …” command:

  - Example: route add -net 10.89.224.1 10.89.232.254

Where: 10.89.224.1 is the destination DNS server IP
              10.89.232.254 is the gateway IP

Step 9   Reset ssh keys:

<hostname># \rm /.ssh/known_hosts

Step 10   sftp the opticall.cfg and resolv.conf from Secondary CA/FS side B and place it under /etc directory.

<hostname># sftp <Side B CA/FS IP>

sftp> lcd /etc

sftp> cd /etc

sftp> get resolv.conf

sftp> get opticall.cfg

sftp> exit

Step 11   Run script program to replace the hostname

<hostname># cd /opt/ems/upgrade

<hostname># DoTheChange -p

- The system will reboot when the script DoTheChange completes its run

Step 12    Wait for the system to boot up. Then Log in as root.

Step 13   Verify interface hardware configuration match to the host configuration:

<hostname># egrep –i “qfe|ce|eri|bge|hme” /etc/path_to_inst

<hostname># ls –l /etc/hostname.*

- If the interface names match from the above two outputs, please continue on Step 15.

- If the interface names do NOT match, please match them by changing the postfix of hostname.*.

For an example:

Output from “egrep –i “qfe|ce|eri|bge|hme” /etc/path_to_inst” is:

"/pci@1f,4000/network@1,1" 0 "hme"

"/pci@1f,4000/pci@4/SUNW,qfe@0,1" 0 "qfe"

"/pci@1f,4000/pci@4/SUNW,qfe@1,1" 1 "qfe"

"/pci@1f,4000/pci@4/SUNW,qfe@2,1" 2 "qfe"

"/pci@1f,4000/pci@4/SUNW,qfe@3,1" 3 "qfe"

"/pci@1f,2000/pci@1/SUNW,qfe@0,1" 4 "qfe"

"/pci@1f,2000/pci@1/SUNW,qfe@1,1" 5 "qfe"

"/pci@1f,2000/pci@1/SUNW,qfe@2,1" 6 "qfe"

"/pci@1f,2000/pci@1/SUNW,qfe@3,1" 7 "qfe"

Output from “ls -l /etc/hostname.*” is:

-rw-r--r--   1 root     other         14 Jun 10 11:25 hostname.hme0

-rw-r--r--   1 root     other         14 Jun 10 11:25 hostname.eri0

-rw-r--r--   1 root     other         13 Jun 10 11:25 hostname.eri1

-rw-r--r--   1 root     other         13 Jun 10 11:25 hostname.eri1:1

-rw-r--r--   1 root     other         14 Jun 10 11:25 hostname.eri1:2

-rw-r--r--   1 root     other         12 Jun 10 11:25 hostname.eri1:3

-rw-r--r--   1 root     other         13 Jun 10 11:25 hostname.eri2

-rw-r--r--   1 root     other         13 Jun 10 11:25 hostname.eri2:1

-rw-r--r--   1 root     other         14 Jun 10 11:25 hostname.eri2:2

-rw-r--r--   1 root     other         12 Jun 10 11:25 hostname.eri2:3

After change, the output should be:

-rw-r--r--   1 root     other         14 Jun 10 11:25 hostname.hme0

-rw-r--r--   1 root     other         14 Jun 10 11:25 hostname.qfe0

-rw-r--r--   1 root     other         13 Jun 10 11:25 hostname.qfe1

-rw-r--r--   1 root     other         13 Jun 10 11:25 hostname.qfe1:1

-rw-r--r--   1 root     other         14 Jun 10 11:25 hostname.qfe1:2

-rw-r--r--   1 root     other         12 Jun 10 11:25 hostname.qfe1:3

-rw-r--r--   1 root     other         13 Jun 10 11:25 hostname.qfe2

-rw-r--r--   1 root     other         13 Jun 10 11:25 hostname.qfe2:1

-rw-r--r--   1 root     other         14 Jun 10 11:25 hostname.qfe2:2

-rw-r--r--   1 root     other         12 Jun 10 11:25 hostname.qfe2:3

Step 14   Reboot the machine to pick up new interface setting:

<hostname># sync; sync; reboot

- Wait for the system to boot up. Then log in as root.

Step 15   Install the applications

<hostname># cd /opt/Build

<hostname># install.sh –upgrade

Step 16   Answer "y" when prompted. This process will take up to 15 minutes to complete.

- Answer "y" if prompted for reboot

- Wait for the system to boot up. Then Log in as root.

Step 17   <hostname># platform start

Step 18   <hostname># mv /etc/rc3.d/_S99platform /etc/rc3.d/S99platform

# Task 5: Restore EMS mate communication

# From EMS side B

Step 1   Log in as root

Step 2   <hostname># /opt/ems/utils/updMgr.sh –restore_hub

Step 3   <hostname># nodestat

- Verify OMS Hub mate port status is established

- Verify HUB communication from EMS side B to CA/FS side A is established

# Task 6: Copying oracle data

# From EMS side A

Step 1   <hostname># svcadm disable system/cron

Step 2   Copying data.

<hostname>$ su – oracle

<hostname>$ cd /opt/oracle/admin/upd

<hostname>$ java dba.dmt.DMMgr –copy -auto

Step 3   Verify the data copy is a success.

<hostname>$ echo $?

- Verify the returned value is 0.

- If not, please sftp /opt/oracle/admin/upd/DMMgr.log file off system and call for immediate technical assistance.

<hostname>$ exit

Step 4   <hostname># svcadm enable system/cron

Step 5   <hostname># mv /etc/rc3.d/_S99platform /etc/rc3.d/S99platform

# Task 7: To install CORBA on EMS side A, please follow Appendix J.

Chapter 8

Finalizing Upgrade

# Task 1: Switchover activity from side B to side A

This procedure will force the active system activity from side B to side A.

# From EMS side B

|  | Note In the commands below, "xxx", "yyy" or "zzz" is the instance for the process on your system. |
| --- | --- |

Step 1   Log in to EMS side B as CLI user.

Step 2   CLI> control call-agent id=CAxxx; target-state=active-standby;

Step 3   CLI> control feature-server id=FSPTCyyy; target-state=active-standby;

Step 4   CLI> control feature-server id=FSAINzzz; target-state=active-standby;

Step 5   CLI> control bdms id=BDMS01; target-state=active-standby;

Step 6   CLI> control element-manager id=EM01; target-state=active-standby;

Step 7   CLI shell session should be terminated when last CLI commands completes.

# Task 2: Enable Oracle DB replication on EMS side B

# From EMS side B

Step 1   Restore Oracle DB to duplex mode:

<hostname># su - oracle

<hostname>$ cd /opt/oracle/admin/utl

<hostname>$ rep_toggle –s optical2 –t set_duplex

- Answer “y” when prompt

- Answer “y” again when prompt

Step 2   <hostname>$ exit

Step 3   Restart applications to connect to Oracle DB in duplex mode.

<hostname># platform stop all

<hostname># platform start

# Task 3: Check and correct sctp-assoc table

# From EMS side A

Step 1   Log in to EMS side B as CLI user.

Step 2   Change the value for field max-init-rto to 1000 in the table sctp-assoc:

CLI> audit sctp-assoc;

- If the audit produces mismatched result for field max-init-rto. Please use the following steps to correct each mismatched record:

CLI> control sctp-assoc id=<Assoc ID>; mode=forced; target_state=oos;

CLI> change sctp-assoc id=<Assoc ID>; max-init-rto=1000;

CLI> control sctp-assoc id=<Assoc ID>; mode=forced; target_state=ins;

Step 3   CLI> exit

# Task 4: Synchronize handset provisioning data

# From EMS side A

|  | Note In the commands below, "xxx", "yyy" or "zzz" is the instance for the process on your system. |
| --- | --- |

Step 1   Log in as ciscouser (password: ciscosupport)

Step 2   CLI>sync termination master=CAxxx; target=EMS;

- Verify the transaction is executed successfully.

Step 3   CLI>sync sc1d master=FSPTCzzz; target=EMS;

- Verify the transaction is executed successfully

Step 4   CLI>sync sc2d master=FSPTCzzz; target=EMS;

- Verify the transaction is executed successfully

Step 5   CLI>sync sle master=FSPTCzzz; target=EMS;

- Verify the transaction is executed successfully

Step 6   CLI>sync subscriber-feature-data master=FSPTCzzz; target=EMS;

- Verify the transaction is executed successfully

Step 7   CLI>exit

# Task 5: Restore customized cron jobs

Please restore customized cron jobs by using the files saved on the network file server during system preparation stage in Chapter 3, Task 5. Please don’t copy the old crontab file over the new one. You may need to compare the back up version of the crontab file to the new crontab file to restore the previous settings. This should be done for all machines in the system.

# Task 6: Enable disk mirroring

Please follow steps in the Appendix I to enable disk mirroring on each machine in the BTS system.

# Task 7: Verify system status

Verify that the system is operating properly before you leave the site.

Step 1   Verify that the side A systems are in the active state. Use Appendix A for this procedure.

Step 2   Verify that call processing is working without error. Use Appendix B for this procedure.

Step 3   Verify that provisioning is operational from CLI command line, and verify database. Use Appendix C for this procedure.

Step 4   Verify that there are no outstanding major or critical alarms. Use Appendix D for this procedure.

Step 5   Use Appendix E to verify that Oracle database and replication functions are working properly.

Step 6   If you have answered NO to any of the above questions (Step 1-5) do not proceed. Instead, use the backout procedure in Appendix G. Contact Cisco Support if you need assistance.

You have completed the Cisco BTS 10200 system upgrade process successfully.

Appendix A

Check System Status

The purpose of this procedure is to verify the system is running in NORMAL mode, with the side A systems in ACTIVE state and the side B systems in STANDBY state.

|  | Note In the commands below, "xxx", "yyy" or "zzz" is the instance for the process on your system, and DomainName is your system domain name. |
| --- | --- |

# From Active EMS side A

Step 1   Log in as CLI user.

Step 2   CLI> status system;

Release 4.4.0 sample output:

Checking Call Agent status ... Checking Feature Server status ... Checking Billing Server status ... Checking Billing Oracle status ... Checking Element Manager status ... Checking EMS MySQL status ... Checking ORACLE status ... CALL AGENT STATUS IS... -> APPLICATION INSTANCE -> Call Agent [CA146] PRIMARY STATUS -> ACTIVE_NORMAL SECONDARY STATUS -> STANDBY_NORMAL FEATURE SERVER STATUS IS... -> APPLICATION INSTANCE -> Feature Server [FSPTC235] PRIMARY STATUS -> ACTIVE_NORMAL SECONDARY STATUS -> STANDBY_NORMAL FEATURE SERVER STATUS IS... -> APPLICATION INSTANCE -> Feature Server [FSAIN205] PRIMARY STATUS -> ACTIVE_NORMAL SECONDARY STATUS -> STANDBY_NORMAL BILLING SERVER STATUS IS... -> APPLICATION INSTANCE -> Bulk Data Management Server [BDMS01] PRIMARY STATUS -> ACTIVE_NORMAL SECONDARY STATUS -> STANDBY_NORMAL BILLING ORACLE STATUS IS... -> Daemon is running! ELEMENT MANAGER STATUS IS... -> APPLICATION INSTANCE -> Element Manager [EM01] PRIMARY STATUS -> ACTIVE_NORMAL SECONDARY STATUS -> STANDBY_NORMAL EMS MYSQL STATUS IS ... -> Daemon is running! ORACLE STATUS IS... -> Daemon is running! Reply : Success:

Release 4.5.0 sample output:

Checking Call Agent status ... Checking Feature Server status ... Checking Billing Server status ... Checking Billing Oracle status ... Checking Element Manager status ... Checking EMS MySQL status ... Checking ORACLE status ... CALL AGENT STATUS IS... -> APPLICATION INSTANCE -> Call Agent [CA146] PRIMARY STATUS -> ACTIVE SECONDARY STATUS -> STANDBY FEATURE SERVER STATUS IS... -> APPLICATION INSTANCE -> Feature Server [FSPTC235] PRIMARY STATUS -> ACTIVE SECONDARY STATUS -> STANDBY FEATURE SERVER STATUS IS... -> APPLICATION INSTANCE -> Feature Server [FSAIN205] PRIMARY STATUS -> ACTIVE SECONDARY STATUS -> STANDBY BILLING SERVER STATUS IS... -> APPLICATION INSTANCE -> Bulk Data Management Server [BDMS01] PRIMARY STATUS -> ACTIVE SECONDARY STATUS -> STANDBY BILLING ORACLE STATUS IS... -> Daemon is running! ELEMENT MANAGER STATUS IS... -> APPLICATION INSTANCE -> Element Manager [EM01] PRIMARY STATUS -> ACTIVE SECONDARY STATUS -> STANDBY EMS MYSQL STATUS IS ... -> Daemon is running! ORACLE STATUS IS... -> Daemon is running! Reply : Success:

Appendix B

Check Call Processing

This procedure verifies that call processing is functioning without error. The billing record verification is accomplished by making a sample phone call and verify the billing record is collected correctly.

# From EMS side A

Step 1   Log in as CLI user.

Step 2   Make a new phone call on the system. Verify that you have two-way voice communication. Then hang up both phones.

Step 3   CLI> report billing-record tail=1;

.. CALLTYPE=TOLL SIGSTARTTIME=2004-05-03 17:05:21 SIGSTOPTIME=2004-05-03 17:05:35 CALLELAPSEDTIME=00:00:00 INTERCONNECTELAPSEDTIME=00:00:00 ORIGNUMBER=4692551015 TERMNUMBER=4692551016 CHARGENUMBER=4692551015 DIALEDDIGITS=9 4692551016# 5241 ACCOUNTCODE=5241 CALLTERMINATIONCAUSE=NORMAL_CALL_CLEARING ORIGSIGNALINGTYPE=0 TERMSIGNALINGTYPE=0 ORIGTRUNKNUMBER=0 TERMTRUNKNUMBER=0 OUTGOINGTRUNKNUMBER=0 ORIGCIRCUITID=0 TERMCIRCUITID=0 ORIGQOSTIME=2004-05-03 17:05:35 ORIGQOSPACKETSSENT=0 ORIGQOSPACKETSRECD=7040877 ORIGQOSOCTETSSENT=0 ORIGQOSOCTETSRECD=1868853041 ORIGQOSPACKETSLOST=805306368 ORIGQOSJITTER=0 ORIGQOSAVGLATENCY=0 TERMQOSTIME=2004-05-03 17:05:35 TERMQOSPACKETSSENT=0 TERMQOSPACKETSRECD=7040877 TERMQOSOCTETSSENT=0 TERMQOSOCTETSRECD=1868853041 TERMQOSPACKETSLOST=805306368 TERMQOSJITTER=0 TERMQOSAVGLATENCY=0 PACKETIZATIONTIME=0 SILENCESUPPRESSION=1 ECHOCANCELLATION=0 CODECTYPE=PCMU CONNECTIONTYPE=IP OPERATORINVOLVED=0 CASUALCALL=0 INTERSTATEINDICATOR=0 OVERALLCORRELATIONID=CA14633 TIMERINDICATOR=0 RECORDTYPE=NORMAL RECORD CALLAGENTID=CA146 ORIGPOPTIMEZONE=CDT ORIGTYPE=ON NET TERMTYPE=ON NET NASERRORCODE=0 NASDLCXREASON=0 ORIGPOPID=69 TERMPOPID=69 TERMPOPTIMEZONE=CDT DIALPLANID=cdp1 CALLINGPARTYCATEGORY=Ordinary Subscriber CALLEDPARTYINDICATOR=No Indication CALLEDPARTYPORTEDIN=No CALLINGPARTYPORTEDIN=No BILLINGRATEINDICATOR=None ORIGENDPOINTADDR=c2421-227-142.ipclab.cisco.com Reply : Success: Entry 1 of 1 returned from host: priems08

Step 4   Verify that the attributes in the CDR match the call just made.

Appendix C

Check Provisioning and Database

# From EMS side A

The purpose of this procedure is to verify that provisioning is functioning without error. The following commands will add a "dummy" carrier then delete it.

Step 1   Log in as CLI user.

Step 2   CLI> add carrier id=8080;

Step 3   CLI> show carrier id=8080;

Step 4   CLI> delete carrier id=8080; 

Step 5   CLI> show carrier id=8080;

- Verify message is: Database is void of entries.

# Check transaction queue

In this task, you will verify that the OAMP transaction queue status. The queue should be empty.

Step 1   CLI> show transaction-queue;

- Verify there is no entry shown. You should get following reply back:

Reply : Success: Database is void of entries.

- If the queue is not empty, wait for the queue to empty. If the problem persists, contact Cisco Support.

# Perform database audit

In this task, you will perform a full database audit and correct any errors, if necessary.

Step 1   CLI> audit database type=full;

Step 2   Check the audit report and verify there is no discrepancy or errors. If errors are found, please try to correct them. If you are unable to correct, please contact Cisco Support.

Appendix D

Check Alarm Status

The purpose of this procedure is to verify that there are no outstanding major/critical alarms.

# From EMS side A

Step 1   Log in as CLI user.

Step 2   CLI> show alarm

- The system responds with all current alarms, which must be verified or cleared before proceeding with next step.

|  | Tip Use the following command information for reference material ONLY. |
| --- | --- |

Step 3   To monitor system alarm continuously.

CLI> subscribe alarm-report severity=all; type=all;

|  | Valid severity: MINOR, MAJOR, CRITICAL, ALL Valid types: CALLP, CONFIG, DATABASE, MAINTENANCE, OSS, SECURITY, SIGNALING, STATISTICS, BILLING, ALL, SYSTEM, AUDIT |
| --- | --- |

Step 4   System will display alarms if alarm is reported.

<------------------- START ALARM REPORT --------------------> TIMESTAMP: 20040503174759 DESCRIPTION: General MGCP Signaling Error between MGW and CA. TYPE & NUMBER: SIGNALING (79) SEVERITY: MAJOR ALARM-STATUS: OFF ORIGIN: MGA.PRIMARY.CA146 COMPONENT-ID: null ENTITY NAME: S0/DS1-0/1@64.101.150.181:5555 GENERAL CONTEXT: MGW_TGW SPECIFC CONTEXT: NA FAILURE CONTEXT: NA <------------------- END ALARM REPORT ---------------------->

Step 5   To stop monitoring system alarm.

CLI> unsubscribe alarm-report severity=all; type=all;

Step 6   CLI> exit

Appendix E

Check Oracle Database Replication and Error Correction

Perform the following steps on the Active EMS side A to check the Oracle database and replication status.

# Check Oracle DB replication status

# From EMS side A

Step 1   Log in as root.

Step 2   Log in as oracle.

<hostname># su – oracle

Step 3   Enter the command to check replication status and compare contents of tables on the side A and side B EMS databases:

<hostname>$ dbadm –C rep

Step 4   Verify that “Deferror is empty?” is “YES”.

OPTICAL1::Deftrandest is empty?           YES

OPTICAL1::dba_repcatlog is empty?       YES

OPTICAL1::Deferror is empty?              YES (Make sure it is “YES”

OPTICAL1::Deftran is empty?                  YES

OPTICAL1::Has no broken job?               YES

OPTICAL1::JQ Lock is empty?                YES

OPTICAL2::Deftrandest is empty?          YES

OPTICAL2::dba_repcatlog is empty?      YES

OPTICAL2::Deferror is empty?             YES (Make sure it is “YES”

OPTICAL2::Deftran is empty?                YES

OPTICAL2::Has no broken job?              YES

OPTICAL2::JQ Lock is empty?               YES

Step 5   If the “Deferror is empty?” is “NO”, please try to correct the error using steps in “Correct replication error” below. If you are unable to clear the error or if any of the individual steps fails, please contact Cisco Support.

# Correct replication error

|  | Note You must run the following steps on standby EMS side B first, then on active EMS side A. |
| --- | --- |

# From EMS Side B

Step 1   Log in as root

Step 2   <hostname># su – oracle

Step 3   <hostname>$ dbadm –C db

Step 4   For each table that is out of sync, please run the following step:

<hostname>$ dbadm -A copy -o <OWNER> -t <TABEL NAME>

- Enter “y” to continue

- Please contact Cisco Support if the above command fails.

Step 5   <hostname>$ dbadm –A truncate_deferror

- Enter “y” to continue

# From EMS Side A

Step 1   <hostname>$ dbadm –A truncate_deferror

- Enter “y” to continue

Step 2   Re-verify that “Deferror is empty?” is “YES” and none of tables is out of sync.

<hostname>$dbadm –C db

OPTICAL1::Deftrandest is empty?           YES

OPTICAL1::dba_repcatlog is empty?       YES

OPTICAL1::Deferror is empty?              YES ( Make sure it is “YES”

OPTICAL1::Deftran is empty?                  YES

OPTICAL1::Has no broken job?               YES

OPTICAL1::JQ Lock is empty?                YES

OPTICAL2::Deftrandest is empty?          YES

OPTICAL2::dba_repcatlog is empty?      YES

OPTICAL2::Deferror is empty?             YES ( Make sure it is “YES”

OPTICAL2::Deftran is empty?                YES

OPTICAL2::Has no broken job?              YES

OPTICAL2::JQ Lock is empty?               YES

Appendix F

Backout Procedure for Side B Systems

# Introduction

This procedure allows you to back out of the upgrade procedure if any verification checks (in "Verify Call/System Status" section) failed. This procedure is intended for the scenario in which the side B systems have been upgraded to the new load, while the side A systems are still at the previous load. The procedure will back out the side B systems to the previous load.

This backout procedure will:

- Restore the side A systems to active mode without making any changes to it

- Revert to the previous application load on the side B systems

- Restart the side B systems in standby mode

- Verify that the system is functioning properly with the previous load

|  | Note In addition to performing this backout procedure, you should contact Cisco Support when you are ready to retry the upgrade procedure. |
| --- | --- |

The flow for this procedure is shown in Figure F-1.

Figure F-1   Flow of Backout Procedure— Side B Only

# Task 1: Force side A CA/FS to active

This procedure will force the side A systems to forced active state, and the side B systems to forced standby state.

|  | Note In the commands below, "xxx", "yyy" or "zzz" is the instance for the process on your system. |
| --- | --- |

# From EMS side B

Step 1   Log in as CLI user.

Step 2   CLI> control call-agent id=CAxxx; target-state=active-standby;

Step 3   CLI> control feature-server id=FSPTCzzz; target-state=active-standby;

Step 4   CLI> control feature-server id=FSAINyyy; target-state=active-standby;

Step 5   CLI> exit

# Task 2: SFTP billing records to a mediation device

# From EMS side B

Step 1   Log in as root

Step 2   <hostname># platform stop

- Answer “y” if prompt for terminating the application platform

Step 3   <hostname># cd /opt/bms/ftp/billing

Step 4   <hostname># ls

Step 5   If there are files listed, then SFTP the files to a mediation device on the network and remove the files from the /opt/bms/ftp/billing directory

# Task 3: Sync DB usage

# From EMS side A

In this task, you will sync db-usage between two releases.

Step 1   Log in as root

Step 2   <hostname># su – oracle

Step 3   <hostname>$ java dba.adm.DBUsage –sync

- Verify Number of tables “unable-to-sync” is 0.

Step 4   <hostname>$ exit

# Task 4: Stop applications and shutdown side B systems

# From EMS side B

Step 1   Log in as root.

Step 2   <hostname># sync; sync

Step 3   <hostname># shutdown –i5 –g0 –y

# From CA/FS side B

Step 1   Log in as root.

Step 2   <hostname># platform stop all

Step 3   <hostname># sync; sync

Step 4   <hostname># shutdown –i5 –g0 –y

# Task 5: Restore side B systems to the old release

# From CA/FS side B

Step 1   Power off the machine

Step 2   Remove disk0 from slot 0 off the machine

Step 3   Place disk labeled “Release 4.4.0 CA/FS side B disk0” in slot 0

Step 4   Power on the machine

- For a Netra 1280 machine, please execute the following command from console:

<lom>poweron

- For other type of hardware, please use the power button to turn on the power.

Step 5   Log in as root.

Step 6   <hostname># platform start

Step 7   <hostname># mv /etc/rc3.d/_S99platform /etc/rc3.d/S99platform

# From EMS side B

Step 1   Power off the machine

Step 2   Remove disk0 from slot 0 off the machine

Step 3   Place disk labeled “Release 4.4.0 EMS side B disk0” in slot 0

Step 4   Power on the machine

- For a Netra 1280 machine, please execute the following command from console:

<lom>poweron

- For other type of hardware, please use the power button to turn on the power.

Step 5   Log in as root.

Step 6   <hostname># platform start

Step 7  <hostname># mv /etc/rc3.d/_S99platform /etc/rc3.d/S99platform

# Task 6: Restore EMS mate communication

In this task, you will restore the OMS Hub communication from EMS side A to side B.

# From EMS side A

Step 1   Log in as root

Step 2   <hostname># /opt/ems/utils/updMgr.sh –restore_hub

Step 3   <hostname># nodestat

- Verify OMS Hub mate port status is established.

- Verify HUB communication from EMS side A to CA/FS side B is established.

# Task 7: Switchover activity to EMS side B

# From Active EMS side A

Step 1   Log in as CLI user.

Step 2   CLI> control bdms id=BDMS01; target-state=forced-standby-active;

Step 3   CLI> control element-manager id=EM01; target-state=forced-standby-active;

Step 4    CLI Log in session will be terminated when switchover is completed.

# Task 8: Enable Oracle DB replication on EMS side A

# From EMS side A

Step 1   Log in as Oracle user:

<hostname># su - oracle

<hostname>$ cd /opt/oracle/admin/utl

Step2   Restore Oracle DB replication:

<hostname>$ rep_toggle –s optical1 –t set_duplex

Answer “y” when prompt

Answer “y” again when prompt

Step 3   <hostname>$ exit

Step 4   Restart applications to connect to Oracle DB in duplex mode:

<hostname># platform stop all

<hostname># platform start

# Task 9: Synchronize handset provisioning data

# From EMS side B

|  | Note In the commands below, "xxx", "yyy" or "zzz" is the instance for the process on your system. |
| --- | --- |

Step 1   Log in as ciscouser (password: ciscosupport)

Step 2   CLI> sync termination master=CAxxx; target=EMS;

- Verify the transaction is executed successfully.

Step 3   CLI> sync sc1d master=FSPTCzzz; target=EMS;

- Verify the transaction is executed successfully

Step 4   CLI> sync sc2d master=FSPTCzzz; target=EMS;

- Verify the transaction is executed successfully

Step 5   CLI> sync sle master=FSPTCzzz; target=EMS;

- Verify the transaction is executed successfully

Step 6   CLI> sync subscriber-feature-data master=FSPTCzzz; target=EMS;

- Verify the transaction is executed successfully

Step 7   CLI> exit

# Task 10: Switchover activity from EMS side B to EMS side A

# From EMS side B

Step 1   Log in as CLI user.

Step 2   CLI> control bdms id=BDMS01; target-state=forced-active-standby;

Step 3   CLI> control element-manager id=EM01; target-state=forced-active-standby;

Step 4    CLI Log in session will be terminated when switchover is completed.

# Task 11: Restore system to normal mode

# From EMS side A

Step 1   Log in as CLI user.

Step 2   CLI> control feature-server id=FSPTCzzz; target-state=normal;

Step 3   CLI> control feature-server id=FSAINyyy; target-state=normal;

Step 4   CLI> control call_agent id=CAxxx; target-state=normal;

Step 5   CLI> control bdms id=BDMS01; target-state=normal;

Step 6   CLI> control element-manager id=EM01; target-state=normal;

Step 7   CLI> exit

# Task 12: Verify system status

Verify that the system is operating properly before you leave the site.

Step 1   Verify that the side A systems are in the active state. Use Appendix A for this procedure.

Step 2   Verify that call processing is working without error. Use Appendix B for this procedure.

Step 3   Verify that provisioning is operational from CLI command line, and verify database. Use Appendix C for this procedure.

Step 4   Verify that there are no outstanding major or critical alarms. Use Appendix D for this procedure.

Step 5   Use Appendix E to verify that Oracle database and replication functions are working properly.

Step 6   If you answered NO to any of the above questions (Step 1 through Step 5), Contact Cisco Support for assistance.

You have completed the side B of Cisco BTS 10200 system fallback process successfully.

Appendix G

System Backout Procedure

# Introduction

This procedure allows you to back out of the upgrade procedure if any verification checks (in "Verify system status" section) failed. This procedure is intended for the scenario in which both the side A and side B systems have been upgraded to the new load. The procedure will back out the entire system to the previous load.

This backout procedure will:

- Revert to the previous application load on the side A systems

- Restart the side A systems and place it in active mode

- Revert to the previous application load on the side B systems

- Restart the side B systems and place it in active mode

- Verify that the system is functioning properly with the previous load

|  | Note In addition to performing this backout procedure, you should contact Cisco Support when you are ready to retry the upgrade procedure. |
| --- | --- |

# Task 1: Disable Oracle DB replication on EMS side B

# From Active EMS

Step 1   Log in as CLI user.

Step 2   CLI> control bdms id=BDMS01; target-state=active-standby;

Step 3   CLI> control element-manager id=EM01; target-state=active-standby;

Step 4   CLI> exit

# From EMS side B

Step 1   Log in as Oracle user:

<hostname># su – oracle

<hostname>$ cd /opt/oracle/admin/utl

Step 2   Set Oracle DB to simplex mode:

<hostname>$ rep_toggle –s optical2 –t set_simplex

- Answer “y” when prompt

- Answer “y” again when prompt

Step 3   <hostname>$ exit

Step 4   Restart applications to connect to Oracle DB in simplex mode:

<hostname># platform stop all

<hostname># platform start

# Task 2: Inhibit EMS mate communication

In this task, you will isolate the OMS Hub on EMS side B from talking to CA/FS side A.

# From EMS side B

Step 1   Log in as root

Step 2   <hostname># /opt/ems/utils/updMgr.sh –split_hub

Step 3   <hostname># nodestat

- Verify there is no HUB communication from EMS side B to CA/FS side A.

# Task 3: Force side B systems to active

This procedure will force the side B systems to go active.

|  | Note In the commands below, "xxx", "yyy" or "zzz" is the instance for the process on your system. |
| --- | --- |

# From EMS side A

Step 1   Log in as CLI user.

Step 2   CLI> control call-agent id=CAxxx; target-state=standby-active;

Step 3   CLI> control feature-server id=FSPTCzzz; target-state=standby-active;

Step 4   CLI> control feature-server id=FSAINyyy; target-state=standby-active;

Step 5   CLI> control bdms id=BDMS01; target-state=standby-active;

Step 6   CLI> control element-manager id=EM01; target-state=standby-active;

Step 7   CLI session will terminate when the last CLI command completes.

# Task 4: SFTP billing records to a mediation device

# From EMS side A

Step 1   Log in as root

Step 2   <hostname># cd /opt/bms/ftp/billing

Step 3   <hostname># ls

Step 4   If there are files listed, then SFTP the files to a mediation device on the network and remove the files from the /opt/bms/ftp/billing directory

# Task 5: Stop applications

# From EMS side A

Step 1   Log in as root.

Step 2   <hostname># platform stop all

Step 3   <hostname># sync; sync

Step 4   <hostname># shutdown –i5 –g0 –y

# From CA/FS side A

Step 1   Log in as root.

Step 2   <hostname># platform stop all

Step 3   <hostname># sync; sync

Step 4   <hostname># shutdown –i5 –g0 –y

# Task 6: Restore side A systems to the old release

# From CA/FS side A

Step 1   Power off the machine

Step 2   Remove disk0 from slot 0 off the machine

Step 3   Place disk labeled “Release 4.4.0 CA/FS side A disk0” in slot 0

Step 4   Power on the machine

- For a Netra 1280 machine, please execute the following command from console:

<lom>poweron

- For other type of hardware, please use the power button to turn on the power.

Step 5   Log in as root.

Step 6   <hostname># platform start

#### Step 7   <hostname># mv /etc/rc3.d/_S99platform /etc/rc3.d/S99platform

# From EMS side A

Step 1   Power off the machine

Step 2   Remove disk0 from slot 0 off the machine

Step 3   Place disk labeled “Release 4.4.0 EMS side A disk0” in slot 0

Step 4   Power on the machine

- For a Netra 1280 machine, please execute the following command from console:

<lom>poweron

- For other type of hardware, please use the power button to turn on the power.

Step 5   Log in as root.

Step 6   <hostname># /opt/ems/utils/updMgr.sh –split_hub

Step 7   <hostname># /etc/rc2.d/S75cron stop

Step 8   <hostname># platform start –i oracle

Step 9   Log in as Oracle user.

<hostname># su – oracle

<hostname>$ cd /opt/oracle/admin/utl

Step 10   Change Oracle DB to simplex mode:

<hostname>$ rep_toggle –s optical1 –t set_simplex

- Answer “y” when prompt

- Answer “y” again when prompt

Step 11   <hostname>$ exit

Step 12   <hostname># mv /etc/rc3.d/_S99platform /etc/rc3.d/S99platform

# Task 7: Stop EMS side B billing application

# From EMS side B

Step 1   Log in as root.

Step 2   <hostname># platform stop -i BDMS01

- Answer “y” when prompt for confirmation

# Task 8: Start EMS side A applications

# From EMS side A

Step 1   <hostname># platform start

Step 2   <hostname># /etc/rc2.d/S75cron start

# Task 9: To continue fallback process, please follow Appendix F.

You have completed the Cisco BTS 10200 system fallback process successfully

Appendix H

# Preparing Disks for Upgrade

This software upgrade will need 8 disks: 2 for each machine. Each set of 2 disks must have the same model number in order for disk mirroring to work.

The NIDS information required for disk preparation must be different from that used on the system to be upgraded.

# Task 1: Locate and label the disks

# Label disks for EMS Side A

Locate two new disk drives identical to the machine to be upgraded and label the first disk drive as “Release 4.5.0 EMS side A disk0, 1” and the second disk drive as “Release 4.5.0 EMS side A disk0, 2”.  Please follow the steps below to prepare the two disk drives. The second disk drive will be used as the backup in case the first disk drive goes bad.

# Label disks for EMS Side B

Locate two new disk drives identical to the machine to be upgraded and label the first disk drive as “Release 4.5.0 EMS side B disk0, 1” and the second disk drive as “Release 4.5.0 EMS side B disk0, 2”.  Please follow the steps below to prepare the two disk drives. The second disk drive will be used as the backup in case the first disk drive goes bad.

# Label disks for CA/FS Side A

Locate two new disk drives identical to the machine to be upgraded and label the first disk drive as “Release 4.5.0 CA/FS side A disk0, 1” and the second disk drive as “Release 4.5.0 CA/FS side A disk0, 2”.  Please follow the steps below to prepare the two disk drives. The second disk drive will be used as the backup in case the first disk drive goes bad.

# Label disks for CA/FS Side B

Locate two new disk drives identical to the machine to be upgraded and label the first disk drive as “Release 4.5.0 CA/FS side B disk0, 1” and the second disk drive as “Release 4.5.0 CA/FS side B disk0, 2”.  Please follow the steps below to prepare the two disk drives. The second disk drive will be used as the backup in case the first disk drive goes bad.

# Task 2: Disk slot lay out

- Netra 240 disk slot lay out:

| Disk 0 | Disk 1 |
| --- | --- |
| DVD-ROM |  |

- SunFire V240 disk slot lay out:

| Disk 2 | Disk 3 |  |
| --- | --- | --- |
| Disk 0 | Disk 1 | DVD-ROM |

- SunFire V440 disk slot lay out:

| Disk 3 | DVD-ROM |
| --- | --- |
| Disk 2 |  |
| Disk 1 |  |
| Disk 0 |  |

- Netra 1280 disk slot lay out:

|  | DVD-ROM |
| --- | --- |
|  | Disk 1 |
|  | Disk 0 |

- Netra 20 disk slot lay out:

| D I S K 0 | D I S K 1 |  | DVD ROM |
| --- | --- | --- | --- |

- Continuous Hardware disk slot lay out:

| CD-ROM | Disk 0 | Disk 2 |
| --- | --- | --- |
|  | Disk 1 | Disk 3 |

# Task 3: Construct opticall.cfg

Step 1   Get a copy of Cisco BTS 10200 Software Release 4.5.0 Network Information Data Sheets (NIDS)

Step 2   Fill in NIDS information for the BTS system used for disk preparation. The NIDS information must be different from that used on the system to be upgraded.

Step 3   Get a copy of Cisco BTS 10200 Software Release 4.5.0 opticall.cfg

Step 4   Fill in parameters in opticall.cfg from NIDS and placed it on a server which will be accessible from the BTS system used for disk preparation.

# Task 4: Disk preparation

Repeat the steps in Task 4 to prepare the second disk.

Note:  Please perform disk preparation for each machine in parallel.

# For both EMS side A and B

Step 1   Locate a system with the identical hardware as the machine to be upgraded

Step 2   Put disk to disk slot 0

Step 3   Jumpstart the machine with Solaris 10 OS

Step 4   Configure the machine with 4/2 network configuration

Step 5   Stage Cisco BTS 10200 Software Release 4.5.0 to the /opt/Build directory.

Step 6   ftp opticall.cfg from the server (where the file was placed in Task 3) and place it under /etc directory.

<hostname># /opt/Build/checkCFG

  - To verify the information entered are free of errors.

Note: The EMS side A and side B installation must be started in parallel.

Step 7   Install Cisco BTS 10200 Software Release 4.5.0 application software.

<hostname># /opt/Build/install.sh

  - Answer “y” when prompt. This installation process could take up to 1hour and 30 minutes.

  - Answer "y” when prompt for “reboot”

  - Wait for the system to boot up. Then Log in as root

Step 8   <hostname># mv /etc/rc3.d/S99platform /etc/rc3.d/_S99platform

Step 9   Remove all network interface configuration information from the machine:

<hostname>#  \rm /etc/hostname.*

Step 10   Shutdown the system

<hostname># platform stop all

<hostname># sync;sync

<hostname># shutdown –i5 –g0 -y

Step 11   Power off the machine and remove the disks to be used for upgrade.

# For both CA/FS side A and B

Step 1   Locate a system with the identical hardware as the machine to be upgraded

Step 2   Put disk to disk slot 0

Step 3   Jumpstart the machine with Solaris 10 OS

Step 4   Configure the machine with 4/2 network configuration

Step 5   Stage Cisco BTS 10200 Software Release 4.5.0 to the /opt/Build directory.

Step 6   ftp opticall.cfg from the server (where the file was placed in Task 3) and place it under /etc directory.

Step 7   Install BTSbase, BTSinst, BTSossh and BTShard packages:

- <hostname># cd /opt/Build

- <hostname># pkgadd –d . BTSbase

- Answer “y” when prompt

- <hostname># pkgadd –d . BTSinst

- Answer “y” when prompt

- <hostname># pkgadd –d . BTSossh

- Answer “y” when prompt

- <hostname># pkgadd –d . BTShard

- Answer “y” when prompt

- <hostname># cd /etc/rc3.d

- <hostname># mv S99platform _S99platform

- <hostname># shutdown –i6 –g0 -y

- Wait for system to boot up and login as root.

Step 8   Remove all network interface configuration information from the machine:

<hostname>#  \rm /etc/hostname.*

Step 9   Update version information:

<hostname># cd /opt/ems/utils

<hostname># echo “900-04.04.00.V00” > Version

Step 10   Shutdown the system

<hostname>#  shutdown –i5 –g0 -y

Step 11   Power off the machine and remove the disks to be used for upgrade.

Appendix I

# Disk Mirroring after Upgrade

This software upgrade will need 4 new disks: 1 for each machine. Each set of 2 disks must have the same model number in order for disk mirroring to work.

## Configuring the Primary Element Management System

To configure the primary EMS, complete the following steps:

Step 1    Login as root.

Step 2    Change directory by entering the following command:

cd /opt/setup

Step 3   Run the setlogic_EMS.sh script to set up the interfaces by entering the following command:

./setlogic_EMS.sh

Step 4    Verify that the /etc/netmasks and /etc/hosts files have the correct values by comparing them to the values in the NIDS.

Step 5    Set up the mirror for the EMS by entering the following command:

./setup_mirror_ems

Note Do not reboot your system if an error occurs. You must fix the error before moving to the next step.

Step 6    Set up the transparent metadevice (transmeta) for the EMS by entering the following command:

./setup_mirror_trans

Step 7    Reboot by entering the following command:

reboot -- -r

Note Wait for the boot before continuing. Then log in to the EMS of the side in which you are working.

Step 8    Log in to the primary EMS as root.

root

Step 9    Change directory by entering the following command:

cd /opt/setup

Step 10    Synchronize the disk by entering the following command:

./sync_mirror

Note Wait for the disks to synchronize before continuing. The synchronization can be verified by running the Resync_status command from the /opt/utils directory. The display will show the resyncing in progress and report resync completion.

Step 11    Exit the primary EMS.

## Configuring the Secondary Element Management System

To configure the secondary EMS, complete the following steps:

Step 1    Login as root.

Step 2    Navigate to the /opt/setup directory by entering the following command:

cd /opt/setup

Step 3    Run the setlogic_EMS.sh script to set up the interfaces.

./setlogic_EMS.sh

Step 4    Verify that the /etc/netmask and /etc/hosts commands have the correct values.

Step 5    Set up a mirror for the EMS by entering the following command:

./setup_mirror_ems

Note  Do not reboot your system if an error occurs. You must fix the error before moving to the next step.

Step 6    Set up the transparent metadevice (transmeta) for the EMS by entering the following command:

./setup_mirror_trans

Step 7    Reboot your system by entering the following command:

reboot -- -r

Note Wait for the boot to finish before continuing. Then log in to the EMS for the side on which you are working.

Step 8    Log in to the secondary EMS as root by entering the following command:

root

Step 9    Change directory by entering the following command:

cd /opt/setup

Step 10    Synchronize the disk by entering the following command:

./sync_mirror

Step 11    Exit the secondary EMS.

## Configuring the Primary Call Agent and Feature Server Installation

To configure the primary CA and FS, complete the following steps:

Step 1    Login as root.

Step 2    Change directories by entering the following command:

cd /opt/setup

Step 3    Run the ./setlogic_CA.sh script to set up the interfaces.

./setlogic_CA.sh

Step 4    Verify that the /etc/netmask, /etc/defaultrouter, and /etc/hosts files have the correct values by comparing them to the values in the NIDS. Make sure all three match the NIDS.

Step 5    Set up the mirror for the CA/FS and watch for errors by entering the following command:

./setup_mirror_ca

Note  Do not reboot your system if an error occurs. You must fix the error before moving to the next step.

Step 6    Setup trans for the CA/FS and watch for errors by entering the following command:

./setup_trans

Step 7    Reboot your system by entering the following command:

reboot

Step 8    Log in to the primary CA as root by entering the following command:

root

Step 9    Mirror the disks as follows:

a. Change directory by entering the following command:

cd /opt/setup

b. Mirror the disks by entering the following command:

./sync_mirror

## Configuring the Secondary Call Agent and Feature Server Installation

To configure the primary CA and FS, complete the following steps:

Step 1    Login as root.

Step 2    Change directories by entering the following command:

cd /opt/setup

Step 3    Run the ./setlogic_CA.sh script to set up the interfaces.

./setlogic_CA.sh

Step 4    Verify that the /etc/netmask, and /etc/hosts files have the correct values by comparing them to the values in the NIDS. Make sure all three match the NIDS.

Step 5    Set up the mirror for the CA/FS and watch for errors by entering the following command:

./setup_mirror_ca

Note  Do not reboot your system if an error occurs. You must fix the error before moving to the next step.

Step 6    Setup trans for the CA/FS and watch for errors by entering the following command:

./setup_trans

Step 7    Reboot your system by entering the following command:

reboot

Step 8    Log in to the secondary CA as root by entering the following command:

root

Step 9    Mirror the disks as follows:

a. Change directory by entering the following command:

cd /opt/setup

b. Mirror the disks by entering the following command:

./sync_mirror

Appendix J

CORBA Installation

This procedure describes how to install the Common Object Request Broker Architecture (CORBA) application on Element Management System (EMS) of the Cisco BTS 10200 Softswitch.

Note This installation process is used for both side A and side B EMS.

Caution This CORBA installation will remove existing CORBA application on EMS machines. Once you have executed this procedure, there is no backout. Do not start this procedure until you have proper authorization. If you have questions, please contact Cisco Support.

# Task 1: Open Unix Shell on EMS

Perform these steps to open a Unix shell on EMS.

Step 1   Ensure that your local PC or workstation has connectivity via TCP/IP to communicate with EMS units.

Step 2   Open a Unix shell or a XTerm window.

Note If you are unable to open a Xterm window, please contact you system administrator immediately.

# Task 2: Install OpenORB CORBA Application

### Remove Installed OpenORB Application

Step 1   Log in as root to EMS

Step 2   Enter the following command to remove the existing OpenORB package:

<hostname># pkgrm BTScis

- Respond with a “y” when prompted

<hostname># pkgrm BTSoorb

- Respond with a “y” when prompted

Step 3   Enter the following command to verify that the CORBA application is removed:

<hostname># pgrep cis3

The system will respond by displaying no data, or by displaying an error message. This verifies that the CORBA application is removed.

### Install OpenORB Packages

The CORBA application files are available for installation once the Cisco BTS 10200 Softswitch is installed.

Step 1   Log in as root to EMS

Step 2   <hostname># cd /opt/Build

Step 3   <hostname># cis-install.sh

You will get the following response, please answer appropriately:

The NameService & CIS modules listen on a specific host interface.

***WARNING*** This host name or IP address MUST resolve on the CORBA

client machine in the OSS. Otherwise, communication failures may occur.

Enter the host name or IP address [ <hostname> ]:

Step 4   If you are running EPOM or you network does not support SSLIOP (secure CORBA protocol), please answer “n”. Otherwise, answer “y” (default).

Should SSLIOP be enabled [ Y ]:

Step 5   The system will give several prompts before and during the installation process. Some prompts are repeated. Respond with a “y” when prompted.

Step 6   It will take about 5-8 minutes for the installation to complete.

Step 7   Verify CORBA Application is running On EMS:

<hostname># pgrep ins3

Note System will respond by displaying the Name Service process ID, which is a number between 2 and 32,000 assigned by the system during CORBA installation. By displaying this ID, the system confirms that the ins3 process was found and is running.

<hostname># pgrep cis3

Note The system will respond by displaying the cis3 process ID, which is a number between 2 and 32,000 assigned by the system during CORBA installation. By displaying this ID, the system confirms that the cis3 process was found and is running.

Step 8   If you do not receive both of the responses described in Step 7, or if you experience any verification problems, do not continue. Contact your system administrator. If necessary, call Cisco Support for additional technical assistance.