## Slide 1: EVPN Unifying control plane
Sudarshan Murali, Product Manager, SP Routing
Jiri Chaloupka, Technical Marketing Engineer, SP Routing

## Slide 2: Agenda
Why EVPN
EVPN Introduction & Value Proposition
EVPN Technical Overview
EVPN Components
EVPN Life of a Packet
EVPN Demo
Summary

## Slide 3
VIRTUALIZE
Speed up service creation with NFV
SIMPLIFY
Consolidate number of data plane and control plane protocols
AUTOMATE
Move network operations
from reactive to
proactive
Efficiency
Agility
Innovation
Cisco Open Network Architecture Cisco Innovations – Simplify, Automate, Virtualize
Notes: Cloud-Scale Networking helps pave the path to central office transformation by focusing on several key tenets:
- Simplify – by consolidating the number of data and control plane protocols
- Automate – by making network operations more proactive from reactive
- Virtualize – by leveraging NFV for faster service creation
This approach ultimately helps service providers drive greater efficiency, agility, and innovation from the network.

## Slide 4: Why is EVPN needed?
Legacy L2 technologies (VPLS, PBB) still rely on flooding and learning to build Layer 2 forwarding database
Network Operators have emerging needs in their network:
  Data center interconnect operation (DCI)
  Cloud and Services virtualization
  Reduce protocol stack and Simplify Network
  Integrated of Layer 2 and Layer 3 Services over the same VPN
SIMPLIFY

## Slide 5: Solving VPLS challenges for per-flow Redundancy
Existing VPLS solutions do not offer an All-Active per-flow redundancy
Looping of Traffic Flooded from PE
Duplicate Frames from Floods from the Core
MAC Flip-Flopping over Pseudowire
  E.g. Port-Channel Load-Balancing does not produce a consistent hash-value for a frame with the same source MAC (e.g. non MAC based Hash-Schemes)
PE1
PE2
PE3
PE4
CE1
CE2
Echo !
PE1
PE2
PE3
PE4
CE1
CE2
Duplicate !
M1
M1
M2
PE1
PE2
PE3
PE4
CE1
CE2
MAC Flip-Flop
M1
M2

## Slide 6: Data Center Interconnect requirements
not fully addressed by current L2VPN technologies
Per-Flow Redundancy and Load Balancing
Simplified Provisioning and Operation
Optimal Forwarding
Fast Convergence
MAC Address Scalability
EVPN with a choice of data plane encapsulation (MPLS, VxLAN, PBB) is the designed to address these requirements.
Notes: Short and relevant: Stay focused on what your audience cares about. Think about what you want them to know, feel and do. Then, say what you need to say and no more.
Bold and human: Be confident in your ideas and in the words you use to express them. Use clear, natural language to connect with your audience and make your message stick.
Show what’s possible and make it real: We call this Dreaming and Doing. When we do it right it's powerful, inspiring, convincing and persuasive.
To learn more, download the brand language guidelines: https://cisco.jiveon.com/docs/DOC-660269

## Slide 7: EVPN Next generation network services
EVPN
ELINE
ELAN
ETREE
L3 VPN
DC Fabric
DCI
VPWS
VPLS
P2MP VPLS
RFC 2547
VXLAN
VPLS / L3 VPN
DC
Agg
Core
Access
Agg
SR
SR-TE
MPLS
VXLAN
E2E control and automation across domains
Single service for any application
EVPN
Reduced OpEx:
Integrated L2 & L3 service, any application: faster time to market, certification
E2E control and automation
Optimized CapEx:
- Open Standards & Multi-vendor
Active-Active multi-homing
Enhanced load balancing
Increased Customer Value
Inter-domain SLA, faster convergence
Better stability: no flood
Granular policy control
Notes: xEVPN family introduces next generation solutions for Ethernet services
  BGP control-plane for Ethernet Segment and MAC distribution and learning over MPLS core
  Same principles and operational experience of IP VPNs

## Slide 8: EVPN: Unifying control plane
Control Plane
Data Plane
MPLS
RFC-7432
NVO
evpn-overlay
PBB
RFC-7623
EVPN MP-BGP
EVPN over MPLS
(E-LAN service)
All-active Multi-homing
SR/SR-TE as underlay
EVPN-VPWS
(E-Line service)
EVPN over NVO Tunnels
(VxLAN, NVGRE)
Data Center Fabric Encapsulation
Integrated L2/L3 services DCI
Overlays over IP networks
PBB Encapsulation
for CMAC scalability
MPLS as underlay
All-active Multi-homing
BMACs advertisement
VPWS
evpn-vpws
P2P services
MPLS as underlay
All-active Multi-homing
Flexible xconnect services

## Slide 9: Ethernet VPN (EVPN) - Overview
Single active multi-homing
All active multi-homing
MAC Routing: Control plane (BGP) advertise the learnt MACs from CE
Data Plane: IP or MPLS
Network Efficiency
Common L2/L3 VPN Operational Mode
Consolidated VPN service with x-EVPN
PE1
PE2
PE3
PE4
CE1
C-MAC:M1
CE3
Notes: Network inefficiency
  Flood-and-learn, broadcast storm
  Active/Standby forwarding, can’t achieve per-flow load balancing like L3 service
  Signaling for pseudowire, not scalable
Different operational models
  L3VPN and L2VPN works in different way
  Different type of the L2VPN: manual configuration, BGP auto-discovery, BGP signaling, LDP signaling, etc
  MPLS data plane vs. IP data plane
Lack of programmability and policy control
  MAC learning happen at data plane
  Can’t have policy control per MAC address
  Difficult to be programmable

## Slide 10: Ethernet VPN
Next generation solution for Ethernet multipoint (E-LAN) services
PEs run Multi-Protocol BGP to advertise & learn Customer MAC addresses (C-MACs) over Core
  Same operational principles of L3VPN
Learning on PE Access Circuits via data-plane transparent learning
No pseudowire full-mesh required
  Unicast: use MP2P tunnels
  Multicast: use ingress replication over MP2P tunnels or use LSM
Standardized at IETF – RFC 7432
Highlights
PE1
PE2
PE3
PE4
CE1
C-MAC:M1
CE3
C-MAC:M3
VID 100
SMAC: M1
DMAC: F.F.F
BGP MAC adv. Route
EVPN NLRI
MAC M1 via PE1
Data-plane address learning from Access
Control-plane address advertisement / learning over Core

## Slide 11: EVPN - Concept
Ethernet Segment
Represents a ‘site’ connected to one or more PEs
Uniquely identified by a 10-byte global Ethernet Segment Identifier (ESI)
Could be a single device or an entire network
Single-Homed Device (SHD)
Multi-Homed Device (MHD)
Single-Homed Network (SHN)
Multi-Homed Network (MHN)
BGP Routes
EVPN and PBB-EVPN define a single new BGP NLRI used to carry all EVPN routes
NLRI has a new SAFI (70)
Routes serve control plane purposes, including:
MAC / IP address reachability
MAC mass withdrawal
Split-Horizon label adv.
Aliasing
Multicast endpoint discovery
Redundancy group discovery
Designated forwarder election
EVPN Instance (EVI)
EVI spans all PEs participating in an EVPN
MAC-VRF: A VRF table for MACs on a PE
Encompass one or more bridge-domains, depending on service interface type
  Port-based
  VLAN-based (shown above)
  VLAN-bundling
  VLAN aware bundling (NEW)
BGP Route Attributes
New BGP extended communities defined
Expand information carried in BGP routes, including:
MAC address moves
C-MAC flush notification
Redundancy mode
MAC / IP bindings of a GW
Split-horizon label encoding
PE
BD
BD
MAC VRF
MAC VRF
SHD
MHD
ESI1
ESI2
Extended Communities
ESI MPLS Label
ES-Import
MAC Mobility
Default Gateway
Router’s MAC
Route Types
[1] Ethernet Auto-Discovery (AD) Route
[2] MAC Advertisement Route
[3] Inclusive Multicast Route
[4] Ethernet Segment Route
(5) IP Prefix Advertisement Route
PE1
PE2
CE1
CE2

## Slide 12: Ethernet Segment
Ethernet Segment is a ‘site’ connected to one or more PEs.
Ethernet Segment could be a single device (i.e. CE) or an entire network.
  Single-Homed Device (SHD)
  Multi-Homed Device (MHD)
  Single-Homed Network (SHN)
  Multi-Homed Network (MHN)
Uniquely identified by global Ethernet Segment Identifier (ESI).
MHD
Definition
MPLS Core
PE
PE
CE
CE
PE
CE
CE
PE
CE
SHD
SHN
MHN

## Slide 13: EVPN BGP route type
Route type | Usage | EVPN | PBB-EVPN | EVPN VPWS
0x1 Ethernet Auto-Discovery (A-D) Route | MAC Mass-Withdraw Aliasing (load balancing) Split-Horizon “Tagged with ESI Label Extended Community” |  | NOT used | 
0x2 MAC Advertisement Route | Advertises MAC addresses /IP for VM reachability Provides MAC/IP address bindings for ARP broadcast suppression “Tagged with MAC Mobility Extended Community” |  |  | NOT used
0x3 Inclusive Multicast Route | Indicates interest of BUM traffic for attached L2 segments Multicast tunnels used to BUM frame “Tagged with PMSI tunnel attribute” (P tunnel type & ID) – RFC6514 |  |  | NOT used
0x4 Ethernet Segment Route | Auto discovery of Multi-homed Ethernet Segments, i.e. redundancy group discovery Designated Forwarder (DF) Election “Tagged with ES-Import Extended Community” |  |  | 
0x5 IP Prefix Route | Advertises IP prefix for a subnet for L3 NLRI only inter-subnet routing via EVPN address family |  |  | NOT used

## Slide 14: Next-Generation Solutions for L2VPN Solving VPLS challenges for per-flow Redundancy
Existing VPLS solutions do not offer an All-Active per-flow redundancy
Looping of Traffic Flooded from PE
Duplicate Frames from Floods from the Core
MAC Flip-Flopping over Pseudowire
  E.g. Port-Channel Load-Balancing does not produce a consistent hash-value for a frame with the same source MAC (e.g. non MAC based Hash-Schemes)
CE1
Echo !
M1
M2
PE1
PE2
PE3
PE4
CE2
CE1
M1
M2
PE1
PE2
PE3
PE4
CE2
Duplicate !
CE1
M1
M2
PE1
PE2
PE3
PE4
CE2
MAC Flip-Flop

## Slide 15: Ethernet Segment
MHD with Multi-chassis LAG
ESI is auto-discovered via LACP.
ESI is encoded using the CE’s LACP parameters:
ESI Auto-Sensing
MHN with MST
ESI is auto-discovered via MST BPDU snooping.
ESI is encoded using the IST’s root parameters:
LACP
LACP
MPLS
MPLS
MST
BPDU
BPDU
PE1
PE2
CE
PE1
PE2
CE1
CE2

## Slide 16: Split Horizon
PE advertises in BGP a split-horizon label (ESI MPLS Label) associated with each multi-homed Ethernet Segment.
Split-horizon label is only used for multi-destination frames (Unknown Unicast, Multicast & Broadcast).
When an ingress PE floods multi-destination traffic, it encodes Split-Horizon label identifying source Ethernet Segment in packet
Egress PEs use this label to perform selective split-horizon filtering over attachment circuit
For Ethernet Segments – E-VPN
Challenge:
How to prevent flooded traffic from echoing back to a multi-homed Ethernet Segment?
CE1
Echo !
M1
M2
PE1
PE2
PE3
PE4
CE2
ESI-1
ESI-2

## Slide 17: Split Horizon
Traffic received from an MPLS tunnel over core is never forwarded back to MPLS core
Similar to VPLS split-horizon filtering rule
For Core Tunnels
Challenge:
How to prevent flooded traffic from looping back over the core?
CE1
Loop!
M1
M2
PE1
PE2
PE3
PE4
CE2
ESI-1
ESI-2

## Slide 18: Designated Forwarder (DF)
PEs connected to a multi-homed Ethernet Segment discover each other via BGP
PEs then elect among themselves a Designated Forwarder responsible for forwarding flooded multi-destination frames to multi-homed Segment
DF Election granularity can be:
  Per Ethernet Segment (Single PE is the DF)
  Per EVI (E-VPN) on Ethernet Segment (Multiple DFs for load-balancing)
DF Election
Challenge:
How to prevent duplicate copies of flooded traffic from being delivered to a multi-homed Ethernet Segment?
CE1
Duplicate
M1
M2
PE1
PE2
PE3
PE4
CE2
ESI-1
ESI-2

## Slide 19: Designated Forwarder (DF)
PE1
PE2
MHD All-Active with Per-Flow Load Balancing
DF Filtering
MPLS
DF Filtering
CE1
Filtering Direction: | Core to Segment
Filtered Traffic: | Flooded multi-destination
Multi-destination Traffic
Unicast Traffic
Legend

## Slide 20: Aliasing
PEs advertise in BGP the ESIs of local multi-homed Ethernet Segments
  All-Active Redundancy Mode indicated
When PE learns MAC address on its AC, it advertises MAC in BGP along with ESI of Ethernet Segment from which MAC was learnt
Remote PEs can load-balance traffic to a given MAC address across all PEs advertising same ESI
E-VPN
Challenge:
How to load-balance traffic towards a multi-homed device across multiple PEs when MAC addresses are learnt by only a single PE?
CE1
MAC1
M2
PE1
PE2
PE3
PE4
CE2
I can reach ESI1
(All-Active)
I can reach ESI1
(All-Active)
MAC1
I can reach MAC1 via ESI1
MAC1 ESI1  PE1
 PE2
ESI-1

## Slide 21: Backup Path
PEs advertise in BGP connectivity to ESIs associated with local multi-homed Ethernet Segments
  Active/Standby Redundancy Mode is indicated
When PE learns a MAC address on its AC, it advertises MAC in BGP along with ESI of Ethernet Segment from which MAC was learnt
Remote PEs will install:
  active path to PE that advertised both MAC Address & ESI
  backup path to PE that advertised ESI only
Challenge:
How to identify PEs that have a backup path to a multi-homed Ethernet Segment?
CE1
MAC1
M2
PE1
PE2
PE3
PE4
CE2
I can reach
ESI1
(Active/Standby)
I can reach
ESI1
(Active/Standby)
MAC1
I can reach
MAC1 via ESI1
MAC1 ESI1  PE1 (Active)
 PE2 (Backup)
ESI-1

## Slide 22: MAC Mass-Withdraw
PEs advertise two sets of information:
  MAC addresses along with ESI from address was learnt
  Connectivity to ESI(s)
If a PE detects a failure impacting an Ethernet Segment, it withdraws route for associated ESI
  Remote PEs remove failed PE from path-list for all MAC addresses associated with an ESI.
  This effectively is a MAC ‘mass-withdraw’ function
Challenge:
How to inform remote PEs of a failure affecting many MAC addresses quickly while the control-plane re-converges?
CE1
MAC1
M2
PE1
PE2
PE3
PE4
CE2
I can reach ESI1
(All-Active)
I can reach ESI1
(All-Active)
MAC1,2, .., n
I can reach MACn via ESI1
MAC1,2,…, n ESI1  PE1
 PE2
ESI-1
I can reach MAC2 via ESI1
I can reach MAC1 via ESI1
I lost ESI1
X

## Slide 23: ARP Broadcast Suppression
Construct ARP caches on E-VPN PEs and synchronize them either via BGP or data-plane snooping
PEs act as ARP proxies for locally attached hosts, thereby preventing repeated ARP broadcast over the MPLS/IP network
Challenge:
How to reduce ARP broadcasts over the MPLS/IP network, especially in large scale virtualized server deployments?
CE1
MAC1, IP1
M2
PE1
PE2
PE3
PE4
CE2
Act as ARP proxy for IP1.
1. ARP Request (IP1)
2. ARP Reply (IP1)
3. ARP Request (IP1)
4. ARP Reply (IP1)

## Slide 24: Life of a Packet
Ingress Replication – Multi-destination Traffic Forwarding
PE1
PE2
PE3
PE4
CE1
CE3
During start-up sequence, PE2 sent Per-ESI Ethernet AD route with ESI MPLS label (split-horizon)
During start-up sequence, DF election between PE1-PE2 and PE3-PE4
PE 2 Eth A-D Route (Per-ESI)
RD = RD20
ESI = ESI1
ESI MPLS Label ext. comm.
Redund. Flag = All-Active
Label = L5
RT ext. community
RT-a, RT-b, RT-c, RT-d
PE 4 Inclusive Multicast Route
RD = RD-4a
PMSI Tunnel Attribute
Tunnel Type = Ing. Repl.
Label = L4
RT ext. community
RT-a
ESI MPLS Label – used by local PEs for split-horizon - downstream assigned (for ingress replication)
Mcast MPLS Label – used to transmit BUM traffic - downstream assigned (for ingress replication)
PE1
PE2
PE3
PE4
CE1
C-MAC:M1
CE3
C-MAC:M3
VID 100
SMAC: M1
DMAC: F.F.F
ESI (split-horizon) MPLS label allocated by PE2 for segment ES1
PE1 receives broadcast traffic from CE1. PE1 forwards it using ingress replication – 3 copies created
PSN MPLS label to reach PE3
 | L3 | 
Mcast MPLS Label assigned by PE3 for incoming BUM traffic on a given EVI
PE3 – as DF, it forwards BUM traffic towards segment
 | L2 | L5 | 
 | L4 | 
PE2 – drops BUM traffic originated on ES1
PE4 – non-DF for given EVI drops BUM traffic
During start-up sequence, PE1, PE2, PE3, PE4 sent Inclusive Multicast route which include Mcast label

## Slide 25: Life of a Packet
Unicast Traffic Forwarding
PE1
PE2
PE3
PE4
CE1
CE3
PE1
PE2
PE3
PE4
CE1
C-MAC:M1
CE3
C-MAC:M3
PSN MPLS label to reach PE1
MP2P VPN Label assigned by PE1 for incoming traffic on a given EVI
PE3 forwards traffic destined to M1 based on RIB information (PE1)
PE1 MAC Route
RD = RD-1a
ESI = ESI1
MAC = M1
Label = L1
RT ext. community
RT-a
PE3 RIB |  | 
VPN | MAC | ESI
RT-a | M1 | ES1
Path List
NH
PE1
VID 100
SMAC: M1
DMAC: F.F.F
MP2P VPN Label – downstream allocated label used by other PEs to send traffic to advertised MAC
 | L1 | 
VID 100
SMAC: M2
DMAC: M1
MAC advertised by route

## Slide 26: Life of a Packet
Unicast Forwarding and Aliasing
PE1
PE2
PE3
PE4
CE1
CE3
PE1
PE2
PE3
PE4
CE1
CE3
PSN MPLS label to reach PE1
PE1 MAC Route
RD = RD-1a
ESI = ESI1
MAC = M1
Label = L1
RT ext. community
RT-a
PE3, PE4 RIB |  | 
VPN | MAC | ESI
RT-a | M1 | ES1
Path List
NH
PE1
PE2
VID 100
SMAC: M1
DMAC: F.F.F
MP2P VPN Label – downstream allocated label used by other PEs to send traffic to advertised MAC
 | L1 | 
VID 100
SMAC: M3
DMAC: M1
MAC advertised by route
During start-up sequence, PE1 sent Per-EVI Ethernet AD route
During start-up sequence, PE2 sent Per-EVI Ethernet AD route
PE 2 Eth A-D Route (Per-EVI)
RD = RD-2a
ESI = ESI1
Label = L2
RT ext. community
RT-a
Aliasing MPLS Label – used by remote PEs to load-balance among local PEs
PE3 forwards traffic on a flow (flow 1) based on RIB information (towards PE1)
PE3 forwards traffic on a flow (flow 1) based on RIB information (towards PE2)
VID 100
SMAC: M4
DMAC: M1
 | L2 | 
Aliasing MPLS Label assigned by PE2 for (ES1, EVI) pair
PSN MPLS label to reach PE2
MP2P VPN Label assigned by PE1 for incoming traffic on a given EVI

## Slide 27: E-VPN Operational Scenarios
MAC Mobility
PE1
PE2
PE3
PE4
CE1
CE3
PE1
PE2
PE3
PE4
CE1
CE3
PE1 withdraws its M1 route and installs a new one pointing to PE3
PE3, PE4 RIB |  | 
VPN | MAC | ESI
RT-a | M1 | ES1
Path List
NH
PE1
VID 100
SMAC: M1
DMAC: M2
VID 100
SMAC: M3
DMAC: M1
PE3 / PE4 install M1 route towards PE1
2
Host M1 moves from CE1 to CE3’s location
3
M1
M1
PE1 MAC Route
RD = RD-1a
ESI = ESI1
MAC = M1
Label = L1
MAC Mobility ext. community
Seq. Num = 1
RT ext. community
RT-a
PE1 advertises MAC route for M1. Route may include MAC mobility community
PE3 MAC Route
RD = RD-3a
ESI = ESI2
MAC = M1
Label = L3
MAC Mobility ext. community.
Seq. Num = 2
RT ext. community
RT-a
5
PE1 / PE2 RIB |  | 
VPN | MAC | ESI
RT-a | M1 | ES2
Path List
NH
PE3
After host sends traffic at new location, PE2 now adv MAC route for M1 incrementing sequence # in MAC mobility community
4
M1

## Slide 28: EVPN VPWS
Benefits of EVPN applied to point-to-point services
  No signaling of PWs. Instead signals MP2P LSPs instead (ala L3VPN)
  All-active CE multi-homing (per-flow LB)
  Single-active CE multi-homing (per-service LB)
  Relies on a sub-set of EVPN routes to advertise Ethernet Segment and AC reachability
  PE discovery & signaling via a single protocol – BGP
  Per-EVI Ethernet Auto-Discovery route
  Handles double-sided provisioning with remote PE auto-discovery
Under standardization: draft-ietf-bess-evpn-vpws
MPLS
PE1
CE1
PE2
CE2
ES1
ES2
BGP Eth. Auto-Discovery Route
EVPN NLRI
AC AC1 via PE1
Control-plane attachment circuit advertisement over the Core
VPWS Service Config:
EVI = 100
Local AC ID = AC1
Remote AC ID = AC2
VPWS Service Config:
EVI = 100
Local AC ID = AC2
Remote AC ID = AC1
I have a P2P service that needs to communicate with the PE(s) that own of AC = AC2
Notes: Inherent inter-AS capability w/o the need for complex stitching (as was the case for PW)
Ease of integration with EVPN and IP-VPN

## Slide 29: EVPN VPWS Operation – All-active
MPLS
PE1
CE1
PE3
CE2
PE 1 Eth A-D Route
RD = RD-1a
ESI = ES1
Eth.Tag ID = AC1
Label (e.g. X)
RT ext. community
RT-a
PE 3 Eth A-D Route
RD = RD-2a
ESI = ES2 (0)
Eth.Tag ID = AC2
Label (e.g. Y)
RT ext. community
RT-a
PE1 & PE2 RIB |  |  | 
VPN | MAC | ESI | Eth.TAG
RT-a | - | 0 | AC2
Path List
NH
PE3
ES1
ES2
RT – RT associated with a given EVI
RD – RD unique per adv. PE per EVI
MPLS Label – (downstream assigned) used by remote PEs to reach segment
ESI – 10 bytes ESI as specify by EVPN Ethernet segment IETF draft
VPWS Service Config:
EVI = 100
Local AC ID = AC1
Remote AC ID = AC2
VPWS Service Config:
EVI = 100
Local AC ID = AC2
Remote AC ID = AC1
1
ES2 – Since CE2 is single homed to PE2, ES2 = 0
Eth.Tag ID – 4-bytes local AC-ID
2
3
4
5
PE2
ES1
VPWS Service Config:
EVI = 100
Local AC ID = AC1
Remote AC ID = AC2
PE3 RIB |  |  | 
VPN | MAC | ESI | Eth.TAG
RT-a | - | ES1 | 
RT-a | - | ES1 | 
RT-a | - | ES1 | AC1
Path List
NH
PE1
PE2
PE1,PE2
6
Both PEs (PE1/PE2) shows as next hop for the remote AC
ALL-Active == per-flow load-baancing CE-PEs
Single bundle on CE device

## Slide 30: EVPN VPWS Operation – Single-active
MPLS
PE1
CE1
PE3
CE2
PE 1 Eth A-D Route
RD = RD-1a
ESI = ES1
Eth.Tag ID = AC1
Label (e.g. X)
RT ext. community
RT-a
PE 3 Eth A-D Route
RD = RD-2a
ESI = ES2 (0)
Eth.Tag ID = AC2
Label (e.g. Y)
RT ext. community
RT-a
PE1 & PE2 RIB |  |  | 
VPN | MAC | ESI | Eth.TAG
RT-a | - | 0 | AC2
Path List
NH
PE3
ES1
ES2
RT – RT associated with a given EVI
RD – RD unique per adv. PE per EVI
MPLS Label – (downstream assigned) used by remote PEs to reach segment
ESI – 10 bytes ESI as specify by EVPN Ethernet segment IETF draft
VPWS Service Config:
EVI = 100
Local AC ID = AC1
Remote AC ID = AC2
VPWS Service Config:
EVI = 100
Local AC ID = AC2
Remote AC ID = AC1
1
ES2 – Since CE2 is single homed to PE2, ES2 = 0
Eth.Tag ID – 4-bytes local AC-ID
PE3 RIB |  |  | 
VPN | MAC | ESI | Eth.TAG
RT-a | - | ES1 | 
RT-a | - | ES1 | 
RT-a | - | ES1 | AC1
Path List
NH
PE1
PE2
PE1
2
3
4
5
6
PE2
ES1
VPWS Service Config:
EVI = 100
Local AC ID = AC1
Remote AC ID = AC2
Only one PE (PE1) shows as next hop for the remote AC
Single-Active == per-vlan load-balancing CE-PEs
Two bundles on CE device

## Slide 31: EVPN Ethernet access Single/Dual Homed Solution, Legacy L2 access
MPLS
Core
PE1
PE2
LACP
A1
EVPN-MPLS
MPLS
Core
PE1
PE2
A1
EVPN-MPLS
A1
Ethernet
Ethernet
PE1
PE2
MPLS
Core
A1
EVPN-MPLS
A2
STP/REP/
G.8032….
A2

## Slide 32: Symmetric Anycast IRB
DC Fabric - MPLS/VXLAN
Leaf
Leaf
Leaf
DCI
DCI
L2: RT2 [MAC/IP]
L2: RT2 [MAC/IP]
Anycast IRB
Anycast IRB
L3 : RT2 [MAC/IP] - host-route RT5: [prefix]
Routing and Bridging in the same instance
All-Active Multi-homed Access WITHOUT:
  mLAG (mLACP)
  VSS/vPCE…
VM
VM
VM

## Slide 33: EVPN DCI Layer 2/3 gateway
MPLS Core
DCI
DCI
DCI
DCI
Spine
Spine
Leaf
Leaf
Leaf
VM
VM
VM
Spine
Spine
Leaf
Leaf
Leaf
VM
VM
VM
EVPN - VXLAN (Nexus9k)
EVPN - MPLS
EVPN - VXLAN (Nexus9k)
Anycast-IRB - ”default GW” (optimal forwarding)
MPLS-VPNv4

## Slide 34: SR & EVPN DC Fabric with Anycast IRB - Demo
MPLS Core
DCI
DCI
Leaf
Leaf
VM
VM
MPLS-VPNv4
Anycast-IRB - ”default GW” (optimal forwarding)
DCI
DCI
Leaf
Leaf
VM
VM
MPLS EVPN with Anycast IRB
MPLS EVPN with Anycast IRB
172.1.1.28/24
172.1.1.29/24
172.1.1.254/24
172.1.2.30/24
172.1.2.254/24
172.1.3.31/24
RT2[MAC/IP]
RT2[MAC/IP]
RT5[Prefix]
VPNv4
RT2[MAC/IP]
172.1.1.30/24
172.1.3.254/24
VM
Leaf
DCI
NCS5500
ASR9000
Spine
Spine

## Slide 35: SR & EVPN-VPWS On-Demand Next-Hop
MPLS Core
DCI
DCI
Leaf
Leaf
VM
VM
Anycast-IRB - ”default GW” (optimal forwarding)
DCI
DCI
Leaf
Leaf
VM
VM
MPLS EVPN with Anycast IRB
MPLS EVPN with Anycast IRB
172.1.1.28/24
172.1.1.29/24
172.1.1.254/24
172.1.2.30/24
172.1.2.254/24
172.1.3.31/24
RT2[MAC/IP]
RT2[MAC/IP]
172.1.1.30/24
172.1.3.254/24
VM
Leaf
DCI
NCS5500
ASR9000
Spine
TE-metric=100
172.9.1.2/24
VM
172.9.2.2/24
VM
172.9.1.36/24
VM
172.9.2.36/24
VM
frame
service
DCI prefixSID
frame
service
Adj-SID
Adj-SID
frame
service
Adj-SID
frame
service
EVI200 - IGP metrics
EVI300 - TE metrics (low latency service)
frame
service
TE-metric=100

## Slide 36: PBB Ethernet VPN
Next generation solution for Ethernet multipoint (E-LAN) services by combining Provider Backbone Bridging (PBB - IEEE 802.1ah) and Ethernet VPN
Data-plane learning of local C-MACs and remote C-MAC to B-MAC binding
PEs run Multi-Protocol BGP to advertise local Backbone MAC addresses (B-MACs) & learn remote B-MACs
  Takes advantage of PBB encapsulation to simplify BGP control plane operation – faster convergence
  Lowers BGP resource usage (CPU, memory) on deployed infrastructure (PEs and RRs)
    RFC7623
Highlights
PE1
PE2
PE3
PE4
CE1
C-MAC:M1
CE3
C-MAC:M3
B-MAC:
B-M1
B-M2
B-M2
B-MAC:
B-M1
BGP MAC adv. Route
EVPN NLRI
MAC B-M1 via PE2
Control-plane address advertisement / learning over Core (B-MAC)
Data-plane address learning from Access
Local C-MAC to local B-MAC binding
Data-plane address learning from Core
Remote C-MAC to remote B-MAC binding
PBB
Backbone Edge Bridge
EVPN
PBB-EVPN PE
Notes:   PBB encapsulation == 18 Bytes

## Slide 37: VPWS / VPLS
Provisioning Model
  What information needs to be configured and in what entities
  Semantic structure of the endpoint identifiers (e.g. VC ID, VPN ID)
Discovery
  Provisioning information is distributed by a "discovery process“
  Distribution of endpoint identifiers
Signaling
  When discovery process is complete, a signaling protocol is automatically invoked to set up pseudowires (PWs)
An abstraction
Discovery
Signaling
Provisioning Model

## Slide 38: VPLS
VPLS Signaling
  LDP-based (RFC 4762)
  BGP-based (RFC 4761)
VPLS with LDP-signaling and No auto-discovery
  Most widely deployed solution
  Operational complexity for larger deployments
BGP-based Auto-Discovery (BGP-AD) (RFC 6074)
  Enables discovery of PE devices in a VPLS instance
Discovery and Signaling Alternatives
Manual
No Auto-Discovery
Border Gateway Protocol (BGP)
Static
No Signaling
BGP
Label Distribution Protocol (LDP)
VPN Discovery
Signaling
Most widely deployed
RFC 6074
RFC 4761

## Slide 39: EVPN - End-to-End Control-Plane
CE1
WAN/Core
Acess
PE1
PE2
DCI
DCI
Spine
Spine
Leaf
Leaf
Leaf
VM
VM
VM
IP, IGP, MPLS (LDP), RSVP-TE, BGP-LU
L2/L3VPN (BGP,T-LDP) - VPLS, EoMPLS
IP, MPLS, L2
VPLS, OTV
L2, STP, VLAN
Trill, Fabric-Path
Service Provider Network
Data Center Network
IP, MPLS (IGP/SR), MPLS-PBB
IP,MPLS,VXLAN
IP,MPLS,VXLAN
Common EVPN Control Plane based on BGP: EVPN, PBB-EVPN, EVPN-VPWS
Existing Solution:
Evolution:
overlap

## Slide 40: Acknowledgment: Jose Liste

## Slide 41: More Information
  RFC 7209: Requirements for Ethernet VPN (EVPN)
  RFC 7432: BGP MPLS-based Ethernet VPN
  RFC 7623: PBB-EVPN
  draft-ietf-bess-evpn-overlay: NVO solutions for EVPN
  draft-ietf-bess-evpn-vpws: VPWS support in EVPN
  draft-ietf-bess-evpn-inter-subnet-forwarding: IRB in EVPN
  draft-ietf-bess-evpn-ip-prefix-advertisement: IP prefixes in EVPN

## Slide 43: Symmetric EVPN IRB (1)
Routing on both ingress and egress VTEPs
Layer-3 VNI
  Tenant VPN indicator
  One per tenant VRF
VTEP Router MAC
Ingress VTEP routes packets onto the Layer-3 VNI
Egress VTEP routes packets to the destination Layer-2 VNI
L3
VTEP
VTEP
VTEP
VTEP
Layer-3 VNI
(VRF VNI)
Layer-2 VNI
(Network VNI)
Layer-2 VNI
(Network VNI)

## Slide 44: To PBB or not to PBB?
What is the value of combining PBB and EVPN functions?
Lower control-plane overhead than EVPN alone
  PBB-EVPN uses only a sub-set of EVPN routes
  Simpler and Faster failure convergence for all-active multi-homing scenarios
  Faster MAC move convergence handled in data-plane
Lower control-plane scale requirements than EVPN alone
  BGP MAC advertisements for smaller Backbone MAC (B-MAC) address space
  Requires less resources (CPU, memory) on deployed infrastructure (PEs / RRs)
Notes: What is the value of combining PBB and EVPN functions?
Lower control-plane overhead than EVPN alone
  PBB-EVPN uses only a sub-set of EVPN routes (i.e. no Ethernet AD BGP route)
    EVPN relies on Ethernet AD route for MAC mass withdrawal, aliasing and split-horizon filtering
  Simpler and Faster failure convergence for all-active multi-homing scenarios
  Faster MAC move convergence handled in data-plane
    EVPN relies on MAC Mobility BGP ext. community to signal MAC moves in the control-plane
Lower control-plane scale requirements than EVPN alone
  Keeps BGP MAC advertisements to the smaller Backbone MAC (B-MAC) address space as opposed to Customer MAC (C-MAC) space
  Requires less resources (CPU, memory) on deployed infrastructure (PEs and RRs)
  Provides confined (conversational) MAC learning to only PEs involved
    EVPN ubiquitous MAC advertisements consumes resources on PEs without active conversations

## Slide 45: PBB Ethernet VPN
Next generation solution for Ethernet multipoint (E-LAN) services by combining Provider Backbone Bridging (PBB - IEEE 802.1ah) and Ethernet VPN
Data-plane learning of local C-MACs and remote C-MAC to B-MAC binding
PEs run Multi-Protocol BGP to advertise local Backbone MAC addresses (B-MACs) & learn remote B-MACs
  Takes advantage of PBB encapsulation to simplify BGP control plane operation – faster convergence
  Lowers BGP resource usage (CPU, memory) on deployed infrastructure (PEs and RRs)
RFC7623
Highlights
PE1
PE2
PE3
PE4
CE1
C-MAC:M1
CE3
C-MAC:M3
B-MAC:
B-M1
B-M2
B-M2
B-MAC:
B-M1
BGP MAC adv. Route
EVPN NLRI
MAC B-M1 via PE2
Control-plane address advertisement / learning over Core (B-MAC)
Data-plane address learning from Access
Local C-MAC to local B-MAC binding
Data-plane address learning from Core
Remote C-MAC to remote B-MAC binding
PBB
Backbone Edge Bridge
EVPN
PBB-EVPN PE
Notes:   PBB encapsulation == 18 Bytes

## Slide 46: EVPN Advantages:
Integrated Services
Integrated Layer 2 and Layer 3 VPN services
L3VPN-like principals and operational experience for scalability and control
All-active Multi-homing & PE load-balancing (ECMP)
Fast convergence (link, node, MAC moves)
Control-Place (BGP) learning. PWs are no longer used.
Optimized Broadcast, Unknown-unicast, Multicast traffic delivery
Network Efficiency
Choice of MPLS, VxLAN or PBB data plane encapsulation
Support existing and new services types (E-LAN, E-Line, E-TREE)
Peer PE auto-discovery. Redundancy group auto-sensing
Operational consistency with L3 IP VPN
Fully support IPv4 and IPv6 in the data plane and control plane
Open-Standard and Multi-vendor support
Service Flexibility
Investment Protection