## Slide 1: Cisco Virtual Topology System
May 2017
Anant Shah, Sr. Technical Product Manager

## Slide 2: Agenda
VTS Key Features
Flexible Overlays with VTS
Introduction to orchestration and virtualization
VTS Demo
Cisco Differentiation
Questions?

## Slide 3: Service Orchestration velocity hindered by manual network process
ToR
ToR
Spine
Spine
ToR
Hypervisor
VM
x86 Server
Hypervisor
VM
x86 Server
Service Orchestration
Compute Orchestration
Network Orchestration
Manual Network Change Request
IP Configuration
Firewall Configuration
VLAN configuration
Automated Compute Request
Virtualized Compute
Auto Instantiation
Hypervisor
VM
x86 Server
VM
Compute is completely Virtualized
Compute Request completed in Seconds
Network is partially Virtualized
Network Change Request completed in days/weeks
Application and Network Services migration towards virtualization & cloud create requirements for agile & automated networks
Notes: Cloud enabled Modern day Datacenter
For an application environment or data center to be ready for cloud environment, data center infrastructure should support scale out architectures based on compute and network
The data center infrastructure that includes computes, network and storage should be virtualized and automated
CLOS fabric scales out based on compute and network, to cater to distributed nature of these applications.
Server Virtualization advancements over the last decade has not only helped to avoid high capex by reducing the server footprint in datacenters
but have also have helped to reduce OPEX by enabling automated provisioning of compute nodes in a matter of seconds.
But there are bottlenecks
The network that connects the physical and virtual nodes are not completely virtualized. It has to provisioned manually and it takes weeks/days to complete and are prone to human configuration errors.

## Slide 4: Network Virtualization & Overlays
Network virtualization: ability to separate, abstract and decouple the physical topology from a ‘logical’ or ‘virtual’ topology. This logical topology is called overlay networks
SDN Based Overlays introduces agility and automation to Network Orchestration
MPBGP-EVPN &VXLAN based Overlays
Notes: : Network overlays disassociates applications from physical topology, allowing a transition to cloud based multi-tenanted & scalable networks.

## Slide 5: MPBGP-EVPN &VXLAN based Overlays
EVPN
Layer-2 MAC and Layer-3 IP information distribution by Control-Plane (BGP)
Overlay Forwarding Table |  | 
T1,S1 | MAC, IP Address | P1/2
T1,S2 | MAC, IP Address | VTEP2
T2,S3 | MAC, IP Address | VTEP3
T2,S4 | MAC, IP Address | VTEP4
Built in multi-tenancy (at scale)
Integrated Routing/Bridging (IRB) for Optimized Forwarding
Minimize flooding through ARP suppression
Fast convergence upon network failures and host movements
Security through VTEP peer-authentication
VXLAN
IP routing – proven, stable, scalable
ECMP – utilize all available network paths
Flexible placement of multitenant segments
Better utilization of network paths
Scalable network domain (16M VNI vs. 4K VLANs)
BGP-EVPN/VXLAN based overlays provides flexibility, manageability, isolation, multi-tenancy, scalability & convergence.
Notes: Industry standard protocol for multi-vendor interoperability
Build-in multi-tenancy support
  Leverage MP-BGP to deliver VXLAN with L3VPN characteristics
Truly scalable with protocol-driven learning
  Host MAC/IP address advertisement through EVPN MP-BGP
Fast convergence upon host movements or network failures
  MP-BGP protocol driven re-learning and convergence
  Upon host movement, the new VTEP will send out a BGP update to advertise the new location of the host
Optimal traffic forwarding supporting host mobility
  Anycast IP gateway for optimal forwarding for host generated traffic
  No need for hair-pinning to to reach the IP gateway
ARP suppression
  Minimize ARP flooding in overlay
Head-end Replication with dynamically learned remote-VTEP list
  Head-end replication enables multicast-free underlay network
  Dynamically learned remote-VTEP list minimizes the operational overhead of head-end replication
VTEP peer authentication via MP-BGP authentication
  Added security to prevent rogue VTEPs or VTEP spoofing

## Slide 6: The Realities of Data Center Operations
Operationalizing a New Workload in the Data Center
t=0
t=n
Connect the Workload to the Tenant Network
✔
Deploy Tenant Workload
✔
Establish a connectivity maps
✔
Create a Tenant Network
✔
Allocate VLANS, VXLAN IDs
Create VRF
Identify Server Resources, Instantiate Workload
Configure the TORs with VLAN. VXLAN, VRF
Expectations are all of this happens in minutes or even seconds!
Automation Required!

## Slide 7: Benefits of Network Automation.

## Slide 8: Service Orchestration & Network Overlays/SDN in the data center
Service Orchestration
Compute Orchestration
Network Orchestration
Automated Network Change Request
Policy based Configuration
Abstraction & Programmability
Virtualized L2/L3 networks
Automated Compute Request
Virtualized Compute
Auto Instantiation
External Network
App
Zone1
Firewall
App
Zone2
Network
Segment A
Network
Segment B
Network
Segment C
External Network
App
Zone1
Firewall
App
Zone2
Network
Segment A
Network
Segment B
Network
Segment C
Tenant A – Topology1
Tenant B - Topology 2
NX-API, CLI, YANG
Network Overlays based Network Virtualization provides flexibility, tenant isolation and allows for resources to be dynamically provisioned
SDN Controller for automation, programmability and NVE management
Compute is completely Virtualized
Compute Request completed in Seconds
Network is completely Virtualized
Network Change Request completed in seconds
SDN/Network Overlays provides end to end data center overlay automation orchestrating instant connectivity as applications are turned up or down
VTS

## Slide 9: Flexible overlay with VTS

## Slide 10: VTS : Realizing the Cloud Enabled Data Center
Scale & Automation Drives Business Success
Flexible, on-demand EVPN/VXLAN based overlays with underlay awareness.
Abstracted & Virtualized
Network As A Service
Declarative, transactional, granular policies
for instantiation of overlays &
secure connectivity
Support Scale out architectures in terms of network and compute
Automation of fabric provisioning for physical and virtual workloads.
Deployment Flexibility, Visibility, management & Troubleshooting
Service Aware Overlay
Policies
Orchestration
Scalable Fabric
Cisco Virtual Topology System

## Slide 11: Cisco Virtual Topology System (VTS)
Open Standards based Overlay Provisioning and Management System
  Simplified Management for Ease of Operations
Embedded Sunstone
Tighter Integration with Orchestrators
Programmable Interfaces
Plugin for openstack
Plugin for VMware
Future for Containers
NB REST API
Standard YANG SB Programming
Automated Overlay and Fabric Provisioning

## Slide 12: VTS Architecture – Hardware VTEP
REST API
NX-API, CLI, YANG
VMware vCenter
Hardware Switches
DC Fabric
(OSPF or BGP as the
Underlay Protocol)
SR-IOV
Tenant VM
Tenant VM
Tenant VM
Host
Border Leaf
&
DCI
(Integrated or
Separated)
Bare Metal
Appliance
(Eg, Firewall)
Host
LEAF
SPINE
OVS/DVS
Appliance VM
Tenant VM
Tenant VM
Host
DC POD
Bare Metal
Application
Spine
Physical Network Appliances
Virtual Topology
Controller
DCI Router
Border Leaf
Network Based
VTEPs
OVS/DVS
Appliance VM
Tenant VM
Tenant VM
Host
Nexus 9300/9500/5000/7x00– Spine (RR)
ASR9000, Nexus 7x00– DCI
Nexus 3000,9200/9300/5600/7x00 – ToR

## Slide 13: VTS Architecture – Software VTEP
REST API
NX-API, CLI, YANG
VMware vCenter
Virtual Topology Forwarder
User space, multitenant, line-rate packet forwarder
Uses Vector Packet Processing technology
Fully integrated with Intel DPDK
Supports VXLAN, can be extended to support MPLSoGRE, L2TPv3, MPLSoUDP, native MPLS, and SR
Programmed by Cisco® VTS using Restconf/YANG
Multi-threaded and 64 bit clean.
Supports both IPv4 and IPv6
NIC
ESXi
VTF
(VM)
Tenant VM
Tenant VM
vSwitch
vSwitch
NIC
KVM
VTF
Tenant VM
Tenant VM
vSwitch
vhost-user

## Slide 14: VTS Architecture
LEAF
DC POD
Multiple workload types and multiple orchestration systems
SPINE
Border Leaf
&
DCI
(Integrated or
Separated)
DC Fabric
(OSPF or BGP as the
Underlay Protocol)
Custom Orchestrator
vCenter
VTS GUI
Container
Cisco VTS
VTF
VTF
VTF
VTF
VTS offers a single overlay networking solution for any type of data center workload enabling customers streamline their operational workflows
Notes: Input two the system is stuff on the left – policies/user-intent + devices and their software/capabilities

## Slide 15
Hardware-Based Overlays
Software (VTF) Based Overlays
Hybrid Overlays
VTS – Flexible Network Overlays
Hardware VTEP
(TOR Leaf Switch)
Software VTEP
(Virtual Topology Forwarder / Fd.io)
VTS
VTS provides architectural and infrastructure independence through a multi-vendor, multi-hypervisor, SW and HW overlay solution

## Slide 16: VTS Customer Use Cases
Multi-Tenant
Data Centers
Network-Function
Virtualization

## Slide 17: VTS Key Features
Plugin for Openstack and Vcenter
VTF
IPV6 support
Service Extension
  Underlay Service Extension
  Overlay Service Extension
VTS integrate VXLAN with WAN
  GRT,L3VPN,L2VPN,VPLS to EVPN
Multi-VMM
  Trusted vs Untrusted
Open stack Enhancements
Multicast on VTF
AAA
ESI based MH

## Slide 18: VTF

## Slide 19: IPv6 Support
VTF
VTF
IPv4/
IPv6
Cisco VTS
IPV4 underlay
Dual stack support
IPv4/
IPv6
IPv4/
IPv6

## Slide 20: Service Extension
  Template driven feature which allows configuration of Overlay and Underlay configurations via VTS which will eliminate requirement of out-of-band configuration (via CLI)
  Can be attached per tenant/per network.
  Single pane of glass for all your device configurations
  !! Not your underlay manager
    No POAP support
Example of Overlay configuration :
VRF,NVE BGP configuration
Example of Underlay configuration :
Physical Interface configuration, VPC , Definition of Policy Map.

## Slide 21
VTS – Integrate VXLAN with WAN
EVPN- VXLAN
DC 1
DC 2
EVPN- VXLAN
DC 3
EVPN- VXLAN
L2 VPN
L3 VPN
Legacy DC
VPLS

## Slide 22
VTS – Integrate VXLAN with WAN
MPLS
Internet
RR

## Slide 23: VTS – Integrate VXLAN with WAN
For Disaster recovery, High Availability
Integrate EVPN/VXLAN to MPLS-L3VPN

## Slide 24: Cisco VTS Operational models
Multi VMM (VTS 2.5)
VMM Initiated
VTS GUI based
VTS Plugin in VMM initiated workflow.
Network objects creation is initiated in VMM
The Network segments are shared across VMMs
Network objects can be created at VMMs or at VTS
Network and Compute groups work in Silos
Port-group and vlan information are exchanged offline as the VMs are attached.
VTS
VTS
vCenter
vCenter
VTS
Degree of Automation

## Slide 25: Multi VMM –Merge L2
TOR
ToR
ToR
Spine
Spine
ToR
KVM
VM2
x86 Server
DCI
VTEP1
VTEP2
Border Leaf
VTEP
KVM
VM1
x86 Server
VTEP4
ESXI
x86 Server
VTEP3
RR
EXSI
VM3
x86 Server
VM4
TenantA View
Project A View
TenantA View
VLAN
VLAN
VLAN
VLAN
Horizon
ProjectA, N1
TenA, N1
vCenter GUI
Notes: Application and Server migration towards virtualization & cloud create requirements for agile and scalable networks. This is driving the current network transition to the SDN. With SDN, there is a migration from intelligent hardware platform components to a more centralized software intelligence. A centralized software helps customers improve their operational efficiencies at cloud scale and also enhance troubleshooting capabilities in the network. This helps the customer better align their network to meet their business goals.
SDN also changes the paradigm on how customer buy products, what features matter in the product. SDN is also shaping a new ecosystem build around SDN applications.
Software Defined Networking and OpenDaylight is transforming how we look at the network. The opportunities it creates are endless, we know some of them and will discuss few in the presentation. What Cisco is doing with OpenDaylight is taking the Open Source SDN Platform and putting capabilities around it to make it the best SDN platform in the market to help you win with customers
The discussion agenda is as above:
[1] What OpenDaylight is from the organization view and the OpenDaylight product
[2] Get into Cisco’s commercial distribution of OpenDaylight -- Cisco Open SDN Controller -- this will sold and supported as any other Cisco product.
[3] How we are enabling developers on the platform. As an open platform it has number of developer and integration opportunities and we are building a developer ecosystem
[4] A quick view of targeted use cases that we see today. Not an exhaustive list but a sample list of use cases we are focusing on initially
[5] Talk about how we are using Open SDN controller in the WAE. An example of an SDN application.
[6] Call to action.

## Slide 26: Multi VMM - Merge L3
TOR
ToR
ToR
Spine
Spine
ToR
KVM
VM2
x86 Server
DCI
VTEP1
VTEP2
VTEP
KVM
VM1
x86 Server
VTEP4
ESXI
x86 Server
VTEP3
RR
EXSI
VM3
x86 Server
VM4
TenantA View
ProjectA View
TenantA View
VLAN
VLAN
VLAN
VLAN
Router is created using VTS API/GUI
L2 VNI
L2 VNI
L3 VNI
Notes: Application and Server migration towards virtualization & cloud create requirements for agile and scalable networks. This is driving the current network transition to the SDN. With SDN, there is a migration from intelligent hardware platform components to a more centralized software intelligence. A centralized software helps customers improve their operational efficiencies at cloud scale and also enhance troubleshooting capabilities in the network. This helps the customer better align their network to meet their business goals.
SDN also changes the paradigm on how customer buy products, what features matter in the product. SDN is also shaping a new ecosystem build around SDN applications.
Software Defined Networking and OpenDaylight is transforming how we look at the network. The opportunities it creates are endless, we know some of them and will discuss few in the presentation. What Cisco is doing with OpenDaylight is taking the Open Source SDN Platform and putting capabilities around it to make it the best SDN platform in the market to help you win with customers
The discussion agenda is as above:
[1] What OpenDaylight is from the organization view and the OpenDaylight product
[2] Get into Cisco’s commercial distribution of OpenDaylight -- Cisco Open SDN Controller -- this will sold and supported as any other Cisco product.
[3] How we are enabling developers on the platform. As an open platform it has number of developer and integration opportunities and we are building a developer ecosystem
[4] A quick view of targeted use cases that we see today. Not an exhaustive list but a sample list of use cases we are focusing on initially
[5] Talk about how we are using Open SDN controller in the WAE. An example of an SDN application.
[6] Call to action.

## Slide 27: Multi VMM - Publish
TOR
ToR
ToR
Spine
Spine
ToR
KVM
VM2
x86 Server
DCI
VTEP1
VTEP2
Border Leaf
VTEP
KVM
VM1
x86 Server
VTEP4
ESXI
x86 Server
VTEP3
RR
EXSI
VM3
x86 Server
VM4
TenantA View
ProjectA View
TenantA View
VLAN
VLAN
VLAN
VLAN
Tenant A, N1
L2 VNI
Notes: Application and Server migration towards virtualization & cloud create requirements for agile and scalable networks. This is driving the current network transition to the SDN. With SDN, there is a migration from intelligent hardware platform components to a more centralized software intelligence. A centralized software helps customers improve their operational efficiencies at cloud scale and also enhance troubleshooting capabilities in the network. This helps the customer better align their network to meet their business goals.
SDN also changes the paradigm on how customer buy products, what features matter in the product. SDN is also shaping a new ecosystem build around SDN applications.
Software Defined Networking and OpenDaylight is transforming how we look at the network. The opportunities it creates are endless, we know some of them and will discuss few in the presentation. What Cisco is doing with OpenDaylight is taking the Open Source SDN Platform and putting capabilities around it to make it the best SDN platform in the market to help you win with customers
The discussion agenda is as above:
[1] What OpenDaylight is from the organization view and the OpenDaylight product
[2] Get into Cisco’s commercial distribution of OpenDaylight -- Cisco Open SDN Controller -- this will sold and supported as any other Cisco product.
[3] How we are enabling developers on the platform. As an open platform it has number of developer and integration opportunities and we are building a developer ecosystem
[4] A quick view of targeted use cases that we see today. Not an exhaustive list but a sample list of use cases we are focusing on initially
[5] Talk about how we are using Open SDN controller in the WAE. An example of an SDN application.
[6] Call to action.

## Slide 28: Multi VMM
Accept Network from VMM-Trusted
Create network from VTS and push it to VTS- Untrusted

## Slide 29: VTS Customer Use Cases
Multi-Tenant
Data Centers
Network-Function
Virtualization

## Slide 30: Customer Proof Points
Customer#1
Workload Agnostic Overlay
Support for both VM and Bare Metal Workloads
Versatile
Support for Multiple VMMs (openstack and VMWare)
Dual Stack Enabled
Tenancy based on IPv4/IPv6(dual stack) capable overlay networks
Custom Service Integrated
Redirect select traffic to the services connected to the Border Leaf

## Slide 31: Customer Proof Points
Customer #2
Multi-Tenant
Support Colocation of Tenants in Common Environment
Services
Internet and VPN as Service Offerings
Firewall and Load Balancing within the Fabric
Resilient
Ability to Connect the Same Customers across Multiple Data Centers
Support Bare Metal
Bare Metal attach to Fabric

## Slide 32: Customer Proof Point
NSO: Network Service Orchestrator
VTS: Virtual Topology System
VTS: Virtual Topology System
ToR: Top of Rack switch
PNF: Physical Network Function
VNF: Virtual Network Function
dVS: distributed Virtual Switch
PE: Provider Edge
NFV Customer
Nexus 9300 (ToR)
Nexus 9300 (ToR)
PNF1
VNF1
VNF2
dVS
PNF2
VNF1
VNF2
dVS
MPLS VPN Network
VPN PE
& VXLAN Gateway
VXLAN
VTS
vCenter
VTS
Plug-in
VLANs
VLANs
VLANs
VLANs
Admin Tools
Customer Portal
OSS/BSS
REST API
BGP-EVPN
Orchestration & Controllers Layer
Virtual Overlay Networking Layer
Virtual Infrastructure, VNF & PNF Layer
NSO
ESC
Notes: 1. Building Virtual IP-based overlay network over multiple DC sites to provide virtual networking services offered by current MGW.
  This is the Scope of this RFI
2. Building End-user portal through which end users can request add/delete/change network services on-demand.
3. The end-user portal should also be able to configure gateway routers(PEs) connecting MGW network to existing L2/L3 VPN or public Internet.

## Slide 33: VTS Demo

## Slide 34
NFV Ecosystem
Full stack NFV solution
Integration with NSO and VNF life-cycle manager ESC
Dynamic service chaining capabilities
Virtual Topology System
(Policy Plane & Control Plane)
Transactional policy models; flag transaction errors & rollback
Architecture to integrate third party network elements
Virtual Topology Forwarder
User space without any kernel modifications
Multi-tenanted, L2/L3 capable including VXLAN & MPLS
Line rate packet forwarder
Network Endpoint
Ecosystems
SW and HW overlays in bare-metal and virtualized environment
N2k-N9k, ASR 9K, and Virtual forwarder support
Cisco Differentiation

## Slide 35: Cisco VTS : Flexible Overlays with Optimized Routing
Scalable
Large Datacenters
Open
VXLAN/EVPN
VPLS/MPLS-L3VPN
Seamless Integration
Multi-hypervisor
Multyi-VMM
Legacy and physical form factor network services
Containers
Analytics/Visibility
Agility and Automation
Bare metal Workloads
Investment Protection
Service Chaining
Policy Driven
Service
Multi Vendor
Best-in-class devices
Muti-pod
Multi-DC
L2/L3 Overlays
Software based overlays
Switch based Overlays
Virtual Workloads
Over the top Overlays
Infrastructure
Notes:   Investment Protection - VTS supports the entire Nexus portfolio, thus bringing the benefits of automation and operational simplicity to the entire Nexus family.
  Faster Network Provisioning - through an automated policy-driven approach across both virtual and physical workloads.
  Seamless Integration - through open APIs with cloud orchestration systems like OpenStack and vCenter
  Improved Resource Utilization - through the creation of a flexible pool of resources which can be securely allocated and re-allocated on demand maximizing the return on infrastructure investment and reducing capex
  Scalability - using standards based BGP-EVPN based control plane to manage VXLAN overlays extending workload placement and mobility diameter seamlessly without compromising performance.
  Multi-Vendor support – Extensible to multi-vendor environments by leveraging Cisco Tail-f technology

## Slide 36: www.cisco.com/go/vts

## Slide 37
Thank You