BCMSN

# 642-812 BCMSN

## Exam Description

The Building Converged Cisco Multilayer Switched Networks (BCMSN 642-812) is a qualifying exam for the Cisco Certified Network Professional CCNP® and the Cisco Certified Design Professional CCDP® certifications. The BCMSN 642-812 exam will certify that the successful candidate has important knowledge and skills necessary to implement scalable multilayer switched networks. The exam includes topics on Campus Networks, describing and implementing advanced Spanning Tree concepts, VLANs and Inter-VLAN routing, High Availability, Wireless Client Access, Access Layer Voice concepts, and minimizing service Loss and Data Theft in a Campus Network.

### Exam Topics

The following topics are general guidelines for the content likely to be included on the Remote Access exam. However, other related topics may also appear on any specific delivery of the exam.

Implement VLANs.

Explain the functions of VLANs in a hierarchical network.

Configure VLANs (e.g., Native, Default, Static and Access).

Explain and configure VLAN trunking (i.e., IEEE 802.1Q and ISL).

Explain and configure VTP.

Verify or troubleshoot VLAN configurations.

Conduct the operation of Spanning Tree protocols in a hierarchical network.

Explain the functions and operations of the Spanning Tree protocols (i.e., RSTP, PVRST, MISTP).

Configure RSTP (PVRST) and MISTP.

Describe and configure STP security mechanisms (i.e., BPDU Guard, BPDU Filtering, Root Guard).

Configure and Verify UDLD and Loop Guard.

Verify or troubleshoot Spanning Tree protocol operations.

Configure and verify link aggregation using PAgP or LACP.

Implement Inter-VLAN routing.

Explain and configure Inter-VLAN routing (i.e., SVI and routed ports).

Explain and enable CEF operation.

Verify or troubleshoot InterVLAN routing configurations.

Implement gateway redundancy technologies.

Explain the functions and operations of gateway redundancy protocols (i.e., HSRP, VRRP, and GLBP).

Configure HSRP, VRRP, and GLBP.

Verify High Availability configurations.

Describe and configure wireless client access.

Describe the components and operations of WLAN topologies (i.e., AP and Bridge).

Describe the features of Client Devices, Network Unification, and Mobility Platforms (i.e., CCX, LWAPP).

Configure a wireless client (i.e., ADU).

Describe and configure security features in a switched network.

Describe common Layer 2 network attacks (e.g., MAC Flooding, Rogue Devices, VLAN Hopping, DHCP Spoofing, etc.)

Explain and configure Port Security, 802.1x, VACLs, Private VLANs, DHCP Snooping, and DAI.

Verify Catalyst switch (IOS-based) security configurations (i.e., Port Security, 802.1 xs, VACLs, Private VLANs, DHCP Snooping, and DAI).

Configure support for voice.

Describe the characteristics of voice in the campus network.

Describe the functions of Voice VLANs and trust boundaries.

Configure and verify basic IP Phone support (i.e. Voice VLAN, Trust and CoS options, AutoQoS for voice).

## Suggested Study Lab Setup

## Overview

The purpose of the Lab Setup section is to assist in the setup and configuration of the suggested study lab for BCMSN 642-812. This section includes these topics:

Lab Topology

Hardware and Software Requirements

Workstation Configuration

Lab Equipment Configuration

General Lab Setup

## Lab Topology

This topic describes the suggested study lab topology for BCMSN 642-812

The lab consists of 2 access switches, 2 distribution switches, of 2 core switches, 1 wireless AP and 1 light weight wireless controller (plus attenuators as needed).

## Lab Equipment Configuration

This lists the recommended equipment to support the laboratory activities. This equipment list reflects the equipment needed to build the lab from scratch.

### Laboratory Equipment List

The equipment suggested here is for study purposes.

#### Student POD Equipment

At least one PC is needed to support wireless access.

PC Router Equipment

| Number of Units | Cisco Part Number | Product Description |
| --- | --- | --- |
| 2 | CISCOSOHO91 (or equivalent device) | PC router with one 10-megabit Ethernet port The selected router must be capable of generating extended pings and supporting a console connection. |
| 2 | CAB-AC2 | AC power cord |

Access Switch Submodule Equipment

| Number of Units | Cisco Part Number | Product Description |
| --- | --- | --- |
| 2 | WS-C2950G-12-E | Cisco Catalyst 2950 with the following options: Twelve 10/100 Fast Ethernet ports with two Gigabit Interface Converter (GBIC) slots IOS Enhanced Image |
| 2 | CAB-AC | 110 V power cord (for Cisco Catalyst 3650) |

Building Distribution Submodule Equipment

| Number of Units | Cisco Part Number | Product Description |
| --- | --- | --- |
| 2 | WS-C3560G-24TS-E | Cisco Catalyst 3560 with the following options: Twenty-four 10/100/1000 Ethernet ports and four SFP ports IOS enhanced image, required to support EIGRP routing |
| 2 | CAB-AC | 110 V power cord (for Cisco Catalyst 3650) |

Wireless LAN Controller

| Number of Units | Cisco Part Number | Product Description |
| --- | --- | --- |
| 2 | AIR-WLC2006-K9 | 2000 Series WLAN Controller for up to 6 Lightweight APs |
| 2 | CAB-AC | 110 V power cord (for WLC2006) |

Lightweight access point

| Number of Units | Cisco Part Number | Product Description |
| --- | --- | --- |
| The lab may be built with access points that have either internal or external antennas. Lightweight access point with external antennas is recommended. The console port of this access point can be connected to the terminal server (optional); however configuration must be done via wireless controller which downloads the OS code and configuration. Power over Ethernet required for lab |
| 2 | AIR-LAP1242AG-x-K9 Replace “x” with country code (e.g., A for US, E for Europe) | 802.11ag LWAPP AP Dual 2.4,5GHz RP-TNC FCC Cnfg |
| 4 | AIR-ANT4941 | Two 2.4 GHz dipole antennas per access point |
| 4 | AIR-ANT5135D-R | Two 5 GHz dipole antennas per access point |
| OR |
| 2 | AIR-AP1020-x-K9 Replace “x” with country code (e.g., A for US, E for Europe) | Alternative lightweight access point with internal antennas (used by default) and external antennas |
| 4 | AIR-ANT4941 | Two 2.4 GHz dipole antennas per access point |
| 2 | AIR-ANT5135D-R | One 5 GHz dipole antenna per access point |

As needed

| Number of Units | Cisco Part Number | Product Description |
| --- | --- | --- |
| 6 to 8 As needed | Attenuators | Suggested option (3 attenuators per AP1020, which has two 2.4 GHz plus one 5 GHz antennas, or else 4 per AP LAP1242AG, which has two 2.4 plus two 5 GHz antennas) Approximately 10 to 40 dBi attenuators to reduce RF power on external antennas. Needed when APs are in very close proximity (same rack). The exact amount of attenuation will depend on AP surrounding environment and APs proximity to each other. Country power regulation and if unit is for 2.4 GHz or 5 GHz will vary the specific type of attenuators you purchase. Example vendor: www.terrawaveonline.com |

Wireless Client

| Number of Units | Cisco Part Number | Product Description |
| --- | --- | --- |
| 1 | Wireless Client | The selected device depends on the implementation of the lab. Optional, but strongly suggested to provide a client to verify configuration via ping. One client is used per AP (SSID) for wireless association and ping verification during lab. The following devices have been tested as wireless clients: Cisco AIR-CB21AG-x-K9 client adapter (PC dependant) Linksys WUSB11 or WUSB54G USB client adapter (PC dependant) Linksys WPS54G USB print server (recommend as the simplified fixed independent client solution) |

#### Core Equipment

Campus Backbone Submodule Equipment (Switch 1)

| Number of Units | Cisco Part Number | Product Description |
| --- | --- | --- |
| 1 | WS-C3560-24PS-E | Cisco Catalyst 3560 with the following options: Twenty-four 10/100 Ethernet ports with Power over Ethernet (PoE) and four SFP ports IOS enhanced image, required to support EIGRP routing |
| 1 | CAB-AC | 110 V power cord (for Cisco Catalyst 3650) |

Campus Backbone Submodule Equipment (Switch 2)

| Number of Units | Cisco Part Number | Product Description |
| --- | --- | --- |
| 1 | WS-C3560G-24TS-E | Cisco Catalyst 3560 with the following options: Twenty-four 10/100/1000 Ethernet ports and four SFP ports IOS enhanced image, required to support EIGRP routing |
| 1 | CAB-AC | 110 V power cord (for Cisco Catalyst 3650) |

#### Additional Equipment

Cabling -Number and lengths will vary depending on physical installation

| Number of Units | Cisco Part Number | Product Description |
| --- | --- | --- |
| As needed |  | Straight-through Category 5 Ethernet cables |
| As needed |  | Console cables |
| As needed |  | Crossover Category 5 Ethernet cables |
| As needed |  | Crossover Gigabit Ethernet cables |

#### Cisco IOS Software Versions

| Cisco IOS Software Versions |
| --- |
| Platform | IOS Image Name | Comment |
| Access Switches |
| WS-C2950G-12-EI | c2950-i6q4l2-mz.121-22.EA1.bin | Cisco Catalyst 2950 |
| Distribution Switches |
| WS-C3560G-24TS-E | c3560-ipservices-tar.122.SEB.tar | For Cisco Catalyst 3560 |
| Backbone Switch (Wireless equipment connects to this switch) |
| WS-3560-24PS-E | c3560-advipservicesk9-tar.122-25.SEE.tar | For Cisco Catalyst 3560 |
| Backbone Switch |
| WS-C3560G-24TS-E | c3560-ipservices-tar.122.SEB.tar | For Cisco Catalyst 3560 |
| PC Router |
| CISCOSOHO91-K9-64 | soho91-k9oy6-mz.124-1.bin |  |
| Wireless Controller |
| AIR-WLC2006-K9 | AIR-WLC2006-K9-3-2-116-21.aes |  |