## Slide 1: VXLAN the Cisco Way: Why, Where, When, What, How
Darren Marinko – DC Consulting Systems Engineer
Phil Lowden – DC Consulting Systems Engineer

## Slide 2: Why?

## Slide 3
VXLAN provides a Network with Segmentation, IP Mobility, and Scale
“Standards” based overlay
Leverages Layer-3 ECMP with all links forwarding
Increased name space from 4K to 16M Layer-2 identifiers
Segmentation and multi-tenancy
Integration of physical and virtual
It’s SDN: centralized controller separate from data plane

## Slide 4
Business Outcomes
Flexibility: Layer-2 everywhere; physical and virtual
Simplicity: Centralized controller (Virtual Topology System)
Scalability: Increased name space from 4K to 16M Layer-2 identifiers; one spine or leaf at a time
Security: Segmentation and multi-tenancy

## Slide 5: Where?

## Slide 6
Large Cloud Provider (Top 10)
Workload Placement using VXLAN Extension
Connect to External Network through WAN
Customer Ask :
Any workload anywhere in their large fabric
Scale to support a 188 Rack Data Center !
Use Case

## Slide 7
Large Cloud Provider (Top 10)
Implementation
Rack 1
VLAN 10
Rack 188
VLAN 10
N9508
N9508
N9508
N9508
N9300
N9300
N9300
N9300
N9300
N9300
IT Core
SVIs
In-Rack VLANs
VXLAN Extended VLANs
Routed Link
Distributed Anycast Gateway
L3 Boundary
App
OS
App
OS
App
OS
App
OS

## Slide 8: When?

## Slide 9: Ethernet VPN is Standards-Based
Control-
Plane
EVPN MP-BGP - RFC 7432
(draft-ietf-l2vpn-evpn)
Data-
Plane
Multi-Protocol Label Switching (MPLS)
draft-ietf-l2vpn-evpn
Provider Backbone Bridges
(PBB)
draft-ietf-l2vpn-pbb-evpn
Network Virtualization Overlay (NVO)
draft-sd-l2vpn-evpn-overlay
EVPN over NVO Tunnels (VXLAN, NVGRE, MPLSoE) for Data Center Fabric encapsulations
Provides Layer-2 and Layer-3 Overlays over simple IP Networks

## Slide 10: Cisco Supported VXLAN IETF Drafts
ID | Title | Ver | Category | Comments
RFC 7348 | Virtual eXtensible Local Area Network |  | Data Plane | Flood and Learn based implemented
RFC 7432 | BGP MPLS based Ethernet VPNs |  | EVPN Control Plane | Control Plane is based on this RFC
draft-ietf-bess-evpn-overlay | A Network Virtualization Overlay Solution using EVPN | 0 | EVPN Control Plane | Implemented
draft-ietf-bess-evpn-inter-subnet-forwarding | Integrated Routing and Bridging in EVPN | 0 | EVPN Control Plane | Implemented
draft-rabadan-l2vpn-evpn-evpn-prefix-advertisement | IP Prefix Advertisement in E-VPN | 2 | EVPN Control Plane | Implemented
Draft-tissa-nvo3-oam-fm | NVO3 Fault Management | 1 | Mgmt Plane | How much of this are we implementing in 2015 ? Vs ICMP based ? Vs Jain draft ?

## Slide 11: VXLAN Evolution
Multicast Independent
Overlay Control-Plane provides dynamic VTEP discovery
Head-End Replication enables Unicast-only mode (aka ingress Replication)
VXLAN Hardware Gateway Redundancy (VPC)
Integrated physical and virtual Overlays (Hybrid Overlays)
Inter-Pod Connectivity
VXLAN Gateway to other Encaps/Networks
External Connectivity
VXLAN Hardware Gateway Redundancy (VPC)
Integrated physical and virtual Overlays (Hybrid Overlays)
Inter-Pod Connectivity
VXLAN Gateway to other Encaps/Networks
Protocol Learning
Workload MAC and IP Addresses learnt by VXLAN Edge Devices (NVEs)
Advertises Layer-2 and Layer-3 Address-to-VTEP Association (Overlay Control-Plane)
Flood Prevention
Optimized ARP forwarding
IP Services
VXLAN Routing
Distributed Anycast Gateway (requires Overlay Control-Plane)
Multi-Tenancy

## Slide 12: VXLAN/EVPN - Interoperability & Feasibility
VXLAN/EVPN interoperability demonstrated during MPLS/SDN World Congress in Paris
Participating Vendors are Cisco, Juniper, Alcatel Lucent & Ixia
Independently Tested at EANTC with public available Whitepaper
http://www.eantc.de/showcases/mpls_sdn_2015/intro.html
APPROVED

## Slide 13: Cisco VXLAN Portfolio
Nexus 1000
Nexus 3100
Nexus 7000
Nexus 5600
L2 Gateway
L3 Gateway
BGP EVPN Control Plane
Anycast Gateway
Head End Replication
Nexus 9000
Cisco VXLAN Solutions
ASR1000
CSR1000
ASR9000
Scale
Secure
Multi-tenancy
Workload Mobility
Workload Anywhere
Nexus 2000

## Slide 14: What?

## Slide 15: VXLAN/EVPN = Ingress Replication
VXLAN with BGP EVPN Control-Plane still requires a technology for Broadcast/Unknown Unicast/Multicast (BUM) replication
Cisco provides 2 Options
  Multicast – Efficient way of sending multi-destination traffic to all participating VTEP (1 Copy per Link)
  Unicast – Sending a copy of multi-destination traffic to all participating VTEP (1 copy per VTEP)

## Slide 16: VXLAN/EVPN was build for Data Center Interconnect (DCI)
VXLAN with BGP EVPN Control-Plane uses the control-plane for integrated Route and Bridge (IRB) decisions
VXLAN has now a Control-Plane like OTV but …
  VXLAN was built for Local Area Network (LAN)
  There are missing features/functions which are not there (we will talk about it)
  VXLAN could be used for Inter-Pod communication

## Slide 17: What is VXLAN/EVPN?
VXLAN is a network overlay technology
  Layer-2 & Layer-3 overlay network on top of an IP routed network
  MAC in UDP encapsulation (UDP destination port 4789)
Standards based overlay (VXLAN) with standards based Control-plane (BGP)
Layer-2 MAC and Layer-3 IP information distribution by Control-Plane (BGP)
Forwarding decision based on Control-Plane (minimizes flooding)
Integrated Routing/Bridging (IRB) for Optimized Forwarding in the Overlay

## Slide 18: VXLAN Gateway Types
VXLAN to VLAN Bridging
  (Layer-2 Gateway)
VXLAN-to-VXLAN Routing
  (Layer-3 Gateway)
VXLAN-to-VLAN Routing
  (Layer-3 Gateway)
VXLAN Taxonomy
V
VXLAN Router
Ingress VXLAN packet
on RED segment
Egress VXLAN packet is ROUTED to new segment
V
VXLAN Router
Ingress VXLAN packet
on RED segment
Egress packet is IEEE 802.1q tagged interface. packet is ROUTED to new VLAN
V
VXLAN Layer-2 Gateway
Ingress VXLAN packet
on RED segment
Egress packet is IEEE 802.1q tagged interface. packet is BRIDGED to new VLAN

## Slide 19: VXLAN Overview (1)
Local LAN Segment
Physical Host
Local LAN Segment
Physical Host
Virtual Hosts
Local LAN Segment
Virtual Switch
IP Network
(Underlay)
Edge Device
Edge Device
Edge Device
IP Interface

## Slide 20: VXLAN Overview (2)
Local LAN Segment
Physical Host
Local LAN Segment
Physical Host
VTEP
VTEP
VXLAN
(Overlay)
VTEP
V
V
V
Encapsulation
Virtual Hosts
Local LAN Segment
Virtual Switch
VTEP – VXLAN Tunnel End-Point
VNI/VNID – VXLAN Network Identifier

## Slide 21: VXLAN Frame Format
MAC-in-IP Encapsulation
Underlay
Outer IP Header
Outer MAC Header
UDP Header
VXLAN Header
Original Layer-2 Frame
Overlay
14 Bytes
(4 Bytes Optional)
Ether Type
0x0800
VLAN ID
Tag
VLAN Type
0x8100
Src. MAC Address
Dest. MAC Address
48
48
16
16
16
20 Bytes
Dest. IP
Source IP
Header
Checksum
Protocol 0x11 (UDP)
IP Header
Misc. Data
72
8
16
32
32
8 Bytes
Checksum 0x0000
UDP Length
VXLAN Port
Source
Port
16
16
16
16
8 Bytes
Reserved
VNI
Reserved
VXLAN Flags RRRRIRRR
8
24
24
8
Src VTEP MAC Address
Next-Hop MAC Address
Src and Dst addresses of the VTEPs
Allows for 16M possible Segments
UDP 4789
Hash of the inner L2/L3/L4 headers of the original frame.
Enables entropy for ECMP Load balancing in the Network.
50 (54) Bytes of Overhead

## Slide 22: VXLAN Flood&Learn
V1
V3
MAC | VNI | VTEP
MAC_A | 30000 | E1/12
Host B
MAC_B / IP_B
MAC | VNI | VTEP
MAC_B | 30000 | E1/4
Virtual Switch
MAC | VNI | VTEP
MAC_C | 30000 | E1/8
V2
Destination Group
239.1.1.1
(01:00:5E:01:01:01)
Host A
MAC_A / IP_A
Host C
MAC_C / IP_C

## Slide 23: VXLAN Packet Forwarding
VXLAN Flood&Learn
Host A
MAC_A / IP_A
Host B
MAC_B / IP_B
V3
4
MAC | VNI | VTEP
MAC_B | 30000 | E1/4
MAC_A | 30000 | V1
MAC | VNI | VTEP
MAC_A | 30000 | E1/12
MAC_B | 30000 | V2
V2
V1
SIP: IP_A
DIP: IP_B
SMAC: MAC_A
DMAC: MAC_B
1
SIP: IP_A
DIP: IP_B
SMAC: MAC_A
DMAC: MAC_B
Underlay
SIP: IP_V1
DIP: IP_V2
SMAC: MAC_V1
DMAC: hop-by-hop
UDP
VXLAN VNID: 30000
SMAC: MAC_A
DMAC: MAC_B
SIP: IP_A
DIP: IP_B
Overlay
2
SIP: IP_V1
DIP: IP_V2
SMAC: hop-by-hop
DMAC: MAC_V2
Underlay
VXLAN VNID: 30000
SMAC: MAC_A
DMAC: MAC_B
SIP: IP_A
DIP: IP_B
UDP
Overlay
3

## Slide 24: VTEP Discovery (1)
Multicast Independent
Host A
MAC_A / IP_A
Host B
MAC_B / IP_B
Virtual Switch
Host C
MAC_C / IP_C
Host Y
MAC_Y / IP_Y
RR
RR
V2
V1
V3
1
1
1
VTEPs advertise their VNI
membership within the Control-Plane
1

## Slide 25: VTEP Discovery (2)
Multicast Independent
Host A
MAC_A / IP_A
Host B
MAC_B / IP_B
Virtual Switch
Host C
MAC_C / IP_C
Host Y
MAC_Y / IP_Y
RR
RR
V2
V1
V3
2
2
2
2
BGP consolidates and
propagates VTEP list for VNI
Peer | VNI | VTEP
V1 | 30000 30001 | V1
V2 | 30000 | V2
Peer | VNI | VTEP
V1 | 30000 | V1
V3 | 3000030001 | V3
Peer | VNI | VTEP
V2 | 30000 | V2
V3 | 30000 30001 | V3
3
VTEP obtains list of VTEP
neighbors for each VNI
3
3
3

## Slide 26: Head-End Replication
Multicast Independent
Host A
MAC_A / IP_A
Host B
MAC_B / IP_B
Virtual Switch
ARP Request for IP_B
Src MAC: MAC_A
Dst MAC: FF:FF:FF:FF:FF:FF
5
ARP Request for IP_B
Src MAC: MAC_A
Dst MAC: FF:FF:FF:FF:FF:FF
5
Underlay
SIP: IP_V1
DIP: IP_V3
SMAC: MAC_V1
DMAC: MAC_V3
UDP
VXLAN VNID: 30000
ARP Request
SMAC: MAC_A
DMAC: FF:FF:FF:FF:FF:FF
Overlay
4
Host C
MAC_C / IP_C
Peer | VNI | VTEP
V1 | 30000 30001 | V1
V2 | 30000 | V2
RR
RR
V2
Peer | VNI | VTEP
V1 | 30000 | V1
V3 | 3000030001 | V3
V1
V3
Peer | VNI | VTEP
V2 | 30000 | V2
V3 | 30000 30001 | V3
1
ARP Request for IP_B
Src MAC: MAC_A
Dst MAC: FF:FF:FF:FF:FF:FF
2
Underlay
SIP: IP_V1
DIP: IP_V2
SMAC: MAC_V1
DMAC: MAC_V2
UDP
VXLAN VNID: 30000
ARP Request
SMAC: MAC_A
DMAC: FF:FF:FF:FF:FF:FF
Overlay
4
3

## Slide 27: How?

## Slide 28: Deployment Considerations
MTU and Overlays
Unicast Routing Protocol and IP Addressing
Multicast for BUM* Traffic Replication
Underlay

## Slide 29: MTU and VXLAN
Underlay
VXLAN adds 50 Bytes to the Original Ethernet Frame
Avoid Fragmentation by adjusting the IP Networks MTU
Data Centers often require Jumbo MTU; most Server NIC do support up to 9000 Bytes
Using a MTU of 9216* Bytes accommodates VXLAN Overhead plus Server max. MTU
Underlay
Outer IP Header
Outer MAC Header
UDP Header
VXLAN Header
Original Layer-2 Frame
Overlay
50 (54) Bytes of Overhead
*Cisco Nexus 5600/6000 switches only support 9192 Byte for Layer-3 Traffic
No Fragmentation Needed

## Slide 30: Building your IP Network – Interface Principles
Know your IP addressing and IP scale requirements
  Best to use single aggregate for all underlay Links and Loopbacks
  IPv4 only
  For each Point-2-Point (P2P) connection, minimum /31 required
  Loopback requires /32
Routed Ports/Interfaces
  Layer-3 Interfaces between Spine and Leaf (no switchport)
VTEP uses Loopback as Source-Interface
Underlay
V2
V1
V3

## Slide 31: Building your IP Network – Routing Protocols; OSPF
OSPF – watch your Network type
  Network Type Point-2-Point (P2P)
    Preferred (only LSA type-1)
    No DR/BDR election
    Suits well for routed interfaces/ports (optimal from a LSA Database perspective)
    Full SPF calculation on Link Change
  Network Type Broadcast
    Suboptimal from a LSA Database perspective (LSA type-1 & 2)
    DR/BDR election
    Additional election and Database Overhead
Underlay
OSPF Area 0
V2
V1
V3

## Slide 32: Building your IP Network – Routing Protocols; IS-IS
IS-IS – what was this CLNS?
  Independent of IP (CLNS)
  Well suited for routed interfaces/ports
  No SPF calculation on Link change; only if Topology changes
  Fast Re-convergence
  Not everyone is familiar with it
Underlay
IS-IS
V2
V1
V3

## Slide 33: Building your IP Network – Routing Protocols; iBGP
iBGP + IGP = The Routing Protocol Combo
  IGP for underlay topology & reachability (e.g. IS-IS, OSPF)
  iBGP for VTEP (loopback) reachability
  iBGP route-reflector for simplification and scale
  Requires two routing protocols
  Separates Links (IGP) from VTEPs (iBGP)
    End-Host information are still in iBGP but different address-family
Underlay

## Slide 34: Building your IP Network – Routing Protocols; eBGP
eBGP
  eBGP Peer is IP interface
    Loopback would require additional IGP and eBGP multi-hop
  Multiple Autonomous-Systems (AS)
    Minimum amount of AS is two
  Many BGP Neighbors
    For each neighboring p2p interface
  AS Path
    Src and Dst AS might be same
  No Route-Reflector
    But next-hop needs to be unchanged
Underlay

## Slide 35: Multicast Enabled Underlay
May use PIM-ASM or PIM-BiDir (Different hardware has different capabilities)
Spine and Aggregation Switches make good Rendezvous-Point (RP) Locations in Topologies
Reserve a range of Multicast Groups (Destination Groups/DGroups) to service the Overlay and optimize for diverse VNIs
In Spine/Leaf topologies with lean Spine
  Use multiple Rendezvous-Point across the multiple Spines
  Map different VNIs to different Rendezvous-Point for simple load balancing measure
  Use Redundant Rendezvous-Pint
Design a Multicast Underlay for a Network Overlay, Host VTEPs will leverage this Network
Underlay
 | Nexus 1000v | Nexus 3000 | Nexus 5600 | Nexus 7000/F3 | Nexus 9000 | ASR 1000 CSR 1000 | ASR 9000
Multicast Mode | IGMP v2/v3 | PIM ASM | PIM BiDir | PIM ASM / PIM BiDir | PIM ASM | PIM BiDir | PIM ASM / PIM BiDir
FYI

## Slide 36: Multicast Enabled Underlay – PIM ASM
PIM Sparse-Mode (ASM)
Redundant Rendezvous-Point using PIM Anycast-RP or MSDP
Source-Tree or Unidirectional Shared-Tree (Source-Tree shown)
  Shared-Tree will always use RP for forwarding
1 Source-Tree per Multicast-Group per VTEP (each VTEP is Source & Receiver)
Example from depicted topology
  3 VTEPs sharing same VNI and Multicast-Group mapping (single Multicast-Group)
  3x Source-Tree (1 per VTEP per Multicast-Group)
Underlay
PIM ASM
V2
V1
V3
RP
RP
Rendezvous-Point
RP

## Slide 37: Multicast Enabled Underlay – PIM ASM
PIM Sparse-Mode (ASM)
Redundant Rendezvous-Point using PIM Anycast-RP or MSDP
Source-Tree or Unidirectional Shared-Tree (Source-Tree shown)
  Shared-Tree will always use RP for forwarding
1 Source-Tree per Multicast-Group per VTEP (each VTEP is Source & Receiver)
Example from depicted topology
  3 VTEPs sharing same VNI and Multicast-Group mapping (single Multicast-Group)
  3x Source-Tree (1 per VTEP per Multicast-Group)
Underlay
PIM ASM
V2
V1
V3
RP
RP
Rendezvous-Point
RP

## Slide 38: Distributed IP Anycast Gateway*
Distributed Routing with IP Anycast Gateway (Integrated Route/Bridge IRB)
  Routing between VNI (Different Subnet)
  Bridging within VNI (Same Subnet)
Inter-VXLAN Routing Leaf/Access Layer
  All Leafs share gateway IP and MAC for a Subnet (No HSRP)
  A Host will always find its Gateway directly attached anywhere it moves
VXLAN/EVPN
Host Y
VNI 30001
Host A
VNI 30000
V1
V3
V2
*Requires EVPN Control-Plane.

## Slide 39: VXLAN/EVPN Fabric External Routing
The Border Leaf/Spine provides Layer-2 and Layer-3 connectivity to external Network
eBGP and OSPF are Layer-3 Routing Protocols available for external routing
Today, VRF-lite allows to extend VRF outside of the fabric
With Nexus 7000/7700 and F3, LISP & MPLS L3VPN becomes available for fabric extension
Overlay
VBL
WAN
V2
V1
V3

## Slide 40: Nexus 9300/9500 External Connectivity
VXLAN FABRIC
Border Leaf
Border Spine
RR
RR
Nexus 9300/9500
  VRF-lite (Layer-3 Classic Ethernet)
  VPC (Layer-2 Classic Ethernet)
BGP AS X
Nexus 9300/9500 as Border Leaf or Border Spine
V
V
BS
BS
core

## Slide 41: Nexus 7000/7700 (F3) Flexible External Connectivity
VXLAN FABRIC
Border Leaf
Border Spine
RR
RR
Nexus 7000/7700 (F3)
  VRF-lite (Layer-3 Classic Ethernet)
  VPC (Layer-2 Classic Ethernet)
  LISP*
  MPLS L3VPN*
BGP AS X
Nexus 7000/7700 as Border Leaf or Border Spine
V
V
BS
BS
core

## Slide 42: VXLAN/EVPN Fabric External Routing
Overlay
V2
V1
V3
VBL
WAN
VRF
A
VRF
B
VRF
C
VRF for External Routing
need to exist on Border Leaf
Interface-Type Options:
Physical Routed Ports
Sub-Interfaces
VLAN SVIs over Trunk Ports
Peering Interface can
be in Global or Tenant VRF

## Slide 43: Interconnecting Classic Ethernet Networks (Layer-2)
Inter-Pod Connectivity
Core
(Layer-3)
Classic Ethernet
vpc
V
V
Classic Ethernet
vpc
V
V
VXLAN/EVPN
VNI 30000
eBGP
Interconnecting Classic Ethernet Pods with VXLAN/EVPN is possible
  EVPN Control-Plane provides ARP suppression and avoids Flood&Learn
Ingress Replication to avoid Multicast requirement in Underlay
  Depends on various communication requirement factors (traffic requirements, amount of Sites, etc)
Multi-Homing requires VPC(!)
Loop in one Classic Ethernet Pod can influence the other Pod(s)

## Slide 44: Interconnecting VXLAN Networks (Layer-2)
Layer-3
Underlay
Layer-3
Underlay
Interconnecting VXLAN/EVPN Pods with VXLAN/EVPN is possible
  Control-Plane Domains (EVPN) can be separated (iBGP/eBGP)
Data-Plane Encapsulation is End-to-End!
  Leaf/TOR knows about all VTEP across the two Data Centers
  BUM Traffic is across Pods
Decision on Ingress Replication (Unicast) or Multicast is across all Pods being interconnected
Use Shared Route-Target to ensure Route Exchange!
Inter-Pod Connectivity
Core
(Layer-3)
V
V
V
VXLAN/EVPN
VNI 30000
VXLAN/EVPN
VNI 30000
V
V
V
eBGP
iBGP

## Slide 45: Interconnecting VXLAN Networks (Layer-3)
Layer-3
Underlay
Layer-3
Underlay
Interconnecting VXLAN/EVPN Pods with VXLAN/EVPN is possible
  Control-Plane Domains (EVPN) can be separated (iBGP/eBGP)
With Layer-3 interconnect, Data-Plane Encapsulation is separated
  Routing decision at DC-Edge results in Decapsulation
  Requires a Transit VNI between Sites
No Layer-2 Interconnect!
Inter-Pod Connectivity
Core
(Layer-3)
V
V
V
V
vpc
V
V
vpc
V
V
V
V
VXLA/EVPN
VNI 99000
VXLAN or VXLAN/EVPN
VNI 31000
VXLAN or VXLAN/EVPN
VNI 30000

## Slide 46: VXLAN/EVPN Designs
Leaf
V
V
V
V
V
Border
V
V
Spine
RR
RR
RR
RR
core
L2/L3
L2/L3
L2/L3
L2/L3
L2/L3
BL
BL
VXLAN Overlay
VPC
OSPF/PIM for Underlay Control-Plane
iBGP for Overlay Control-Plane
eBGP for External Connectivity (vrf-lite)
eBGP
BGP AS X
Nexus 9300 or 9500 as Spine (RP/RR)
Nexus 9300 or 9500 as Leaf (VTEP)
Nexus 9300 or 9500 as Border Leaf (VTEP)

## Slide 47: VXLAN/EVPN Designs
Leaf
V
V
V
V
V
Border
V
V
Spine
RR
RR
RR
RR
core
L2/L3
L2/L3
L2/L3
L2/L3
L2/L3
BL
BL
VXLAN Overlay
VPC
OSPF/PIM for Underlay Control-Plane
iBGP for Overlay Control-Plane
eBGP for External Connectivity (vrf-lite)
eBGP
BGP AS X
Nexus 7000/7700 as Spine (RP/RR)
Nexus 9300 or 9500 as Leaf (VTEP)
Nexus 7000/7700 with F3 as Border Leaf (VTEP)

## Slide 48: VXLAN/EVPN Designs
Leaf
V
V
V
V
V
Border
V
V
Spine
RR
RR
RR
RR
core
L2/L3
L2/L3
L2/L3
L2/L3
L2/L3
BL
BL
VXLAN Overlay
VPC
OSPF/PIM for Underlay Control-Plane
iBGP for Overlay Control-Plane
eBGP for External Connectivity (vrf-lite)
eBGP
BGP AS X
Nexus 5600 as Spine (RP/RR)
Nexus 5600 as Leaf (VTEP)
Nexus 7000/7700 with F3 as Border Leaf (VTEP)

## Slide 49: VXLAN/EVPN Designs
Border Spine
RR
RR
VXLAN Overlay
OSPF/PIM for Underlay Control-Plane
iBGP for Overlay Control-Plane
eBGP for External Connectivity (vrf-lite)
BGP AS X
Nexus 7000/7700 as Border Spine (VTEP/RP/RR)
Nexus 9300 or 9500 as Leaf (VTEP)
V
V
BS
BS
core
Leaf
V
V
V
V
V
V
V
L2/L3
L2/L3
L2/L3
L2/L3
L2/L3
L2/L3
L2/L3
VPC

## Slide 50: VXLAN/EVPN Designs
Border Spine
RR
RR
VXLAN Overlay
OSPF/PIM for Underlay Control-Plane
iBGP for Overlay Control-Plane
eBGP for External Connectivity (vrf-lite)
BGP AS X
Nexus 7000/7700 as Border Spine (VTEP/RP/RR)
Nexus 5600 as Leaf (VTEP)
V
V
BS
BS
core
Leaf
V
V
V
V
V
V
V
L2/L3
L2/L3
L2/L3
L2/L3
L2/L3
L2/L3
L2/L3
VPC

## Slide 51: VXLAN/EVPN Designs
Leaf
V
V
V
V
V
Border
V
V
Spine
RR
RR
RR
RR
core
L2/L3
L2/L3
L2/L3
L2/L3
L2/L3
BL
BL
VXLAN Overlay
VPC
OSPF/PIM for Underlay Control-Plane
iBGP for Overlay Control-Plane
eBGP for External Connectivity (vrf-lite)
eBGP
BGP AS X
Nexus 7000/7700 as Spine (RP/RR)
Nexus 9300 or 9500 as Leaf (VTEP)
Nexus 7000/7700 with F3 as Border Leaf (VTEP)

## Slide 52: VXLAN/EVPN Designs
Leaf
V
V
V
V
V
Border
V
V
Spine
RR
RR
RR
RR
core
L2/L3
L2/L3
L2/L3
L2/L3
L2/L3
BL
BL
VXLAN Overlay
VPC
OSPF/PIM for Underlay Control-Plane
iBGP for Overlay Control-Plane
eBGP for External Connectivity (vrf-lite)
eBGP
BGP AS X
Nexus 5600 as Spine (RP/RR)
Nexus 5600 as Leaf (VTEP)
Nexus 7000/7700 with F3 as Border Leaf (VTEP)

## Slide 54: Questions?