## Slide 1: Introduction to Cisco Virtual Topology System (VTS)
Vijay Arumugam Kannan - Product Manager, VTS

## Slide 2: Agenda
Cisco Data Center SDN Strategy
Cisco Virtual Topology System (VTS)
VTS Use Cases
VTS Functionality & Workflows
VTS Demo
Q & A
Cisco Virtual Topology System

## Slide 3: Data Center Trends
Traditional Applications
Monolithic Model
Multi-tier Apps
Manual Interaction
Static Networks, L2 based Data Center
Complex, Custom & Closed
Cloud-native applications
Business Agility with cloud model
Micro-services / Bi-Modal IT / DevOps
Policy Driven Automation
L3 Fabric Data Center, SDN Framework for cross-domain automation, and abstraction, analytics (visibility) and programmability
Application Shift
Networking Shift
Physical and Manual
Single Tenant, L2 based Data Center
Limited Mobility, Bare metal workloads
”
Distributed and Automated
Multi-tenant,.
Dynamic and virtual workloads
Cloud Shift
Agile: CI/CD, Devops,
Scale Out, Containers,
Microservices
Integration: APIs,
IOT, M2M, Cloud
Social Media
Scale: Connectivity, Tenancy,
Secure Access
Data: Volume,
Streaming & Predictive Analytics
+
+
+
Today’s App
Application and Server migration towards virtualization & cloud create requirements for agile networks
Notes: Today’s applications are changing
They are moving away from monolithic model to micro-services model and are becoming highly distributed in nature.
The way these applications are delivered and consumed have also changed.
With the trends such as BYOD, IOT, Big Data, enterprise customers are constantly looking to cloud based development and delivery models for these applications so that they can be provisioned made available to their users in a matter of seconds irrespective of location of these end devices
The huge growth in traffic driven by video, mobile and cloud usage are overwhelming current SP networks and SPs are looking o transform their networks
As a part of this transition, SPs are using cloud technology to support network functions to provide agility on delivering services to customers with greater agility and operational efficiency. The motivation here is to realize CAPEX reduction and OPEX benefits.
Cloud computing has become relevant to enterprise and SP customers. Because this enables them able to provide on-demand automated provisioning of applications and services for their end users irrespective of the location or devices and also enable rapid elasticity of these services.

## Slide 4: Service Orchestration velocity hindered by manual network process
ToR
ToR
Spine
Spine
ToR
Hypervisor
VM
x86 Server
Hypervisor
VM
x86 Server
Service Orchestration
Compute Orchestration
Network Orchestration
Manual Network Change Request
IP Configuration
Firewall Configuration
VLAN configuration
Automated Compute Request
Virtualized Compute
Auto Instantiation
Hypervisor
VM
x86 Server
VM
Compute is completely Virtualized
Compute Request completed in Seconds
Network is partially Virtualized
Network Change Request completed in days/weeks
Notes: Cloud enabled Modern day Datacenter
For an application environment or data center to be ready for cloud environment, data center infrastructure should support scale out architectures based on compute and network
The data center infrastructure that includes computes, network and storage should be virtualized and automated
CLOS fabric scales out based on compute and network, to cater to distributed nature of these applications.
Server Virtualization advancements over the last decade has not only helped to avoid high capex by reducing the server footprint in datacenters
but have also have helped to reduce OPEX by enabling automated provisioning of compute nodes in a matter of seconds.
But there are bottlenecks
The network that connects the physical and virtual nodes are not completely virtualized. It has to provisioned manually and it takes weeks/days to complete and are prone to human configuration errors.

## Slide 5: Technology Trends
Each addressing an aspect of challenges and opportunities
  Scalable Fabric Data Center CLOS Fabric to scale out based on Network and Compute
  SDN Control & Data Plane separation…Centralized Control (automation & programmability)
Scalable Fabric
Open APIs
Network
Virtualization
SDN
  Open APls Distributed control plane components, Bare Metal, Physical network entities, all exposing APIs (programmability)
  Network Virtualization
  Abstract network connectivity and services in to logical virtual networks that are decoupled from underlying physical infrastructure (abstraction, multi-tenancy and agility)

## Slide 6: Service Orchestration velocity increased by Network Overlays/SDN in the data center
Service Orchestration
Compute Orchestration
Network Orchestration
Automated Network Change Request
Policy based Configuration
Abstraction & Programmability
Virtualized L2/L3 networks
Automated Compute Request
Virtualized Compute
Auto Instantiation
External Network
App
Zone1
Firewall
App
Zone2
Network
Segment A
Network
Segment B
Network
Segment C
External Network
App
Zone1
Firewall
App
Zone2
Network
Segment A
Network
Segment B
Network
Segment C
Tenant A – Topology1
Tenant B - Topology 2
NX-API, CLI, YANG
L3 CLOS fabric that scales out based on compute and network to cater to distributed nature of applications is the foundation of business agility
Network Overlays based Network Virtualization provides flexibility ], tenant isolation and allows for resources to be dynamically provisioned
SDN Controller for automation, programmability and NVE management
SDN Based Overlays introduces agility and automation to Network Orchestration
Compute is completely Virtualized
Compute Request completed in Seconds
Network is completely Virtualized
Network Change Request completed in seconds

## Slide 7: Network Virtualization and Overlays
Network virtualization: ability to separate, abstract and decouple the physical infrastructure & topology from a ‘logical’ topology or infrastructure typically by creating overlay networks..
External Network
App
Zone1
Firewall
App
Zone2
Network
Segment A
Network
Segment B
Network
Segment C
External Network
App
Zone1
Firewall
App
Zone2
Network
Segment A
Network
Segment B
Network
Segment C
Tenant A - Topology 1
Tenant B - Topology 1
Network overlays disassociates applications from physical networks infrastructure & topology, allowing a transition to cloud based multi-tenanted & scalable networks.
Application and Server migration towards virtualization & cloud are driving the current network transition to the SDN/Network Overlays in the data center
Notes: Network Overlays provides flexibility and cater to scale and elasticity of Virtualized datacenters which is defined by extreme dynamism of VM orchestrators for the rapid creation, modification, and deletion of virtual networks
Network Overlays provides topology independence and location independence. Decoupling from physical infrastructure provides agility and Operational efficiency, thereby transforming data center economics

## Slide 8: MPBGP-EVPN &VXLAN based Overlays
EVPN
Layer-2 MAC and Layer-3 IP information distribution by Control-Plane (BGP)
Overlay Forwarding Table |  | 
T1,S1 | MAC, IP Address | P1/2
T1,S2 | MAC, IP Address | VTEP2
T2,S3 | MAC, IP Address | VTEP3
T2,S4 | MAC, IP Address | VTEP4
Built in multi-tenancy (at scale)
Integrated Routing/Bridging (IRB) for Optimized Forwarding
Minimize flooding through ARP suppression
Fast convergence upon network failures and host movements
Security through VTEP peer-authentication
VXLAN
IP routing – proven, stable, scalable
ECMP – utilize all available network paths
Flexible placement of multitenant segments
Better utilization of network paths
Scalable network domain (16M VNI vs. 4K VLANs)
BGP-EVPN/VXLAN based overlays provides flexibility, manageability, isolation, multi-tenancy, scalability & convergence.
Notes: Industry standard protocol for multi-vendor interoperability
Build-in multi-tenancy support
  Leverage MP-BGP to deliver VXLAN with L3VPN characteristics
Truly scalable with protocol-driven learning
  Host MAC/IP address advertisement through EVPN MP-BGP
Fast convergence upon host movements or network failures
  MP-BGP protocol driven re-learning and convergence
  Upon host movement, the new VTEP will send out a BGP update to advertise the new location of the host
Optimal traffic forwarding supporting host mobility
  Anycast IP gateway for optimal forwarding for host generated traffic
  No need for hair-pinning to to reach the IP gateway
ARP suppression
  Minimize ARP flooding in overlay
Head-end Replication with dynamically learned remote-VTEP list
  Head-end replication enables multicast-free underlay network
  Dynamically learned remote-VTEP list minimizes the operational overhead of head-end replication
VTEP peer authentication via MP-BGP authentication
  Added security to prevent rogue VTEPs or VTEP spoofing

## Slide 9: Cisco SDN: Providing Choice in Automation and Programmability
Programmable Network
Programmable Fabric
Application Centric Infrastructure
DB
DB
Web
Web
App
Web
App
VxLAN-BGP EVPN standard-based
3rd party controller support
Turnkey integrated solution with security, centralized management, compliance and scale
Automated application centric-policy model with embedded security
Broad and deep ecosystem
VTS for software overlay provisioning and management across N2K-N9K
VTS
Modern NX-OS with enhanced NX-APIs
Automation Ecosystem (Puppet, Chef, Ansible etc.)
Common NX-API across N2K-N9K
Service Providers
Mega Scale Datacenters
9
Mass Market (commercial, enterprises, public sector)
Notes: Application and Server migration towards virtualization & cloud create requirements for agile and scalable networks. This is driving the current network transition to the SDN. With SDN, there is a migration from intelligent hardware platform components to a more centralized software intelligence. A centralized software helps customers improve their operational efficiencies at cloud scale and also enhance troubleshooting capabilities in the network. This helps the customer better align their network to meet their business goals.
SDN also changes the paradigm on how customer buy products, what features matter in the product. SDN is also shaping a new ecosystem build around SDN applications.
Software Defined Networking and OpenDaylight is transforming how we look at the network. The opportunities it creates are endless, we know some of them and will discuss few in the presentation. What Cisco is doing with OpenDaylight is taking the Open Source SDN Platform and putting capabilities around it to make it the best SDN platform in the market to help you win with customers
The discussion agenda is as above:
[1] What OpenDaylight is from the organization view and the OpenDaylight product
[2] Get into Cisco’s commercial distribution of OpenDaylight -- Cisco Open SDN Controller -- this will sold and supported as any other Cisco product.
[3] How we are enabling developers on the platform. As an open platform it has number of developer and integration opportunities and we are building a developer ecosystem
[4] A quick view of targeted use cases that we see today. Not an exhaustive list but a sample list of use cases we are focusing on initially
[5] Talk about how we are using Open SDN controller in the WAE. An example of an SDN application.
[6] Call to action.

## Slide 10: Flexible Overlays with VTS

## Slide 11: Cisco Virtual Topology System (VTS)
  Simplified Management for Ease of Operations
Open standards based Overlay Provisioning and Management System
Automates Overlay provisioning across Cisco Datacenter Top of Rack Nexus switches (Nexus 2000- Nexus 9000), Virtual Switches & DCI routers
Automates fabric provisioning for both virtual and bare metal workloads.
Programmable using North Bound REST APIs
Tighter Integration with Orchestration systems such as Openstack, vCenter and Cisco NSO

## Slide 12: VTS : Realizing the Cloud Enabled Data Center
Scale & Automation Drives Business Success
Flexible, on-demand EVPN/VXLAN based overlays with underlay awareness.
Abstracted & Virtualized
Network As A Service
Declarative, transactional, granular policies
for instantiation of overlays &
secure connectivity
Support Scale out architectures in terms of network and compute
Automation of fabric provisioning for physical and virtual workloads.
Deployment Flexibility, Visibility, management & Troubleshooting
Service Aware Overlay
Policies
Orchestration
Scalable Fabric
Cisco Virtual Topology System
Cisco Virtual Topology System (VTS) is the cornerstone of Cisco SP DC SDN strategy with increased investment and customer deployment across Worldwide Tier 1 Service Providers

## Slide 13: Model based provisioning – What does the user see?
External Network
App
Zone1
Firewall
App
Zone2
Network
Segment A
Network
Segment B
Network
Segment C
User Policy – Conceptual, Simple & Abstract
VTF
DCI
TOR/Leaf
OVS/DVS
Services
Inventory (Devices, Software, Capabilities, Groups & Topology)
Policy & Models
to
Infrastructure
Mapping
Provisioning
Actions
VTF
Appliance VM
Tenant VM
Tenant VM
Host
DC Fabric
(OSPF or BGP as the
Underlay Protocol)
SR-IOV
Tenant VM
Tenant VM
Tenant VM
Host
Border Leaf
&
DCI
(Integrated or
Separated)
Bare Metal
Appliance
(Eg, Firewall)
Host
LEAF
SPINE
OVS/DVS
Appliance VM
Tenant VM
Tenant VM
Host
Bare Metal
Application
Spine
Physical Network Appliances
Virtual Topology
Controller
DCI Router
Border Leaf
Network Based
VTEPs
Host Based VTEPS
VNFs
Notes: Input two the system is stuff on the left – policies/user-intent + devices and their software/capabilities

## Slide 14
VTF
DVS
Cisco Nexus 2000, 3000,
5000, and 7000 Series
Cisco Nexus 9000 Series
Cisco ASR 9000 Series
Virtual Compute Environment
VTS Architecture
NETCONF/YANG – CLI – NXAPI – SNMP – REST API
REST API
Notes: If you double click on VTS you can break it down as the policy and control plane.
VTS offers a robust policy plane and a control plane.
The policy plane helps you provide service definitions and infrastructure polices. It also houses an inventory of devices.
The control plane is used for device management using one of the southbound protocols and it also used to understand and distribute reachability information using MP-BGP protocols.

## Slide 15: VTS Architecture – Hardware VTEP
Cisco VTS
REST API
NX-API, CLI, YANG
VMware vCenter
ToR
ToR
Spine
Spine
ToR
Hypervisor
VM
x86 Server
Hypervisor
VM
x86 Server
Hypervisor
VM
x86 Server
VM
Border Leaf
VTEP
DCI
Nexus 9300/9500/5000/7x00– Spine (RR)
ASR9000, Nexus 7x00– DCI
VTEP
VTEP
VTEP
VTEP
Nexus 9200/9300/5600/7x00 – ToR
Hardware Switches

## Slide 16: VTS Architecture – Software VTEP
DCI
ToR
Hypervisor
Cisco VTS
ToR
ToR
Spine
Spine
Hypervisor
VM
x86 Server
Hypervisor
VM
VM
x86 Server
REST API
NX-API, CLI, YANG
VTEP
VTEP
Border Leaf
VTEP
VMware vCenter
Hypervisor
VM
x86 Server
VTF
VTF
VTEP
Virtual Topology Forwarder

## Slide 17
Cisco VTS
ToR
ToR
Spine
Spine
ToR
Hypervisor
VM
x86 Server
Hypervisor
VM
VM
x86 Server
REST API
DCI
NX-API, CLI, YANG
VTEP
VTEP
Border Leaf
VTEP
VMware vCenter
Hypervisor
VM
x86 Server
VTF
VTF
VTEP
User space, Multi-tenant, line rate packet forwarder
Uses Vector Packet Processing technology
Fully integrated with Intel DPDK
Supports VXLAN, can be extended to support MPLSoGRE, L2TPv3, MPLSoUDP, native MPLS and SR
Programmed by VTS using Restconf/YANG
VTS Architecture – Virtual Topology Forwarder
Cisco US Patent 7,931,636 (filed 2004)

## Slide 18: Virtual Topology Forwarder
User space, Multi-tenant, line rate packet forwarder
Uses Vector Packet Processing technology
Fully integrated with Intel DPDK
Supports VXLAN, MPLSoGRE, L2TPv3, MPLSoUDP, native MPLS and SR
Programmed by VTS
Open Sourced at http://www.fd.io
Multi-threaded and 64-bit clean
Supports for IPv4 & IPv6
Kernel Space
User Space
virtio
virtio
virtio
Guest 1
Guest 2
NIC
PCI Pass through/SR-IOV
VPP
vhost-user
Server
VM/Container
VM/Container
VM/Container
Notes: By increasing cores,
VPP can run as both as use space virtial machine or as host process

## Slide 19: VPP vs OVS Performance Benchmarking

## Slide 20
Hardware based Overlays
Software (VTF) based Overlays
Hybrid Overlays
VTS – Flexible Network Overlays
Hardware VTEP
(TOR Leaf Switch)
Software VTEP
(Virtual Topology Forwarder / Fd.io)

## Slide 21: VTS – Forwarding North-South Traffic (DCI, WAN)
NX-API, CLI, YANG
Cisco VTS
REST API
VMware vCenter
ToR
ToR
Spine
Spine
ToR
Hypervisor
VM
x86 Server
Hypervisor
VM
VM
x86 Server
DCI
VTEP
VTEP
Border Leaf
VTEP
Hypervisor
VM
x86 Server
VTF
VTF
VTEP
L2 or L3 default route to BL/DCI
L2 (VLAN)
L2/L3 VxLAN
Extend L3 VXLAN to DC-gateways
Associate L3 VNID to VRF
Configure external VRF peering on DC-gw
Optionally, configure DCI VRF peering, VPN
Default route-policy
Configure internal subnets attached to Router as aggregates on DC-gw (Towards DCI)
Configure default-originate on DC-gw or DCI (Towards overlay)
Notes: Application and Server migration towards virtualization & cloud create requirements for agile and scalable networks. This is driving the current network transition to the SDN. With SDN, there is a migration from intelligent hardware platform components to a more centralized software intelligence. A centralized software helps customers improve their operational efficiencies at cloud scale and also enhance troubleshooting capabilities in the network. This helps the customer better align their network to meet their business goals.
SDN also changes the paradigm on how customer buy products, what features matter in the product. SDN is also shaping a new ecosystem build around SDN applications.
Software Defined Networking and OpenDaylight is transforming how we look at the network. The opportunities it creates are endless, we know some of them and will discuss few in the presentation. What Cisco is doing with OpenDaylight is taking the Open Source SDN Platform and putting capabilities around it to make it the best SDN platform in the market to help you win with customers
The discussion agenda is as above:
[1] What OpenDaylight is from the organization view and the OpenDaylight product
[2] Get into Cisco’s commercial distribution of OpenDaylight -- Cisco Open SDN Controller -- this will sold and supported as any other Cisco product.
[3] How we are enabling developers on the platform. As an open platform it has number of developer and integration opportunities and we are building a developer ecosystem
[4] A quick view of targeted use cases that we see today. Not an exhaustive list but a sample list of use cases we are focusing on initially
[5] Talk about how we are using Open SDN controller in the WAE. An example of an SDN application.
[6] Call to action.

## Slide 22: VTS - EVPN Control Plane Reachability information
ToR
ToR
Spine
Spine
ToR
Hypervisor
VM4
VM2
x86 Server
DCI
NX-API, CLI, YANG
VTEP1
VTEP2
Border Leaf
VTEP
Hypervisor
VM1
x86 Server
Hypervisor
VM5
x86 Server
VTF
VTF
VTEP4
TOR
Hypervisor
VM3
x86 Server
VTEP3
RR
VTEPs advertise host routers (IP+MAC) to local hosts
Cisco VTS
REST API
VMware vCenter
2
MP—BGP propagates routes for hosts to all other VTEPs
2
Hostt routes are installed in the RIB
2
RestConf
VTS is used to deploy the RR at the Spines or in VTS Control plane
Use MP-BGP with EVPN Address Family on Nexus ToR and VTS to distribute reachability information
VTS then provisions VTFs with information through RestConf interface
Overlay Forwarding Table |  | 
VM4 | MAC, IP Address | VTEP2
MP BGP

## Slide 23: VTS Use Cases

## Slide 24: VTS Use Cases
Multi-Tenant
Data Centers
Network-Function
Virtualization

## Slide 25: Multi Tenant Data Center
US Tier1 Service Provider
Leaf
OTNGN
(CORE MPLS)
PE
Border / Services Leaf
Spine
VTS
Bare
Metal
Host
Host
VM
Business Unit1
Business Unit2
Business Unit3
Bare
Metal
Host
Host
Bare
Metal
POD1
PE
DCNM
UCSD
Vcenter
Host
VTS
BMA
vRR
Host
Border Leaf
Rack1
Rack2
Business Unit4
VTF
Underlay Manager
POD2
POD3
POD4
Multi VMM environment with different trust zones
Tenancy based on IPv4/IPv6(dual stack) capable overlay networks
Hybrid overlays
Redirect select traffic to the services connected to the BL

## Slide 26: Multi Tenant Colocation Environment
Service Provider in Europe
Internet and VPN as service offerings
End Customers attached directly via Baremetal to Fabric
Ability to connect the same customers across multiple Data Center.
FW and LB within the Fabric.

## Slide 27: Multi Site Data Centers
Community Cloud Provider in Asia
For Disaster recovery, High Availability
Integrate EVPN/VXLAN to MPLS-L3VPN
IP/MPLS WAN

## Slide 28: Cisco NFV Integration with VTS
ToR
ToR
Spine
Spine
ToR
Hypervisor
NFV VM
x86 Server
Hypervisor
NFV VM
x86 Server
VTF
VTF
VTEP
VTEP
x86 Server
VTEP
VXLAN
Bare Metal Network
Function

## Slide 29: NFV Use case
NSO: Network Service Orchestrator
VTS: Virtual Topology System
VTS: Virtual Topology System
ToR: Top of Rack switch
PNF: Physical Network Function
VNF: Virtual Network Function
dVS: distributed Virtual Switch
PE: Provider Edge
Service Provider in Asia
Nexus 9300 (ToR)
Nexus 9300 (ToR)
PNF1
VNF1
VNF2
dVS
PNF2
VNF1
VNF2
dVS
MPLS VPN Network
VPN PE
& VXLAN Gateway
VXLAN
VTS
vCenter
VTS
Plug-in
VLANs
VLANs
VLANs
VLANs
Admin Tools
Customer Portal
OSS/BSS
REST API
BGP-EVPN
Orchestration & Controllers Layer
Virtual Overlay Networking Layer
Virtual Infrastructure, VNF & PNF Layer
NSO
ESC
Notes: 1. Building Virtual IP-based overlay network over multiple DC sites to provide virtual networking services offered by current MGW.
  This is the Scope of this RFI
2. Building End-user portal through which end users can request add/delete/change network services on-demand.
3. The end-user portal should also be able to configure gateway routers(PEs) connecting MGW network to existing L2/L3 VPN or public Internet.

## Slide 30: VTS Functionality & Workflows

## Slide 31: VTS Functionality: Discovery & Topology
VMware vCenter
Cisco VTS
ToR
ToR
Spine
Spine
ToR
Hypervisor
VM
x86 Server
Hypervisor
VM
x86 Server
VTF
VTF
Hypervisor
VM
VM
x86 Server
REST API
DCI
NX-API, CLI, YANG
VTEP
VTEP
VTEP
Border Leaf
VTEP
VM Discovery
VMM Integration
Dynamic Provisioning
Device Topology Discovery
LLDP
Import configuration file
Server Discovery
LLDP
Import Server to TOR Connection

## Slide 32: VTS Functionality - Resource Pools
VMware vCenter
Cisco VTS
ToR
ToR
Spine
Spine
ToR
Hypervisor
VM
x86 Server
Hypervisor
VM
x86 Server
VTF
VTF
Hypervisor
VM
VM
x86 Server
REST API
DCI
NX-API, CLI, YANG
VTEP
VTEP
VTEP
Border Leaf
VTEP
Local Device Resource Pools
VLAN
Global Resource Pools
VNI (VXLAN Network Identifier)
Multicast IP Pool
Manual resources management leads to errors and misconfigurations
Automated Resource Allocation and de-allocation on provisioning
Automated VLANs to VNIs to ensure connectivity

## Slide 33: VTS Functionality: Infrastructure Policy
ToR
ToR
Spine
Spine
ToR
Cisco VTS
VTF
VTF
VM
VM
Spine
Spine
ToR
ToR
VTF
VTF
VM
VM
Border Leaf
Border Leaf
VTF
VTF
VM
VM
DC POD A
DC POD B
[L2GW]
[L3GW – BL]
[L3GW – DCI]
[L2GW]
[L2GW]
[L2GW]
[L2GW]
[L3GW – DCI]
[L3GW – DCI]
[L3GW – DCI]
[L3GW – BL]
[L3GW – BL]
[L3GW – BL]
[L3GW – L3]
[L3GW – L3]
Distributed L2/L3 gateway Mode
Centralized L3 Gateway

## Slide 34: Cisco VTS Operational models
Multi VMM (Roadmap)
VMM Initiated
VTS GUI based
VTS Plugin in VMM initiated workflow.
Network objects creation is initiated in VMM
The Network segments are shared across VMMs
Network objects can be created at VMMs or at VTS
Network and Compute groups work in Silos
Port-group and vlan information are exchanged offline as the VMs are attached.
VTS
VTS
vCenter
vCenter
VTS
Degree of Automation

## Slide 35
Create a Tenant
Add Network to the Tenant
  Add Subnet
  Select the ToR and host facing ports
VLAN and VNID is automatically allocated
Layer-2 VXLAN segment is configured on the ToR switches
VTS Functionality: Overlay Configuration through GUI

## Slide 36
ToR
ToR
Spine
Spine
ToR
Hypervisor
VM
x86 Server
Cisco VTS
OpenStack Project View
Hypervisor
VM
x86 Server
VTF
VTF
VTEP
VTEP
Hypervisor
VM
VM
x86 Server
VTEP
Create Tenant Networks
1
VNID assigned for each network
3
Tenent and Tenant Networks Created
2
REST API
VM Host info captured by VTS and mapped to the right ToR & ToR port using topology database
5
Attach VM to Network
4
VXLAN
NX-API, CLI, YANG
VTS : OpenStack Workflow

## Slide 37
ToR
ToR
Spine
Spine
ToR
Hypervisor
VM
x86 Server
Cisco VTS
OpenStack Project View
Hypervisor
VM
x86 Server
VTF
VTF
VTEP
VTEP
Hypervisor
VM
VM
x86 Server
VTEP
Create Tenant Networks
1
VNID assigned for each network
3
Tenent and Tenant Networks Created
2
REST API
Attach VM to Network
4
VM Host info captured by VTS and mapped to the right ToR & ToR port using topology database
5
Neutron agent modified to request VLAN information from VTS before programming vSwitch
7
VLAN
VLAN
VLAN
VLAN
VXLAN
VXLAN
NX-API, CLI, YANG
VTS provisions VTEP, VLAN for each VTEP and EVPN on ToR/VTF
6
vlan 1,1700-711,2000
vlan 1706
vn-segment 46006
evpn
evi 46006 vni
bgp
rd auto
route-target import auto
route-target export auto
interface nve1
no shutdown
source-interface loopback0
member vni 46006
host-reachability protocol bgp
mcast-group 224.1.1.1
VTS : OpenStack Workflow

## Slide 38
ToR
ToR
Spine
Spine
ToR
Hypervisor
VM
x86 Server
Cisco VTS
OpenStack Project View
Hypervisor
VM
x86 Server
VTF
VTF
VTEP
VTEP
Hypervisor
VM
VM
x86 Server
VTEP
Create Tenant Networks
1
VNID assigned for each network
3
Tenent and Tenant Networks Created
2
REST API
Attach VM to Network
4
VM Host info captured by VTS and mapped to the right ToR & ToR port using topology database
5
Neutron agent modified to request VLAN information from VTS before programming vSwitch
7
VLAN
VLAN
VLAN
VLAN
VXLAN
VXLAN
NX-API, CLI, YANG
VTS provisions VTEP, VLAN for each VTEP and EVPN on ToR/VTF
6
Create router and attach interfaces to tenant networks
8
VTS provisions L3 VXLAN (distributed L2/L3) , Anycast gateway with EVPN
9
vlan 1708
vn-segment 46008
vrf context vni-46008
vni 46008
rd auto
address-family ipv4 unicast
route-target both auto
fabric forwarding anycast-gateway-mac 0002.0002.0002
#Anycast Gateway MAC, identically configured on all VTEPs
interface Vlan1706
no shutdown
vrf member vni-46008
ip address 192.168.4.1/24 ---> Anycast GW Address
fabric forwarding mode anycast-gateway
interface Vlan1708
no shutdown
vrf member vni-46008
ip forward
router bgp 23
router-id 4.4.4.4
address-family ipv4 unicast
address-family l2vpn evpn
retain route-target all
…..
vrf vni-46008
address-family ipv4 unicast
advertise l2vpn evpn
evpn
evi 46008 vni
bgp
rd auto
route-target import auto
route-target export auto
VTS : OpenStack Workflow

## Slide 39: Demo: VTS Functionality & Workflow

## Slide 40: Summary

## Slide 41: Why Cisco VTS?
Seamless Integration
Multi-Hypervisor
Multi-VMM
Heterogeneous
Workloads
Automated
DCI/WAN
Service Assurance
Agility and Automation
Network as a
Service
Investment Protection
Policy Driven
Infrastructure
Bare metal
Apps/Services
N2k-N9k, ASR
Support
Integration with
Orchestrators
Host Based
Overlays
Network
Connectivity
Custom NB
Integration
Group Based
Policies
Multi-Tenancy
Services
Integration (P&V)
Interoperability
Scale
Performance
Efficiency
Scale-Out PODs
Fabric Efficiency
Multi-POD &
Multi-DC
Open
Control &
Data Plane
Programmable
Architecture
(NB & SB)
Interoperability
(MPLS/VPN, OTV)
Notes:   Investment Protection - VTS supports the entire Nexus portfolio, thus bringing the benefits of automation and operational simplicity to the entire Nexus family.
  Faster Network Provisioning - through an automated policy-driven approach across both virtual and physical workloads.
  Seamless Integration - through open APIs with cloud orchestration systems like OpenStack and vCenter
  Improved Resource Utilization - through the creation of a flexible pool of resources which can be securely allocated and re-allocated on demand maximizing the return on infrastructure investment and reducing capex
  Scalability - using standards based BGP-EVPN based control plane to manage VXLAN overlays extending workload placement and mobility diameter seamlessly without compromising performance.
  Multi-Vendor support – Extensible to multi-vendor environments by leveraging Cisco Tail-f technology

## Slide 42
NFV Ecosystem
Full stack NFV solution
Integration with NSO and VNF life-cycle manager ESC
Dynamic service chaining capabilities
Virtual Topology System
(Policy Plane & Control Plane)
Transactional policy models; ability to flag transaction errors & rollback
Architecture to easily integrate third party network elements
Virtual Topology Forwarder
User space without any kernel modifications
Multi-tenanted, L2/L3 capable including VXLAN & MPLS
Line rate packet forwarder
Network Endpoint
Ecosystems
Enabling SW and HW overlays in bare-metal and virtualized environment
N2k-N9k, ASR 9K, and Virtual forwarder support
Cisco Differentiation

## Slide 43: For More Information
http://www.cisco.com/go/vts

## Slide 45: Backup

## Slide 46: VTS VM Requirements
VM | Memory | CPU
VTC | 16 Gb (16777216) | 8 cores
VTF | 16 Gb (16777216) | 2 cores
XRVR | 32 Gb (33554432) | 6 cores

## Slide 47: VTS Scalability Numbers