## Slide 1: IOS-XR Zero Touch Provisioning
Patrick Warichet TME
February 2017

## Slide 2
Introduction
iPXE
  iPXE Demo
Zero Touch Provisioning (ZTP)
  ZTP Demo
Agenda

## Slide 3: Introduction

## Slide 4: Traditional NetOps Upended by Evolved Needs of SP Customers
* Source: Google
Evolved SP/Cloud Scale
Network Operations
SW Modularity & Extensibility
Automation
Visibility & Control
Day 1
CONFIGURE
Day 2
MANAGE
& OPTIMIZE
Day 0
INSTALL
Traditional Network Operations
Inflexible
SW
Manual
Provisioning
Fragmented Topology View and Complex Routing
DevOps
Automated services
Simple to scale
Agile, open software
Notes: To gain a better perspective, let’s take a look at network operations. It basically breaks down into 3 buckets:
Day 0 operations – new device installation
Day 1 operations – initial configuration of new device
Day 2 operations – management & optimization of current network infrastructure
Day 0 and Day 1 operations are one-off operations versus Day 2 operations which are on-going throughout the lifecycle of the network infrastructure.
The Traditional Network Operations model is characterized by:
- Inflexible software where it is tightly coupled with hardware. There is little room for customization
- Manual provisioning: CLI-based (Human Readable Interface), limited automation mainly through CLI scripts
- Fragmented view of topology and complex routing: limited capabilities to steer traffic from shortest path determined by routing protocols
There is also the DevOps model from the IT world which is based on automated services, simplicity in scale, and agile and open software
Consider these large scale challenges which Google cited during a recent NANAOG conference, referring to their own operational environment (https://www.nanog.org/sites/default/files/meetings/NANOG64/1011/20150604_George_Sdn_In_The_v1.pdf):
Over 30,000 configuration changes occur each month
Over 20,000 CLI commands are issued and scrapped every five minutes
Over 4 million lines of configuration files are under management at all times
This all means that today’s networks are not equipped to deal with the demands of digitization. When you combine DevOps with networking, the result is Cloud Scale.
Cloud Scale Networking Operations
- SW modularity & extensibility: ability to install some specific SW packages only, asynchronous software upgrade (no need to go through a full SW release qualification to benefit from new features), application hosting
- Automation: enhanced device onboarding through the use of Automated Boot & Auto-provisioning, extensive Data Model support
- Visibility & control: streaming Telemetry to get near real-time, fine-grained visibility into the network and Application Engineered Routing to get ultimate control over network optimization

## Slide 5: Cisco Evolved IOS XR Innovations Designed for Operational Fit
Software Modularity and Extensibility
Service Agility
Open Innovation
Visibility and Control
Application Engineered Routing
Telemetry
Visibility
Control
Automation
Automated Boot &
Auto-provisioning
Data Model Driven APIs
Third-party Agents Support
Application
Hosting
Docker
Linux Container
Extensibility
Asynchronous Upgrade
Modularity
Granular packaging
Operational Efficiency
Simplification
Better Customer Experience
Notes: To ensure operations meet the requirements of Cloud Scale Networking, Cisco is announcing a set of IOS XR innovations.
These innovations have been designed to ensure networking platforms can be easily integrated into Software Tool chains, that have been developed by Cloud Scale providers. These tool chains are key for them to achieve very high-level of Operational Efficiency.
Software Modularity & Extensibility
- Asynchronous Software Upgrade
- Granular packaging
- Application Hosting
This gives customers agility for new services, simplification of software release management, and open innovation to add new applications
Automation
- Automated Boot
- Auto-provisioning
- Data Model Driven APIs
- Support for 3rd-party agents
This drives better operational efficiency.
Visibility & Control
- Telemetry
- Application Engineered Routing
These capabilities enable more efficient performance as service providers can run their networks at much higher utilization rates with full visibility into resources, better SLAs, and ultimately a better customer experience.
Let’s take a closer look

## Slide 6: iPXE

## Slide 7: IOS-XR 6.X Boot Process - iPXE
All NCS routers are equipped with a UEFI 64-bit Firmware (aka BIOS).
Supports initial booting from USB drive or iPXE.
iPXE is an open source boot firmware.
Fully backward compatible with PXE with several enhancements.
  Boot from a web server via HTTP.
  Control the boot process with scripts and menus.
  DNS support.
iPXE is supported on the management interfaces.
Supports both IPv4 and IPv6.

## Slide 8: IOS-XR Boot Process with iPXE

## Slide 9: iPXE DHCP Server Configuration
######### Network 172.30.12.0/24 ################
shared-network 172-30-12-0 {
subnet 172.30.12.0 netmask 255.255.255.0 {
option subnet-mask 255.255.255.0;
option broadcast-address 172.30.12.255;
option routers 172.30.12.1;
option domain-name-servers 172.30.0.25;
option domain-name "cisco.local";
}
####### Pool #########
pool {
range 172.30.12.10 172.30.12.100;
next-server 172.30.0.22;
if exists user-class and option user-class = "iPXE" {
filename = "http://172.30.0.22/ncs5k-mini-4";
} else if exists user-class and option user-class = "exr-config" {
filename = "http://172.30.0.22/scripts/ncs-ztp.sh";
}
Option 77
Option 77

## Slide 10: DHCP Server Configuration (Mac Address)
######## Hosts #########
host ncs-5001-a {
hardware ethernet c4:72:95:a7:ef:c2;
if exists user-class and option user-class = "iPXE" {
filename = "http://172.30.0.22/ncs5k-mini-1";
}
fixed-address 172.30.12.50;
}
Simple Matching on the Mac Address inside the DHCP Pool definition

## Slide 11: DHCP Server Configuration (option 60)
Option 60 “vendor-class-identifier” Identify 4 elements separated by columns.
Example: PXEClient:Arch:00009:UNDI:003010:PID:NCS-5001
  Type of client: e.g.: PXEClient
  System Architecture (Arch): e.g.: 00009 Identify an EFI system using a x86-64 CPU
  Universal Network Driver Interface (UNDI): e.g.: 003010 (first 3 octets identify the major version and last 3 octets identify the minor version)
  Product Identifier (PID): e.g.: NCS-5001
Inside the DHCP Server we define a class that match partially option 60
######### Class #########
class "ncs-5k" {
match if substring (option vendor-class-identifier, 0, 9) = "PXEClient";
if substring (option vendor-class-identifier, 37, 6) = "NCS-50" {
filename = "http://172.30.0.22/ncs5k-mini-3";
}
}
1
2
3
4

## Slide 12: DHCP Server Configuration (option 61)
Option 61 ”dhcp-client-identifier“ contains the Serial Number of the device.
Serial Number is written on the package
######## Hosts #########
host ncs-5001-b {
option dhcp-client-identifier "FOC1947R144";
if exists user-class and option user-class = "iPXE" {
filename = "http://172.30.0.22/ncs5k-mini-2";
}
fixed-address 172.30.12.52;
}

## Slide 13: Dynamic URL
The URL provided by the DHCP server does not have to be a static. For example, you could direct iPXE to boot from the URL
http://172.30.0.22/boot.php?mac=${net0/mac}&product=${product:uristring}&serial=${serial:uristring}
Which would expand to a URL such as:
http://172.30.0.22/boot.php?mac=c4:72:95:a7:ef:c0&product=NCS5001&serial=FOC1947R143
The boot.php program running on the web server could dynamically generate a script based on the information provided in the URL.
<?php
header ( "Content-type: text/plain" );
echo "#!ipxe \n";
echo "set myURL http://172.30.0.22/Cisco/NCS/NCS5001/FOC1947R143 \n";
echo "boot myURL \n";
?>

## Slide 14: iPXE Scripting and Chainloading
Chainloading is the capability to jump from one boot statement to another.
Using chainloading and the embedded scripting capability of iPXE we can have a very detail and complex selection mechanism for the boot image.
Chainloading remove the need to create DHCP host definition
Agnostic IPv4 or IPv6

## Slide 15: Chainloading Flow of Operations

## Slide 16: Demo

## Slide 17: Chainloading Example
!ipxe
# Global variables used by all other iPXE scripts
chain --autofree boot.ipxe.cfg ||
# Boot <boot-url>/<boot-dir>/hostname-<hostname>.ipxe
# if hostname DHCP variable is set and script is present
isset ${hostname} && chain --replace --autofree ${boot-dir}hostname-${hostname}.ipxe ||
# Boot <boot-url>/<boot-dir>/uuid-<UUID>.ipxe
# if SMBIOS UUID variable is set and script is present (not usable see CSCuz28164)
isset ${uuid} && chain --replace --autofree ${boot-dir}uuid-${uuid}.ipxe ||
# Boot <boot-url>/<boot-dir>/mac-010203040506.ipxe if script is present
chain --replace --autofree ${boot-dir}mac-${mac:hexraw}.ipxe ||
# Boot <boot-url>/<boot-dir>/serial-FOC1947R143.ipxe if script is present
isset ${serial} && chain --replace --autofree ${boot-dir}serial-${serial}.ipxe ||
# Boot <boot-url>/<boot-dir>/pid-<product>.ipxe if script is present
isset ${product} && chain --replace --autofree ${boot-dir}pid-${product}.ipxe ||
# Boot <boot-url>/menu.ipxe script if all other options have been exhausted
chain --replace --autofree ${menu-url} ||
chain --replace --autofree ${menu-url6} ||

## Slide 18: Chainloading Example
#!ipxe
echo
echo Booting NCS5K Mini ISO 6.0.0 from ISO for ${initiator}
chain --replace --autofree ${boot-url}ncs5k-mini-x.iso-6.0.0 ||
chain --replace --autofree ${boot-url6}ncs5k-mini-x.iso-6.0.0
Example: serial-FOC1947R143.ipxe

## Slide 19: Chainloading Example
iPXE> autoboot net0 <- autoboot from the mgmt interface
net0: c4:72:95:a7:ef:c0 using dh8900cc on PCI01:00.1 (open)
[Link:up, TX:108 TXE:0 RX:5188624 RXE:5186887]
Configuring (net0 c4:72:95:a7:ef:c0).......... Ok
net0: fe80::c672:95ff:fea7:efc0/64
net0: fd:30:12::1124/64 gw fe80::fa72:eaff:fe8b:ce80 <- ipv6 statefull address assignment
Filename: http://[fd:30::172:30:0:22]/boot.ipxe <- ipv6 boot URI from DHCPv6 http://[fd:30::172:30:0:22]/boot.ipxe... ok <- boot script is downloaded
/boot.ipxe.cfg... ok <- boot variable are chained
/ipxe/uuid-03000200-0400-0500-0006-000700080009.ipxe No such file or directory (http://ipxe.org/2d0c618e)
/ipxe/mac-c47295a7efc0.ipxe... No such file or directory (http://ipxe.org/2d0c618e)
/ipxe/serial-FOC1947R143.ipxe... No such file or directory (http://ipxe.org/2d0c618e)
/ipxe/pid-NCS-5001.ipxe... No such file or directory (http://ipxe.org/2d0c618e)
http://172.30.0.22/menu.ipxe... Network unreachable (http://ipxe.org/280a6090)
http://[fd:30::172:30:0:22]/menu.ipxe... ok <- boot menu is executed

## Slide 20: ZTP

## Slide 21: What is ZTP?
“ZERO” touch provisioning.
A collection of IOS-XR scripts scheduled from processmgr.
Invoked at the end of the boot process
Executed if the system does not have a valid username.
Uses DHCP to request a script or a configuration file.
Scripts are shell scripts (Python support is being added)
Can use shell commands and Linux tools.
Helper functions (ztp_helper.sh) to facilitate access to IOS-XR.

## Slide 22: How does it works ?
If no username is configured, ztp.sh forks a DHCP client (dhclient) on mgmt interface
dhclient starts a timer waiting for a response from the DHCP server.
If DHCP response has 'filename' (option 67), ZTP framework downloads it
If downloaded file is not ASCII text, ZTP will remove the file and exit
First line of the text file should contain following string:
Configuration file: !! IOS XR
Script file: #!/bin/bash or #!/bin/sh
ZTP either applies the configuration, or execute the script and quit

## Slide 23: ZTP Flow of Operations
HTTP SERVER
DHCP SERVER
DHCP Response
IP address
Next-server
Filename=http://<http-srv>/script.sh
or
Filename=http://<http-srv>/config.txt
script.sh
config.txt
Apply config
Execute script
Additional
Scripts
Packages, etc…
Username
configured
DHCP Request
1
GET script-SN.sh or config-SN.txt
2
GET scripts/pkg/conf
3
ZTP start
Start DHCP Client
ZTP
end
Y
Option 67 or 59
ZTP
end
N
Download
Text file
< 100 MB
Delete file
End ZTP
N
config
or
script
Delete file
End ZTP
N
Download
config
script

## Slide 24: IPv4 DHCP Options
Option | Description | Details
77 | user-class | Identify the type of applications. Eg: “iPXE” to identify iPXE client or exr-config to identify ZTP client
61 | dhcp-client-identifier | Chassis Serial number
67 | boot-file | Bootfile Name : ISO, Config or Script
60 | vendor-class-identifier | Used by DHCP clients to optionally identify the vendor type and configuration of a DHCP client. Servers that respond should only use option 43 to return the vendor-specific information to the client. PnP uses 43 to send PnP server info

## Slide 25: IPv6 DHCP Options
Option | Description | Details
15 | dhcp6.user-class | Identify the type of applications. Eg: “iPXE” to identify iPXE client or exr-config to identify ZTP client
1 | client-identifier | Chassis Serial number
59 | dhcp6.bootfile-url | Bootfile Name : ISO, Config or Script
16 | vendor-class-identifier | Used by DHCP clients to optionally identify the vendor type and configuration of a DHCP client. Servers that respond should only use option 43 to return the vendor-specific information to the client. In PnP uses 43 to send PnP server info
60 | dhcp6.bootfile-parameter | required to be present but not in use.

## Slide 26: Sample dhcpd.conf
ZTP requires operator to pre-map physical entity (router chassis) and its configuration. Chassis serial number can be used to uniquely identify the device
host asr9k-01-rsp0 {
fixed-address 1.83.55.171;
option dhcp-client-identifier "FOX1739G951"; -> DHCP 61
if exists user-class and option user-class = "iPXE" { -> DHCP 77
filename "http://172.30.0.22/iso/asr9k-full-x64.iso"; -> DHCP 67
} else {
# Auto-provision request, script/config
filename "http://172.30.0.22/config/FOX1739G951.config";
}
}

## Slide 27: ZTP Feature Support
IOS-XR 6.0.1
  Initial support for bootstrapping.
  ZTP supported only on Management port
  ztp_helper.sh with some simple utilities (xrcmd, etc.)
IOS-XR 6.1.3
  Customer scripts now run inside global-vrf namespace
  Exec mode cli added:
    ZTP initiate / breakout / terminate
  Configure mode cli added:
    ZTP bootscript
    ztp_helper.sh extensions

## Slide 28: ZTP XR exec mode CLI
ztp initiate
  Invokes a new ZTP DHCP session
  Logs will go to the console and /disk0:/ztp/ztp.log
ztp terminate
  Terminates any ZTP session in progress
ztp breakout
  NCS5000/NCS5500 only, performs 4x10 breakout detection
ztp clean
  Removes all ZTP files saved on disk
New CLI added, help customers who want to provision their routers in stages:
RP/0/RP0/CPU0:bob#ztp ?
breakout Invoke breakout interface detection
clean Remove all ZTP logs and temporary files.
initiate Forceably inititate the ZTP, ignoring username configuration
terminate Terminate all existing ZTP processes

## Slide 29: ZTP Initiate
Manually invoke ZTP (including DHCP request)
Bypass the username check.
Can be executed on Data Port
RP/0/RP0/CPU0:bob#ztp initiate ?
apply XR configuration commands to apply
breakout Invoke platform breakout interface detection
dataport Send DHCP requests on all ADMIN UP physical LC interfaces
debug Run with additional logging to the console
dhcp4 Send only DHCP IPv4 requests
dhcp4-client-identifier Override default dhcp-client-identifier
dhcp6 Send only DHCP IPv6 requests
dhcp6-client-id Override default dhcp6-client-id
dscp DSCP/Prec Value
hostname XR hostname to set
interface Send DHCP requests only on the given interface
management Send DHCP requests on the platforms management interf ace
noprompt Run without prompting
verbose Run with logging to the console
<cr>

## Slide 30: ZTP breakout
RP/0/RP0/CPU0:bob#ztp breakout debug verbose
RP/0/RP0/CPU0:bob#ztp initiate datport debug verbose
Invoke ZTP? (this may change your configuration) [confirm] [y/n] :
Performs a 4x10 breakout detection on all 40 Gig interfaces.
If no link is detected on any of the 4x10Gig, ports remain in 40Gig mode.
The subcommand “nosignal-stay-in-breakout-mode” forces the port in breakout mode even if no link is detected but places the interfaces in shutdown mode.
The subcommand “nosignal-stay-in-state-noshut” will leave the port in breakout mode but will place the four 10Gig in no shutdown mode.
The command “ztp breakout” may not be supported on the ASR9K routers.

## Slide 31: ZTP bootstrap CLI
Some customers want a hardcoded script to run on boot each boot
This will run as soon as possible on boot (but 3rd party may not be setup)
Whereas this will run once IP routing is enabled in 3rd party:
linux$ chmod +x /disk0:/onboot_early
linux$ cat /disk0:/onboot_early
source /pkg/bin/ztp_helper.sh
echo onboot_early running > /dev/console
xrcmd "show running”
ztp
bootscript /disk0:/onboot
bootscript preip /disk0:/onboot_early
!
linux$ chmod +x /disk0:/onboot
linux$ cat /disk0:/onboot
source /pkg/bin/ztp_helper.sh
echo onboot running > /dev/console
ifconfig
xrcmd “ztp initiate debug verbose noprompt”r

## Slide 32: ZTP bootstrap CLI Example
#!/bin/bash exec &> /dev/console # send logs to console
source /pkg/bin/ztp_helper.sh
# If we want to only run one time:
xrcmd "show running" | grep -q myhostname
if [[ $? -eq 0 ]]; then
echo Already configured
fi
# Set the hostname
cat >/tmp/config <<%%
!! XR config example
hostname myhostname
%%
xrapply /tmp/config
#
# Force an invoke of ZTP again. If there was a username normally it would not run. This forces it.
# Kill off ztp if it is running already and suppress errors to the console when ztp runs below and
# cleans up xrcmd that invokes it. ztp will continue to run however.
#
xrcmd "ztp terminate noprompt" 2>/dev/null
xrcmd "ztp initiate noprompt" 2>/dev/null

## Slide 33: Functions in ztp_helper.sh
ztp_helper.sh provides simple tools to access XR functionality.
Must be sourced inside the customer script
(Note all scripts run in the XR namespace and this is hidden from the customer to make scripting simpler)
xrcmd:
  Runs an IOS-XR exec command
if [[ -z $(xrcmd "show crypto key mypubkey rsa") ]]; then
echo "1024" | xrcmd "crypto key generate rsa"
else
echo -ne "yes\n 1024\n" | xrcmd "crypto key generate rsa"
fi

## Slide 34: Functions in ztp_helper.sh
xrapply
  Applies the block of configuration, specified in a file:
xrapply_with_reason
  As above, but specifies a reason for commit history tracking:
cat >/tmp/config <<%%
!! XR config example
hostname mars
%%
xrapply /tmp/config
cat >/tmp/config <<%%
!! XR config example
hostname saturn
%%
xrapply_with_reason "this is an important name change" /tmp/config

## Slide 35: Functions in ztp_helper.sh
xrapply_string
Applies a block of configuration specified in a string.
Use “\n” to delimit line of configuration statement.
xrapply_string_with_reason
  As above, but specifies a reason for commit history tracking:
xrapply_string "hostname pluto\ninterface GigabitEthernet0/0/0/0\nipv4 address 1.2.3.44 255.255.255.0\n”
xrapply_string_with_reason ”system renamed" "hostname venus\n interface GigabitEthernet0/0/0/0\n ipv4 address 1.2.3.44 255.255.255.0\n”

## Slide 36: Demo

## Slide 37: ZTP logging
ZTP logging has been enhanced significantly in IOS-XR 6.1.1:
ios-xr# bash
$ cd /disk0:/ztp/
$ cat ztp.log # lots of logs....
venus:~/ztp]$grep State ztp.log
(Global VRF NS ) Mon Jun ... (/pkg/bin/ztp.sh) : State change to IS_STARTING
(Global VRF NS, eth0) Mon Jun ... (/pkg/etc/dhclient-exit-hooks.ztp) : State change to IS_DOWNLOADING_START
(Global VRF NS, eth0) Mon Jun ... (/pkg/etc/dhclient-exit-hooks.ztp) : State change to IS_DOWNLOADING_END
(Global VRF NS, eth0) Mon Jun ... (/pkg/etc/dhclient-exit-hooks.ztp) : State change to IS_APPLYING_CONFIG
(Global VRF NS, eth0) Mon Jun ... (/pkg/etc/dhclient-exit-hooks.ztp) : State change to IS_COMPLETE
venus:~/ztp]$grep env ztp.log
+ (dhclient env) requested_host_name=1
+ (dhclient env) new_domain_name=cisco.com
+ (dhclient env) new_subnet_mask=255.255.255.0
...
+ (dhclient env) new_routers=10.57.1.1
+ (dhclient env) ztp_interface=eth0
+ (dhclient env) new_domain_name_servers=64.102.6.247
+ (dhclient env) new_broadcast_address=10.57.1.255
+ (dhclient env) new_filename=http://10.57.1.1:8080/node1-mgmt.sh
e.g. state transitions during ZTP
e.g. what we got back from the DHCP server

## Slide 38: ZTP logging
Old logs are now preserved, along with timestamps of state transitions
Also customer configuration script logs from DHCP:
[router:~/ztp]$ls -la old_logs/
-rw-r--r-- 1 root root 45820 Jun 27 18:59 ztp.log.Mon_Jun_27_at_19_05
[router:~/ztp]$ls -la state/
-rw-r--r-- 1 root root 6 Jun 27 19:05 state_is_applying_config
-rw-r--r-- 1 root root 6 Jun 27 19:06 state_is_complete
-rw-r--r-- 1 root root 6 Jun 27 19:06 state_is_complete.v4
-rw-r--r-- 1 root root 6 Jun 27 19:05 state_is_downloading_end_config
-rw-r--r-- 1 root root 6 Jun 27 19:05 state_is_downloading_start_config
-rw-r--r-- 1 root root 5 Jun 27 18:55 state_is_restarting
-rw-r--r-- 1 root root 6 Jun 27 19:05 state_is_starting
[router:~/ztp]$ls -la old_logs/
-rw-r--r-- 1 root root 45820 Jun 27 18:59 ztp.log.Mon_Jun_27_at_19_05
[router:~/ztp]$ls -la customer/
-rwxr-xr-x 1 root root 1167 Jun 27 19:05 config.applied
-rwxr-xr-x 1 root root 1167 Jun 27 19:05 config.candidate.original
-rw-r--r-- 1 root root 3807 Jun 27 19:06 customer.script.alltime.log
-rw-r--r-- 1 root root 3705 Jun 27 19:06 customer.script.log

## Slide 39: Debug ZTP
All framework log will be saved under /disk0:/ztp.
You may be able to figure out issue by looking at the file, so I would recommend you to go through those files first. Output is relatively short.
If triage request has to be filed, please collect all the files inside /disk0:/ztp
DHCP clinet config - /etc/dhcp/dhclient.conf.ztp

## Slide 40: Golden ISO

## Slide 41: ISO Customization : Golden ISO
Boot ISO
Install PKG/SMUs
Reboot
Apply Configuration
Open ISO
Install PKG/SMUs
Apply Configuration
gisobuild.py
Golden ISO
  iPXE
  USB
  System Upgrade
Notes: Caveats:
No Async package support for building and booting Golden ISO.
No XR config verification by offline Golden ISO build tool.
Install upgrade with giso is not supported
Renaming and then installation of GISO is not supported

## Slide 42: Want to know more ?
IOS-XR Documentation, blogs, tutorial, etc ..
  https://xrdocs.github.io/
IPXE Deep Dive
  https://xrdocs.github.io/software-management/tutorials/2016-07-27-ipxe-deep-dive/
Working with ZTP
  https://xrdocs.github.io/software-management/tutorials/2016-08-26-working-with-ztp/
Software Management blogs, tutorial, etc …
  https://xrdocs.github.io/software-management/